## Slide 1: Evaluation of Thermal Contact Conductance in HL-LHC Collimator Jaws: Experimental Tests and Multiphysics Simulations
L. Puddu EN/MME
With the contribution of C. Accettura EN/MME, F. Carra EN/MME, R. Viscardi SY/STI
15th HL-LHC collaboration meeting, CERN, 29 September – 2 October 2025

## Slide 2: Outline
Introduction and motivation
Workflow
Simulations:
  Evaluation of the TCC
  Operational scenarios
Final correlation
Conclusions

## Slide 3: Introduction and motivation
The HL-LHC project requires the design of new collimators able to withstand high thermal loads.
Efficient cooling depends on the Thermal Contact Conductance (TCC) between components.
TCC strongly affects both temperature rise and jaw deformation, which are subject to strict operational limits.
Direct measurement of TCC is challenging because of the transient, non-linear and multiphysics nature of the problem.
water
cooling pipe interface
Heat
Empirical correlation for thermal contact conductance

## Slide 4: Introduction and motivation
Dedicated test bench developed by SY-STI, using the characteristic time (τ) as an indirect indicator measured on each pre-series and series jaw:
Hot water at 70 °C is circulated through the cooling channels, while thermocouples placed on the active surface of the blocks record the temperature evolution.
The characteristic time (τ) is defined as the time required for the thermocouples to measure a temperature increase from 35 °C to 55 °C.
Chart: Time [s]
 | 35 | 35
0 200 | 55 | 55
In parallel, multiphysics simulations (thermal, structural, fluid-dynamic) were used to link the experimental test and the functional specifications.
Correlating τ and TCC provides a powerful predictive method:
  speeds up production,
  avoids repeating simulations for each test,
  defines acceptable τ values compatible with operational requirements.
Courtesy of D. Baillard

## Slide 5: Outline
Introduction and motivation
Workflow
Simulations:
  Evaluation of the TCC
  Operational scenarios
Final correlation
Conclusions

## Slide 6: Workflow
Experimental TCC test
Numerical simulations
How to link TCC experimental data to functional specifications:

## Slide 7: Workflow
Experimental TCC test
Numerical simulations
How to link TCC experimental data to functional specifications:

## Slide 8: Workflow
Experimental TCC test
Numerical simulations
TCC
How to link TCC experimental data to functional specifications:

## Slide 9: Workflow
Experimental TCC test
Numerical simulations
TCC
How to link TCC experimental data to functional specifications:
To be checked

## Slide 10: Workflow
Experimental TCC test
Numerical simulations
Functional specification
TCC
Deformation
Temperature
How to link TCC experimental data to functional specifications:
To be checked
To be compared with the limits imposed by

## Slide 11: Workflow
Experimental TCC test
Functional specification
TCC
Deformation
Temperature
How to link TCC experimental data to functional specifications:
To be checked
TCC test bench (COMSOL)
Operational Condition (ANSYS)
2 different cases to be simulated:
To be compared with the limits imposed by

## Slide 12: Workflow
Experimental TCC test
Numerical simulations
Functional specification
TCC
Deformation
Temperature
How to link TCC experimental data to functional specifications:
To be checked
To be compared with the limits imposed by
Chart: Maximum deformation in operational condition as a function of characteristic time
| 18.149999999999999 | 20.55 | 23.262499999999999 | 31.3 | 39.287500000000001 | 50.037499999999994
 | 8.6658 | 9.4938 | 10.4129 | 13.1741 | 16.842 | 26.3613
During production:
TCC [kW/m2/K]

## Slide 13: Outline
Introduction and motivation
Workflow
Simulations:
  Evaluation of the TCC
  Operational scenarios
Final correlation
Conclusions

## Slide 14: Evaluation of the TCC Benchmarking of test bench
Chart: Characteristic time as a function of the percentage of the theoretical value of TCC for brazing
| 1000 | 50 | 25 | 10 | 5 | 2.5
 | 18.15 | 20.55 | 23.2625 | 31.3 | 39.2875 | 50.0375
TCC
𝜏
COMSOL multiphysics model coupling fluid-dynamics & thermal analysis:
Transient problem.
Input: TCC value.
Output: characteristic time (τ).
Correlation established between TCC and τ.
t=0 s
t=14 s
t=20 s
t=45 s
Chart: Comparison Water cooling system

## Slide 15: Operational scenarios
TCC
DEFORMATION
Power deposition
(FLUKA MAP)
TEMPERATURE
Chart: Maximum temperature and deformation in operational condition for different values of TCC for brazing
| 2.5 | 5 | 10 | 25 | 50 | 1000
temp | 38.193 | 34.379 | 32.416 | 31.209 | 30.799 | 30.381
The operational case simulations are divided into thermal and structural simulations.
Technical specifications: define the maximum admissible deformation (most critical) and temperature.
Outcome: determination of the maximum acceptable TCC in agreement with the limits from the technical specifications
Chart: Brazing TCC [kW/m2/K]
| 2.5 | 5 | 10 | 25 | 50 | 1000
def | 26.3613 | 16.842 | 13.1741 | 10.4129 | 9.4938 | 8.6658
Deformation perpendicular to the beam [mm]
Temperature [°C]

## Slide 16: Outline
Introduction and motivation
Workflow
Simulations:
  Evaluation of the TCC
  Operational scenarios
Final correlation
Conclusions

## Slide 17: Correlation
By combining the results, the relationship between the limits from the functional specification and the characteristic time (τ) is obtained.
Allows setting a τ limit for each collimator family.
We verified that the temperature is always ok and for this reason the driving parameter limiting the TCC is the maximum deformation.
Chart: Maximum deformation in operational condition as a function of characteristic time
| 18.149999999999999 | 20.55 | 23.262499999999999 | 31.3 | 39.287500000000001 | 50.037499999999994
 | 8.6658 | 9.4938 | 10.4129 | 13.1741 | 16.842 | 26.3613
TCC [kW/m2/K]

## Slide 18: Correlation
Collimator | Thermo-mechanical deflection* (um) | Self-weight deflection (um) | Geometrical tolerance (um) | Total deflection in steady-state operation (um) | Jaw type | Comments, References
TCSG | 75 | 30 | 40 | 145 | Brazed | Design case: skew TCSG.A6R7 [4]
TCSP | 50 | 30 | 40 | 120 | Brazed | [5]
TCSPM (MoGr) | 55 | 30 | 40 | 125 | Brazed | Design case: skew TCSG.A6R7 [4]. However: in that slot, a CFC TCSG is finally kept. Therefore, this is a pessimistic assumption for MoGr TCSPMs
TCSPM (graphite) | 15 | 30 | 40 | 85 | Brazed | Design case: TCSPMB4R7 [6]
TCTW | 65 | 30 | 40 | 135 | Brazed | When wire is off [7] Attention: when wire ON @350A à total deflection goes above 150 um
TCTP | 50 | 30 | 40 | 120 | Brazed | [2]
TCLPX | 15 | 0 | 100 | 115 | Bolted | [8]
TCLP** | 15 | 0 | 50 | 65 | Bolted | For TCLP5 (most loaded TCLP) [1],[9]
TCTPXH | <10 | 0 | 100 | 100 | Bolted | Thermomech. deflection considered negligible, as thermal loads are a factor 5 smaller than TCLP’s [1],[9]
TCTPXV | <10 | 30 | 100 | 130 | Bolted | Thermomech. deflection considered negligible, as thermal loads are a factor 7 smaller than TCLP’s [1],[9]
TCTPM** | <10 | 0 | 50 | 50 | Bolted | Thermomech. deflection considered negligible, as thermal loads are a factor 7 smaller than TCLP’s [1],[9]
F. Carra, ‘LHC Collimators: total jaw deflections in operation’, EDMS n. 2839280

## Slide 19: Outline
Introduction and motivation
Workflow
Simulations:
  Evaluation of the TCC
  Operational scenarios
Final correlation
Conclusions

## Slide 20: Conclusions
The proposed method is an effective tool to assess the quality of collimator thermal contacts during production (~70 jaws currently being manufactured).
It provides a practical link between experimental measurements and operational requirements, enabling the definition of acceptance criteria consistent with functional specifications.
Test bench results have shown good stability and reproducibility, with an uncertainty of about ±2 s in the characteristic time (τ).
Combining experiments and multiphysics simulations offers a reliable framework to ensure adequate thermal contacts and safe HL-LHC operation.

## Slide 21: Thanks for your attention!