## Slide 1
Quantum Communication Experiments at CERN
QuIC Business Community Summit 25/11/2025
Annick Teepe

## Slide 2
News !

## Slide 3
Main challenges in large-scale quantum networks
      Photon losses
      Synchronisation
      Variable transmission conditions
         transmission time (length changes)
         polarisation state (vibrations/other)
      Work in low-loss wavelength bands
      ( Telecom C-band & O-band )
Transmitting quantum information via photons over long optical fiber links
Notes: Espeically losses of photons in visible range are great
Single photon wavepackets can be as short as picoseconds, high-accuracy sync is required
Changes in environment, such as temperature increase which results in length increase

## Slide 4
Main challenges in large-scale quantum networks
      Photon losses
      Synchronisation
      Variable transmission conditions
         transmission time (length changes)
         polarisation state (vibrations/other)
Transmitting quantum information via photons over long optical fiber links
multiplexer
Single photons
      Quantum-Classical Coexistence
Notes: White Rabbit is ethernet based , classical optical two-way time transfer protocol, providing sub-ns synchronisation accuracy and picosecond-scale precision
Same fiber = Same environmental conditions
 WR for synchronisation & as probe !

## Slide 5
Today: Quantum Networks at CERN
Source
White Rabbit Switch
DWDM
DWDM
White Rabbit Switch
Detection
Alice
Bob
15xx nm
15xx nm
1320 nm
1320 nm
TimeTagger
TimeTagger
      Entanglement distribution of polarisation photon pairs co-existing with White Rabbit synchronization signals on the same optical fiber
Detection
785 nm
Notes: 2 node network

## Slide 6
Start at the beginning
Setting up quantum networks lab from scratch!
Notes: Start at the beginning… An empty room.
Procuring, arranging , installing and testing all equipment
Interlock installation

## Slide 7
Source and Detectors

## Slide 8
Demonstrating entanglement distribution
Measuring coincidence counts as a function of detection time difference in different polarisation bases
Coincidences
Laser
Fiber coupler
½ waveplate
Fiber coupler
Fiber coupler
Polarising beamsplitter
Alice
Bob
To detectors

## Slide 9
Demonstrating entanglement distribution
Measuring coincidence counts as a function of detection time difference
Coincidences

## Slide 10
Demonstrating entanglement distribution
Extracting coincidence peak value for different half-wave plate positions
Laser
Fiber coupler
Bob @ [0 °, 22.5 °, 45 °, 67.5 ° ]
Fiber coupler
Fiber coupler
Polarising beamsplitter
Alice
Bob
To detectors
Alice in range 0 – 180°

## Slide 11
Demonstrating entanglement distribution
CHSH test
Plot coincidence peak value as a function of waveplate position + calculate
5 km of fiberspool
Average visibility
V = 0.97 +/- 0.02
CHSH S-parameter
S = 2.70 +/- 0.04
Maximum S = 2√2 ≈ 2.83
Notes: Entanglement fringe visibility

## Slide 12
Fiber link (Loop-Back configuration)
29.5km fiber link from lab to CMS site and back
10.94 dB of attenuation (8% transmittance)

## Slide 13
Demonstrating entanglement distribution
CHSH test
29.5 km of real fiber
Average visibility
V = 0.85 +/- 0.01
CHSH S-parameter
S = 2.50 +/- 0.05
5 km of fiberspool
Average visibility
V = 0.97 +/- 0.02
CHSH S-parameter
S = 2.70 +/- 0.04

## Slide 14
  LOOPBACK (Alice & Bob @ CERN)
  Quantum-classical coexistence experiments
    - monitor WR parameters
    - track polarisation state of WR light
    Explore effects of different WR wavelengths and powers
    - Visibilities and S-parameters (CHSH test)
    - Quantum state (full tomography)
    TWO-SITE (Alice @ CERN, Bob @ Unige)
Outlook
Demonstrate metropolitan scale entanglement distribution with WR multiplexed on the same fiber

## Slide 15
Quantum Networks at CERN
Source
White Rabbit Switch
DWDM
DWDM
White Rabbit Switch
Detection
Alice
Bob
15xx nm
15xx nm
1320 nm
1320 nm
TimeTagger
TimeTagger
      Entanglement distribution of polarisation photon pairs co-existing with White Rabbit synchronization signals on the same optical fiber
Detection
785 nm
Notes: 2 node network

## Slide 16
Questions?