## Slide 1: Performance studies of small Straw Tracker prototypes
Speaker: Margarita Banchshikova
Supervisors: Katerina Kuznetsova, Giuseppe Pezzulo
Date: 05/08/2025

## Slide 2: Content
Introduction
Different types of tracking detectors
Scintillating fiber trackers
Solid state detectors
Gaseous detectors
July Test Beam Data Analysis
Setup characteristics
MicroMegas data analysis
Timepix data analysis
MWPC tests
Setup
Gain value
Conclusion

## Slide 3: Introduction
  Objectives:
  to get experience in operation of gas filled detectors and in corresponding data taking and analysis
  to investigate performance of small straw tracker prototypes using muon beam data acquired at SPS H4 beam line in July.
  Tasks:
  Research on different types of tracking detectors.
  Development of data processing technique for StrawTrackerRD setup using April Test Beam data.
  July Test Beam data analysis (MicroMegas, Timepix, Straw Tracker prototype).
  Tests for MWPC detector for IRRAD.

## Slide 4: Different types of tracking detectors
  Scintillating
  trackers
  Solid-state
  detectors
  Gaseous
  detectors
Fiber trackers
Pixel/strip trackers
The light is collected by SiPM/ PMT
Compact and fast trackers
High spatial resolution
Compact
Expensive
High spatial resolution
Compact
Can be of large area
Detectors based on ionization loses of charged particles
MWPC
Drift Chambers
Straw
TPC
MM
GEM
Charged particles excite molecules of scintillators -> photons collection

## Slide 5: Gaseous detectors
MWPC
2 cathode planes and parallel array of anode wires.
Electrons drift toward wires, avalanche near the wire due to high electric field.
Position inferred from wire hit (or cathode strip)
General operating principle: a charged particle traverses a gas volume, producing ion-electron pairs. The electrons drift in the electric field and are amplified near thin wires or meshes, creating a detectable signal.
Drift gap (few mm) and a thin amplification gap (~100 µm) separated by a micromesh.
Electrons drift to mesh, then undergo avalanche near the readout plane.
Gas gain is lower than in MWPC or straw.
Thin cylindrical tubes with central anode wire and cathode wall.
Electrons drift radially to the wire, where amplification occurs.
Coordinate derived from drift time.
MicroMegas
Straw

## Slide 6: Test beam setup
Reference timing:
Scintillators:
Reference time measurements (t0)
Straws:
Ar/CO2: 70/30%.
Prototype 1: diameter – 10 mm.
Prototype 2: diameter – 5, 10, 20 mm.
MicroMegas 3
MicroMegas 2
MicroMegas 4 and 5
Timepix
Straw tracker 2
Straw tracker 1
Scintillator 1
Scintillator 2
MicroMegas 0
Reference tracking:
1. MicroMegas:
Ar/CO2: 93/7%.
Readout: TIGER ASIC.
2. Timepix-4:
Pixel size: 55 um.
Number of pixels: 448 x 512.
Axis | MicroMegas ID
X | MM 0
X | MM 2
X | MM 3
Х (XY) | MM 4
Y (XY) | MM 5

## Slide 7: July Test Beam Analysis. Timepix Detector data
Input number | Purpose | Pixels
1 | Scintillator coincidence | {2,508}, {6,509}, {443,510}, {447,511}
2 | Scintillator 1 | {0,508}, {4,509}, {441,510}, {445,511}
3 | Scintillator 2 | {0,0}, {4,1}, {441,2}, {445,3}
4 | STM-VMM | {2,0}, {6,1}, {443,2}, {447,3}
105
104
103
102
10
1
Digital pixels
Masking digital pixels
105
104
103
102
10
106
0
5
15
25
35
10
20
30
40
Entries
Number of hits

## Slide 8: July Test Beam Analysis. MicroMegas data quality
Axis | MM ID | Readout area, cm2 | Strip pitch, um
X | MM 0 | 3x3 | 250
X | MM 2 | 3x3 | 250
X | MM 3 | 3x3 | 250
Х (XY) | MM 4 | 10x10 | 400
Y (XY) | MM 5 | 10x10 | 400
0 1 2 3 4 5
25
0 1 2 3 4 5
Active detectors amount
Detectors ID
50
75
100
125
150
Entries
50
100
150
200
250
300
Entries
0
0
Correlation: MM 0 and MM 4
X coordinate (MM 4)
X coordinate (MM 0)
50
100
150
200
250
0
0 50 100 150 200 250
Correlation: MM 2 and MM 4
X coordinate (MM 4)
X coordinate (MM 2)
50
100
150
200
250
0
0 50 100 150 200 250
Correlation: MM 3 and MM 4
X coordinate (MM 4)
X coordinate (MM 3)
50
100
150
200
250
0
0 50 100 150 200 250
Correlation: MM 0 and MM 2
X coordinate (MM 2)
X coordinate (MM 0)
50
100
150
200
250
0
0 50 100 150 200 250
175
200
103
103
350
MM planes per event
MM plane ID

## Slide 9: Prompt look at Straw Time vs Reference coordinate (Timepix only)
10 minutes of data tacking
Future tasks:
Tracking with complete reference tracking system
Straw prototype data analysis
Knowledge and Skills Acquired:
PyROOT, Uproot
Basic definitions and concepts of accelerator physics
Timepix, MicroMegas, Straw detectors operation principles and features
Results interpretation
Study to be continued…

## Slide 10: Additional studies: MWPC for Beam Instrumentation
  Goal: to investigate the uniformity of MWPC response.
  Following studies were performed:
  Source 90Sr was moved along different quadrants on Top Plane and Bottom Plane of MWPC.
  Several amount of such “spills” was taken for each quadrant.
  Average signals over “spills” were calculated for each quadrant.
  Charge values (sum) were determined for Vertical and Horizontal profiles of two planes in different quadrants.
  Vertical profile charge values should correspond to Horizontal profile charge values.
  Comparison between value of charge in corresponding quadrants was plotted.
  Problem: at some point fired channel occurred;
  Problem solution: fired channel was masked.

## Slide 11: MWPC tests setup
Q1
Q2
Q3
Q4
Q5
Q6
Q7
Q8
Q9
Q7
Q8
Q9
Q4
Q5
Q6
Q1
Q2
Q3
Bottom plane of BI MWPC with the source on it
Top Plane Map
Bottom Plane Map
Bottom plane of IRRAD MWPC
2250 V, Horizontal profiles for Top plane
IRRAD MWPC
Chart: 
Profile shape with fired channel

## Slide 12: BI MWPC test. Results
Source on the Bottom plane.
Bottom Plane vertical and horizontal profile charge
Applied voltage = 2650 V
Applied voltage = 2250 V
Source on the Top plane.
Top Plane vertical and horizontal profile charge
V charge
H charge
V charge
H charge
V charge
H charge
V charge
H charge
*H – Top plane, V – Bottom plane

## Slide 13: BI MWPC test. Mean values of charge
Applied voltage = 2650 V
Applied voltage = 2250 V
Source on Bottom plane.
Charge mean values
Source on Top plane.
Charge mean values

## Slide 14: IRRAD MWPC test. Results
Source on the Bottom plane. Voltage = 2750 V
Vertical and horizontal profile charge
Source on the Top plane. Voltage = 2750 V
*H – Top plane, V – Bottom plane
Mean values of
Vertical and horizontal profile charge

## Slide 15: Results
The repeatability and symmetry of the profiles indicate correct operation. It is noticeable that at higher voltage, we obtain higher signals — an amplification effect.
It was found that it is necessary to wait some time before starting measurements to obtain proper profiles => chamber needs time to stabilize.
Charge value varies from quadrant to quadrant.
Although coincidence of vertical and horizontal plane charge values in each quadrant was expected, it can be seen that in most cases the situation is not ideal.
Statistical error less than 1%.
Response in different points of MWPC is not the same.
The results will be discussed with our BI colleagues.
Data from IRRAD MWPC was acquired. The analysis will be included in final report.
Knowledge and Skills Acquired
MWPC operation principle.
Data analysis with python.

## Slide 16
I thank my supervisors for their guidance, support, and encouragement throughout this work!
I am grateful to everyone who contributed to this work:
Katerina Kuznetsova
Giuseppe Pezzullo
Federico Ravotti
Aleksandr Lapkin
Sergey Romakhov
Dmitriy Sosnov
Jaroslaw Szumega
And the team!
Acknowledgements

## Slide 17
Thank you for your attention!