## Slide 1: FCC-ee LCC progress LNO section meeting
2025-09-07
M. Jebramcik

## Slide 2: Activities regarding LCC lattice
LCC straight sections are rather “basic”: FODO cells with some beam crossing. No collimation, no injection, promising (but not perfect) for RF
Tackling the issue at two fronts:
Pantaleo the quadrupole distance for the RF requirements and modified the DS for the correct separations. He started working on a collimation section (hopes that one could do momentum cleaning close to the SCRAB in the IPs)
Myself, I have created an LCC branch with Oide’s universal straight section matched into two straights. Idea here is NOT that this is eventually being used in our final design  Allows tests of injection, collimation…
M. Jebramcik
LCC
GHC
Modified LCC
“new” LCC straight

## Slide 3: Matching with transparency conditions
M. Jebramcik
Besides linear optics, matching of Wx, Wy, ddx, sextupole RDTs (locally) + Survey matching with constant k0
960mm separation in straight;
350mm separation start/end of arc.

## Slide 4: DA and MA before and after insertion
M. Jebramcik
LCC
92a 107
LCC
92a 107
Mod.

## Slide 5: A lot of things on the plate
M. Jebramcik
LCC optics files not harmonized at this point in time – LCC non-linear optimization only available in pyAT on Zenodo  Kyriakos is tackling this. In addition, we have to agree on how to share “intermediate” optics versions.
It appears that collimation could improve by quite a bit compared to the GHC. Giacomo had a very basic first look. TCPs could(!) open from X: 9.5 σx  13-14 σx; Y: 50 σy  75-90 σy
Modified arcs: Pantaleo has reduced the number of quadrupole families for ttbar (no release yet). Same procedure for Z might be pending.  Medium term: We will need to provide a “representative” FODO cell (with photon-stopper placement…) to SY-STI
Inner and outer arc still have the same path length  Will chat with Riccardo tomorrow. Want to stick to the LHC concepts here.
SR with quantum is a big problem right now since it also holds back the collimation study  If the DA breakdown is real, then we might end up modifying the doublet? (Pantaleo mentioned current doublet is result of a DA-vs-MA study)
LEIR: Sadly(!), I will take over Felix’s LEIR responsibilities. SY-ABT is looking at some slow extraction from LEIR to a proposed HEARTS experiment (ESPP submission?).

## Slide 6: Thank you for your attention.