## Slide 1
Christiana Staudinger1, Corentin Pueyo2, Luisa Ulrici2, Maha-Deeb Collet3, Pascal Boivin3, Ali Kanso4, Gaylord Machinet4, Maha Chalhoub5, Philippe Bataillard5, Samuel Coussy5, Charles Cartannaz5 , Noémie Dubrac5, Markus Marchhart6, Hannes Pavetits7, Hans-Peter Kaul1, Olivier Duboc1, Johannes Gutleber2
1University of Natural Resources and Life Sciences (BOKU), Vienna, Austria, 2CERN, Geneva, Switzerland,
3University of Applied Sciences of Western Switzerland (HEPIA), Geneva, Switzerland, 4Microhumus, Vandoeuvre-les-Nancy, France, 5French Geological Survey (BRGM), Orléans, France, 6Business Engineering for Control Centers GmbH , Vienna, Austria, 7Pavetits Consultancy, Soral, Switzerland
A platform for developing quality-managed processes for constructing soil from geological excavation materials

## Slide 2: Soils provide important ecosystem services
Natural soils are a non-renewable resource, with an average global geological rate of soil formation1 of 0.01 mm y-1.
The European Commission has defined seven key soil functions as part of its soil protection and environmental policy, which are related to ecosystem services and SDGs as defined by the UN2.
Fundamental soil properties form the basis of soil functions3:
  Chemical: mineralogy, soil organic carbon, pH, EC, cation exchange capacity (CEC), available water and nutrients.
  Physical: texture (sand, silt, clay and coarse fragments), bulk density, temperature, soil porosity and air permeability, hydraulic conductivity and infiltration.
  Biological: activity and abundance of soil biota.
Soil structure and aggregation are key determinants of soil functionality.
1 Banwart et al., 2019, 2 EC, 2006, 3soil parameters assessed in OSL

## Slide 3: Soils provide important ecosystem services
Natural soils are a non-renewable resource, with an average global geological rate of soil formation1 of 0.01 mm y-1.
The European Commission has defined seven key soil functions as part of its soil protection and environmental policy, which are related to ecosystem services and SDGs as defined by the UN2.
Fundamental soil properties form the basis of soil functions3:
  Chemical: mineralogy, soil organic carbon, pH, EC, cation exchange capacity (CEC), available water and nutrients.
  Physical: texture (sand, silt, clay and coarse fragments), bulk density, temperature, soil porosity and air permeability, hydraulic conductivity and infiltration.
  Biological: activity and abundance of soil biota.
Soil structure and aggregation are key determinants of soil functionality.
1 Banwart et al., 2019, 2 EC, 2006, 3soil parameters assessed in OSL, 4 Heckova et al., 2025, 5 Or et al., 2019
Natural and managed soil structure5
µCT scan of soil porespace4
natural
agricultural
For a certain target environment, which soil construction workflows result in a rapid and stable acquisition of soil functionality?

## Slide 4
A collaboration between academia and industry
Site at Cessy provided by CERN (1 ha, France, 2024-2028)
Quality-managed approach to the development of soil construction and monitoring of pedogenic processes during first 4 years  predict future outcomes
Documentation of a process for soil construction from molasse for different use cases and plant species
Optimisation of mixing techniques and inoculation techniques
Pedological study showed heteregeneous anthropogenic soil with 40% of coarse elements, topsoil moderated fertility, poor drainage capacity  Ideal site for the experiment

## Slide 5: Automated field monitoring
ATMOS 41
Atmospheric monitoring station
TEROS 21
Temperature, water potential
TEROS 12
Temperature, bulk EC, moisture
Developed by M. Marchhart/H. Pavetits : OpenSkyView field monitoring system
Cameras
+
Drone imaging of plant cover
+
Manual sampling
+

## Slide 6: A platform to develop soil construction processes
OpenSkyLab, Cessy, France:
Replicated plots: to test for repeatability of soil construction procedure, account for spatial heterogeneity of site.
Plant nursery plots: within plot replication to evaluate which shrub and tree species/genotypes are best adapted to molasse-based soils.
Elevated hedgerows to test whether molasse can be used as a support material for landscape features.
OSL, May 2025
Aim: characterise the gradual acquisition of soil functions in molasse-based constructed soils
 predict the possible reuse of constructed soils in various scenarios
Replicated plots
Elevated hedgerows
Plant nursery plots

## Slide 7: Engineering plant-soil systems in the OSL
The process of engineering plant-soil systems based on molasse excavation materials aims at addressing current and future regional needs and involves two major steps:
1) Habitat creation  designing soils for specific target applications.
  Molasse mixture to optimise soil texture
  Organic matter (compost) addition for enhanced nutrient content, biological activity, physical properties and pH buffering
  +/- clay amendment: locally sourced by-product
  +/- biological amendment: biopile, soil transplant
  +/- granulation method
2) Soil structure management  enhancing early pedogenesis (structure formation) in constructed soils.
Ab-initio (soil) structure generation
Luisa Ulrici

## Slide 8
Management systems to enhance soil structure
  Physiological requirements for chosen plant species
    Alkaline conditions
    Elevated carbonate content
    Low nutrient availability
    Intermittent droughts
  Rationale
  Functional soils are a highly sought-after resource, their development is slow and takes years. This study assesses the impact of different agricultural management practices (perennial versus annual) on the early functionality of constructed soils.
  Expected outcome
  Documented, application-specific soil management processes for accelerated soil structure formation and the closing of nutrient cycles within the first years after installation.
Miscanthus
Cover crop rotation
Perennial wheat
Pasture
perennial
annual

## Slide 9
Multispectral drone imaging
NDVI
orthomosaic
Drone mapping: 30/05/205

## Slide 10: Shapes of hedgerows, benefits and drawbacks
  Definition
  A row of bushes, trees and plants usually growing along a bank bordering a country land or between fields. Size limits for classification depend on country (min 20-25 m length, 1 row of trees to 5 or 25 m width).
  Benefits
  Soil erosion mitigation
  Beneficial microclimate: flood and drought prevention
  Biodiversity: e.g. long-term habitat for wild bees
  Pest control
  Carbon stock: 1 km of hedge stores 600 – 800 kg C for up to 20 years
  Timber, fuel, fruits  local economy, improved self-sufficiency
  Drawbacks
  Cost of installation
  Loss of arable land
  Maintenance costs
  Limited access of heavy machinery
Main functions of hedgerows1
1 Office Français pour la Biodiversité (OFB), 2023, 2 EC, 2023, image credit: Devon Hedge Group, Francois Bourdet.
EU‘s Common Agricultural Policy and national funding programmes2

## Slide 11: Elevated hedgerows in the OSL
  Construction
  Trapezoid cross-sectional area covered by repurposed natural topsoil. Average depth of horizon A in Lac Léman region: 30 cm.
  Plant species
  Ornamental, nectar producing species (plot 40)
  Locally adapted species mixture recommended by the French chamber of agriculture for mitigating pests in arboriculture, horticulture and for field crops (Auxil’haie), supplemented with:
    Legume species (atmospheric N-fixation)
    Species with complementary root traits potentially allowing for root growth across layers.
  Expected outcome
  Propose a landscape feature with variable species composition as a tool to:
  Mitigate erosion and direct nutrient flows
  Enhance ecosystem connectivity
  Increase climate resilience of agroecosystems
Plot 40
Plot 43
Multispectral drone imaging
of hedgerows (NDVI)

## Slide 12: Current state
Vicia faba, 30 days after seeding, presenting functional root nodules, 10 cm max. rooting depth
OSL, Plant nursery plot, May 2025.
Five recipes for molasse-based soils have been developed.
All modalities exhibit so far positive results regarding plant growth (30 days after seeding).
Continuous data acquisition operational, including soil sensor data and drone imaging.
July milestone: first comprehensive soil sampling campaign, visit of 60 soil scientists and practitians

## Slide 13: Conclusions
The OpenSkyLab collaboration aims at:
Developing quality-managed processes for the construction of functional plant-soil systems created from molasse minerals addressing potential regional needs
Demonstrate legal and regulatory compliance
Develop guidelines for optimal soil management
A reuse of molasse material as functionalised soil along roadsides, as support for elevated hedgerows, has potential to valorise important volumes and create beneficial outcomes for the region in terms of biodiversity, climate resilience, regional independence1,2.
The creation of new terrestrial surfaces may contribute to C sequestration and could lead to further agronomic, or forestry uses.
A successfully developed industrial-scale reuse pathway for molasse materials is of value for construction projects beyond the “FCC-region”.
1 Montgomery et al., 2020, 2 OFB, 2023

## Slide 14: Thank you for your attention!
14
This project has received funding from the European Union's Horizon 2020 research and innovation programme agreement No 951754.

## Slide 15: References
15
Banwart, Steven A., et al. Soil functions: connecting earth's critical zone. Annual Review of Earth and Planetary Sciences 47 (2019): 333-359.
European Commission. (2006). Thematic Strategy for Soil Protection.
European Commission. (2023). Approved 28 CAP strategic plans (2023-2027), p. 79.
Haas, Maximilian, et al. Integrated stratigraphic, sedimentological and petrographical evaluation for CERN’s Future Circular Collider subsurface infrastructure (Geneva Basin, Switzerland-France). Swiss Journal of Geosciences 115.1 (2022): 16.
Heckova, P., Koestel, J., Klement, A., Kodesova, R., & Snehota, M. (2025). Soil structure dynamics in constructed Technosols for bioretention cells: X-ray microtomography study. Journal of Soils and Sediments, 25(2), 591-608.
ILF. Feasibility Study Cost, December 2024
Keesstra, Saskia D., et al. The significance of soils and soil science towards realization of the UN sustainable development goals (SDGS). Soil Discussions 2016 (2016): 1-28.
Montgomery, Ian, et al. Hedgerows as ecosystems: service delivery, management, and restoration. Annual Review of Ecology, Evolution, and Systematics 51 (2020): 81-102.
OFB. (2023). L’essentiel sur la haie. Comprendre pour agir.
Or, D., Keller, T., & Schlesinger, W. H. (2021). Natural and managed soil structure: On the fragile scaffolding for soil functioning. Soil and Tillage Research, 208, 104912.
Scalenghe, R., & Ferraris, S. (2009). The first forty years of a Technosol. Pedosphere, 19(1), 40-52.
Stolte, Jannes, et al., eds. Soil threats in Europe. Luxembourg: Publications Office, 2015.

## Slide 16: Selected materials for substrate composition
Molasse
2 different types of molasse,
providing a representative sample of the region’s geology
Compost
Improve physical, chemical, biological properties
Clay
Mineral amendment and test of a novel mixing technique developed at BRGM to form stable soil granulates
Substrate mixes
Biopile
Improve biological activity by using depolluted materials