## Slide 1: CTPPS Roman Pot – Impedance Studies for HL
Leonardo Sito, Benoit Salvant, Joanna Swieszek, Carlo Zannini, C. Antuono, N. Mounet
With the support of:
PPS team: N. Minafra, D. Druzhkin, J. Baechler, J. J. Hollar, M. Deile.
FOS team: G. Breglio, S. Buontempo, F. Fienga, V.R. Marrazzo
101st Impedance Working Group
CERN, Geneva, Switzerland
15 July 2025

## Slide 2: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 3: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 4: CTPPS Roman Pot – What an acronym!
CTPPS Roman Pots
CMS
TOTEM
Precision
Proton
Spectrometer
«Roman» 
Technique used for the first time by CERNRome group in the 70s
A «parasitic» subdetector for:
Proton tracking
Time detection (time-of-arrival)
Beam profile

## Slide 5: CTPPS Roman Pot – What an acronym!
CMS
TOTEM
In the context of forward physics:
Intercept particles that after “collision” have been only slightly deflected
In IP5 the closest detectors are:
Barrell Pixel Tracker
Forward Pixel Tracker
In general:
«Thin» vessel (pots) hosting detectors, electronics and cooling
Pots connected to the beam vacuum chamber with bellows
This allows moving the detector in respect to the beam
CMS Central Beam Pipe
IP
Need of silicon detectors that can go as close as possible to the beam!
From 40 mm = Parking
Up to 1 mm = Operational

## Slide 6: CTPPS Roman Pot – PPS2
PPS are installed on both sides of IP5 and have (are) run (running) sucessfully during Run 2 and Run 3
PPS2 is the upgraded version of PPS for running from Run 4 to Run 6
 Need for an update of the devices and an impedance study for the HL beam parameters
https://edms.cern.ch/document/2915345/0.2
3 stations on each side with 2 horizontal pots
4th pot station at 420 under discussion
(XRP-220 also has a pair of vertical pots used only for alignemnt)

## Slide 7: CTPPS Roman Pot – PPS2
PPS are installed on both sides of IP5 and have (are) run (running) sucessfully during Run 2 and Run 3
PPS2 is the upgraded version of PPS for running from Run 4 to Run 6
 Need for an update of the devices and an impedance study for the HL beam parameters
https://edms.cern.ch/document/2915345/0.2
3 stations on each side with 2 horizontal pots
4th pot station at 420 under discussion
(XRP-220 also has a pair of vertical pots used only for alignemnt)

## Slide 8: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 9: The need for a new Impedance Study
In HL LHC there is the need to also account for how the increase in beam intensity and decrease in bunch length will affect:
  Dissipate power (Beam-Induced Heating).
  Instabilities.
The impedance study included:
Pots already installed in the LHC (horizontal, vertical and box pots)
Pots that are under study for PPS2 (external groove)
Transverse Impedance
Modelling
Model Order Reduction
Mesh Convergence
Consistency Check
      Computation in CST
      Power Loss computation with BIHC
      Power Loss map
      Thermal Calculations
Computation in CST
Stability study
Measurements
Longitudinal Impedance
General Procedure
Stretched wire
Probes

## Slide 10: Modelling and Model Order Reduction
The model used for EM simulations is a simplified version of the complete ones.
V4 Horizontal, Operational Position
Stainless Steel 316LN
Compressed bellow
Vacuum Pipe
Beam Pipe
Ferrite (TT2-111R) ring
And
Springs
Fully parametric simplified model:
No flanges
No Vacuum Pipe
Metal “filled” (Stainless Steel 316LN ())
Simplified housing of the Ferrite Ring
Courtesy of D. Druzhkin

## Slide 11: Consistency Check
Results are consistent and consistent with previous studies by Nicola Minafra and Lorenzo Teofili.
V4, Distance beam-pot
Preliminary:
Mesh consistency study (check convergence of the mesh)
Model consistency study (check agreement with two solvers: Eigenmode and Wakefield)
Eigenmode solver: frequency domain solver (, , ).
Wakefield solver: time domain solver (Impedance as FFT of Wake field)
https://cds.cern.ch/record/2715363
https://cds.cern.ch/record/1557361

## Slide 12: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 13: Studied Models for the HL LHC upgrade
The models studied are:
  V4: No outer groove on the pot surface
  V5.3: Large outer groove on the pot surface
  V6: Narrow outer groove on the pot surface
V5.3, Garage Position
V4, Garage Position
V6, Garage Position
Inner grooves for mechanical stability (where the detector are located)
https://edms.cern.ch/document/2915345/0.2

## Slide 14: Longitudinal Impedance - Comparison
Comparison of the models:
Beam-pot distance: 1 mm.
V5.3 and V6 have a lower last peak (around 2 GHz)
V5.3 and V6 have modes below 1.4 GHz at lower frequencies.
V5.3, Garage Position
V4, Garage Position
V6, Garage Position

## Slide 15: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study  Measurements
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 16: Longitudinal Impedance - Single Wire Measurements of Version 6
Operational Position – 1 mm
In backup also 3.3 mm, 7.7 mm, and 40 mm

## Slide 17: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 18: Power loss computations - BIHC
Varying the distance between beam and the top side of the pot:
Simulations of power lost were performed with:
25ns_2748b_2736_2258_2374_288bpi_12inj
2.3e11 ppb
qGaussian with 1 ns bunch length
V4
V5.3 or V6

## Slide 19: Power loss computations – Power distribution map
Simulations of power lost were performed with:
25ns_2748b_2736_2258_2374_288bpi_12inj
2.3e11 ppb
qGaussian with 1 ns bunch length
V5.3 or V6
 | Average [W] | Max [W]
Total Power on the device | 148 | 160
Power in the ferrite | 126 | 136
Power on the top part of the pot | 14.2 | 15.6
Actual field distribution considered for thermal study
Assumed to be uniformly dissipated in the ferrite ring
Losses contributions and distribution
The most “dangerous” configuration was studied:
1 mm distance pot-beam

## Slide 20: Boundary conditions
Natural convection boundary 22 °C, 5 W/m2K
Radiation
136 W power deposited on ferrite
Imported heat flux from the electro-magnetic simulations
Radiation (1 enclosure defined)
Steady-state thermal
Enclosure 1: OPEN
22 °C
natural convection 5 W/m2K
136 W
Internal heat generation
Forced convection by water at 20 °C
Imported heat flux
Imported heat flux
Courtesy of Joanna Swieszek

## Slide 21: Results, without cooling channel
Max temp. in the coil: 424 °C
Temperature in the SS housing
Max temperature in the coil
Steady-state thermal
Temparature distribution in the assembly
Courtesy of Joanna Swieszek
Curie temperature around 375 °C

## Slide 22: Results, with cooling channel
Max temp. in the coil: 365 °C (~60 °C difference on the ferrite compared with the solution without cooling)
Max temperature in the coil
Steady-state thermal
Temparature distribution in the assembly
Temperature in the SS housing
Courtesy of Joanna Swieszek
Curie temperature around 375 °C

## Slide 23: Temperature dependency wrt thermal contact conductance
Thermal contact conductance | Max temperature in the ferrite |  | dT with/without cooling | Max temperature in the housing |  | Max temperature on the contact surface with ferrite | 
 | without cooling | with cooling |  | without cooling | with cooling | without cooling | with cooling
20 W/m2K | 424 °C | 365 °C | 59 °C | 200 °C | 148 °C | 177 °C | 25 °C
40 W/m2K | 378 °C | 287 °C | 91 °C | 200 °C | 147 °C | 182 °C | 25 °C
100 W/m2K | 304 °C | 168°C | 136 °C | 200 °C | 145 °C | 187 °C | 26 °C
Emissivity: 0.3 for SS 316LN (conservative approach) |  |  |  |  |  |  | 
20 W/m2K | 464 °C | 403 °C | 61 °C | 233 °C | 166 °C | 182 °C | 25 °C
Courtesy of Joanna Swieszek
Improving the contact between the ferrite ring and the steel flange will improve dramatically the situation!

## Slide 24: Thermal Study – Comparison with Run 3
Sensor
somewhere around here
Issue raised: even with cooling and good thermal contact, 160 degrees on the ferrite are not acceptable.
However, let’s look at measurements of the temperature on the flanges of the CTPPS during operation in Run 3.
Courtesy of Joanna Swieszek
During FILL 10690 
2.5mm distance pot-beam for impedance simulations
Pots in ‘aggressive positions’ (thanks to Mario Deile)
Nb = 1.6 E11 ppb
With Gaussian Bunch and bl=1.3ns
25ns_2460b_2448_2089_2227_144bpi_20inj
(Thermal data from Alexander Kurepin)
55 degrees max temperature measured on flange

## Slide 25: Thermal Study – Comparison with Run 3
Issue raised: even with cooling and good thermal contact, 160 degrees on the ferrite are not acceptable.
However, let’s look at measurements of the temperature on the flanges of the CTPPS during operation in Run 3.
Total power on the ferrite 28 W
During FILL 10690 
Nb = 1.6 E11 ppb
With Gaussian Bunch and bl=1.3ns
25ns_2460b_2448_2089_2227_144bpi_20inj
From these computations we reached over 100 degrees on the ferrite in 2025

## Slide 26: Need for in-vacuum temperature monitoring
Gap between the temperature measured on the flange and the actual ferrite temperature
Knowing the actual ferrite temperature:
  Info on target max temperature to assume for PPS2 design
  Estimated temperatures of ferrite over 100 degrees already in 2025!
  Possibility of monitoring during operation
Fiber Optic Sensing with Fiber Bragg Grating:
Minimal dimension
Perfect for the temperature range
Radiation robustness
In-vacuum operation (in steel capillary)
Or naked fiber with possible interesting R&D activity
Minimal modifications to the design
Already widely and successfully used in CMS
Courtesy of Joanna Swieszek
In the order of hundreds of degrees

## Slide 27: In-vacuum temperature monitoring needs
Technical competences:
Full availability for a collaboration and further discussions!
Selection and installation of the sensor
Minimal R&D for sensor’s placing in PPS
Infrastructures:
Availability of resources from CMS side for testing:
  Optical fibers are already in CMS and extending toward PPS (in case it is not difficult to extend even more)
Interrogation system from CMS can host another channel!
Expertise and experience of CMS team and UNINA Optopowerlab
              Optical fiber extending to PPS stations
Readout system
              E.g. inserting and brazing a steel capillary in the flange

## Slide 28: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 29: Transverse Impedance Studies
Beam
Integration path
x
y
z
Beam
Integration path
Dipolar
Quadrupolar

## Slide 30: V4 - Dipolar Impedance Curves:
Parking 40 mm
Operational 1 mm

## Slide 31: V5.3/V6 - Dipolar Impedance Curves:
Parking 40 mm
Operational 1 mm

## Slide 32: HL-LHC Roman Pot (PPS2): scenarios
PPS2s operate in different scenarios:
  parking position: to be considered at flat top
    start of levelling ()
    All Pots at 40 mm
  operational position: to be considered during collision
    end of levelling ()
    Pots in XRP-196 at 7.7 mm
    Pots in XRP-220 at 3 mm
    Pots in XRP-243 at 1 mm
Stability assessment usually done only at flat top
Given the presence of:
12 non-colliding bunches
Non negligible impedance of PPS2s
stability assessment performed also during collision
Maximum increase of octupolar threshold in x: < 0.5%
Maximum increase of octupolar threshold in y: 0.8%
Courtesy of Chiara Antuono

## Slide 33: Outline
CTPPS Roman Pots
1.1 Introduction
1.2 PPS2: upgrade for HL LHC
Longitudinal Impedance Studies
2.1 Introduction and preliminary studies
2.2 Longitudinal Impedance Study
2.3 Power loss study
2.4 Thermal study
Transverse Impedance Studies
Conclusions

## Slide 34: Conclusions
CTPPS Roman Pots Studies for PPS2 (HL LHC upgrade) have been performed with different pot design (not all of them were shown here)
With 1 mm distance pot-beam, there is risk of overheating the ferrite ring! Possible solutions:
2.1 Increase thermal contact between ferrite and steel flange,
2.2 Increase water cooling flow
2.3 Need for temperature measurements of the ferrite in-vacuum
Transverse Impedance is not an issue since the device is inserted only when stable beam is declared. More considerations on non-colliding bunches are under study.
Still, this is not considering the detectors and electronics warming up

## Slide 35: Thanks for your attention!
101st Impedance Working Group
CERN, Geneva, Switzerland
15 July 2025

## Slide 36: Backup
101st Impedance Working Group
CERN, Geneva, Switzerland
15 July 2025

## Slide 37: What is the beam-coupling impedance (pt 1)
For the analytical modeling of the Wakefield:
Source Particle (position )
Test Particle (position )

## Slide 38: What is the beam-coupling impedance (pt 1)
For the analytical modeling of the Wakefield:
Source Particle (position )
Test Particle (position )

## Slide 39: What is the beam-coupling impedance (pt 1)
Energy loss/gained by a test charge behind a source charge:
Longitudinal Wake Function:
For the analytical modeling of the Wakefield:
Source Particle (position )
Test Particle (position )
Same analysis can be made with transverse kicks () leading to transverse Impedance studies.

## Slide 40: What is the beam-coupling impedance (pt 2)
The Longitudinal Wake Impedance is the Fourier Transform of the longitudinal Wake Function.
Advantages:
Easier to consider resonant modes of the structure.
Modeling of instabilities due to impedance (longitudinal and transverse).
Convenient analytical expression of the dissipated power (longitudinal).
,
With the speed of the particle
number of particles in the beam
beam revolution frequency
normalized beam spectrum

## Slide 41: Model Order Reduction
The model used for EM simulations is a simplified version of the complete one.
No flanges
No Vacuum Pipe
Metal “filled” (Stainless Steel 316LN ())
Simplified housing of the Ferrite Ring
V4, Distance beam-pot

## Slide 42: Model Order Reduction
The model used for EM simulations is a simplified version of the complete one.
No flanges
No Vacuum Pipe
Metal “filled” (Stainless Steel 316LN ())
Simplified housing of the Ferrite Ring

## Slide 43: Simulations plan
V4, Distance beam-pot , without Ferrite Ring
Preliminary:
Mesh consistency study (check convergence of the mesh)
Model consistency study (check agreement with two solvers: Eigenmode and Wakefield)

## Slide 44: Version 6 – Measurements Zz 1 mm
H:\user\l\lsito\CTPPS\V6\Measurements\Longitudinal

## Slide 45: Version 6 – Measurements Zz 3.3 mm
H:\user\l\lsito\CTPPS\V6\Measurements\Longitudinal

## Slide 46: Version 6 – Measurements Zz 7.7 mm
H:\user\l\lsito\CTPPS\V6\Measurements\Longitudinal

## Slide 47: Version 6 – Measurements Zz 40 mm
H:\user\l\lsito\CTPPS\V6\Measurements\Longitudinal

## Slide 48: Model 4 – Impedance curves and power loss
Varying the distance between beam and the top side of the pot (the parameter is called dB)
Eos/user/l/lsito/CTPPS/ThermalStudies_2023/V4_ZLongitudinal_Sweep
Simulations of power lost were performed with:
25ns_2748b_2736_2258_2374_288bpi_12inj.csv
2.3e11 ppb
1.2 ns bunch length
Simulations of power lost were performed with:
25ns_2748b_2736_2258_2374_288bpi_12inj.csv
1.63e11 ppb
1.2 ns bunch length
Beam-pot distance increasing:
Overall, as expected, the peaks are getting lower and broader.
Peaks at higher frequencies (1.5 and 2 GHz) are shifting toward higher frequencies.
Peaks below 1.4 GHz are shifting toward lower frequencies.

## Slide 49: Model 5.3 – Impedance curves and power loss
Varying the distance between beam and the top side of the pot (the parameter is called dB)
Simulations of power lost were performed with:
25ns_2748b_2736_2258_2374_288bpi_12inj.csv
2.3e11 ppb
1.2 ns bunch length
Beam-pot distance increasing:
Overall, as expected, the peaks are getting lower and broader.
Peaks at higher frequencies (1.5 and 2 GHz) are shifting toward higher frequencies.
Peaks below 1.4 GHz are shifting toward lower frequencies.
Peak above 2 GHz shift lower in frequency!
Eos/user/l/lsito/CTPPS/ThermalStudies_2023/V4_ZLongitudinal_Sweep
How do V4 and V5.3 compare in terms of dissipated power?
(Same beam parameter as the plot on the left)

## Slide 50: Model 5.3
Varying the distance between beam and the top side of the pot (the parameter is called dB)
Eos/user/l/lsito/CTPPS/ThermalStudies_2023/V4_ZLongitudinal_Sweep
Now, simulations of power lost were performed with:
25ns_2748b_2736_2258_2374_288bpi_12inj.csv (This filling scheme)
2.3e11 ppb
1.2 ns bunch length

## Slide 51: Power loss computations with bunch length = 1 ns
Varying the distance between beam and the top side of the pot (the parameter is called dB)
Now, simulations of power lost were performed with:
25ns_2748b_2736_2258_2374_288bpi_12inj.csv (This filling scheme)
2.3e11 ppb
1 ns bunch length
180.94 W
182.3 W
V4
V5.3

## Slide 52: Version 6 – No Radiation cooling, bad thermal contact
 | Average [W] | Max [W]
Total Power on the device | 148 | 160
Power in the ferrite | 126 | 136
Power on the top part of the pot | 14.2 | 15.6
Convection: 4 W/m^2 K

## Slide 53: Transverse Impedance Curves
Parking position with 40 mm distance pot-beam
x
y
z
Operational position with 1 mm distance pot-beam