## Slide 1: Cooling Demo R&D Plan
Marco Statera, INFN
With the contribution of
Lucio Rossi and Stefano Sorti, UNIMI and INFN
Dario Giove, Barbara Caiffi and Mattia Castoldi INFN
Giuseppe Scarantino, Roma Sapienza and INFN
Luca Bottura, Cédric Garion and Rui Franqueira Ximenes CERN

## Slide 2: Outline
6D cooling R&D: a common development with HFM
The R&D for the cooling cell demo: time, people and cost
  Magnets
  RF
  Adsorber and vacuum
Conclusion

## Slide 3: R&D MC and HFM
What do want to build?
What is a good intermediate goal?
building S5 like cell
All R&D by ourself?
building RFMFTF
Radio Frequency in Magnetic Field
Test Facility
See L. Rossi and G. Scarantino
No
Strong synergies with HFM
HTS magnets program

## Slide 4: INFN HFM-HTS Roadmap: target
Already identified some conceptual designs:
B centre | Aperture diameter | Top | Straight section | Fiel quality target | Target JCu
10 T | 50 mm | 20 K | 400 mm | units | 800 A/mm2
8.5 km da 4 mm equiv.
13 km da 4 mm equiv.
12 km da 4 mm equiv.
15 km da 12 mm

## Slide 5: HTS R&D: experimental activities
Tape QA and characterization → ordered EF Mcorder (with visual inspection module)
Splicing and joints repeatable manufacturing online (while winding)
Small coils with different insulation technologies → multi-tape winding machine
Under-development apparatus for variable-temperature tests, with optional background field
Commissioned in-house Additive Manufacturing polymeric & metallic (3D printer), starting R&D activity on mechanical structures for advanced 3D winding of tapes.
55K
20 K

## Slide 6: HTS R&D : numerical tools
Jc×mm2
Matlab + FEMM for Magnet design, aiming at ad-hoc routines for HTS,
allowing for:
  Estimation of losses and dynamic field quality from the beginning (semi-analytical models)
  (Cost) optimization of magnet design accounting for tape features → also to explore non-standard geometries
Mariani, Mariotto, Scarantino, Sorti
(in addition to commercial software)
Optimization
Courtesy of T. Boulder, CERN
Protection
Quench simulations
Littel Beast Engineering
CERN
QLASA including HTS
Quench development over time is critical for detection and protection schemes
Define margin for HTS tape
The margin may vary on cross section of the tape

## Slide 7: HTS R&D: numerical tools
For Magnet operation: Aiming at modern automation for HTS magnets:
  Model + data online monitoring, measurements and diagnostic
  Optimal control of charge/discharge:
Charging optimization based on Pontryagin's Min. Principle [Balconi et al. IEEE TAS (2024)]
Model-order reduction through Proper Orthogonal Decomposition for real time applications [Sorti et al. IEEE TAS (2025)]
Strongly physics-based approach: full 3D model of magnet, E.M., thermal and possibly mechanical + model order-reduction and data-driven correction
The same code will serve also as complementary to QLASA, for quench of NI magnets
(in addition to commercial software)
Effort to develop protection schemes based on
quench prevention
Digital twin

## Slide 8: HTS R&D
IRIS
Modeling
Conductor
Design
Construction
Test
CONDUCTOR
MODELING
DESIGN
Explore
conductor
geometry
design
protection
10 T Demonstrator
14 T
conceptual design
Cooling cell Demo
RF in Magnetic Field Test Facility

## Slide 9: TRL Drives the R&D
We wish to reach a TRL 6 for the decision of construction, the level of readiness appropriate to enter the industrialization
Courtesy of L. Bottura

## Slide 10: Split coils Demonstrator
Updates
ESMA dipole in construction
1.5 km 12 mm tape eq.
Test coils
Demonstrator 2028
Delivered
5 km of 4 mm tape form SST by INFN R&D MC
Funding requests
HE-EPITA 50k€ tape
ASTRA (MUR, IRIS continuation)): 685 k€ for Cryo-mechanics mechanics

## Slide 11: People and Cost profiles
Ongoing , partially completed or expected to be completed within 2026

## Slide 12: RF
Courtesy of Dario Giove
R&D
Aluminum foils production and positioning
Custom waveguide
About 10 months - 40k€
Cavity design done and integrated
Production of one test cavity about 7 months - 120 k€
8 person month required
Issue on 704 MHz modulator and klystron
2 years + 2 M€
Showstopper? See discussion in the dedicated session

## Slide 13: Adsorber and Vacuum
Operation
Safety
Integration
Procurement Manufacturing
Lithium hydride (LiH)
Melts at ~690 C
Coated is compatible with low vacuum
Reactive!
  w/ H2O produces Li hydroxide and H2 gas
  Can explode even with humid air or due to static electricity
  Flammable, corrosive, toxic…
Courtesy of Rui Franqueira Ximenes
MICE experience
R&D

## Slide 14: Adsorber and Vacuum
Pillow seal system
To be fully integrated
NIMB 317 734-738
Tanaka et al.
Courtesy of Cédric Garion and Rui Franqueira Ximenes
Axial force
Double differential vacuum metal/metal
Single vacuum for oring
Migth be bulky

## Slide 15: Conclusion 1
Clear vision of the R&D goals: RFMFTF and S5-like cell are technology demonstrators
HTS R&D
  Probe tapes specs (to be able to better specify next procurements)
  Test winding techniques and conductor
  Incremental complexity tests
  Both common and complementary studies with the final cooling solenoid development
Some infomations will arrive by ESMA magnet by IRIS
Strong improvements in modeling
  Some tools are available, some are in development
  We need experimental crosschecks

## Slide 16: Conclusion 2
Magnets
  a path has been prepared, it has to be financed
  many synergies with final cooling and HFM
  Some funding requested
RF
  a baseline design has been finalized
  Main issues have been highlighted
Adsorber and Vacuum
  Baseline solution have been identified for vacuum connections and adsorber
  Solutions have to be developed
Takeaway message
Funding R&D and device construction is crucial for technology development
We are looking for funding through different lines and by sinergies with HFM