## Slide 1: Funded by the European Union (EU). Views and opinions expressed are however those of the author only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.
R. Losito
CERN
EU Project MuCol
Status and Plans

## Slide 2: IMCC International Muon Collider Collaboration
2
Collaboration formed 2022, currently hosted by CERN
61 formal member institutions, still growing
Currently centred in Europe, strong US contribution
R&D progamme developed with global community
In response to strategic requests:
Last ESPPU demanded integration into European Accelerator R&D Roadmap
EU is co-funding design study MuCol since 2023
Different US recommendations: Snowmass, P5 and National Academy of Science

## Slide 3: Muon Cooling Lattice Design
better
better
Previous design (MAP)
Goal
Achieved
Challenges:
Novel, complex lattice with cavities and absorbers in solenoids
High magnetic field
Achieved:
Much improved lattice design
Developed simulation tools: BDSIM and RFTrack
This allowed to start collective effects studies
Magnet scaled and conceptual designs for 6D cooling
40 T final cooling solenoid conceptual design (55 T is identified to be the limit)
Key conclusions:
Can in principle reach or exceed performance target
Magnet models and prototypes need to be built
Much improved longitudinal, is useful for collider ring
Study of collective effects important

## Slide 5: Muon Cooling Demonstrator Programme
v2.0 Split Coil >704 MHz RF testing
v3.1 Single Coil >1 GHz RF testing
v3.2 Split Coil >1 GHz RF testing
Radio Frequency in Magnetic Field Test Facility (RFMFTF)
… A Technological Point of View

## Slide 9: Plasma Sheath Formation around a Muon Beam
1. Ionization
Send high energy in neutral hydrogen atom
Ionization happens (dashed line)
2. Charge neutralization (within ~10 ps)
Beam attracts ionized electrons near the beam
Within the beam volume (gas and beam are neutral)
Outside beam volume (gas is positively charged)

## Slide 10: Proton beam for Ionization-Cooling Demo
Producing a proton beam is relatively easier than producing a muon beam
The proton is a hadron and experiences strong interactions
  For kinetic energy below 200 MeV, the dominant strong-interaction mode is elastic scattering
  The muon, as a lepton, interacts only electromagnetically
Proton is 9 times heavier than muon
  Therefore, matching parameters between proton and muon beams requires compromises
    Match momentum
    Match velocity
Basic equations for ionization cooling

## Slide 11: Summary and Outlook
Collective electromagnetic fields induced in the absorber
  Beam-induced plasma neutralizes the space charge of the beam
  The beam current generates an axial magnetic field that focuses the beam (plasma z-pinch)
  The betatron function can be 10-20 % shorter than the design value
  Numerical simulations are planned to validate the model
Enhancement of energy-loss rate using intense plasma
  Nominal plasma density in the absorber is too low to significantly increase the energy-loss rate
  If 10 % of the absorber electrons are ionized, the energy-loss rate increases by about 10 %
  Preforming plasma with a laser and particle beam could further enhance the effect
Possible ionization cooling demo using a proton beam
  Two cases were evaluated: same momentum and same beta
  The results indicate that hadronic interactions can be eliminated by momentum-cuts
  Search low-energy proton beam facility

## Slide 12: RFMFTF_v3: re-scaled for a 3 GHz cavity 170 mm RT bore, Baxis=7 T
RFMFTF_V3.2 – 170 mm RT free bore
250 mm coil aperture, Baxis= 7 T, G = 68 T/m
HTS: 4 mm SST tape, 2 mm spacers.
I = 580 A, 201 turns.
8.53 km tape needed, 24 units of 178 m.
Peak field: 13.6 T, E = 0.690 MJ.
Tot. Fz = 0.780 MN.
B field gradient ():

## Slide 13: Funding for the RFMFTF_V3 [Magnet PART] Deadline for decision: March 2026
INFN MuCol: 145 k€ (5 km of 4 mm tape form SST): done!
INFN IRIS: tape 120 k€ (1.5 km 12 mm tape or 4 km of 4 mm or a mix)
In pipeline (under scrutiny…)
HE-EPITA: 50 k€ with 95% CL (2)
ASTRA (MUR, IRIS continuation)): 685 k€ for Cryo-mechanics mechanics: 68% CL (1) response by Dec.2025
INFN (and UMIL) have already put some 4 FTE-y on this project and 50% of a PhD and 3 MS thesis.
INFN-UMIL can continue to put further 6 FTE-y (2 FTE rate), 1 PhD thesis + 3 MS thesis
Necessary from CERN to INFN (or UMIL) (HFM program, dedicate task, or other)
V3.1 (single coils) : 600 k€
  200 k€ mainly for mechanics
  400 k€ for 4 FTE (2 y x 2 people in TD, 1 Academic, 1 Technician )
V3.2 (Split coil): + 800 k€
  200 k€ for 7 km 4 mm tape
  200 k€ for mechanics
  200 for cryogenics
  200 for 1 y extending both TDs)
TOTAL for the project: 1400 k€ (HTS tapes, other cryomechanical part or design activity can be in-kind…)

## Slide 14: Demo Cooling Cell Module MAG 2.4

## Slide 18: Beam pipe overview
LiH holder
(adgiustable support)
LiH
Custom pillow seal system

## Slide 19: Cooling Cell Integration Short Movie (version 2.4)

## Slide 20: Initial – Final Module Evaluation
Initial - final module design not yet considered.
Loss of symmetry: 10 T peak field on axis
  25% current reduction: match peak field on axis.
Unbalanced forces in the first (last) two inter-cell units.
Adiabatic matching?

## Slide 21: Quench Simulations – Forces Unbalance Courtesy of T. Mulder (CERN)
Quench – no protection system:
Quench initiated on one of the inner turns of C1
Quench propagation in C1 and neighbouring coils.
5.4 MN unbalanced force in the central inter-cell module.
  Support structure designed for max 1 MN unbalance!
C0
C1
C2
C3
5.4 MN Unbalance

## Slide 22: O-ring based pillow seal
Absorber flange
Cavity flange
O’ring
Bellows
Ø150mm
Ø230mm
Vacuum
Disconnection
Pressure
Connection
Interspace pumping
O-ring: Ø 3.5 mm
Compression 20% => ≈2 kg/cm
Total force (two O-ring)  < 240 kg
P  1 bar (spring force not considered)
Single O-ring seems also feasible (no interspace vacuum) => Increase pressure may reduce space between the internal and external bellow => Less radial space

## Slide 23: What about pumping?
Two separate volumes: Absorber and RF cavity
RF cavity:
Pumping and instrumentation on the waveguide => To be checked if that is enough
Absorber:
Small tube for primary pumping and monitoring
Pumpdown from atmospheric with both volumes connected (control P) to avoid damaging the RF windows
Control system to ensure the P do not exceed a certain threshold that could damage the window => Safety valve connecting both volumes

## Slide 24: Immediately Available Solutions
Existing solutions at 704MHz are typically single beam devices with peak powers <2MW
VKP7952 | VKP8292A
Frequency - 704MHz | Frequency - 704MHz
Peak Power – 1.3MW | Peak Power – 1.5MW
Efficiency – 65% | Efficiency – 65%
µPerveance – 0.71 | µPerveance – 0.58
Total Length – 4.72m | Total Length - 3.88m
TH2180
Frequency - 704MHz
Peak Power – 1.5MW
Efficiency – 69%
µPerveance – 0.6
Total Length – 4.5m
E37504
Frequency - 704MHz
Peak Power – 1.5MW
Efficiency – 66%
µPerveance– 0.59
Total Length – 3m
Thales TH2180
CPI VKP-8292A

## Slide 25: Direct Scaling Solution
A medium-term (3-4 years) solution.
Directly scaling allows the reuse of elements (gun, focussing, collector*)
*Collector size can be reduced for this scaling example due to lower duty cycle, lower thermal load.
Frequency: 1.0 GHz
Peak RF Power: 20 MW
Efficiency: 70%
Frequency: 1.3 GHz
Peak RF Power: 10 MW
Efficiency: 65%
Notes: Canon E37503, Thales TH1803 is 10 Beam device.
Cavities would still have to be designed – may as well redesign the interaction region with equivalent gun.
Introduction of MBK on this slide – simply multiple beams, perveance is per beam not overall system, shared interaction geometry, interdependent + more points of failure

## Slide 26: Conclusion
Existing single-beam klystrons are readily available at this frequency. (Higher power MBKs exist at 1GHz and 1.3GHz)
Feasible medium-term prospects are presented: reuse of component designs and direct scaling. (3-4 years)
Entirely Custom 22-Beam CSM Klystron as a potential long timescale solution.
Two-Stage Klystrons may be viable at this frequency – is the increased complexity worth the size / efficiency improvements?

## Slide 27: Example of cooling at 20 K - SHiP
Courtesy L. Baudin (Indico)
Large aperture (4 m x 6 m) superferric magnet
Conductor: MgB2 operating at 18-20 K
Significant energy savings w.r.t. normal conducting option (even when considering cryogenic consumption!)
Installation in area without He infrastructure (ECN3), and relatively low heat load → ideal case for use of use of cryocoolers and a remote supercritical He loop
Three loops using He gas @ ~10 bara and
18-20 K for the cold mass (~ 5 g/s)
70-80 K for the thermal screen (~ 6 g/s)
50-55 K for the current leads (~ 2 g/s)
Advantages:
Cooling infrastructure 15 m away from magnet (high penalty if conduction cooled)
Almost no He inventory
Operation at higher T

## Slide 28: (Qualitative) comparison of cryo system options
Cryocoolers + turbo-Brayton or LN2
Independent cooling circuit for each temp. level
TB system installed at surface level
Modularity with increasing # cells, can add cryocoolers as cooling channel grows
Cryocoolers + compressors installed underground (needs cooling water + electricity)
High energy consumption (12 kW/cryocooler + TB (?))
Maintenance of cold heads every 15’000 h
Requires trained operators for TB part
He liquefier/refrigerator
(can have) independent cooling circuit for each temp. level
Cold box + ancillary services all at surface level, only transfer line to cooling channel
Most energy-efficient option
Likely higher cost than cryocooler + TB option
High He inventory incl. gas management + storage
Complex maintenance of cryoplant every 8’000 h
Requires trained operators

## Slide 49: A possible plan for 1st Cooling Module
2025 2026-I 2026II 2027-I 2027-II 2028-I 2028-II 2029-I 2029-II 2030-35
RF test material LASA (1 T resistive magnet)
RF test stand SLAC 3 GHz  1.3 GHz?
Cryomagnets RFMFTFV3.1 V3.2
Prototypes RF cells
Prototype C. cell magnets
RFMFTFV3.1 V3.2 operation
Design C. Module – ends  Design 1st Cooling cell
Construction & test 1st Cooling Module
construction 1st Cooling cell
It assume only a moderate increase of resources wrt today

## Slide 50: R&D MC and HFM
What do want to build?
What is a good intermediate goal?
building S5 like cell
All R&D by ourself?
building RFMFTF
Radio Frequency in Magnetic Field
Test Facility
See L. Rossi and G. Scarantino
No
Strong synergies with HFM
HTS magnets program

## Slide 51: TRL Drives the R&D
We wish to reach a TRL 6 for the decision of construction, the level of readiness appropriate to enter the industrialization
Courtesy of L. Bottura

## Slide 52: Conclusion 1
Clear vision of the R&D goals: RFMFTF and S5-like cell are technology demonstrators
HTS R&D
  Probe tapes specs (to be able to better specify next procurements)
  Test winding techniques and conductor
  Incremental complexity tests
  Both common and complementary studies with the final cooling solenoid development
Some infomations will arrive by ESMA magnet by IRIS
Strong improvements in modeling
  Some tools are available, some are in development
  We need experimental crosschecks

## Slide 53: Conclusion
Many thanks to Nadia and Dario!
Excellent progress on every aspect of the Demonstrator
Eagearly waiting for the conclusion of the EUSPP…. Don’t forget to contact editors of national inputs!!!
Have a safe trip