## Slide 1
J. Ferradas Troitino, A. Haziot, E. Fernandez Mora, S. Izquierdo Bermudez,
E. Todesco and J.C. Perez
14T - Update on design
TE-MSC-SMT
July 2025

## Slide 2: Intro - Mechanical analysis
Figures of merit
Coil stresses
Coil contact pressure
Stress limits in the structure
Coil displacements
Coil strain
σVM < 120 MPa at RT
σVM < 150 MPa at cold
Roughly:
εz < 2000 µstr
Roughly:
All components below yield limits. We check S1 for brittle materials in first order
Try to maintain an average contact pressure > 5 MPa while respecting the stress limits
Check the coil displacements during powering

## Slide 3: 14 T Magnet design
Conductor parameters - UPDATED
40 strands x 1.1 mm
14 T Conductor

## Slide 4: 2D Mechanical analysis – Mat. Props.
MQXF Model |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Coil |  |  |  | Stainless Steel |  |  |  | AlBr |  |  |  | Iron |  |  |  | Aluminum |  |  |  | G10 |  |  |  | Nitronic |  |  |  | Ti |  |  |  | HiMn Steel |  | 
 | 4.3 | 293 |  |  | 4.3 | 293 |  |  | 4.3 | 293 |  |  | 4.3 | 293 |  |  | 4.3 | 293 |  |  | 4.3 | 293 |  |  | 4.3 | 293 |  |  | 4.3 | 293 |  |  | 4.3 | 293
Ex | 20 | 20 |  | Ex | 210 | 193 |  | Ex | 120 | 110 |  | Ex | 224 | 213 |  | Ex | 79 | 70 |  | Ex | 30 | 30 |  | Ex | 225 | 210 |  | Ex | 130 | 130 |  | Ex | 210 | 193
Pr | 0.3 | 0.3 |  | Pr | 0.28 | 0.28 |  | Pr | 0.3 | 0.3 |  | Pr | 0.28 | 0.28 |  | Pr | 0.34 | 0.34 |  | Pr | 0.3 | 0.3 |  | Pr | 0.28 | 0.28 |  | Pr | 0.3 | 0.3 |  | Pr | 0.28 | 0.28
Alpx | 1.35E-05 |  |  | Alpx | 9.83E-06 |  |  | Alpx | 1.08E-05 |  |  | Alpx | 6.82E-06 |  |  | Alpx | 1.45E-05 |  |  | Alpx | 2.44E-05 |  |  | Alpx | 9.00E-06 |  |  | Alpx | 6.03E-06 |  |  | Alpx | 5.55E-06 | 
Th. Strain | 3.89E-03 |  |  | Th. Strain | 2.84E-03 |  |  | Th. Strain | 3.12E-03 |  |  | Th. Strain | 1.97E-03 |  |  | Th. Strain | 4.18E-03 |  |  | Alpy | 2.44E-05 |  |  | Th. Strain | 2.60E-03 |  |  | Th. Strain | 1.74E-03 |  |  | Th. Strain | 1.60E-03 | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Alpz | 8.34E-06 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Th. Strain | 7.04E-03 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Th. Strain | 7.04E-03 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Th. Strain | 2.41E-03 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: 2D Mechanical analysis – Stress criteria
RMM

## Slide 6
Conceptual design
Outline

## Slide 7: 2D Mechanical analysis
Simplified geometry accounting for main features
Criteria
Use same modelling assumptions as MQXF, which we know well
Target similar coil peak stress limits at warm/cold as MQXF:
  RT below 110 - 120 MPa
  CD below 150 MPa
For reference, our MQXF reference preload gives in the model:
  RT peak azimuthal stress = 80 MPa
  CD peak azimuthal stress = 110 MPa
Gap = 100 µm

## Slide 8: 2D Mechanical analysis
Bladder positioning:
  3 short bladders in the split yoke (horizontally)
  One long and half short bladders in the Hpad (per quadrant)
  Half long bladder in the vertical pad
Short bladders = 37 mm (34 mm active)
Long bladders = 54 mm (51 mm active)

## Slide 9: 2D Mechanical analysis
The top bladder in the pad helps to open a larger clearance, we increase the bladder surface.
However it pushes in the non-supported part of the pad and creates a large bending. That’s why we’re obliged to have a very thick pad.

## Slide 10
Engineering design version of the structure
Outline

## Slide 11: 2D Mechanical analysis
New model accounts for:
  New cable specification
  Encapsulated bladders
  Split pole

## Slide 12: Figures of merit
Yoke OR = 290 mm
Shell thickness = 50 mm
Magnet OD = 680 mm
Hpad thickness = 60 mm
Bladder sizes as in the picture.
  We have more shell thickness, so we gain more during CD.
  We need less interference at warm and thus we need to open less clearance.
  We come back to a small bladder at the midplane, which allows us to bring the interference key down.
3 large bladders
57 mm
Intermediate
47 mm
Small
37 mm

## Slide 13: 2D Mechanical analysis
Transverse stress (Horizontal)
Contact pressure at 14 T
Conceptual
Engineering design
Peak at RT = 91 MPa
Peak at CD = 177 MPa
Peak at 14 T = 143 MPa
Peak at RT = 104 MPa
Peak at CD = 168 MPa
Peak at 14 T = 147 MPa

## Slide 14: 2D Mechanical analysis
VM Equivalent stress
Peak at RT = 86 MPa
Peak at CD = 175 MPa
Peak at 14 T = 128 MPa
Contact pressure at 14 T
Conceptual
Bladder
Peak at RT = 98 MPa
Peak at CD = 169 MPa
Peak at 14 T = 134 MPa

## Slide 15: 2D Mechanical analysis
VM Equivalent stress
Without bladder simulation

## Slide 16: 2D Mechanical analysis
VM Equivalent stress
With bladder simulation
Step DisplcY DisplcX
1 202.3 7.2
2 50.1 9.2
3 36.8 866.0
4 41.0 635.4
Step DisplcY DisplcX
1 153.1 -2.1
2 51.8 -0.7
3 42.3 837.5
4 45.3 636.7

## Slide 17: 2D Mechanical analysis
VM Equivalent stress

## Slide 18: 2D Mechanical analysis
Engineering design
Conceptual:
Current = 20005 A.
Bore field = -13.9996405 T.
Peak field layer 2 = 14.7270832 T.
Peak field layer 1 = 14.1192093 T.
Current density = 330.725494 A/mm^2.
F shell ratio (CD/Warm) = 2.22
Shell th. = 50 mm / Yoke OR = 270 mm
Interference = 0.65 mm
F shell ratio (CD/Warm) = 2.28
Shell th. = 50 mm / Yoke OR = 290 mm
Interference = 0.65 mm
Current = 20005 A. Bore field = -14.0065861 T. Peak field layer 2 = 14.7078485 T. Peak field layer 1 = 14.2343845 T. Current density = 343.277084 A/mm^2.

## Slide 19: 2D Mechanical analysis
Engineering design
Conceptual:
Current = 20005 A.
Bore field = -13.9996405 T.
Peak field layer 2 = 14.7270832 T.
Peak field layer 1 = 14.1192093 T.
Current density = 330.725494 A/mm^2.
F shell ratio (CD/Warm) = 2.22
Shell th. = 50 mm / Yoke OR = 270 mm
Interference = 0.65 mm
F shell ratio (CD/Warm) = 2.28
Shell th. = 50 mm / Yoke OR = 290 mm
Interference = 0.65 mm
Current = 20005 A. Bore field = -14.0065861 T. Peak field layer 2 = 14.7078485 T. Peak field layer 1 = 14.2343845 T. Current density = 343.277084 A/mm^2.

## Slide 20: 2D Mechanical analysis
Engineering design
Conceptual:
Current = 20005 A.
Bore field = -13.9996405 T.
Peak field layer 2 = 14.7270832 T.
Peak field layer 1 = 14.1192093 T.
Current density = 330.725494 A/mm^2.
F shell ratio (CD/Warm) = 2.22
Shell th. = 50 mm / Yoke OR = 270 mm
Interference = 0.65 mm
F shell ratio (CD/Warm) = 2.28
Shell th. = 50 mm / Yoke OR = 290 mm
Interference = 0.65 mm
Current = 20005 A. Bore field = -14.0065861 T. Peak field layer 2 = 14.7078485 T. Peak field layer 1 = 14.2343845 T. Current density = 343.277084 A/mm^2.
Normalizing both with the same Fem

## Slide 21
Structure limit
Outline

## Slide 22: 2D Mechanical analysis
CD:
Peak = 206 MPa
RT Assy:
Peak = 150 MPa
14 T:
Peak = 190 MPa
1 mm interference
15.5 T

## Slide 23: 2D Mechanical analysis
Results without bladder simulation
1 mm interference
RT Assy:
Peak = 200 MPa
RT Assy:
Peak = 204 MPa

## Slide 24: 2D Mechanical analysis
With bladder simulation
Peak = 220 MPa
Step DisplcY DisplcX
1 305.2 6.0
2 50.0 9.2
3 31.6 1221.9
4 35.6 979.2

## Slide 25: 2D Mechanical analysis
1 mm interference
Results without bladder simulation

## Slide 26: 2D Mechanical analysis
With bladder simulation
Peak stress during bladders = 310 MPa
1 mm interference

## Slide 27: 2D Mechanical analysis
VM Equivalent stress