Vacuum downstream of the plasmas
Spectrometer
quadrupoles
Start of CNGS decay pipe
Laser insertion
mirror
? What do we do here
Spectrometer
 dipole
End of the 2nd plasma
 Topic of this meeting

---
What elements will need to be in this region?
Laser insertion
mirror
Beam Screens
3-5

---
Spectrometer dipole chamber
Separate meeting:
https://indico.cern.ch/event/1563270/
Dipole aperture is 78 or 80 mm and need 2 mm gap
Pipe diameter is 72 mm, could be made wider ~50cm after the exit of the yolk

---
Physics considerations  deflection
Spectrometer dipole can either be on or off, if on bending angle is ~3 mrad  ~10 cm offset at the cavern end
30-40 m
Spectrometer dipole off
Spectrometer dipole on

---
Physics considerations  defocused protons
Beam core
Defocused protons are an important physics tool!
 Can be more than half of the beam ~1.5e11 p+
Beam halo
~ 15 cm
30 m

---
Vertical plane
z = 0 m, dipole exit
Plasma 1
Plasma 2
Quads
Dipole

---
Horizontal plane
Spectrometer dipole off
Spectrometer dipole on

---
Options discussed so far…
Large diameter vacuum pipes, elliptical?
Expensive?
Collimate the defocused protons (~50% of the beam)
Non-ideal for physics
Radiation?
Propagate the beam in air after coupling in the laser pules (+SC screens)
RP  from Claudia:30 m of air in the downstream TCC4 area, we would expect proton losses of 4.1% (lambda in air is of 7.17E4 cm, L/lambda = 4.19E-2). Thus, it would create losses a slightly bit more than what we expect for the laser coupling mirror (SiO2 of 1.2 cm length)
Inserting a second dipole magnet to bend the proton beam back straight