## Slide 1: LLRF and RF power prospects for PERLE
Christophe Joly (CNRS/IN2P3/IJCLab)
On behalf of the PERLE collaboration
N. Belouchrani*, X. Lafay, S. Berthelot, J-F. Yaniche, O. Frossard, A. Martens, F. Bouly, A. Buthod, C. Guérin with a strong interaction with the IDROGEN Team :
D. Charlet, A. Back, C. Esnault, M. Taurigna, C. Cheik-ali , C. Soulet, Gaetan Seuillot, Mathias Vecchio, Sid Ali Cherrati in collaboration with P-E. Potty , Michel Lours( LTE lab) , Cédric Viou (ORN lab).
PhD student CIFRE IJCLab & ASC

## Slide 2: RF system overview
Master Oscillator (MO)
Accelerator Phase Reference Distribution system ( PRDS)
LLRF feedback system (LLRF)
Frequency Tuning System (FTS)
Timing system (LLRF, Diagnostics,…)
RF powers Sources and RF power distribution
Linked to C&C, MPS and PSS
Using a ultra low noise version of the WR system
(same protocol but with HW and SW improvements)
More details : see presentation A. Back (WR workshop 2025)

## Slide 3: Distributed Master Oscillator (DMO)
Aim : to develop an architecture of one Distributed Master Oscillator with ultra low phase noise @[1Hz to 1MHz)] using WR thanks to the IDROGEN boards and the REFIMEVE infrastructure, for PERLE, waiting a new solution, White Fox project (jitter < 100fs) for future applications.
LTE
PARIS
IJCLab
PARIS
Mode switch LN
IDROGEN board
IDROGEN board
Atomic Clock
Mode Master
Rubidium
10MHz + PPS
IDROGEN board
Crate
MTCA
Booster
ERL
IDROGEN board
Crate
MTCA
IDROGEN board
Crate
MTCA
Buncher
Mode Slave
To diagnostics,
…
Requirements in progress from beam dynamics
Base line (rms) : +/-0.1% and +/-0.1°
to distribute between MO, PRDS and LLRF
Time and frequency

## Slide 4: Distributed Master Oscillator (DMO)
IDROGEN board
Master Mode
Rubidium
10MHz + PPS
Improvements of the Master’s jitter 100MHz@offset range [1Hz-1MHz] : 260 fs
Thanks to PLL simulation
IDROGEN board
Crate
MTCA
Slave Mode
100MHz@offset range [1Hz-1MHz] at the end point (Slave) : 1.04 ps
Frequency distribution Amplifier
Today best result obtained by D. Charlet : 866fs
Courtesy : Nawal Belouchrani

## Slide 5: Distributed Master Oscillator (DMO)
Master Mode
Rubidium
10MHz + PPS
Frequency distribution Amplifier
Courtesy : Nawal Belouchrani
Jitter (rms) 10MHz@offset range [1Hzto 1MHz] =968fs Manufacturer 2
Jitter (rms) 10MHz@offset range [1Hzto 1MHz] =1380fs Manufacturer 1
IDROGEN Switch version
in mode GM ?
Very interesting !!
WR switch Low noise references

## Slide 6: Distributed Master Oscillator (DMO)
IDROGEN board
Master Mode
Rubidium
10MHz + PPS
IDROGEN board
Crate
MTCA
Switch Mode
Frequency distribution Amplifier
Mode Slave
REFGEN FMC board
With a SI5362
10 MHz (synchronization of Scopes, …)
200.395 MHz (LLRF reference)
400.79 MHz (Laser reference)
801.58 MHz (Accelerator reference)
Or others frequencies in function of need
for diagnostics
Next step : To measure this configuration

## Slide 7: New PLL : preliminary results
Morion
10MHz
SKY 63102
Courtesy : Nawal Belouchrani
Jitter (rms) 400.79MHz@offset range [1Hzto 1MHz] =282fs
Jitter (rms) 176.1MHz@offset range [1Hzto 1MHz] =282fs
Jitter (rms) 125MHz@offset range [1Hzto 1MHz] =285fs
Jitter (rms) 88MHz@offset range [1Hzto 1MHz] =284fs
Jitter (rms) 10MHz
@offset range [1Hzto 1MHz]
=150fs
-10fs better than Si5362 used on FMC REFGEN board in offset range [12kHz to 1MHz]  validated
- Need characterization in the offset range [1Hz to 1MHz]
Jitter (rms) 10MHz@offset range [1Hzto 1MHz] =249fs (Rubidium)
Jitter (rms) 10MHz@offset range [1Hzto 1MHz] =150fs (Morion) from LTE

## Slide 8: LLRF MTCA-based architecture

## Slide 9: Timing Distribution
REFGEN FMC is realized and tests in progress but already improvements planned.
New IDROGEN version in progress due to obsolete components and some improvements

## Slide 10: IOXOS boards
IFC_1411
  CPU POWERPC
  FPGA Kintex ultrascale
DAQ_1430
  10 ADC 16bits-250MSPS
  4 DAC 16bits-1000 MSPS
IFC-1420
  4 channels Downconverter linked to ADC
  2 channels Upconverters liked to DAC
  RF synthetiser + PLLs producing
  all clocks and LOs
RDC_1470v2
Hardware IOXOS technologies
-based of the LLRF feed back
System with New version of
the RF front-end received last week
Modification of the configuration
Characterisation to do (SNR, …)

## Slide 11: Timing Distribution
Timing disciplined by WR distribution µRTM
Requirements close to be finalized
Design will be started in November
Example of Schematic

## Slide 12: Timing Distribution
Courtesy : X. Lafay
Voie 1
Voie 0
Tests in progress to implement this solution to the FPGA of the IDROGEN board,
waiting the final requirements of the timing system planned before this end of year.
Configuration

## Slide 13: C&C Frequency Tuning system
Design and CAD schematic realized
Layout in progress at IP2I Lyon with a first prototype beginning of 2026.

## Slide 14: FTS : Piezo Amplifier
Adaptation in progress of a solution developed in the framework of the MYYRHA project by LPSC and IJCLab :
Modification of the layout of the two electronic boards due to obsolete components
Air Cooling system changed by Water cooling system
Limitation of the height of the rack 19” ( from 3U to 2U)
Courtesy: J-F Yaniche and S. Berthelot

## Slide 15: RF power systems : requirements
Parameters | Booster elliptic Single cell | ERL elliptic 5-cells
Frequency [MHz] | 801.58 | 
β | 1 | 1
Q0 | 1010 | 3,0 1010
r/Q [Ω] | 109,25 | 524
Qext required | 1,7 106 | 8,0 106
Bandwidth [Hz] | 471,5 | 100
[µs] | 337 | 1588
Eacc [MV/m] | 9,5 | 22,33
Lacc [m] | 0,187 | 0,918
Minimum required RF power (20mA) | 40 kW | 25,1 kW
RF Power amplifier output (20 mA) | ~45 kW | ~30 kW
Parameters | Booster elliptic Single cell | ERL elliptic 5-cells
Frequency [MHz] | 801.58 | 
β | 1 | 1
Q0 | 1010 | 3,0 1010
r/Q [Ω] | 109,25 | 524
Qext required | 1,7 106 | 8,0 106
Bandwidth [Hz] | 471,5 | 100
 | 337 | 1588
Eacc [MV/m] | 9,5 | 22,33
Lacc [m] | 0,187 | 0,918
Minimum required RF power (20mA) | 40 kW | 25,1 kW
RF Power amplifier output (20 mA) | ~45 kW | ~30 kW
Efficient FTS regulation
Coupling chosen

## Slide 16: RF system implantation
RF Circulator WR1150
RF power load WR1150
RF bi-direction Coupler WR1150
Waveguide WR1150
To implement with the IGLOO
constraints and for limiting the distance:
Booster Amplifiers +on the roof close to the booster
ERL amplifiers close to the cryomodule with probably one on the roof to keep a free space for the valve box
- Two options needed for the amplifier output position ( top and bottom) to facilitate the implantation
Images of WR1150 components extracted to web site ferriteinc.com, aft-microwave.com and megaind.com
Ferriteinc.com
microwave.com
292.1 mm x 146.05 mm

## Slide 17: RF Power Solid State Amplifier
Basic premise is : one RF power amplifier by cavity and lower RF power needed
Modularity interest : To adapt the RF power to needs
- for the booster in function of the Beam current phase
and regulation margins
- for the ERL cryomodule, in function of the recuperation performances
- Spread out the financial expenses
Call for tender preparation in progress of a
~10kW Solid State Amplifier upgradable to 60kW
JEMA FRANCE
example

## Slide 18: LLRF and RF power prospects
Thank you for your attention