## Slide 1: CP-5: Laser beam system
Eduardo Granados (SY-STI)
On behalf of the LP section

## Slide 2: Agenda
Optical boxes design and integration
Control systems
Diagnostics
Timing
Access and safety systems
Cabling
Services required
Compressor procurement

## Slide 3: Optical boxes design
N. Chritin
UHV turning box
Primary vacuum - transport
Similar to run 1, but narrower
Left-hand / right-hand versions
Design of supports is next
Built in-house, design stage not completed
Top cover attachment under study (hinges)
Clamping -> ISO-KF 100 for now

## Slide 4: Integration
Compressor 1 optical table split
UV lines – Good progress
IR lines
Laserlab
Split
Compressor 1
Compressor 2
Need anchors in ceiling for compressor lids

## Slide 5: Diagnostics
Laser transport lines:
  Position -> debate between quadrant detectors or cameras (binned)
  Pulse energy -> can use sum signal of quadrant or power meters
Laser beam delivery lines:
  Best overlap possible -> virtual line with minimal optical elements
  Timing -> For installation phase, cross-correlator
  UV shaping capability -> to be tested in CTF2 (upcoming stretcher + iris)

## Slide 6: Quadrant detectors
PROs:
High bandwidth / low latency
Robust and compact, great dynamic range (think of high power and low power shots)
Possibly does not need filterwheel
Insensitive to ambient light
Similar price to a CCD camera
Energy measurement possible
CONs:
Requires development, and integration into DAQs
No beam profile information (what if shape changes?)
Requires accurate centering (if large drift happens?)
Solution? Perhaps a combination of CCDs and QPDs…

## Slide 7: Multiplexing QPDs (BI team idea)
x1
y1
Delay
x2
y2
Delay
…
…
…
y2
x2
y1
x1
To acquisition card
Box 1
Box 2
Box N
…
Combiner
Combiner
Combiner
In principle, a single BNC-type cable connecting the boxes could act as ‘bus’, and the entire signal decoded using a single acquisition card

## Slide 8: IR timing
Unfortunately this device is located at the injection point of e- bunch to 2nd cell
PC1
PC2
X(2)
CCD
Reflective prism
Definition of IR beam crossing point:
For initial timing, cross-correlator will be needed
After synchronization is achieved, the correlator will be placed in the virtual lines

## Slide 9: IR timing
New T0 reference
Vapor source #2 is shifted downstream by 0.5 m, making the IR beam delivery path #2 longer. Easy to compensate by using the delay lines in the compressor #2 conditioning optical table.
BTV
BTV
BTV
BTV
Virtual plasma source 1
Virtual plasma source 2

## Slide 10: Motorization
Transport line steering
Delay control
Power control
Focusing control
Motorized iris
Delivery line:
UHV picomotors

## Slide 11: Controls
PLC
(MPS)
PLC
(picomotors)
LBDPs
Vetos / Access
Filter positions
Laser trigger
LSS
Screen Vetos
Flip mounts
UHV Pico motors
Power meters
Standa controllers
Position / power
CMW / beam pos
Delay / irises
“Beam transport”
“Beam delivery”
“Machine protection”
LBDPs / Shutters
BI

## Slide 12: Cabling overview
IRBL0.1
IRBL0.2
IRBL0.3
IRBL0.4
IRBL0.5
IRBL1.1
IRBL1.2
IRBL2.1
IRBL2.2
PP1
PP2
PP3
PP4
PP5
UVBL1
UVBL2
UVBL3
UVBL4
IRC2
IRC1
84
85
26
27
28
29
30
31
BI racks for cameras is #42
UVC1
UVC2
PP6
Pending to define diagnostics to complete cabling request!!

## Slide 13: Cabling overview
Essentially only laser beam controls and diagnostics so far
Not included:
Access systems
Laser safety systems
Timing and RF links
PLCs and interlocks (both MPS and LSS)
Ethernet for racks, powering
Vetos for screens…

## Slide 14: Open questions – some answers
IR beams
  Compressor lids -> need anchoring / crane
  Compressor #2 procured.
  Time 0 defined. To recalculate position of elements in IR line #2.
  To define: areas between LBDPs
  Access system requirements / modes of operation
UV beams
  Testing in CTF2 with improved relay imaging?
  Pulse shaping in transverse/longitudinal capabilities? -> Replicate capabilities existing in run 2a,b but keep the design open for future upgrades.
  Procurement of control components started
  Construction of UV stretcher started.

## Slide 15
Thank you for
your attention!

## Slide 16: Schedule of activities and spending profile