## Slide 1
Status of the Inner vertex layout for FCC-ee
Gherardo Ammirabile
Filippo Bosi, Andrea Moggi, Maurizio Massa,
Fabrizio Palla
INFN Pisa
CERN, DRD8 Collaboration Meeting
14/10/2025

## Slide 2
Layer 1:
15 staves of 6 modules each
Power budget ≈ 12 W
227.4 mm
13.7
Layer 2:
24 staves of 10 modules each
Power budget ≈ 32 W
Layer 3:
36 staves of 16 modules each
Power budget ≈ 77 W
356.2 mm
23.7
549.4 mm
35.6
Inner vertex
Gherardo Ammirabile, INFN Pisa
DRD8-Collaboration meeting

## Slide 3
Gherardo Ammirabile, INFN Pisa
Mockup of the vertex detector
Silicon modules replaced by a brass strip with the same thickness = 50 μm
Thermal load created by a bonded heater
W
H
Glue ~ 90 μm
CF strip = 360 μm
Brass strip = 50 μm
Heater = 150 μm
Stave dimensions (mm) |  | 
 | H | W
Design | 10.5 | 1.4
Real | 10.8 | 2.6*
* increase in thickness of Rohacell (best compromise between cost & manufacturing)
R
E
S
U
L
T
DRD8-Collaboration meeting

## Slide 4
Gherardo Ammirabile, INFN Pisa
Flowmeters
Absolute Pressure sensor
Temperature/Humidity sensor
Valve group
RTD
1600 mm
380 mm
Test section
6 bar
0.5 m3
Serbatoio
Settling chamber
Drier
Test section
Diffuser
Compressed air system
Designed to:
Be adaptable
Be controlled
Allow CFD result verification
DRD8-Collaboration meeting

## Slide 5
Gherardo Ammirabile, INFN Pisa
Staves under thermal testing
6
5
Stave 6
Stave 5
Power density (sensor) = 50 mW/cm2
Total power (each stave) = 2.2 W
The Middle section has the highest temperature
Without cooling > 65°C
With cooling < 40°C
Top view
First test: 60° angular sector of only layer 3
DRD8-Collaboration meeting
Chart: T_air_in=22.5°C, Stave n°6
| 40.299999999999997 | 60 | 84 | 103.4 | 127 | 163
Middle | 40.7 | 36.7 | 33.5 | 31.9 | 30.9 | 29.6
In | 29.6 | 27.5 | 25.9 | 25.5 | 25.3 | 25
Out | 38.4 | 34.8 | 31.6 | 30.3 | 29.4 | 28.4
ΔT | 11.1 | 9.2 | 7.6 | 6.4 | 5.6 | 4.6
Chart: T_air_in=22.5°C, Stave n°5
| 40.299999999999997 | 60 | 84 | 103.4 | 127 | 163
Middle | 40 | 35.6 | 32.3 | 30.9 | 30 | 28.9
In | 28.9 | 27.2 | 25.9 | 25.5 | 25.4 | 25.1
Out | 37.6 | 34.1 | 31.1 | 29.8 | 29 | 28
ΔT | 11.1 | 8.4 | 6.4 | 5.4 | 4.6 | 3.8

## Slide 6
Timeline for next steps:
Assembly on the same 60°angular sector of the staves of Layer 2 and Layer 1
Gherardo Ammirabile, INFN Pisa
Expected results: by the end of the year
Targets:
Flow rate to cool each layer
Pressure drop
Thermal connection between them
Details to study:
Air induced vibrations with optical instrument
Inlet shape:
Circular Slotted
60°
Staves:
5 for Layer 3
3 for Layer 2
2 for Layer 1
Advantage:
The compressed air system offers versatility, enabling specific testing for single and multi layer solution
DRD8-Collaboration meeting

## Slide 7
Thank you for your attention!