## Slide 1: CLIC electronics chapter
E. Van der Kraaij, L. Linssen, P. Roloff,
G. Blanchot, C. F. Rojas, P. V. Vyvre, J. Strube, X. Llopart
presented by A. Kluge
October 19, 2011

## Slide 2: Outline
Aim of chapter
Overview of detector readout channels
Implementation options for few subdetectors
Powering scheme
DAQ aspects
Summary

## Slide 3: Aim of chapter
Overview of detector readout requirements
Verifies consistency of requirements
Evaluates principle implementation feasibility
Summarizes priority areas for further research and development

## Slide 4: Scope of components
Front-end electronics
Data read-out from detector to off-detector electronics
Power pulsing
DAQ – data volumes

## Slide 5: Introduction
Electronics requirements resemble
  LHC detectors for
    pile-up and time stamping aspects with more precision
  ILC detectors
    for trigger-less readout
    high channel count
    low material budget
    power pulsing aspects
    Radiation similar to situation at ILC (factor 104 lower than LHC)

## Slide 6: Introduction
Requirements driven by:
  beam structure and high beam-induced background
  need for high precision measurements.
Interesting e+e− events are rare (at most one event per bunch train).
beam-induced background
  additional particles and high cell occupancies.
  recorded hit data must contain timing information for offline separation between physics and background hits
  Required timing information: few bunch crossings (1 ns to 10 ns )

## Slide 7: Introduction
0.5 ns time separation between bunch crossings
sequence of 312 bunch crossings in train
   156 ns long bunch train
bunch train repetition each 20 ms
CLIC
20 ms
0.5 ns
156 ns

## Slide 8: Introduction
challenging targets for impact parameter, track momentum and jet energy resolution.
compared to LHC the amount of material in the trackers needs to be reduced significantly.
cooling and power supply connections contribute strongly to material budget.
important to reduce the power consumption in front-end electronics and current through the power cables.
progress of micro-electronics technologies and corresponding reduction in power consumption will be counterbalanced by higher channel count and more complex functionalities.
In order to reduce power consumption
  use of the low accelerator duty cycle  power-pulsing scheme
  new cooling techniques

## Slide 9: Overview of sub detectors
overview of the readout takes CLIC_ILD concept as an example.
  channel number
  cell size
  occupancies during the bunch train per cell,
  expected data word on the total data volume
  time-resolution for individual hits
  possible readout sampling
Occupancies and data volumes
  Occupancies averaged and maximum values
  for full bunch train
  include charge sharing between pixels/strips.
  safety factors of 5 for incoherent pairs
  safety factors of 2 γγ → hadrons
  no safety for TPC

## Slide 10: 5 detector categories with similar readout specifications
Silicon pixel detectors
  Arrival time for 1 hit readout per train
  Zero suppression
Silicon strip detectors
  Arrival time for >1 hits per train
  Sampling of pulse at regular interval
  No zero suppression due to the large occupancies
TPC
  Analog pad readout for 1000 voxels per channel
Calorimeters
  Arrival time for >1 hits per train
  Sampling of pulse at regular interval
  Pulse heights higher than strip detectors  time resolution
  No zero suppression
Muon detectors
  Digital readout of > 1 hits per train with a multi-hit TDC
  Zero suppression

## Slide 11
Safety factor 2/5 for
incoherent pairs/γγ to hadrons, TPC no safety

## Slide 12: Overview of sub detectors
Readout studies for subdetectors just started
Implementation schemes based on LHC, ILC, other developments
Illustration of feasibility
examples
  pixel detector
  TPC
  Calorimeter
accommodate up to 5 hits per train in high-occupancy regions
Currently, some regions show occupancies exceeding this value further detector optimisation in the next project phase.

## Slide 13: Implementation Example: Pixel Detector
single point resolution: ≈3 μm
timing precision: 5-10 ns.
pixel sizes: 20 μm × 20 μm
material budget: 0.2% X0 per layer.
Power dissipation: 50 mW/cm2 with power pulsing

## Slide 14: Implementation Example: Pixel Detector
several technologies considered
   example based on a hybrid pixel detector and Timepix1 ASIC
ASIC 512×512 pixels with 20 μm × 20 μm
  each pixel
    4 bit arrival time measurement (16 time-slices of 10 ns)
    4 bits Time-Over-Threshold (TOT) measurements
    clock = time binning of 10 ns (100 MHz)
  Zero- suppressed data readout between trains
  Vertex Barrel:
    Occupancy 1%,  56 Megabytes per bunch train
  ≤ 65 nm CMOS technology
  Offline, the combination of the arrival time information and the time-over-threshold pulse width allows to derive precise arrival time information with time-walk correction
  The absolute time reference will be given by the time interval from particle arrival to the end of the bunch train. Thus the end of bunch train signal needs to be sent to all pixels with a controlled skew (below 1 ns) in order to ensure the requested time resolution. With such an architecture the reference clock can be distributed as a pixel-by-pixel inverted clock network which minimises coupling and digital power consumption as demonstrated in the Timepix1 chip
  Recently a complete front-end in 65 nm technology was produced in order to evaluate this CMOS technology node.

## Slide 15: Implementation Example: Pixel Detector
Analog circuitry dominant power consumer
  Expected power of 10 μW/pixel  2.5 W/cm2
power pulsing factor of ≈50  50 mW/cm2
  analog part on during 40 μs per bunch train
  digital part on ~ 400 μs
Data flow
   50 Mbyte/s instantaneous data transfer rate during digital power-on time
Material budget
  sensor thickness
     minimum detectable charge, preamplifier noise
  detector integration process
  Research targets Through-Silicon Vias (TSV)
    for both hybrid pixel detectors and integrated CMOS detectors.

## Slide 16: Implementation Example: TPC Pad Readout
drift length 2.25 m 
  maximum drift time ≈ 30 μs, depending on gas mixture
end plates: 1.5 million readout pads of 1×6 mm2 size
40 MHz read out during drift time per pad
10-bit pulse height data for 1000 time-voxels per pad
TPC hit occupancies
  max 32% of the time-voxels for inner row
  1% outer row
  no safety factors

## Slide 17: Implementation Example: TPC Pad Readout
SAltro readout based on ASIC (integrate comment of Lucie)
  low-noise programmable amplifier
  high-speed 10-bit ADC
  programmable digital filters
  Current SAltro-16 channels used for qualification of TPC prototypes
  Current SALTRO first system level TPC power pulsing studies
In a next phase
  optimised ADC with a reduced power consumption, smaller surface, more channels
  power pulsing
  reduced power consumption
An alternative TPC readout scheme using 55 μm × 55 μm pixels is also under study

## Slide 18: Implementation Example: Analog Calorimeter Readout
ECAL dynamic range 12 bits
HCAL dynamic range 14 bits
time resolution 1 ns (shower start)
Occupancies high in forward regions
  max 150% ECAL occupancy (5×5 mm2)
  max 5200% HCAL (3×3 cm2)

## Slide 19: Implementation Example: Analog Calorimeter Readout
  timing and energy information
    preamplifier-shaper peaking time slower than the time-stamping resolution, pulse length ~ 100 ns
    digitation at 40 MHz with 14-16 bits
  Comparison
    ATLAS liquid argon calorimeter electronics samples at 40 MHz
    Overall hit time resolution <1 ns was at system level

## Slide 20: Implementation Example: Analog Calorimeter Readout

## Slide 21: Implementation Example: Analog Calorimeter Readout
Alternative
  signal stored using fast analog memory
  digitised at low speed at end of bunch train
  today fast analog memory option 12-13 bits
  multi-stage amplification to cover dynamic range

## Slide 22: Implementation Example: Analog Calorimeter Readout
maximum data rate
  no suppression (no address bits)
  16 bits every 25 ns during bunch train of 156 ns
  + 100 ns shower development
  + 100 ns front-end shaping time
data transmission
  350 ns * 50/second * 120 *106 channels = 170 GB/s
  comparison
    ATLAS liquid argon calorimeter 1600 1.6 Gbit/s links

## Slide 23: Implementation Example: Analog Calorimeter Readout
power consumption for 40 MHz digitisation option
  dominated by ADC
  existing 16-bit 40 MHz ADCs 70 mW per channel during conversion
  future devices even less
  < 350 μs to recover after a power down
  consumption of de-randomising buffers and links
    low by using low power memories and minimising the number of links
  50 Hz power pulsing scheme
    ADC active time ≈18 ms every second  ~150 kW
power consumption for analog memory option
  low speed ADCs are used  150 μW per channel at 10 ksamples/s ~150 nW standby
  each train 14 samples per channel are digitised
  ADCs active during 70 ms every second
  ADC consumption ~10 μW per channel~1.2 kW
    consumption doubled if a two-gain scheme is used
    small amount of power needs to be added for the analogue memory

## Slide 24: Implementation Example: Analog Calorimeter Readout
power consumption for 40 MHz digitisation option
  dominated by ADC
  existing 16-bit 40 MHz ADCs 70 mW per channel during conversion
   ~150 kW
power consumption for analog memory option
  low speed ADCs are used  150 μW per channel at 10 ksamples/s ~150 nW standby
  ~1.2 kW
    consumption doubled if a two-gain scheme is used
    small amount of power needs to be added for the analogue memory

## Slide 25: Implementation Example: Analog Calorimeter Readout
readout solutions for BeamCal and LumiCal
  resemble those of ECAL and HCAL
  occupancy in BeamCal is very high
    possibility for readout is a gated integrator with correlated double sampling
    charge collected in time slices of about 10 ns
      either sampled by fast ADC
      or stored in an analog memory and digitised after the bunch train
      integrator is reset for the next train
      Signal amplitudes are obtained from subtracting subsequent samples.
      Subtraction acts as noise filtering
      concept also applicable for LumiCal.
      For low-occupancy regions in LumiCal alternative solution
        similar to ECAL and HCAL
        chain of fast preamplifier and shaper
        followed by digitiser and deconvolution algorithm applied to the ADC output is investigated

## Slide 26: Power delivery & power pulsing
Motivation
  high number of channels
  large masses and volumes for cooling systems and cables
CLIC beam structure
  bunch trains 156 ns
  repeated every 20 ms
   duty cycle 7.8 · 10−6 @ 50 Hz

## Slide 27: Power delivery & power pulsing
Vertex and silicon tracking system power
   need to reduce the material of the cooling systems
   reduce unwanted multiple coulomb scattering of charged particles
CLIC_ILD TPC tracker
  Dead material at TPC endplates is undesirable
   avoid photon conversions before the ECAL
ECAL/HCAL
  particle showers  compact to ensure
   optimal separation of clusters for the application of particle flow algorithms
   active layers as thin as possible and effective nuclear interaction length of the absorber material has to be as short as possible
 all sub detectors power pulsing

## Slide 28: Power delivery & power pulsing
DC-DC voltage step-down or low drop out (LDO) regulator and capacitor near the front-end
Powering branch
  back-end power supply
  long cables
  front-end voltage regulator
  front-end circuits

## Slide 29: Power delivery & power pulsing
Power switching applied selectively to various parts of circuit
  Analog off most of the time
  turned on only to acquire hit signal
digital and data transmission active during the bunch train gap
Turning on front-end electronics results in periodic in-rush current (several Amperes)
   voltage regulation circuit
Ideally power gating feature is implemented at the ASIC level
  Fast turn-on time of few tens of μs (typ 50 µs assumed)
  Configuration data are permanently maintained

## Slide 30: Power delivery & power pulsing
peak current delivered by a storage capacitor
  close to the front-end system
    voltage drop in example resulting from the charge transfer during the active time 100-200 mV with 5 mF capacitor
Electrolytic capacitors up to 400 mF are available
  however they are large

## Slide 31: Power delivery & power pulsing
load current, storage capacitor current and back-end cable current in the example configuration with an LDO regulator
  load current can be high, for a much reduced current in the back-end cable
  The load voltage drop amounts to 100 mV in this case.

## Slide 32: Power delivery & power pulsing
Similar results were obtained in the simulation for the DC-DC converter configuration
  radiation tolerant buck converter ASICs developed for the LHC experiment upgrades.
  voltage conversion ratio N reduces the input current by N compared to the output current and the losses in the back-end cable are reduced by N2.
  The conversion efficiency is typically better than 80%

## Slide 33: Power delivery & power pulsing
Initial power pulsing tests applied to ILC calorimetry demonstrated validity of the concept
Extensive R&D to demonstrate
  feasibility for application in all subdetectors
  particular for vertex and tracking

## Slide 34: DAQ aspects
possible architecture
  using available technologies for estimate of system dimension
ongoing improvement of data communication  new opportunities

## Slide 35: DAQ aspects

## Slide 36: DAQ aspects
readout block diagram
  front-end electronics directly connected to optical links
  data transferred to off-detector readout system (custom electronics or commodity computers).
    data concentrated, re-formatted and possibly zero-suppressed
  event-building switch connected to a processor farm.
Apart from zero suppression processor farm first place where data is filtered

## Slide 37: DAQ aspects
total data volume
  ~4 Gbyte per bunch train  200 Gbyte/s
Assuming data link bandwidth of 10 Gbit/s
  number of links is 160
Inefficiency
  detector segmentation and limited connectivity between detector sub-modules
  power pulsing
Assume efficiency reduction factor of 10 
  effective sustained data rate of only 1 Gbit/s per link 
  1600 optical links
  For comparison, CMS 80000 links

## Slide 38: DAQ aspects
If one off-detector readout processor has
  10 optical inputs
  & 1 output to event-building switch
   160 readout processors
Switches close to this requirement already exist
  160 10 Gbit/s input ports and 300 output ports
  Depending on number of processors in farm
    each of ports connected
      directly to a processor node
      or via distributor node consisting of a processor and a sub-switch.

## Slide 39: DAQ aspects
Based on current reconstruction algorithms and required CPU time to process a bunch train
   estimate number of required processing nodes
time for bunch train reconstruction
  3000 seconds (Intel® Xeon® E5520 CPU 2.27 GHz 2 Gbyte RAM) 
  150000 seconds processing time in a second of beam operation
today’s technology with four cores per CPU and two CPUs per node
  ~19000 processing nodes.
  Comparison: CMS event farm size in 2011, 7500 nodes
    In online farm full reconstruction not be needed
    Development of faster online algorithms
    Improvements in available technology reduce amount of nodes

## Slide 40: DAQ aspects
data suppression factor studies
  contributions from γγ → hadrons events can be reduced by a factor of 10 by dismissing out-of-time hits
  Identifying hits from incoherent pairs suppress the data volume further by a factor 5 to 10
Overall reduction of 15-20
  sustained data rate of ~10 Gbyte/s to permanent storage.
    Comparison ALICE 2011 5 Gbyte/s to disk.

## Slide 41: Summary
state of detector definition 
  preliminary specifications for detector front- end and data acquisition systems
specifications are driven
  short bunch crossing interval
  particle arrival time stamping
  reduction of material budget
    silicon tracker system material budget minimisation
    calorimeter electronics compact in physical space

## Slide 42: Summary
For silicon vertex detectors technologies approaches are available to pursue research to be conducted to define a full system concept
  research on the sensor and front-end electronics level
  field of low mass integration
  interconnect
  opto-electronics
  power pulsing
  cooling needs
  further detector optimisation
    to optimise cell sizes
    cell occupancy values in order

## Slide 43: Summary
TPC
  pad readout and pixel readout are in advanced development
  next phase pad readout
    profit from technology trends to achieve reduced power consumption
  next TPC pixel readout
    will also have more advanced functionalities on the chip

## Slide 44: Summary
Calorimeter
  material reduction in active calorimeter systems
    low power implementations
  Further R&D for
    detector layout
    occupancy
    front-end signal and shaping time especially in high occupancy regions

## Slide 45: Summary
Power pulsing
  For all detectors power pulsing
  research effort
    for front-end ASIC
    power pulsing system level
    detector specific studies to define feasibility and system requirements
    inner tracking systems integration issues
      control communication
      positioning of the power pulsing

## Slide 46: Summary
off-detector readout schemes and data acquisition system
  are manageable and no further research is required at present