## Slide 1
Background Suppression
Mark Thomson
University of Cambridge
This Talk:
Introduction
Simulation/Reconstruction
Backgrounds and Timing
Jet Finding
Beam Halo Muons
Conclusions
on behalf of CLIC Physics and Detector Study

## Slide 2: Introduction
CLIC provides the potential for e+e- collisions up to √s = 3 TeV
  But machine environment is much more challenging than ILC
    Background levels are high
    0.5 ns bunch-structure ➡ integrate over multiple bunch
    crossings of background
  One of the main aims of the CDR was to demonstrate possibility
  of precision physics measurements in this environment
  A second aim was to understand the requirements for the
  detector readout – guide future R&D direction
Both aims require detailed simulation and reconstruction
  Including pile-up from background is essential
  Significant software challenge
  Fortunately, not starting from scratch
    builds on existing work developed for the ILC

## Slide 3: Simulation and Reconstruction

## Slide 4: Simulation
For CDR defined two GEANT 4 detector models: CLIC_ILD and CLIC_SiD
 | CLIC_ILD | CLIC_SiD
Tracker | TPC, r = 1.8 m | Silicon, r = 1.2 m
B-field | 4 T | 5 T
ECAL | SiW | SiW
HCAL barrel | W-Scint | W-Scint
HCAL endcap | Steel-Scint | Steel-Scint
Both ILD and SiD have developed full GEANT 4 based detector simulations:
  Mokka (ILD) : already quite detailed, e.g. realistic gaps between detector
  elements for support/services
  SLIC (SiD): fairly detailed and very flexible
Extensively validated/used for the ILD and SiD LoI documents
Main modifications to existing detector models
  Thicker HCAL + Tungsten absorber for HCAL barrel
  Design of forward region + location of inner detectors

## Slide 5: Reconstruction
All studies use full event reconstruction
  Highly non-trivial exercise
    Need full reconstruction chain - developed for ILC (twice)
    Needs to be able to cope with CLIC environment
    Ideally would have common framework for CLIC_ILD and CLIC_SiD
      but only had common data format (nevertheless important)
ILC LoIs:
Simulation:
Tracking:
Particle Flow:
Vertex Reco.:
Mokka
SLIC
TPC Tracking
Silicon Tracking
PandoraPFA
LCFIVertex
IowaPFA
ILD:Mokka/Marlin
SiD:SLIC/org.lcsim
JAVA

## Slide 6: Reconstruction
Simulation:
Tracking:
Particle Flow:
Vertex Reco.:
Mokka
SLIC
TPC Tracking
Silicon Tracking
PandoraPFA
LCFIVertex
SLICPandora
Overlay:
MarlinPandora
Overlay
Overlay
All studies use full event reconstruction
  Highly non-trivial exercise
    Need full reconstruction chain - developed for ILC (twice)
    Needs to be able to cope with CLIC environment
    Ideally would have common framework for CLIC_ILD and CLIC_SiD
      but only had common data format (nevertheless important)
CLIC CDR:
ILD:Mokka/Marlin
SiD:SLIC/org.lcsim
JAVA

## Slide 7: Software Challenges
Major effort to develop and validate software for CLIC CDR
  + two parallel software frameworks
A number of significant challenges
  Tracking work in high occupancy
  environment
  High hit multiplicities in
  calorimeters
  Reconstruction times/memory
  footprint
  GRID production with background
  overlay
Despite challenges and a few remaining rough edges …
  All studies in CDR use full reconstruction including overlay from
  most significant background gg→ hadrons
Fig. 5.9

## Slide 8: Backgrounds and Timing Requirements

## Slide 9
Background from gg→ hadrons
Pair Background largely affects very low angle region
Background in calorimeters, central tracker dominated by gg→ hadrons “mini-jets”
At 3 TeV, average 3.2 events per BX (approximately 5 tracks per event)
For entire bunch-train (312 BXs)
  5000 tracks (mean momentum 1.5 GeV) giving total track momentum : 7.3 TeV
  Total calorimetric energy (ECAL + HCAL) : 19 TeV
Largely low pT particles
20 BXs
Irreducible background – it is physics
Fig. 2.3

## Slide 10
Backgrounds in the Calorimeters
Detector | gg→ hadrons
ECAL endcaps | 11 TeV
ECAL barrel | 1.5 TeV
HCAL endcaps | 6 TeV
HCAL barrel | 0.3 TeV
Total | 19 TeV
Calorimeter backgrounds per bunch-train (3 TeV)
ECAL
Calorimeter backgrounds per bunch-crossing are manageable, ~ 60 GeV
Hence want to integrate over as few as possible BXs
Tight timing requirements – O(ns) !
….
….
0.5 ns
Fig. 2.8

## Slide 11: Calorimeter Timing
But at ns timescale there are issues…
Can’t just “assume” arbitrarily short time-stamping capability
Time needed to accumulate all calorimetric energy (due to low energy
particles, nuclear break-up etc.) significant compared to 0.5 ns Bx
HCAL resolution depends on time window
Steel (Endcap): ~10 ns
Tungsten (Barrel): ~100 ns
Fig. 6.3
Fig. 6.3

## Slide 12: CLIC Timing cont.
Tension between calorimeter integration time and desire
to minimize number of BXs of gg → hadrons background
Fig. 2.10
e.g di-jet mass resolution from isolated
decays
< 10 BX

## Slide 13: CLIC Timing cont.
Similar conclusions for reconstruction of high mass states
  e.g. reconstructed di-jet mass in
But < 2.5 ns not long
enough for calorimetry
Fig. 2.10
< 10 BX

## Slide 14
Timing Requirements:
  integrate over > 20 BXs to accumulate calorimetric signals
  integrate over < 5 BXs for acceptable gg → hadrons backgrounds
  …
The Solution - a combination of:
  excellent time resolution
  high granularity calorimetry
  sophisticated reconstruction

## Slide 15
CLIC Timing Strategy
Based on trigger-free readout of detector hits all with time-stamps
  assume multi-hit capability of 5 hits per bunch train
Assume can identify t0 of physics event in offline trigger/event filter
  define “reconstruction” window around t0
….
….
Hits within window passed to track and particle flow reconstruction
Subdetector | Reco Window | Hit Resolution
ECAL | 10 ns | 1 ns
HCAL Endcap | 10 ns | 1 ns
HCAL Barrel | 100 ns | 1 ns
Silicon Detectors | 10 ns | 10/√12
TPC (CLIC_ILD) | Entire train | n/a
Sufficient calorimeter
integration window
CLIC hardware
requirements

## Slide 16: Reconstruction in Time
PandoraPFA
Tracking
TPC : 30 ns*
Si trackers : 10 ns
ECAL: 10 ns
HCAL (End): 10 ns
HCAL (Barrel): 100 ns
“10 ns of tracks”
Additional background rejection still required post reconstruction
1.2 TeV
gg → hadrons
Sufficient time
window for
calorimetry
*TPC readout integrates over whole train – only 60 BXs used due to limitations in heritage (LEP ) tracking software
Input to reco:

## Slide 17: Reconstruction in Time
After reconstruction have a list of particles (PFOs):
  charged particles – mostly matched to clusters
  photons – EM clusters
  neutral hadrons – clusters
tCluster
High granularity calorimeter - even low energy clusters have many hits
  calculate energy weighted truncated mean time of each cluster
    calo hit times corrected for time-of-flight (straight-line)
    sub-ns resolution
  use times to reject clusters
  also can reject associated tracks
    account for helical propagation time
Reject PFOs from background
  e.g. neutral hadrons in Endcap
Neutral hadrons

## Slide 18: PFOSelection
Table B.2
Only apply to “low” pT PFOs
Three sets of timing cuts applied in reconstruction
  Loose, Default, Tight

## Slide 19: Impact of Timing Cuts
1.2 TeV
Table 12.1

## Slide 20: Impact of Timing Cuts
85 GeV
1.2 TeV
Table 12.1
Reject 93 % of background energy and < 1% of physics event
  much more effective than simple pT cut

## Slide 21: Forward Events
+
TightSelectedPFOs
Also effective in forward region
  qualitative example for hard case,
  3 TeV

## Slide 22: Jet Finding

## Slide 23: Jet Finding at CLIC
At LEP, preferred jet-finding algorithm: Durham kT
  all particles in event clustered into the jets
  not appropriate for CLIC
Events at CLIC
  significant background from forward-peaked gg → hadrons
  events are often boosted along beam axis (beamstrahlung)
  “hadron collider” type algorithms more appropriate
Jet finding at CLIC
  studied for benchmark physics analyses (FASTJET package)
  preferred option “kT” with distance measure
    invariant under longitudinal boosts
  particles either combined with existing jet or beam axis
    reduces sensitivity to gg → hadrons

## Slide 24: Jet Finding at CLIC
e.g.
  two jets + missing energy
TIGHT
timing
Fig. 12.7
Using Durham kT à la LEP
  all particles clustered
  timing cuts are
  effective

## Slide 25: Jet Finding at CLIC
e.g.
  two jets + missing energy
TIGHT
timing
Two “weapons” against background: timing cuts + jet finding
Fig. 12.7
“hadron collider” kT : R = 0.7
  much of background
  clustered with beam axis
  timing cuts do less work
  relative impact of timing
  and jet-finding depends
  on event topology

## Slide 26: Does it all work ?
Aim was to show that can make precise measurements in CLIC environment
  topic of talk by Frank Simon (quantitative results)
Pair production and decay:
Test of di-jet mass reconstruction
82 %
17 %
Full Simulation with background
Separate using di-jet invariant masses (test of PFA)
Fig. 12.9
Here - just a taster (a particularly challenging case)

## Slide 27
Fig. 12.25
Take a close look at the reconstructed W mass in
  here the timing cuts do most of the work…
  jet finding alone gives broad peak at 100 GeV
  with timing cuts not too far from ideal no background case
kT alone
kT + PFO sel.

## Slide 28: Beam Halo Muons

## Slide 29
Simulated events with entire bunch train of beam halo muons
  for study assumed a bad case: 5 muons/BX crossing detector
Beam Halo Muons
In 150 ns from start of bunchtrain:
  ECAL
    Total = 1.5 TeV (54k hits)
    Barrel = 0.8 TeV (18k)
    Endcap = 0.7 TeV (36k)
  HCAL
    Total = 10.8 TeV (128k hits)
    Barrel = 5.3 TeV (32k)
    Endcap = 5.5 TeV (96k)
Most work for CDR concentrated on impact of
  also looked at beam halo muons
gg → hadrons
12 TeV
For this very conservative
level of background:

## Slide 30: Software Mitigation
Three steps of background reduction
  Initial reconstruction window of 10 ns (50 ns in HCAL barrel)
  Timing cuts at cluster level (TightPFOSelection)
  Build in beam halo muon rejection into particle flow reconstruction
For very conservative assumption of 5 muons per BX
2.2 TeV
420 GeV
30 GeV
Readout window
TightPFOSelection
+ dedicated reco. Alg.
Background rejection very effective: due to high granularity of calorimeters

## Slide 31: Impact on Physics
Tested in by looking at W reconstruction in
  Sample of 500 GeV hadronic W decays
  Again very conservative assumptions (5 muons/BX)
Two effects observed
  Extra energy from clusters from beam halo muons: 30 GeV
  Energy of reconstructed jets also biased “pick” up hits from muons: 30 GeV
Readout window
TightPFOSelection + reco. alg.

## Slide 32: Impact on W Reconstruction
muon halo (5/BX)
gg → hadrons
muon halo (1/BX)
Compare W mass reconstruction
  no background
  gg → hadrons
  5 muons per BX (very conservative)
  1 muon per BX (conservative)
Worst case as pattern recognition not optimal
Conclude: a beam halo muon background of 1 muon/BX is acceptable
  Machine background likely to be much lower than this

## Slide 33: Conclusions
Understanding of impact of background studied in detail
  Full GEANT 4 simulation + full reconstruction
  Developed strategy to mitigate effects of background
    requires high granularity in space and time
  Defines detector timing requirements - guide future R&D
I believe we have achieved the initial goal
  Demonstrated ability to perform high precision physics
  measurements in CLIC machine environment
  [More in Frank Simon’s talk on physics benchmarks]