## Slide 1: DRD 8 WP1 Introduction and Status Report
C. Gargiulo (CERN)
F. Palla (INFN Pisa)
CERN, 2 September 2025

## Slide 2
The Vertex Region of Future Particle Physics Experiments
  Development of the next generation mechanics for advanced vertex layouts, including
    Curved and tilted silicon sensors
    Low radii vertex and retractable detectors
    Ultra-light, high-vacuum leak tight beam pipes and vessels
    Low mass hardware alignment systems for future vertex detectors
    Machine Detector Interface and impact on Detector
Robots in the HEP Experimental Caverns
  Development of robotic systems for inspection, monitoring, and first intervention in future high energy physics experiments even during the operation of beams
    Legged ground robotic platform
    Aerial robotic platform
    Mini-robots swarm and mobile mesh network
DRD8 – WP1 projects

## Slide 3: DRD8 –WP1.3 (new!)
Will study the mechanics for a large gaseous central tracker.
It will simulate, design and build a prototype of a stereo drift chamber with unprecedented dimensions.
  Study the carbon fibre based mechanical structure as well as the tension recovery system for the wires.
  Careful selection of the wires with the help of a company for coating as light available wires are either electrically resistive, or prone to corrosion.
  Current interested institutes
    JCLAB Orsay (France)
    INFN Bari and Lecce (Italy)
We will hear today

## Slide 4
DRD8 – Deliverables and milestones

## Slide 5
D1.1.1 Ultra-thin beam pipes
  On track
    IHEP: CepC
      Design study done
      To be fabricated
    LNF: FCC-ee
      Design study done
      Prototypes delivered and under test (in aluminium)
  Big differences
  Started
    CERN: Carbon fibre based for FCC-ee
DRD8 – WP1.1
LNF
IHEP
 | CepC | FCC-ee
Inner layer thickness (mm) | 0.20 | 0.35
Outer layer thickness (mm) | 0.15 | 0.35
Gap width (mm) | 0.2 | 1
Inner gold coating shield (µm) | 10 | 5

## Slide 6
M1.1.1 & M1.1.2 Vertex detectors (curved and tilted detector mechanics)
  On track:
    CERN: Retractable and curved detectors mechanics
      Retractable mechanic prototype in hand
    Pisa: air cooled reinforced stave
      Module mechanics designed and few prototypes done
      Air cooling setup up and running
DRD8 – WP1.1

## Slide 7
D1.1.2 Mock up and integration
  On track
    CERN: ALICE ITS3
      Mechanics FPC for power/signals & wire bonds and dummy modules
    IHEP: CepC
      Design finished
      Prototype to be built
    LNF- Pisa & CERN: FCC-ee
      Design finished
      Prototype to be built
DRD8 – WP1.1
IHEP
LNF

## Slide 8
D1.2.1 & M1.2.2 Legged robots and robotic airships in magnetic field
  On track:
    CERN EP R&D and BE-CEM-MRO: Legged robots
      Sensorless EM motor withstanding magnetic fields up to 100 mT
      Model for estimation of mechanical disturbances induced by magnetic field on EM motors
      Control system for rejection of magnetic disturbances on EM motors
    CERN EP R&D: Blimp
      Autonomous flight inside cavern background magnetic field
      Virtual environment for control system validation
DRD8 – WP1.2

## Slide 9
D1.2.2 Legged robots and robotic airships in cavern
  On track:
    CERN EP R&D and BE-CEM-MRO: Legged robots
      Mobility test in the cavern (no magnetic field, no beam)
      Test in the cavern background magnetic field monitoring the field intensity throughout the test
    CERN EP R&D: Blimp
      3D spatial mapping of the cavern background magnetic field
DRD8 – WP1.2

## Slide 10
M1.2.1 & M1.2.3 Mobile mesh network
  On track:
    CERN EP R&D:
      Developed a mobile mesh network
      and tested it in a controlled environment
DRD8 – WP1.2
CERN Network
Remote Control Station
CERN Network Not Available

## Slide 11: News
DRD8 Collaboration meeting
  October 14 2025 at CERN
  https://indico.cern.ch/event/1573561/
DRDC Jamboree
  October 29 2025 at CERN
  https://indico.cern.ch/event/1552124/