## Slide 1: Longitudinal beam stability RF system studies MD#4: 8 h on Friday 4th November 13:00-21:00 (+2h ramp down)
LSWG 18 October 2011
E. Shaposhnikova for MD team: T. Argyropoulos, C. Bhat, P. Baudrenghien, T. Bohl, A. Burov, T. Mastoridis, J. Esteban Muller, G. Papotti, J. Tuckmantel, U. Wehrle + …

## Slide 2: Motivation and previous results
Multi-bunch beam:
  to study long-lasting dipole oscillations after injection during filling
  In MD#1: 4 different fillings, varying the total beam current (keeping intensity per bunch constant), the number of bunches per batch and the distance between batches
Single bunches
  to study loss of Landau damping as a function of longitudinal emittance, beam energy and intensity
  Damping of dipole oscillations on the flat bottom for single bunches with emittances > 0.4 eVs, V=8, 6, 3.5 MV with phase loop on
  Dipole instability during the ramp for bunches with emit = 0.4 eVs and small, but non-zero initial phase oscillations for Beam2 with phase loop on, no instability for Beam1
  Dipole and quadrupole(?) instability on the flat top with phase loop on
  Dipole instability during ramp for longitudinal emittances < 0.7 eVs with phase loop on one bunch only (off)

## Slide 3: Part I: Multi-bunch beam @450 GeV
Beam: 12b+36b+36b at 50ns to study dependence of longitudinal stability on emittance and voltage at injection.
0.5 eVs, 8 MV (DR settings, higher voltage better for IBS?)
0.5 eVs, 3.5 MV (for reference, 2010 situation)
0.7 eVs, 6 MV (larger emittance, better for IBS)
0.4 eVs, 6 MV (situation with SPS low γt : no controlled emittance blow-up plus lower SPS voltage at extraction?)
Keep previous beam (0.4 eVs, 6 MV) and reduce the RF FB gain (all cavities). Observe bunch-by-bunch phase and detect the onset of coupled-bunch instability. Keep AGC on.
0.5 eVs, 6 MV (nominal situation in 2011). Refill with 12b+72b+72b spaced by ½ turn. Intensity 1.4E11/bunch, nominal transverse emittances. Reduce the RF FB gain, observations as in (5)

## Slide 4: Part II: ramp with 8 single bunches
8 bunches per ring (9 equally spaced buckets) + pilot with
filling pattern: 401 +(k-1)*3960, k=1,..9
longitudinal emittance: controlled blow-up in SPS 0.35-0.8 eVs
transverse emittance: nominal
injected intensity: (1.2-1.4) x1011
Phase loop settings:
  Inject with phase loop ON (as used in normal operation with reference on all bunches), let it damp
  Open phase loop. Wait (for transients).
  Ramp with phase loop OFF.
  → Identify the instability mode: quadrupole (observed May 2010) or dipole mode (observed in last MDs). Acquire bunch profiles.