## Slide 1
25 ns MD
Status and request
G. Arduini, V. Baglin, H. Bartosik, P. Baudrenghien, N. Biancacci, C. Bracco, S. Claudet, O. Dominguez Sanchez De La Blanca, J. Esteban Muller, B. Goddard, W. Hofle, G. Iadarola, JM Jimenez, E. Metral, M. Pojer, G. Rumolo, B. Salvant, E. Shaposhnikova, R. Steinhagen, L. Tavian; D. Valuch; W. Venturini Delsolaro, F. Zimmermann

## Slide 2: 25 ns MD
Setting-up
Reference meas. variable spacing
6.325 ms
732 + 660 b
3.625 ms
1092 + 1020 b
0.925 ms
1020 + 156 b
Limited by pressure rise on MKI8. Now limited to 2.5x10-9 mbar. No injection interlock level during the scrubbing run and pressures of up 10-8 mbar reached.

## Slide 3: Heat load
Reference meas. variable spacing
6.325 ms
732 + 660 b
3.625 ms
1092 + 1020 b
L. Tavian

## Slide 4: Vacuum
Reduction of approx. Factor 4 in all the Cold Warm Transition of Stand Alone Magnets after 2 hours
After that period possible to inject >1.4x1011 p/b with no important vacuum instability so far  would be good to have another period of ~24 h this week to test potential effects on high intensity 50 ns operation
G. Bregliozzi

## Slide 5: Emittances along trains

## Slide 6: RF stable phase shift along batches
E. Shaposhnikova, JF Esteban Muller

## Slide 7: Aim
Explore the operation with ~2000 bunches with 25 ns and give input for the understanding of the vacuum dynamic behaviour in the machine
This test should take place well before the end of the proton run to have the possibility to test the (hopefully) positive impact on 50 ns operation at high intensity and it would provide vital input for the operation in 2012.
2100 bunches (trains of 72 bunches - 25 ns spacing ) x 1.1x1011 = 1400 bunches (50 ns spacing) x 1.5x1011

## Slide 8: Proposal
Possibly end of this week (Friday):
  Setting-up of injection with 25 ns beams (72 bunches) and checks – 2-3 hours
  Accumulation of up to ~2100 bunches in trains of 72 bunches spaced by 925 ns and measurement of heat load and vacuum evolution, possibly inject a few trains of 288 bunches (16 hours)
  Reference measurements for SEY, reflectivity (3 hours)
  Recovery (1 hour)
Test the impact on 50 ns operation pushing intensity to ~1.5x1011 p/bunch during week-end and following week.