AWAKE Run 2c: Layout Downstream of the Plasmas
Streak room ‘2’
Spectrometer
quadrupoles
Start of CNGS decay pipe
Streak room ‘1’
Laser insertion
mirror
Possible end of vacuum
(tbd)
Spectrometer
 dipole
End of the 2nd plasma

---
p+, Laser Beam Alignment
 Must ensure sufficient diagnostics for proton beam and laser pulse alignment
Longer distance allows for
 more accurate alignment
Plasma 2
2 screens
and BPMs?
Electron
injection
dipole
Double use?
Injection region  very challenging
Hot & very limited space
2 screens (p+ & ph)
and BPMs?
19.08.2025
Plasma 1
Angle = 0.1 mrad
 Important for beam alignment
p+, ph

---
Proton Beam Size and Position
CNGS
Decay Pipe
Spectrometer dipole off
Plasma 2
Beam position will change based on dipole current
 Not ideal for alignment references
Spectrometer dipole on
Plasma 2
H / V [m]
H [m]

---
Beam Instrumentation
 orders approximate
Camera array
BCT
?
?
?
Edu
Only diagnostics for
backward ionization
May need more space
Diagnostics for forward ionization
May be able to reuse parts from Run 2b

---
To discuss today…
Are we missing anything?
  - What parts of what was mentioned today is already included?
Possible screen to align p+ and laser in the second plasma
How to deal with the large proton beam size / displacement towards the end of the beamline and the movements?
  - Is a there a screen/BPM design that would work?
Presenter | Presentation Title