## Slide 1: Beam Instrumentation Pre-TDR work package breakdown
Robert Kieffer, and Thibaut Lefevre, on behalf of the CERN BI group.
September 22th 2025, BI FCC meeting

## Slide 2: Aim of the talk
Today we will describe the proposal for the Work Package 3.4.7 dedicated to the FCC Beam Instrumentation management for the Pre-TDR phase (2025 -2028)
Task 1: Coordination, Collaboration and Cost/Industrialisation
Task 2: Beam Intensity and Tune Monitoring
Task 3: Beam Loss Monitoring
Task 4: Beam Position Monitoring
Task 5: Transverse Beam Size/Profile Monitoring
Task 6: Longitudinal profile Monitoring
Task 7: Energy Calibration and Polarisation
Task 8: Luminosity monitoring

## Slide 3: Task 1: Coordination, Collaboration and Cost/Industrialisation
External collaborations for the FCC beam instrumentation R&D
KIT : EOS for longitudinal profile
ALBA / Uni Milano : X- ray Heterodyne Near Field Speckles for transverse profile.
EIC Brookhaven : synergies on polarised beam and lepton machine instrumentation.
IJCLab : polarimetry and related laser developments.
SOLARIS : BPM test line / Tune measurement developments
KEK : Synchrotron radiation transverse profile techniques.
(Apologies if any institute is missing from that list)
Industrialisation and cost optimisation
Solutions needed for instruments that will be produced in large quantities : BPMs , BLMs

## Slide 4: Task 2: Beam Intensity and Tune Monitoring
Current stage
Collect the specifications for beam intensity and tune measurements in the FCCee collider rings from others WP in terms of resolution, accuracy and dynamic range.
Design of tune monitoring systems adapting existing technologies.
A dedicated line for R&D is foreseen to be installed at the Solaris light source
Work to be started after the project approval
Design both DC beam and bunch-by-bunch intensity measurement systems

## Slide 5: Task 3: Beam Loss Monitoring
Current stage (conceptual stage)
Collect the specifications for the FCCee BLM system linked to Machine protection and operation needs: fast bunch by bunch monitors and slower (turn by turn) monitors
Design a BLM monitoring system capable of identifying losses from main rings vs booster
-> Simulation for the placement of ionisation chambers currently on going.
Next steps
Design Beam loss monitors insensitive to SR X/g-rays.
Design a Rad-hard, rad-tolerant arc cell electronic acquisition system
Prototyping phase will only start in 2028 when budget will be available.
The large number of units to be produced (10000) will require three years industrialisation study for cost optimization.

## Slide 6: Task 4: Beam Position Monitoring
Current stage focussed on arc BPM
EMG Simulations of the pickup design to evaluate signal strength and heat load (CST).
Test at CLEAR of similar BPM, new line for R&D in Solaris.
Collect the expected BPM precision requirement : 10um after BBA
Next steps
Mechanical design of the BPM integrated into the machine layout and associated tolerances.
Design of the water cooling system
Prototyping and validation of new designs in lab and beam tests (CLEAR and Solaris).
Work more actively on IR BPM requiring more precision
Design of a cost efficient acquisition system for turn by turn, rad-hard electronics in bunker.
Industrialisation study for cost optimisation (expected need of >9000 BPM )

## Slide 7: Task 5: Transverse Beam Size/Profile Monitoring
Current stage
Design and prototype of a Beam Size monitoring system based on Synchrotron Radiation interferometer
  Simulations of the Synchrotron radiation source properties and of the SR extraction system.
  X-ray monitor systems using Pinhole imaging systems and interferometric systems HNFS (collaboration with external partners)
Next steps
Design of a Beam Profile monitoring system based on Laser wire scanner (similar to polarimeter)
Design of a Beam imaging system (‘screens’) reusing standard solution adapted to FCCee needs

## Slide 8: Task 6: Longitudinal profile Monitoring
Current stage
Design and prototype of a Bunch Length monitoring system based on Electro-Optical (EO) Spectral Decoding with low impedance EO pick-up (tests at KARA)
Design and prototype of a Bunch Length monitoring system based on beam induced radiation
Testing of incoherent Cherenkov Diffraction radiation (KEK and IOTA)
Testing of coherent radiation monitoring (test at CLEAR)
Next steps
Design of a bunch-by-bunch, turn-by-turn acquisition system with sub-picosecond time resolution
Design of radiation source adapted to FCCee: Synchrotron radiation or Cherenkov Diffraction radiation

## Slide 9: Task 7: Energy Calibration and Polarisation
Current stage
Development of the polarimeter system mainly followed within the EPOL work package.
(Polarimeter + Kickers + study on beam polarisations + study on energy calibration)
Design of the laser system (with IJClab), and laser transport (SY-STI).
Specifically in BI
Integration of the polarimeter in both LCC and GHC optics for performances comparison.
Simulation of the Laser Compton Backscattering chamber and extraction chamber.
Simulation of the sensor response for the Compton products
Development of the fitting algorithm for 3D polarisation measurement (with IJClab),
Next steps
Test detector technology in existing facilities
Civil engineering for the integration of the polarimeter and laser system

## Slide 10: Task 8: Luminosity monitoring
Current stage
BhaBha monitoring sensors for the bunch by bunch luminosity, collaboration with KEK LumibelleII project who have a similar monitoring system based on Diamond and LGAD sensors.
Beamstrhalung profile monitoring instrument screens in the dedicated BS extraction channels to feedback on the IP tuning. Very high radiation levels expected need for non-invasive monitors to avoid damage (new PhD starting on this in October 2025 in BI)
Next steps
Test of potential technologies for those instruments in existing facilities.
Design and integration in the four experimental insertions

## Slide 11: Conclusion Outlook
There is a lot of different topics with a very heterogeneous level of advancement.
Huge amount of work ahead to design the needed instruments and industrialize them.
Up to now the instrumentation related work has mainly been focused on the FCC collider rings but the booster and injector will also require dedicated studies.
Discussion started with PSI for the injectors and with CEA for the booster.

## Slide 12: Thank you for your attention.
12
Robert Kieffer