## Slide 1: Thermal insulation for the Einstein Telescope (ET) beam pipe vacuum system
Carlo Scarcia on behalf of the ET beampipe vacuum studies group at CERN
CERN-PIEP meeting, 29th August 2025

## Slide 2
Why ET beampipes ultra high vacuum?
The ET beam pipes require ultra-high vacuum (UHV) to minimise the noise due to gas pressure ﬂuctuations along the laser trajectory (scattering and photon phase shift).
= gas density  pressure distribution
= gas optical polarizability
= interferometer arm length
For a gas species, [3]:
Where:
Detectable signal
[3] M. E. Zucker and S. E. Whitcomb. “Measurement of optical path fluctuations due to residual gas in the LIGO 40-meter interferometer” (1994)

## Slide 3
Why ET beampipes ultra high vacuum?
Sketch inspired from ET design report update 2020 and XIII ET symposium (2023).
Dimensions in mm.
Partial pressure requirements
H2 ≈ 10-10 mbar
H2O ≈ 10-11 mbar
HxCy (> 100 amu) < 10-14 mbar
Dimensions
Beampipes internal diameter: 1 m
Total beampipe vacuum system
length: 120 km

## Slide 4: How we can achieve UHV?
Sojourn time (): time spent by a molecule on a surface with a binding energy at temperature
with
After an initial volume evacuation, the pressure decay (pumpdown) is limited by the water vapour molecules adsorbed on the tube surface with an inverse law of the pumping time:
Two solutions:
1. : Cryogenic pumping the tubes
2. : Heating aka “bakeout” the tubes
Start bakeout
End bakeout

## Slide 5: The bakeout of ET beam pipes
To efficiently bakeout the ET beam pipes, we can use direct joule effect (beam pipe = conductor).
Electrical test of a power supply on an
ET corrugated prototype
(400 A max)
LIGO bakeout
electrical heating power
(LIGO-G970071-00-P)

## Slide 6: Why do we need insulation?
Limiting heat losses = limiting needed current = lower costs
The system is foreseen to be baked one, maximum two times over 50 years of operation (150°C max).
Kmineral wool : 3.65E-7 ΔT2+1.44E-4*ΔT+4.89E-2 W m-1 K-1, ΔT: 130°C (150°C-20°C). Convection coefficient (h): 5 W m-2 K-1 (calm air, no forced ventilation)

## Slide 7: The problem of LIGO and VIRGO approach
Insulation: 15 cm mineral wool (double layer of 7.5 cm) permanently installed.
For ET
Surface to be covered: ~380.000 m2 (120 km)
Cost of insulation (mineral wool 10 - 15 cm): ~48 – 60 €/m2
Total insulation cost [€]: ~ 18 - 23 M €
Other concerns:
Depreciation cost if permanently installed?
Storage?
Sustainability?
Cleanliness and dust generation?
Safety (smoke, fire generation, installation, etc.)?
Images courtesy of M. Zucker and R. Weiss

## Slide 8: Requirements for the ET insulation
 | Target value | Maximum value
Insulation thickness [cm] | 10 | 
Form | Reusable shells | 
Maximum operating temperature [°C] | 400 | 300
Thermal conductivity k [W m-1 K-1] (at 20°C) | < 0.04 | < 0.05
Thermal conductivity k [W m-1 K-1] (at 150°C) | < 0.05 | < 0.06
Reaction to fire (EN 13501-1) | Euroclass A1 | Euroclass A2
Smoke production (EN 13501-1) | S1 | S1
Droplets generation (EN 13501-1) | D0 | D0
Water vapour resistance factor | <1 | Not specified
Mechanical properties yet to be determined
No explicit requirement from the project (ET)

## Slide 10
Source: KNAUF insulation