## Slide 1: Injection foils and handling system
Review on PSB 160 MeV H- Injection
9-10 November 2011
W. Weterings
C. Boucly, M. Hourican, R. Noulibos, Y. Sillanoli

## Slide 2: Abstract
The linac4 beam will be injected horizontally into the PSB by means of an H- charge-exchange injection system using a graphite stripping foil to paint the beam into the required emittance.
This presentation will describe the hardware requirements and constraints, the performance specifications of the stripping foil and the conceptual design of the foil exchange unit and motorisation.

## Slide 3: Outline
Introduction
Requirements
Constraints
Stripping foil specifications
  Stripping efficiency
  Beam losses
  Emittance growth
Conceptual design
Motorisation
Outstanding issues

## Slide 4: Requirements
Number of foils
  The foil lifetime is expected to be dominated by mechanical effects or by accidents.
  A minimum of 4 foils per ring, and per type, should be available in the exchange unit.
Positioning and adjustment
  Horizontal movement of 8 mm will be needed for injection adjustment.
  No vertical adjustment necessary, the foil should cover the total vertical acceptance of the PSB.
  The foil position known and adjustable at the level of ±0.1 mm.
Alignment
  Mechanism aligned with ±0.5mm precision, including manufacture and assembly tolerances .
Vacuum isolation
  Possibility to isolate foils from PSB vacuum to avoid foil damage due to differential pressure.
  Interlock to avoid venting of the PSB vacuum system before isolation of foil exchange unit.
Radiation considerations
  Reduced radiation exposure of personnel during replacement, repair or maintenance (ALARA).
  Remove complete systems without dismantling and replaced by spare assembly.
Foil recuperation
  Foil dust-debris recuperation system for activated foils that break or disintegrate during operation or maintenance (inhalation or pollution inside vacuum).

## Slide 5: Constraints
148mm

## Slide 6: Constraints
148mm
Top-View
~120mm
  Small vacuum tank shared with BI (Camera and BTV)
  Limited space between BSW magnets, Vacuum equipment and support structure
  Entrance area with concrete wall and outside passage PSB

## Slide 7: Foil specification - 1
Stripping Efficiency
  H-, H0 and p+ yield as a function of stripping foil thickness.
  Stripping efficiency of > 99%
  Foil thickness < 150 µg/cm2
Beam loss by nuclear scattering
  Beam loss through nuclear scattering as a function of stripping foil thickness, assuming 10 and 25 hits per proton on average, for zero and matched dispersion, respectively.
  Uncontrolled beam loss < 10-4 level
  Foil thickness < 250 µg/cm2

## Slide 8: Foil specification - 2
Thickness
  Foil thickness of 200 μg/cm2 (~1 μm) has been chosen.
The benefits of a thicker foil outweighs the disadvantages of extra foil heating, beam losses and emittance blow-up.
  Composition
    Carbon Stripping foil material (Amorphous carbon or diamond form)
    Thermal stability
    High sublimation temperature
    Radiation resistance
    sufficient strength
    low Z (atomic number Z=6)
Self-supported carbon foils having natural isotopic composition are made by evaporation from a vacuum arc onto glass microscope slides or substrates. Evaporated carbon foil bulk density is 1.7-2.0 g/cm3.
Emittance growth by Coulomb scattering
Emittance growth by multiple coulomb scattering as a function of foil thickness, assuming 10 and 25 hits per proton on average. The required LHC beam emittance was  2 π ·µrad (now “as small as possible”).
  Emittance growth < 0.15-0.25 π·µrad
  Foil thickness < 200 µg/cm2
160MeV

## Slide 9: Foil specification - 2
Foil Dimensions
  Sufficiently large to cover the incoming H- beam fully.
  Small enough to avoid larger numbers of foil hits per proton during injection.
  Foil holder outside the acceptance of the PSB.
  Foil and support size and clearances required for zero dispersion (left) and matched (-1.4 m) dispersion (right) at injection point.
Foil changer system pulley (Ø24mm)
Beam envelope (Ø54mm)

## Slide 10: Foil heat generation
Temperature rise in carbon foil for CNGS beam. The peak is about 280 K.
Thermal dynamic stresses currently studied by technical student
Evolution of maximum temperature in carbon foil for 1.3  1013 p+ CNGS beam injected at 1.2 s intervals. The equilibrium peak temperature is about 650 K.

## Slide 11: Foil exchange unit - 1
Vacuum Valve
Foil Mechanism
Compensation Bellow
Motorisation
Bellow
Retraction system
Injection zone

## Slide 12: Foil exchange unit - 2
Foil “in beam” position
Foil “retracted” position
Valve can now close to isolate system
Minimum required length for retraction

## Slide 13: Foil mechanism
Limited space for foil rotation
Possibility for ‘in situ’ foil changing
Valve Closed
Avoid interference with BTV screens.
Valve open

## Slide 14: Foil carrier
Foil support band from NEC* Foil/Target Changer Model
* National Electrostatics Corp.
7540 Graber Rd., P.O. Box 620310, Middleton, WI 53562-0310 USA
Magnetic rotary vacuum feedthrough*
VSS25 Phytron
stepping motor
90° angle worm gearbox
Foil frame with bracket for
micro-switch foil position indexation
Foil fitting on frame (manipulation, gluing, storage, transport )
Types of foils:
- ACF-200 Carbon
- MicroMatter DLC
- ?

## Slide 15: Foil positioning control
Horizontal movement:
260mm stroke, 8mm rough injection adjustment
Horizontal movement: 90mm stroke, 2 mm fine adjustment, speed ~1mm/sec
4-10 foils / carrier
Radiation hard VSS25 Phytron stepping motor
0.45° step size, ~1160 steps/foil change
Radiation hard Yaskawa JKPM-9ZFG DC servo motor with reduction gear

## Slide 16: Prototype
NEC FS6 foil changer used in Pelletron® Systems
316 SST belt with riveted foil holder attachments
Simulating vacuum chamber walls and DN100 flanges

## Slide 17: Space limitation - 1
Blocking of the passage acceptable ?
~20 cm
Present Situation
Future Situation

## Slide 18: Space limitation - 2
Obstruction of the outside PSB passage.
Limited space for removal of complete foil mechanism.
Possibility to remove part of the wall to be discussed.
~20 cm

## Slide 19: Summary & Outstanding issues
Stripping foil mechanism with 4-10 foils, replacement of single foils or complete system to be studied (ALARA).
How to recuperate damaged foils and debris inside the vacuum system.
Vacuum isolation system foreseen, but will valve shock damage foils? (manual or automatic valve)
Foil thickness < 200 µg/cm2, handling and foil fitting issues to be studied.
Prototype with ACF© and MicroMatter© DLC foils, other suggestions?
Guidance system to prevent bellows sagging to be studied.
Space between equipment and concrete wall tight.
Limited space for support structure (integration still to be studied).
Influence BSW2-3 leak field on foil performance (see talk J. Borburgh).

## Slide 20
Thank you for your attention