## Slide 1
Marion Vanwelde
19th September
Parametric IR optics studies for key parameters

## Slide 2: IR design – Radial build
Tungsten shielding thickness:
Still need to determine which power load is acceptable from the cryo perspective
Tungsten shielding of 2.53cm probably not sufficient
Aperture= W shieldingcm
Local heat extraction issues must be addressed, considering a representative coil section and the cooling channels design.
Cryogenics issues
@D. Calzolari
Study the impact of increased W shielding thickness on the optics and collider performance
1
Discussion at annual meeting & https://indico.cern.ch/event/1573241/
Notes: Daniele summarized the results regarding radiation and power loads to the final focusing magnets. Power deposition was computed for several shielding thicknesses inside the quadrupoles ([shielding+clearance] of 4cm, 4.5cm, 5cm, and 6cm); for the dipoles in the chicane, a total clearance of 6 cm was set to avoid hot spots.
For the arcs, the design target for total power to the cold mass is 1-2% of the radiated power. If we can slightly exceed this limit for the IR quadrupoles, a total clearance of 4.5 cm could be acceptable, resulting in approximately 10W/m of power deposition per unit length in the first quadrupole of the FF triplet (IQF1(_a, _b)).
The longitudinal distribution of the heat deposition along the magnets indicates that the most exposed section of the IP is the third part of the first focusing quadrupole (IQF1_b).
One cryogenic issue highlighted during the annual meeting was local heat extraction. To address this, further studies were required, considering representative coil sections, the design of the cooling channels, and the distribution of the deposited heat load.
Patricia presented some preliminary studies using helium cooling from outside the coil, Nb3Sn as the magnet material, an operating temperature of 4.5K, and a cooling length of 50 m. The maximum acceptable deposited power (W/m) strongly depends on the maximum allowable temperature of the coil (𝑇_ℎ𝑜𝑡). In addition, it is important to remember that the heat load to the cold mass also depends on the absorber temperature, and an extra 1-4W/m may need to be added to account for this. The results will differ for HTS magnets, particularly because the effective thermal conductivity of HTS coils must be considered.
current radial build, a clearance of only 0.1 mm is assumed for the liquid helium
adjust the tungsten shielding thickness depending on the power load (some IR quadrupoles show lower power deposition, which could allow for reduced tungsten thickness).
In terms of beam optics, increasing the tungsten shielding leads to higher maximum 𝛽-functions in the IR (as well as stronger chromatic effects), and increases the overall length of the interaction region. Although the increase in 𝛽-function from 4cm to 5cm of total clearance does not seem dramatic, 𝛽_𝑦 reaches 1000 km for 5cm clearance, which is significantly higher than what was expected in the original design of the collider lattice (~600km).

## Slide 3: IR design – Interconnects length & L*
L*+ nozzle-quadrupole interconnect
  Need to account for the interconnect length between the nozzle and the first triplet quadrupole (currently not included in design: L* = 6m).
  Either increase L* (modify IR layout) or reduce detector length.
Interconnect length >1m
  Current assumption: 30cm  Increase by more than a factor of 3!
  Longer interconnects Increased IR length and modified optics.
Include interconnects of 1m in the IR design and evaluate their impact on collider performance.
3
Study the impact of an increased L* on optics and collider performance
2
Sensitivity analysis of the 3 parameters to assess their individual impact
Notes: Realistic space requirements for magnet-magnet interconnects in IR
▪ Presently, there is no space included in the present layout
▪ In order to account for the necessary space, likely have to increase L* which in turn will increase the
length of the final focus  increase also the maximum beta function, so the chromatic effects and performances of the collider
Realistic space requirements for nozzle-magnet interconnect
The presently assumed interconnect lengths are probably not sufficient
Possibly need to increase the interconnect length, which will increase the length of the final focus
Increase the length for element interconnection
no space included in the current design
More realistic IR baseline: account for more realistic interconnect length: L* (to account for space between the detector nozzle and the first quad of triplet)
To move toward a more realistic IR baseline, we should account for more realistic interconnect lengths in the lattice design:
We need an initial estimate of the space required between the detector/nozzle and the first quadrupole of the IR triplet. This additional length will impact L*. Although the Final Focusing length is not dominated by L*, we still need to assess the L* increase effect on the collider performance.
The interconnect length between magnets: 𝐿_𝐹𝐹𝑀𝐿 > 1000/1200 mm. Additional length should also be considered if longitudinal shielding is required. The IR lattice design should be updated to account for this increased interconnect length; the current lattice design assumes only 30cm between the IR quadrupoles.
I will try to account for a larger L* (7.5 m and 8m) in the current lattice and assess the impact on collider performance (first matching a new interaction region for both L* values and evaluating the maximum beta functions accordingly). Although I believe that an increase of 0.5m in L* alone will probably not significantly affect the collider performance, it is the accumulation of changes in the IR lattice (including the increased L*, longer interconnects, and thicker tungsten shielding) that will be challenging and likely degrade the overall performance.

## Slide 4: IR design – collider performance
Baseline lattice:
Sensitivity studies carried out independently for the 3 parameters to assess their individual impact on collider performance
Long Straight 110m
Chicane
No combined-function
L* = 6m
Short drift = 30cm
Aperture = Bore radius = + 4cm
set with AG plot (T = 4.5K)
Performance evaluation:
Maximum , , (chromatic effects)
Momentum acceptance for several transverse DA
Sextupole strength in the Chromatic Correction section
Goals & Beam constraints
(=)
Required performance:
Transverse DA: 3-4
Momentum acceptance: 2-3
(Total clearance)
~20m

## Slide 5: Sensitivity study on total clearance
Study the impact of increased W shielding thickness on the optics and collider performance
1

## Slide 6: Sensitivity study on total clearance
The IR lattice has been adapted for each value of W shielding thickness (total clearance: 3.5 to 5.5cm) using similar matching and optimization procedures.
The length of the long straight is kept at 110m.
The gradients of IR quads are maximized according to AG plot constraints.
The ratio between the maximum of and in the final focusing triplet is kept nearly constant ().
The 𝛽-functions in the ring (except in the IR) and the working point are similar across all updated lattices.
Long Straight 110m

## Slide 7: Results - and W functions
Larger W shielding thickness  higher maximum and aperture, and lower gradients in the IR quadrupoles. The maxima of W increase accordingly
Maximum-functions increase by ~35-40% as total clearance goes from 3.5cm to 5.5cm.

## Slide 8: Length of the Final focusing triplet
An increased W shielding thickness leads to larger magnet apertures  smaller gradients, longer magnets.
Doublet quads lengths also adapted to match the CC
W thickness increases
W thickness increases

## Slide 9: Performance and sextupole strenght
No significant degradation of momentum acceptance by increasing the total clearance, BUT large increase of sextupole strengths in the CC (chromatic effects increase):
  Larger magnetic field in sextupole magnets, larger feed-down for given offsets;
  Lattice more sensitive to errors.
DA on 100 turns
Change in 𝑘2→ ~15 T change in sextupole

## Slide 10: Total clearance – Tune spread
Large differences in tunes for off-momentum particles, but similar energy dependence across all updated lattices.
Difference in tunes for particles with
Notes: Remarques: Performances for the different 𝛽^∗ strongly depend on small optimizations and phase advances in the machine:
Possible particle loss when crossing resonance (perhaps not observed here due to the discretization used for momentum acceptance computations).
Similar tune dependence on energy for all updated lattices
The tune spread with energy offset remains significant, covering a large area of the tune diagram:
though it decreases as 𝛽^∗ increases
The tune shift with momentum offset remains significant, though it decreases as 𝛽^∗ increases
  Still covering a large area of the tune diagram
   Possible particle loss when crossing resonance.
Tune shift dominated by high-order chromaticities Mitigation strategies to be investigated.
Performances strongly depend on small optimizations and phase advances in the lattice  Better optimisation required for each 𝜷^∗
Large tune differences for off-momentum particles, but similar energy dependence across all updated lattices

## Slide 11: Sensitivity study on L*
Study the impact of an increased L* on optics and collider performance
2

## Slide 12: Sensitivity study – L*
Minimum space between the nozzle and the first final focusing quadrupole: ~1-2m (to be confirmed) : L* = 6m + (1-2)m
Scan of L* from 6m to 9m
The IR lattice has been adapted for each value of L* using the same procedure and matching/optimization methods as before (maximize triplet quads field, maintain nearly the same ratio and -function shape, same tune dependance on energy)
Notes: (maximize magnetic field in triplet quads, same ratio of 𝛽, similar 𝛽-functions shape, same tune dependance on energy)

## Slide 13: Sensitivity study on L* - Results
Increase of the maximum -functions of ~25% (L* from 6m to 9m).
No significant momentum acceptance degradation by increasing L* (L* small compared to triplet length); Increase of sextupole strengths in the CC.
𝑘2 for sextupoles in CCY

## Slide 14: Sensitivity study on interconnects length
Include interconnects of 1m in the IR design and evaluate their impact on collider performance.
3

## Slide 15: Baseline preliminary changes
Adapt the IR lattice to keep the magnet lengths reasonable (~10m, to be confirmed):
  The triplet defocusing quadrupole (IQD1) and last focusing quadrupole (IQF2) are split into 2 pieces each.
  Impact 30cm interconnects is small compared to 1m.
D. Novelli, https://indico.cern.ch/event/1410212/
Maximum magnetic field based on AG plots for 800k€/m (vs. 1200k€/m)
  Only minor differences between the two curves
~20m

## Slide 16: Sensitivity study- interconnects
The IR lattice has been adapted for each value of interconnect length (30cm, 60cm, 100cm), using the same procedure as before.
The quadrupole fields have been maximized for each piece, assuming IR quads can be custom-made.
The interconnects length are changed only in the IR, not (yet) in other parts of the collider.
Similar 𝛽-functions, working point and tune dependence on energy across all updated lattices
Notes: Comme maintenant o a plusieurs bouts d’aimants, évidemment je dois maximiser les champs dans les 2 bouts d’aimants (changer les strengh dans ls 2 bouts de quads).
Quads sur mesuredans l’IR (de toute manière apertures seront ajustées
Une fois que c’est bon, je vais commencer mon étude de sensibilité en fonction de la longueur d’interconnects. Pour le matching de l’IR, je me base sur ce que j’ai fait avant pour l’étude de sensibilité pour W shielding. Le principe est que je match toujours les champs magnétique à leur maximum, puis je joue sur les longueurs des aimants dans l’IR pour :
Garder plus ou moins le même ratio entre le maximum de 𝛽_𝑥 et 𝛽_𝑦
Garder la même longueur de long straight (entre le triplet et les 2 derniers quads)
Matcher la cellule de l’IR, puis matche l’IR dans la CC ok de la « baseline ».

## Slide 17: Interconnects - Results
Larger length of interconnects
Increase in maximum -functions
 Increase in the magnet apertures  smaller gradients.
Increase of the maximum -functions of ~20-35% for interconnects from 30cm to 1m.

## Slide 18: Interconnects - Results
Similar conclusion as for the the W shielding thickness sensitivity study: no significant changes in momentum acceptance for DA ~ 2-3, but a significant increase in sextupole strength in the CC
𝑘2 for sextupoles in CCY

## Slide 19: Conclusion and Next steps

## Slide 20: Rough estimate of combining effects
First rough estimate of maximum if we combine the effects:
Assume interconnects length of 1m, L*=8m, and total clearance of 4.5cm
~ 1064
Increase of ~15% in
for L* = 6m  8m
Increase of ~8% in
for clearance = 4cm  4.5cm
-functions >1000 km in both planes ( ~ 1300km, ~ 1050km).
Quadrupole aperture at limit (35.2cm) – to be confirmed.
Huge sextupole strengths, high sensitivity to errors in IR triplet and CC sextupoles.
Sensitivity studies carried out independently for the 3 parameters to assess their individual impact on collider performance
More precise results  complete lattice design

## Slide 21: Conclusions and next steps
For each parameter (total clearance, L*, interconnect):
  Impact on optics: maximum can exceed 1000km
  Tighter constraints on magnet apertures and field quality
  Higher sextupole strength required in the CC section, and increased lattice sensitivity to errors.
Need to combine the effects
Performances strongly depend on small lattice optimizations
   Better optimisation required for each updated lattices.
Explore slight improvements of the IR triplet
  Evaluate the impact of splitting the first focusing quadrupole in the IR triplet, with 1 m interconnects.
To assess the impact on luminosity: fix maximum -functions to chosen values and adapt (and the luminosity accordingly).
Notes: Étudier l’impact d’avoir 1, 2, 3 morceaux avec interconnects + long
Evaluate the impact of the number of pieces on the first focusing quad in the IR triplet, with 1 m interconnects.
Autre:
High (unrealistic) magnetic field values in CC and arcs Try to limit the magnetic field for the lattice with 4 cm W shielding.
Long drift for IP (𝐿^∗=6𝑚), triplet for the final focusing, chicane to reduce the BIB, long straight section to smoothly reduce the 𝛽 functions without increasing W functions, 2 quads at the end to control lattice functions.
The IR long straight sections result in many secondary particles from muon decay that accumulate. A chicane before the FF helps remove these particles as much as possible before reaching the nozzle, with parameters depending on the BIB requirements.
No combined-function magnet in FF triplet. IR quadrupole magnetic fields have been adapted to respect the AG plots constraints for HTS quadrupoles with T = 4.5K.
The first quadrupole is divided into three magnets to maximize the field gradient.

## Slide 22
Thank you for your attention
The lattice presented is still a work in progress and subject to change in the future

## Slide 23: Back-up slides

## Slide 24: Impact of interconnects for IQD1/IQF2
For the same line, splitting IQD1 et IQF2 into two pieces has a small impact for interconnects of 30cm, but a significant impact for interconnects of 1m.
Interconnect length of 30cm
Interconnect length of 1m

## Slide 25: Interconnects - and W functions

## Slide 26: L* - and W functions

## Slide 27: Muon Collider: Interaction region
Montague chromatic functions:
W describe variations of Twiss 𝛼 and 𝛽 for (small) momentum offsets.
The very small at the IP induce very large -function in the strong focusing FF quadrupoles, resulting in significant chromatic effects.
 Very large W functions at the end of the IR.
 Need for a local Chromatic Correction section.