## Slide 1
Application to join
DRD4 collaboration
Prof. Dr. Ivor Fleck
Experimental Particle and Medical Physics
Universität Siegen

## Slide 2: Working group
experimental particle physics and medical imaging
member of ATLAS since 2002, BabyIAXO since 2019, ILD since 2014, LCTPC since 2014
previous experiments: D0 at Tevatron, OPAL at LEP, ZEUS at HERA
working on medical imaging using SiPMs since 2015
group has currently: one postdoc, four PhD students, five master students
academic positions:
Professor of Physics since 2005
Dean of Research since 2015
Founding Chairman “Centre of Particle Physics Siegen”
Collaboration Board Chairman LCTPC collaboration since 2018
Ivor Fleck

## Slide 3: Equipment - SiPMs
 | 2x2B (AFBR-S4N22P014M) | 4x4B (AFBR-S4N44P014M) | 6x6B (AFBR-S4N66P014M) | 3x3OH (S13361-3075CS) | 3x3NH (S13360-3075UVE)
Manufacturer | Broadcom |  |  | Hamamatsu | 
Active Area [mm²] | 2 x 2 | 3.72 x 3.63 | 6 x 6 | 3 x 3 | 3 x 3
Cell Size [µm] | 40 |  |  | 75 | 
Fill Factor [%] | 60 | 75 | 83 | 82 | 78
N_SPADs | 2464 | 8334 | 22428 | 1600 | 1584
3x3OH
3x3NH
Broadcom

## Slide 4: Equipment – Readout Electronics
Oscilloscope
Rohde & Schwarz
Capturing waveforms for offline charge integration via LAN using Pyvisa
4 Channels
1GHz and 5GSa/s
TOFPET v2c
PETsys Electronics
Online ToT and QDC measurements
64 Channels
30 ps time binning
KLauS6
University of Heidelberg
Online charge integration
36 Channels
Optimised for small photon numbers
200 ps time binning
Oscilloscope
Tektronix
Capturing waveforms for offline charge integration via LAN using Pyvisa
4 Channels
4GHz and 25GSa/s

## Slide 5: Further Lab Equipment
Dark Box
Climate Chamber

## Slide 6: Waveform Comparison for Broadcom SiPMs
Fast component and slow component of waveforms are observable
Larger active area leads to larger capacitance → low-pass filter
Larger SiPMs have suppressed fast and slightly longer slow component
4pe amplitudes
4pe amplitudes

## Slide 7: Dark Count – Staircase Plots
Analysing noise characteristics with staircase plots (using KLauS or TOFPET)
1pe plateau gives DCR
Ratio of 2pe plateau over 1pe plateau gives CTP
3x3NH
2x2B

## Slide 8: Noise versus Temperature using climate chamber
DCR depends exponentially on temperature
DCR decreases by ~40% when reducing temperature by 10°C
2x2B

## Slide 9: LED Measurements
Indirect measurements of the PDE
Bias voltage optimisation
12 ns pulse for LED
LED pulse as external trigger for data taking
LED colour | Wavelength in nm
Red | 625
Amber Yellow | 585
Green | 540
Blue | 460
NUV | 420
UV1 | 375
UV2 | 355
UV3 | 300 - 320
UV4 | 260 - 270
2x2B
UV4

## Slide 10: Indirect Measurements of the PDE
3x3NH
2x2B
→ Optimal bias voltage depends on wavelength for Broadcom
→ Optimal bias voltage consistent over different wavelengths for Hamamatsu

## Slide 11: SiPM Arrays produced in house
3x3 array of 4x4B
3x3 array of 2x2B
5x5 array of 2x2B
under construction

## Slide 12: CMOS SPADs
working together with electrical engineering:
Institute of Analogue Circuits and Image Sensors, Prof. Choubey
developing SPADs with UV sensitivity and
integrated digital counter
measurement of PDE ongoing
Signal for 260 nm LED

## Slide 13: New Research Facility: INCYTE
Siegen University invested 100 M€ in new research building.
Building is completed and will be operational in 2026.
Research facility for sensor processing
600 m2 of clean rooms

## Slide 14: Contribution to DRD4
Main interests:
Development and characterization of SiPMs, especially with small pixels (< 1mm2)
NUV sensitivity of SiPMs
digital SiPMs with 2.5D oder 3D integration
CMOS SPAD development
contributions to WG1, WP1
For WP4, task 4.1, we are using UV transparent PMMA (n=1.49 at 400 nm and transmission down to 270 nm), which greatly improves the number of produced Cherenkov photons.
Funding:
research fund for development of Compton Camera for medical imaging, still running until mid 2027, including characterization and development of SiPMs.
2 PhD students who can work 0.2 FTE on DRD4, one to two master students for thesis project ( which takes one full year in Germany), Ivor Fleck 0.2 FTE
further fund applications foreseen once topics are defined

## Slide 15: The Working Group
From left to right:
Yazeed Balasmeh
Lars Maczey
Devanshi Mehta
Prof. Dr. Ivor Fleck
Daniel Berker
Mara Fries
Atharva Bahekar
Darshil Vagadiya
Rutwik Kachare