## Slide 1: Update on longitudinal impedance simulation of SPS-TECA goniometer
H. Pommerenke for the Impedance Team
Impedance Working Group #106
07-Oct-2025

## Slide 2: Context
Installation of new crystal assemblies inside the TECA.41777 in SPS LSS4
References: L.S. Esposito https://indico.cern.ch/event/1578706/ ECR: [pending], EMDS [pending] “install new optimized crystal assemblies during the YETS 2025-26 to reduce the losses in LSS2 during the SPS slow extraction to the North Area and test their performance during MD in 2026.” (ECR draft)
L.S. Esposito

## Slide 3: Changes in geometry
Before: 2 identical crystal holders
After:
  downstream crystal holder: 1 → 4 crystals
  Larger openings in RF shield necessary → expect higher coupling to shielded volume

## Slide 4: Impedance simulation
CST longitudinal impedance simulation (bunch σ = 44 mm/c = 0.15 ns)
Slight worsening of spectrum, but still ok for beam (exact frequency of peaks hard to simulate)
Modes shift downwards by ~15 MHz because of higher coupling through shield
~50 % higher impedance and on beam spectral line
Split in two because of asymmetry in RF shield

## Slide 5: Impedance simulation
280 MHz

## Slide 6: Impedance simulation
564 MHz

## Slide 7: Impedance simulation
593 MHz

## Slide 8: RF power loss
Assuming SPS-LIU beam
Straight-forward calculation taking raw CST results: 0.6 W → 9 W (x15 power loss) but this depends on exact position of impedance peaks
Worst-case scenario evaluated (C. Zannini): 30 W total, 0.1 W on crystal → Still OK ??