## Slide 1: Prototyping Thermal Control Tuning Unit for a Photonic μ-Ring Modulator
Paweł Kozłowski (EP-ESE-BE) BE Seminar Talk
15.10.2025

## Slide 2: Silicon Photonics Links for Particle Detectors
Particle sensor
PIC
>> 100 m Single-mode fibre
Photodiode
Modulator
Fiber coupler
ASIC
OPTO
FPGA
System concept under development in the
EP R&D WP6 project
Future particle detectors
  up to 100 Gbps per fibre (VTRx+ 10Gbps)
  Small size, high level of radiation tolerance (~10x compared to VTRx+)
  Low power
    Locate laser outside of radiation zone
Driver ASIC
  Co-packaged with the PIC
Single mode fibre
  Supporting long distance ~1km
Proposition for Opto-layer:
  Photonic Integrated Circuits (PICs)
WP6
  EP-ESE-BE/ME
Focus of the presentation
Notes: Future particle detectors require significantly higher data transmission rates—up to 100 Gbps—far exceeding the capabilities of current optical links such as VTRx+. Typically, detectors interface with electrical ASIC that control the optical transmitters, which in turn propagate the signal in optical domain. In the new system a key innovation is relocating the laser source outside the radiation zone, which enhances radiation hardness and improves power efficiency. Single-Mode Fiber enables long-distance transmission, allowing backend processing electronics to be located far from radiation areas. To enable efficient electronics-to-photonics data conversion, a Photonic Integrated Circuit (PIC) is proposed. It offers high-speed data transmission and enhanced radiation hardness, making it well-suited for deployment in high-energy physics environments.

## Slide 3: Silicon Photonics for Optical Readout of Particle Detectors
PIC based transmitter
  Micro-ring modulator (MRM)
  Fast electro-optic modulation by means of MRM
    CMOS silicon chip
    Modulating the beam over p-n junction embedded in the ring
    Intensity modulation of the optical power in the coupling region
  Wavelength Division Multiplexing (WDM)
Notes: Plasma-dispersion effect
Optical phase modulation in the ring
Intensity modulation of the wave in the coupling region due to input and in-the-ring wave interference By electro-optically modulating the ring resonator, electrical data is encoded into an optical signal.

## Slide 4: Micro-ring
b’1100
Gbps
kHz
Modulator
Resonator
λ-laser
Notes: The diagram illustrates the previously introduced structure: the microring resonator. It features three ports, each accompanied by a representative diagram. Input Port: Shows a single-wavelength signal generated by a laser and propagating through the waveguide. Through Port: Displays a transfer function with filtering behavior, where certain wavelengths are attenuated or passed. Drop Port: Represents the complementary response to the through port, effectively forming an inverted version of the through port filter.
For the purpose of clarification of the topic, to visualize both time and frequency domain I will introduce a concept of intervals in which the incoming wave of specific wavelength is handled. Keep in mind: in reality, these changes occur rapidly and continuously, but visualizing them as intervals helps us better understand the underlying mechanisms.

## Slide 5: Micro-ring Modulator Control Loop
kHz

## Slide 6: Control System Perspective
kHz
Conversion of physical quantities to ADC and DAC code
Notes: Move operating point to the optimal modulation window by performing initialization procedure.
Keep the setpoint by counter-reacting against environmental changes.

## Slide 7: Control System Perspective
kHz
Startup
Notes: Move operating point to the optimal modulation window by performing initialization procedure.
Keep the setpoint by counter-reacting against environmental changes.

## Slide 8: Control System Perspective
kHz
Startup
Initialization procedure
  Power/temperature sweep
  Find the setpoint that is offset from Max. photodiode value
  Mitigates process-induced variations
Notes: Move operating point to the optimal modulation window by performing initialization procedure.
Keep the setpoint by counter-reacting against environmental changes.

## Slide 9: Control System Perspective
kHz
Startup
Initialization procedure
  Power/temperature sweep
  Find the setpoint that is offset from Max. photodiode value
  Mitigates fabrication process-induced variations
Run PID to keep the setpoint
  Counteract environmental disturbances
Notes: Move operating point to the optimal modulation window by performing initialization procedure.
Keep the setpoint by counter-reacting against environmental changes.

## Slide 10: Prototyping the System with FPGA and discrete components
Ongoing SPRINT development controlling the PIC
  Temperature Control Unit
PIC + ASIC + control system
  Completeness of Multiphysics simulations
  Costly ASIC manufacturing runs
Notes:   Developing a system that validates and prototypes the thermal control unit for SPRINT ASIC
  Starting from a prototype
  Following the work done colleagues from u-electronics group and opto-team and updating the prototype system in parallel
  Using FPGA and analog components for validating the ASIC implementation
  Aim: enhancing the stability of data-carrying photonic signals through thermal tuning of a microring modulator.
  10Gbit/s -> 25Gbit/s
  WDM -> 100Gbit/s
FPGA fw
Sweep from 2V to 0
Finding max point
Offsetting it
Running PID
Slow switching off the heater
The filter is not really one filter. CIC is just for downsampling. A FIR is needed for the rest of filtering.
The update refers to change requirements (e.g. heater power)
PID - a control algorithm used in engineering to maintain a desired output by minimizing the error between a setpoint and a measured process variable

## Slide 11: Prototyping the System with FPGA and discrete components
Ongoing SPRINT development controlling the PIC
  Temperature Control Unit
PIC + ASIC + control system
  Completeness of Multiphysics simulations
  Costly ASIC manufacturing runs
Develop a prototype
  FPGA
  Analog structures compatible with ASIC ADC and DAC
Notes:   Developing a system that validates and prototypes the thermal control unit for SPRINT ASIC
  Starting from a prototype
  Following the work done colleagues from u-electronics group and opto-team and updating the prototype system in parallel
  Using FPGA and analog components for validating the ASIC implementation
  Aim: enhancing the stability of data-carrying photonic signals through thermal tuning of a microring modulator.
  10Gbit/s -> 25Gbit/s
  WDM -> 100Gbit/s
FPGA fw
Sweep from 2V to 0
Finding max point
Offsetting it
Running PID
Slow switching off the heater
The filter is not really one filter. CIC is just for downsampling. A FIR is needed for the rest of filtering.
The update refers to change requirements (e.g. heater power)
PID - a control algorithm used in engineering to maintain a desired output by minimizing the error between a setpoint and a measured process variable

## Slide 12: Prototyping the System with FPGA and discrete components
Ongoing SPRINT development controlling the PIC
  Temperature Control Unit
PIC + ASIC + control system
  Completeness of Multiphysics simulations
  Costly ASIC manufacturing runs
Develop a prototype
  FPGA
  Analog structures compatible with ASIC ADC and DAC
Using development board and IP Bus for fast prototyping
Aim: continue development of SPRINT with fast validation of the system
Notes:   Developing a system that validates and prototypes the thermal control unit for SPRINT ASIC
  Starting from a prototype
  Following the work done colleagues from u-electronics group and opto-team and updating the prototype system in parallel
  Using FPGA and analog components for validating the ASIC implementation
  Aim: enhancing the stability of data-carrying photonic signals through thermal tuning of a microring modulator.
  10Gbit/s -> 25Gbit/s
  WDM -> 100Gbit/s
FPGA fw
Sweep from 2V to 0
Finding max point
Offsetting it
Running PID
Slow switching off the heater
The filter is not really one filter. CIC is just for downsampling. A FIR is needed for the rest of filtering.
The update refers to change requirements (e.g. heater power)
PID - a control algorithm used in engineering to maintain a desired output by minimizing the error between a setpoint and a measured process variable

## Slide 13: Choosing ADC type
Characteristics
  Compact
  Precise
  Low speed
Aim:
  Measuring current from the photodiode
Delta-Sigma
ADC
Notes: Generating pulses and transforming a density of them over a filer to a proper value. I could deliver here the whole derivation for the noise shaping (have a look into Gabriele Atzeni presentation, if someone is interested).

## Slide 14: Delta-Sigma Modulator for ADC
Aim:
  Measuring current from the photodiode
Delta-Sigma
ADC
Notes: Generating pulses and transforming a density of them over a filer to a proper value. I could deliver here the whole derivation for the noise shaping (have a look into Gabriele Atzeni presentation, if someone is interested).

## Slide 15: Delta-Sigma Modulator for ADC
Aim:
  Measuring current from the photodiode
Delta-Sigma loop (40MHz)
Pulse density modulation (almost)
Noise shaping
Notes: Generating pulses and transforming a density of them over a filer to a proper value. I could deliver here the whole derivation for the noise shaping (have a look into Gabriele Atzeni presentation, if someone is interested).

## Slide 16: Delta-Sigma Modulator for ADC
Aim:
  Measuring current from the photodiode
Delta-Sigma loop
Pulse density modulation (almost)
Noise shaping
Notes: Generating pulses and transforming a density of them over a filer to a proper value. I could deliver here the whole derivation for the noise shaping (have a look into Gabriele Atzeni presentation, if someone is interested).

## Slide 17: Delta-Sigma Modulator for ADC
Aim:
  Measuring current from the photodiode
Delta-Sigma loop
Pulse density modulation (almost)
Noise shaping
      Gabriele Atzeni seminar talk
Notes: Generating pulses and transforming a density of them over a filer to a proper value. I could deliver here the whole derivation for the noise shaping (have a look into Gabriele Atzeni presentation, if someone is interested).

## Slide 18: Delta-Sigma ADC
Aim:
  Measuring current from the photodiode
Delta-Sigma loop
Pulse density modulation (almost)
Noise shaping
      Gabriele Atzeni seminar talk
Adding a filter/integrator makes it Delta-sigma ADC
Final bandwidth 10kHz
Notes: Generating pulses and transforming a density of them over a filer to a proper value. I could deliver here the whole derivation for the noise shaping (have a look into Gabriele Atzeni presentation, if someone is interested).

## Slide 19: Delta-Sigma ADC
Aim:
  Measuring current from the photodiode
Delta-Sigma loop
Pulse density modulation (almost)
Noise shaping
      Gabriele Atzeni seminar talk
Adding a filter/integrator makes it Delta-sigma ADC
Final bandwidth 10kHz
Use FPGA resources
FPGA

## Slide 20: Delta-Sigma ADC – First Attempt
  Idea: emulate ASIC
  Current mirror + capacitor with current MUX + capacitor
Notes:   Observing a problem of too slow discharging causing a plateau in the middle of the range. If charges up too slowly to go up behind some voltge level to keep the ff out state the same for more than 1 clock cycle. Doing a research of components available on the market
  Building LTSpice proof of concept
  Soldering board and testing in the lab
  A frequency sweep proved that lower frequencies eliminate that problem
  Fixing the MUX state to be always on
  Dropping the idea of external current source
  Switching directly in FPGA
  The effect disappears
  Further removing the MUX itself with no improvement
  Should the output buffer switch between 0 and 1 or ‘Z’ and 1? -> 1,0

## Slide 21: Delta-Sigma ADC – First Attempt
  Idea: emulate ASIC
  Current mirror + capacitor with current MUX + capacitor
  Limitation:
  Dynamic characteristics of the current source.
  Solution:
  Eliminate the MUX
Notes:   Observing a problem of too slow discharging causing a plateau in the middle of the range. If charges up too slowly to go up behind some voltge level to keep the ff out state the same for more than 1 clock cycle. Doing a research of components available on the market
  Building LTSpice proof of concept
  Soldering board and testing in the lab
  A frequency sweep proved that lower frequencies eliminate that problem
  Fixing the MUX state to be always on
  Dropping the idea of external current source
  Switching directly in FPGA
  The effect disappears
  Further removing the MUX itself with no improvement
  Should the output buffer switch between 0 and 1 or ‘Z’ and 1? -> 1,0

## Slide 22: Design Space Exploration
Current steering
Notes:   Bipolar (0/1)
    Higher range, worse quality
    Worse linearity (due to capacitance in the buffer that discharges on top of the default cap)
  Unipolar (‘Z’/1)
    Even though the range is half of unipolar one it is better mimicking the final system, therefore that’s the way to go
    Additional current sink during ‘0’ state
    FPGA buffering problem – high state gets capacitor into floating mode, possible capacitance from the buffer
In addition a discrete transistor based current switch was considered (ADV301N)

## Slide 23: Design Space Exploration
Current steering
Resistor Driven
Unipolar
Resistor Driven
Bipolar
Notes:   Bipolar (0/1)
    Higher range, worse quality
    Worse linearity (due to capacitance in the buffer that discharges on top of the default cap)
  Unipolar (‘Z’/1)
    Even though the range is half of unipolar one it is better mimicking the final system, therefore that’s the way to go
    Additional current sink during ‘0’ state
    FPGA buffering problem – high state gets capacitor into floating mode, possible capacitance from the buffer
In addition a discrete transistor based current switch was considered (ADV301N)

## Slide 24: Design Space Exploration
Current steering
Resistor Driven
Unipolar
Resistor Driven
Bipolar
Notes:   Bipolar (0/1)
    Higher range, worse quality
    Worse linearity (due to capacitance in the buffer that discharges on top of the default cap)
  Unipolar (‘Z’/1)
    Even though the range is half of unipolar one it is better mimicking the final system, therefore that’s the way to go
    Additional current sink during ‘0’ state
    FPGA buffering problem – high state gets capacitor into floating mode, possible capacitance from the buffer
In addition a discrete transistor based current switch was considered (ADV301N)

## Slide 25: Delta Sigma ADC in Final PCB
  Bipolar, resistor driven approach
    Configurable gain (dynamic range)
  Configurable capacitance
  Isolating with buffers
Notes: For the requirements investigation please refer to Gabriele Atzeni presentation.

## Slide 26: Delta Sigma ADC in Final PCB
  Bipolar, resistor driven approach
    Configurable gain (dynamic range)
  Configurable capacitance
  Isolating with buffers
Notes: For the requirements investigation please refer to Gabriele Atzeni presentation.

## Slide 27: Delta Sigma ADC in Final PCB
  Bipolar, resistor driven approach
    Configurable gain (dynamic range)
  Configurable capacitance
  Isolating with buffers (lower parasitics)
Notes: For the requirements investigation please refer to Gabriele Atzeni presentation.

## Slide 28: Delta Sigma ADC in Final PCB
  Bipolar, resistor driven approach
    Configurable gain (dynamic range)
  Configurable capacitance
  Isolating with buffers (lower parasitics)
  External DS loop (even lower parasitics)
Notes: For the requirements investigation please refer to Gabriele Atzeni presentation.

## Slide 29: Delta Sigma ADC in Final PCB
  Bipolar, resistor driven approach
    Configurable gain (dynamic range)
  Configurable capacitance
  Isolating with buffers (lower parasitics)
  External DS loop (even lower parasitics)
Notes: For the requirements investigation please refer to Gabriele Atzeni presentation.

## Slide 30: Delta Sigma loop – FPGA or ICs?
FPGA driven loop
Disc. components driven loop

## Slide 31: Delta Sigma loop – FPGA or ICs?
FPGA driven loop
Disc. components driven loop

## Slide 32: Comparison of INLs - Capacitance
Discrete components driven Delta Sigma ADC loop
Larger capacitor
  lower SDM noise, for ASIC more space
  different RC time constant (nonlinearity)
  Stronger filtering behaviour – up to 10khz (max 1.3nF)
  Closer to the comparator noise ( )
Higher capacitance (in that range), better INL
100pF 1.1nF 10.1nF
Adjust depending on
scenario
Notes: Optimisation problem: higher capacitor – lower noise (more stable voltage), for asic more space filtering behaviour – up to 10khz (max 1.3nF)
By having smaller capacitor, we are further away from the comparator noise
1. Signal-to-Noise Ratio (SNR) Improves Initially
With a larger capacitor, the voltage changes slowly, and the signal may be buried in comparator noise.
As you reduce the capacitor, the signal becomes more dynamic and easier to distinguish from noise.
This improves INL (Integral Non-Linearity) and DNL (Differential Non-Linearity).
2. Beyond a Threshold, Non-Idealities Dominate
If the capacitor is too small, the system becomes:
  Too sensitive to jitter
  More prone to overshoot and ringing
  Affected by parasitic capacitance and layout imperfections
The comparator may start reacting to glitches or high-frequency noise, degrading precision.
3. Mismatch with Sampling Rate
The RC time constant must be well-matched to the sampling frequency.
Too small a capacitor → RC time constant too short → system may not settle properly between samples.
📈 INL Behavior Explained
Initial improvement: Better signal swing, clearer quantization.
Later degradation: Increased noise sensitivity, instability, and non-linear charge/discharge behavior.
✅ What You Can Do
Sweep capacitor values and plot INL/DNL vs. capacitance.
Simulate noise and jitter effects to find optimal operating point.
Consider adding damping or bandwidth-limiting to avoid instability at low capacitance.

## Slide 33: TCU Prototype vs ASIC
ADC
Very low capacitance
Current driver approach -> Capacitor and current source-based integrator
12 bit
40Mhz DSM
PCB/FPGA implementation:
ASIC implementation:
ADC
ADC (with/without FPGA in the loop)
Limiting parasitic capacitance with buffers
Bipolar (resistor) driven approach -> Resistor and capacitor-based integrator
11 bits for unipolar operation
33Mhz DSM
Notes: Making the design more reproducible and closer to the ASIC reality (less capacitance, more resistors), isolating with buffers

## Slide 34: DAC in Final PCB

## Slide 35: DAC in Final PCB
  Multiple levels
    Thermometric encoding
    16 levels bring 4 bits of resolution

## Slide 36: DAC in Final PCB
  Multiple levels
    Thermometric encoding
    16 levels bring 4 bits of resolution
    External buffering

## Slide 37: DAC in Final PCB
  Multiple levels
    Thermometric encoding
    16 levels bring 4 bits of resolution
  A flavor of delta sigma modulation (DSM)
    additional 12 bits
DSM

## Slide 38: DAC in Final PCB
  Multiple levels
    Thermometric encoding
    16 levels bring 4 bits of resolution
  A flavor of delta sigma modulation (DSM)
    additional 12 bits
  Dynamic element matching (DEM)
    Circulating the outputs to average out the resistance
DEM

## Slide 39: DAC in Final PCB
  Multiple levels
    Thermometric encoding
    16 levels bring 4 bits of resolution
  A flavor of delta sigma modulation (DSM)
    additional 12 bits
  Dynamic element matching (DEM)
    Circulating the outputs to average out the resistance
  DAC Requirements
    100uW resolution
    About 9.6 bits
    0-80mW range
    Monotonic transfer function
      To be ensured by DEM

## Slide 40: DAC in Final PCB
  Multiple levels
    Thermometric encoding
    16 levels bring 4 bits of resolution
  A flavor of delta sigma modulation (DSM)
    additional 12 bits
  Dynamic element matching (DEM)
    Circulating the outputs to average out the resistance
  DAC Requirements
    100uW resolution
    About 9.6 bits
    0-80mW range
    Monotonic transfer function
      To be ensured by DEM
Next slide

## Slide 41
  Expected: non-linear, but monotonic at least
DAC in Final PCB

## Slide 42: Problem: Discontinuities (Power)
  Expected: non-linear, but monotonic at least
  Switching SDM algorithms (Strong, lower priority region)
  Unknown source
  (Weak ~100uW, high significance region)

## Slide 43: Characterizing PIC
Setpoint

## Slide 44: Final PCB 1.0 (DAC and ADC)
DAC
16 levels implemented with resistors 4bits
Thermometric encoding
Additional 12 bits provided by DSM
16 bits resolution in total
DAC
64 levels implemented with transistors 6bits
Thermometric encoding
Additional 10 bits provided by DSM
16bits resolution in total
ADC (with/without FPGA in the loop)
Adding buffers to remove capacitance
Bipolar (resistor) driven approach -> Resistor and capacitor-based integrator
11 bits for unipolar operation
33Mhz DSM
ADC
Very low capacitance
Current driver approach -> Capacitor and current source-based integrator
12 bit
40Mhz DSM
PCB/FPGA implementation:
ASIC implementation:
+ linear regulator
DAC
Notes: Making the design more reproducible and closer to the ASIC reality (less capacitance, more resistors), isolating with buffers

## Slide 45: Current State of The Thermal Tuning System and Prospective for Future Developments
  Status
  Reaching a final shape of ADC and DAC
  Characterizing ADC & DAC
  Some discontinuities in DAC transfer function
  ADC effective bits : 9 with 10.1nF cap
  The PID loop has been closed and tried
  Plan
  Focusing on PID – studying stability and performance
  Resolving the issue of DAC discontinuities or at least understanding them
  Testing with real data
  Developing a system with 4 MRR for WDM

## Slide 46: Thank You

## Slide 47: The system under operation

## Slide 48: The system under operation

## Slide 50: No Tuning vs Poor Tuning vs Proper Tuning

## Slide 51: Comparison of INLs - Capacitance
100pF 10.1nF
FPGA driven Delta Sigma ADC loop

## Slide 52: Delta-Sigma ADC loop with generic components
Keeping the same voltage from the voltage source during discharging the capacitor.
Charging/discharging
pattern
Digital output reflecting the current with a frequency of
digital signal.
FPGA
External components
Notes: Flexible – one could even imagine a compiler that could implement architecture based on certain requirement

## Slide 53: Evolution of PCBs
Notes: ADC: 1. Starting from a topology performing internal current sourcing to the MUX based current switching
2. Changing pins, mitigating MUX problems by eliminating multiplexing (0.1->0.2) and upgrading 0.1 to 0.5 by allowing user to choose one of the 3 modes including external current source switching.
3. Not only eliminating multiplexing but also the multiplexer on the path
4. Propagating the design to the final board by isolating it with the buffers and adding a version of ADC based exclusively on external IC components
DAC
Starting with 10 bit dac + internal FPGA output tristate buffers
Increasing the number of bits to 18 and keep using the internal buffers with DAC 0.9. Also used to verify the pin layout (different standards of pins, different levels) while waiting for manufacturing the final PCB v.1.0. Successful verification.
Removing buffers from FPGA gateware, placing them on PCB 1.0.

## Slide 54: Evolution of PCBs
Notes: ADC: 1. Starting from a topology performing internal current sourcing to the MUX based current switching
2. Changing pins, mitigating MUX problems by eliminating multiplexing (0.1->0.2) and upgrading 0.1 to 0.5 by allowing user to choose one of the 3 modes including external current source switching.
3. Not only eliminating multiplexing but also the multiplexer on the path
4. Propagating the design to the final board by isolating it with the buffers and adding a version of ADC based exclusively on external IC components
DAC
Starting with 10 bit dac + internal FPGA output tristate buffers
Increasing the number of bits to 18 and keep using the internal buffers with DAC 0.9. Also used to verify the pin layout (different standards of pins, different levels) while waiting for manufacturing the final PCB v.1.0. Successful verification.
Removing buffers from FPGA gateware, placing them on PCB 1.0.

## Slide 55: Evolution of PCBs
Notes: ADC: 1. Starting from a topology performing internal current sourcing to the MUX based current switching
2. Changing pins, mitigating MUX problems by eliminating multiplexing (0.1->0.2) and upgrading 0.1 to 0.5 by allowing user to choose one of the 3 modes including external current source switching.
3. Not only eliminating multiplexing but also the multiplexer on the path
4. Propagating the design to the final board by isolating it with the buffers and adding a version of ADC based exclusively on external IC components
DAC
Starting with 10 bit dac + internal FPGA output tristate buffers
Increasing the number of bits to 18 and keep using the internal buffers with DAC 0.9. Also used to verify the pin layout (different standards of pins, different levels) while waiting for manufacturing the final PCB v.1.0. Successful verification.
Removing buffers from FPGA gateware, placing them on PCB 1.0.

## Slide 56: DAC implementation

## Slide 57: Problem: Discontinuities

## Slide 58: Non-monotonicity zoom in

## Slide 59: Digital simulation Mash2

## Slide 60: Capacitor discharging problem (Unipolar)
  Discharges way longer than expected
    Investigating the parasitics based on the damped frequency and RC discharge time constant
  Checking different capacitor values and different implementations of S-D ADC
  Result : order of few uH and few nF
  Conclusion: isolate the ADC with buffers
Notes: The PD simulator (current sink) set to -5 uA (For unipolar and external CS case) and 95uA For bipolar mode. This is done to separate pulses from each other to see the discharging pattern. Unipolar way

## Slide 61: Pulsing patterns

## Slide 62: WDM

## Slide 63: Micro-ring
b’1100
Gbps
kHz
Modulator
Resonator
λ-laser