## Slide 1: Ballistic transfer of antiprotons with reflection and transmission target - Updates
Bharat, Benji, Sruthy, Carsten and the AEgIS collaboration
AEgIS collaboration meeting
CERN, December 2025

## Slide 2
Target geometry- Current configuration
Arrived at the current configuration with the previous comparison studies.
Centered
Off-centre
Transmission Centered
54mm
2mm
12mm
8mm
Current

## Slide 3
Parabolic potential well
Varying the vertex of the parabola using the inverse solver.
More positive the vertex faster the transfer.
150 V
0 V
-30 V
Vertex
Target
Launch trap

## Slide 4
Pulsed P9 signal
P6
P9
Stored pbars
Pbars are pulsed and immediately launched with their initial distribution.
Particle transport is simulated using the ES-PIC solver in CST.
Credits: Ruggero

## Slide 5
P6-P9 Launch Trap
Source parameters
Density:2×1012 m-3
Num of simulated pbars =70000
Ttail=500K, Tcore=300K
Rmax=1.5mm
L=5mm
P6-P9 trap and parabolic potential

## Slide 6
0V vertex
Controlling the transmission of pbars by varying A0T.
Axial potential profile

## Slide 7
Axial and radial velocities at A0R=-70V
The first reflection
The axial velocities is around 20000m/s for this parametric sweep.
Vrms X
Vrms Z

## Slide 8
SrNo | A0R | A0T
1 | -60V | -50V,-52V,-54V,-56V,-58V,-60V
2 | -70V | -60V,-62V,-64V,-66V,-68V,-70V
3 | -80V | -70V,-72V,-74V,-76V,-78V,-80V
4 | -90V | -80V,-82V,-84V,-86V,-88V,-90V
Parametric scan for A0R and A0T (0 V vertex)
Loss curve
A0R=-60V
A0R=-70V
A0R=-80V
A0R=-80V, A0T=-80V
More parameter scan to find minimal axial velocity.

## Slide 9
Effect of A0T on axial velocities of pbars for 0V vertex parabola
The minimum axial velocity achieved is around 10000m/s! for the given transmission values.
Still haven’t found the A0T for the lowest Vz for the 0V setting .
Vz≈10000m/s

## Slide 10
150V parabola vertex
150V
A0T=-38V, A0R=-70V
Deeper parabola faster transfer (150V, 7.6 μs), Flatter parabola slower transfer (0V, 12 μs).

## Slide 11
Particle loss curve for A0R=-70V and A0T=-30V to -70V
Values of A0T=-30V to -40V at A0R=-70V allows some transmission of pbars towards the reflection target.

## Slide 12
Axial and radial velocities 150V vertex
VrmsZ
VrmsX
The axial velocities of pbar reach < 2000m/s.
The radial velocities is around few 100’s m/s.

## Slide 13
Comparison axial velocities for different parabolas (A0R=-70V)
For a constant A0R=-70V parabola with 150V vertex gives the minimal VrmsZ.
Vz≈2500m/s

## Slide 14
Parametric scan for A0R and A0T (150V vertex)
The transmission values A0T >-40V no transmission takes place, but velocity is reduced.
Still need to scan higher values of A0T to allow some transmission towards reflection target.
A0T=-54V
A0R=-60V
Vrmz=2054m/s
A0T=A0R=-90V
SrNo | A0R | A0T
1 | -60V | -50V,-52V,-54V,-56V,-58V,-60V
2 | -70V | -60V,-62V,-64V,-66V,-68V,-70V
3 | -80V | -70V,-72V,-74V,-76V,-78V,-80V
4 | -90V | -80V,-82V,-84V,-86V,-88V,-90V

## Slide 15
  GUI based MAD-X model
MADX model available on the transfer line from ELENA-AEgIS.
Transport lines from ELENA to AEgIS
Beam profiles at different locations
MADX ML model

## Slide 16
MADX ML model
Credits: Alex Hill (UoL)
Twiss plot

## Slide 17
MADX ML model
ML learning model takes 0.26ms compared to the MADX simulation model.
Credits: Qiyuan Xu (UoL)

## Slide 18
Towards Global Digital Twin model
Future goal towards the Digital Twin model of the AEgIS.

## Slide 19
Conclusion and Future goals
The simulation studies indicate that steeper parabola leads to lower pbar energy spread in both axial and radial directions.
Continue working on further optimization of to find the minimal axial velocity setting under different conditions of pulse shape, space charge, plasma length, effect of pbar temperature etc.
Working on building the ML based model for G4 Beamline and MADX using NVIDIA’s Phys Nemo framework.

## Slide 20
Extra slides

## Slide 21
0V Parabola Effect of A0T

## Slide 22
Mean velocity under reflection target

## Slide 23
-30V Parabola

## Slide 24
-30V Parabola

## Slide 25
-30V Parabola

## Slide 26
-30V Parabola

## Slide 27
-50V Parabola

## Slide 28
-50V Parabola

## Slide 29
-50V Parabola

## Slide 30
-50V Parabola

## Slide 31
-50V Parabola
-30V Parabola
0V Parabola

## Slide 32
150V Parabola

## Slide 34
The ES-PIC simulations identified high-probability impact regions (using the feature particle monitor on solid) for antiprotons on the grid, allowing precise tuning of launch potentials and alignment parameters.