## Slide 1: Design progress of the synchrotron radiation absorber for the FCc-ee
P. Krkotić, M. Ady, M. Bammer, G. De Gois Saretti, C. Garion, V. Giovinco, S. Grozavu, M. Morrone
28th of October / 107th Impedance Working Group Meeting

## Slide 2: Outline
FCC-ee: Synchrotron Radiation
Synchrotron Radiation Absorber (SRA)
Optics Layouts Overview
Beam Impedance Analysis
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Summary and Next Steps

## Slide 3: Outline
FCC-ee: Synchrotron Radiation
Synchrotron Radiation Absorber (SRA)
Optics Layouts Overview
Beam Impedance Analysis
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Summary and Next Steps

## Slide 4: Outline
FCC-ee: Synchrotron Radiation
Synchrotron Radiation Absorber (SRA)
Optics Layouts Overview
Beam Impedance Analysis
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Summary and Next Steps

## Slide 5: Outline
FCC-ee: Synchrotron Radiation
Synchrotron Radiation Absorber (SRA)
Optics Layouts Overview
Beam Impedance Analysis
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Summary and Next Steps

## Slide 6: Outline
FCC-ee: Synchrotron Radiation
Synchrotron Radiation Absorber (SRA)
Optics Layouts Overview
Beam Impedance Analysis
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Summary and Next Steps

## Slide 7: Outline
FCC-ee: Synchrotron Radiation
Synchrotron Radiation Absorber (SRA)
Optics Layouts Overview
Beam Impedance Analysis
Summary and Next Steps
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee

## Slide 8: FCC-ee: Synchrotron Radiation
Origin & impact on design
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
synchrotron radiation
electron beam
Running Mode | Z | WW | ZH | ttbar
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Energy loss per turn [GeV] | 0.04 | 0.37 | 1.86 | 9.94
Synchrotron radiation power [MW] | 50 | 50 | 50 | 50
Beam current [mA] | 1294 | 135 | 26.8 | 5.1
Highest surface power density
vacuum chamber
Highest penetration into the material

## Slide 9: Synchrotron Radiation Absorber (SRA)
Conceptual Design
S. Grozavu, Design, simulations and testing of the FCC–ee synchrotron radiation absorber, VSC Seminars, June, 2025
M. Bammer, Layer by Layer, FCC Week 2025, Vienna, May, 2025,
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Sawtooth pattern
vacuum chamber
390 mm
45°
7°
15°
Material: CuCrZr (70–85% IACS)
Manufacturing: Powder Bed Fusion 3D printing
Design: slanted surface (45°), tilt (7°), taper-transition (15°)
Sawtooth: 0.9 mm step height
Integration: Laser welding
Cooling: water circuit
Placement: insight the winglet – dependence on
Optics Layout

## Slide 10: Optics Layout Overview
Optics Layout
Arc dipoles:
  2 magnet split
  12 m + {7.74 m, 9.19 m, 10.69 m}
  17 cm interconnection gap
Global Hybrid Correction
Arc dipoles:
  3 magnet split
  9.06 m + 9.06 m + 9.06 m
  17 cm interconnection gap
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Local Chromatic Correction
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
D
D
Q
S
GHC
D
D
D
Q
S
LCC
M. A. Jebramcik, Status of the Optics used for comparison, 11th Meeting of the FCC-ee Layout and Optics Design

## Slide 11: Optics Layout Overview
Global Hybrid Correction
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
D
D
Q
S
GHC
55 / 75 cm reserved for shielding
Synchrotron radiation absorber
Arc dipoles:
  2 magnet split
  12 m + {7.74 m, 9.19 m, 10.69 m}
  17 cm interconnection gap
– Absorber Placement
M. Ady, Comparison criteria for GHC vs LCC:Vacuum, 8th Meeting of the FCC-ee Layout and Optics Design
- 3.25 mm
+ 0.75 mm
+ 4.00 mm
Courtesy Marton Ady
Courtesy Marton Ady

## Slide 12: Surface Current Density
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
P. Krkotić, Investigation of Beam-Induced Heating in the FCC-ee Vacuum Chamber, EDMS Report 3352561, 2025

## Slide 13: Optics Layout Overview
Global Hybrid Correction
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
D
D
Q
S
GHC
55 / 75 cm reserved for shielding
Synchrotron radiation absorber
Arc dipoles:
  2 magnet split
  12 m + {7.74 m, 9.19 m, 10.69 m}
  17 cm interconnection gap
– Absorber Placement
M. Ady, Comparison criteria for GHC vs LCC:Vacuum, 8th Meeting of the FCC-ee Layout and Optics Design
- 3.25 mm
+ 0.75 mm
Hybrid solution: 4+1

## Slide 14: Optics Layout Overview
Arc dipoles:
  3 magnet split
  9.06 m + 9.06 m + 9.06 m
  17 cm interconnection gap
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Local Chromatic Correction
D
D
D
Q
S
LCC
55 / 75 cm reserved for shielding
Synchrotron radiation absorber
M. Ady, Comparison criteria for GHC vs LCC:Vacuum, 8th Meeting of the FCC-ee Layout and Optics Design
– Absorber Placement
- 3.25 mm

## Slide 15: Optics Layout Overview
Arc dipoles:
  2 magnet split
  12 m + {7.74 m, 9.19 m, 10.69 m}
  17 cm interconnection gap
  Quantity: 5680
Absorbers: 14200 / beam
  13064 – nominal position
  1136 – 4 mm closer towards beam
Global Hybrid Correction
Arc dipoles:
  3 magnet split
  9.06 m + 9.06 m + 9.06 m
  17 cm interconnection gap
  Quantity: 6624
Absorbers: 13248 / beam
  13248 – nominal position
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
Local Chromatic Correction
D
D
Q
S
GHC
D
D
D
Q
S
LCC
55 / 75 cm reserved for shielding
Synchrotron radiation absorber

## Slide 16: Beam Impedance Analysis
Numerical Model and Simulation Constraints
CST model SRA nominal position
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
No symmetry – full 3D model
Gaussian bunch length σz = 5 mm (20 GHz)  1.4 mm (70 GHz)
Low TM0,1 cut-off frequency: 3.8 GHz
Integration technique: Indirect interfaces
Mesh setup: Lines per sigma \ mesh cell geometry

## Slide 17: Beam Impedance Analysis
Preliminary – 125 M cells, 10 m wakelength
CST model SRA nominal position
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
TM01
TE11
TE21
TM11
TE31
TM21
TE12
Surface current density – 6.7 GHz
Electric field top view cross-section – 6.7 GHz
Electric field– 6.7 GHz

## Slide 18: Beam Impedance Analysis
Preliminary – 125 M cells, 10 m wakelength
CST model SRA nominal position
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee

## Slide 19: Beam Impedance Analysis
Peculiarities – convergence studies
Wakelenght = 10 m
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee
CST model testing phase
Change in simulation time (nominal → +4 mm): ×20
Similar effect observed in convergence study with Wakelength
Angle variation produces a similar trend

## Slide 20: Summary
Impedance Factors
Material Properties
CuCrZr Conductivity < OFS copper
  → Increase in resistive wall
Geometry
Angles and roughness
  → Impedance dominated by geometry
Beam proximity
Breaking locally symmetry of the vacuum chamber
  → travelling wakes
    → perturbation into the vacuum chamber
    Novel simulation regime:
    Computationally demanding
    Many limitations
Input required by end of year for the optics report
Final decision enables improved impedance estimates
Next step: SRA placement studies for refinement including tolerances
Optics Strategy Decisions - 2026
Outlook
  Eigenmode open boundary
    Travelling wave measurement setup
      Design optimisation
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee

## Slide 21: Thank you for your attention.
14
28th of October / 107th Impedance Working Group Meeting
P. Krkotić – Design Progress SRA FCC-ee