## Slide 1: SPS 200 MHz RF Upgrade
Eric Montesinos
On behalf of LIU-SPS 200 MHz Upgrade team

## Slide 2: Contents
What ? Existing system
Why ? Motivations
How ? Technical choices
When ? Schedule
Who ? Persons involved

## Slide 3: A bit of history
The SPS-RF started up in 1976 with two accelerating cavities
Since 1980, for the new role of SPS as proton-antiproton collider, there are four power plants operating @ 200 MHz
2010
2000
1976
TWC#1 / TX1
TWC#2 / TX2
1978
TWC#3 / TX3
1979
TWC#4 / TX4
1990
1980
1980
TWC#1 / TX1+TX2
TWC#2 / TX3+TX4
TWC#3 / TX5+TX6
TWC#4 / TX7+TX8
1975
1985
1995
2005
Fire in BA3 HVPS TX#3
New RF power couplers
HVPS upgrade for
Pulse mode
Transmitter (TXB)
mW
Dummy load
Coaxial transmission line
(feeder line)
125 to 160 meters
Accelerating cavity
Terminating loads
Configuration of one of the four
200 MHz power plant
Transmitter (TXA)
Power
combiner

## Slide 4: Existing amplifiers
20 x 135 kW RS2004
‘Siemens’ plant (1976 to 1979)
68 x 35 kW YL1530
‘Philips’ plant (1980)
GSM
1 W
YL1530
35’000 W
RS2004
135’000 W
700’000 W
700’000 W
700’000 W
700’000 W
20 x 135 kW RS2004
‘Siemens’ plant (1976 to 1979)
68 x 35 kW YL1530
‘Philips’ plant (1980)

## Slide 5: Travelling Wave Cavities: 2 x four sections & 2 x five sections
One four sections cavity
(four power couplers and two terminating power loads)
One section = 11 drift tubes

## Slide 6: Cavities redistribution
2011 : 4 cavities (18 sections)
2 x 4 sections
2 x 5 sections
+ 3 spare sections
2018 : 6 cavities (20 sections)
4 x 3 sections
2 x 4 sections
+ 1 spare section

## Slide 7: Motivations
With present 4 cavities configuration we will have difficulties at high intensity LHC beam in the SPS : IPAC11, Upgrade of the 200 MHz RF system in the CERN SPS
Increasing number of shorter cavities with 2 extra power plants should significantly improve the RF performance for higher LHC intensities
The best new compromise is 6 cavities:
  4 x 3 sections cavities with 1.0 MW
  2 x 4 sections cavities with 1.4 MW
Courtesy of Elena Shaposhnikova
Available RF voltage as a function of Irf
Available RF voltage as a function of # section with 1.0 MW RF and with 1.5 A and 2.5 A Irf

## Slide 8: SPS 200 MHz RF system upgrade
Existing Amplifiers upgrade
New RF Amplifiers
New RF Building
LSS3 Tunnel integration
RF amplifier
1 mW
Coaxial transmission line
150 meters
Accelerating cavity
1.7 MW
RF amplifier
1 mW
Accelerating cavity
1.7 MW
New RF Building

## Slide 9: Existing amplifiers upgrade
Philips air cooling plant has to be modified to allow higher power
Siemens HVPS need a full re-cabling and an air cooling improvement
Be ready to pay for new tubes
Ratings | Present | Future
Pulsed 10 us/43 kHz | 700 kW | 1100 kW
Siemens HVPS damaged HV cabling and diode bridge
during high power tests
Philips burnt tube because of lack of air cooling

## Slide 10: New 1.7 MW amplifier, i.e 1.4 MW cavity
Pulse mode: 1.7 MW max (10 µs / 43 kHz)
Average: 850 kW (thermal limitations)
A major improvement to existing systems will be to have individual SSA drivers per Final
Combiners and lines will be the same as with existing systems
Four contracts :
  Drivers (SSA)
  Finals (SSA or Tetrodes)
  Combiners (3 dB above 100 kW)
  Transmission lines (coaxial, 345 mm outer)
Drivers
16 SSA
Final
16 PAs
3 dB
combiners
and power loads
120 m and 180 m
Coaxial lines
To cavity input 120 m away
From Beam Control
1/16 splitter
1.7 MW
-0.6 dB total
1.5 MW
-0.2 dB
1.4 MW

## Slide 11: Two new power amplifiers
Qualified solution must have demonstrated to be reliable under scientific operation (not only broadcast operation)
Reliability and overall efficiency will be part of the adjudication
16 x 138 kW Tetrodes, i.e 32 tetrodes
128 x 910 W
SSA
16 x 128 x 910 W SSA, i.e. 4096 transistors
2 x 1.7 MW Klystron | 2 x 8 x 225 kW tetrodes Equivalent to ‘Siemens’
2 x 8 x 225 kW IOTs | 2 x 16 x 106 kW tetrodes Equivalent to ‘Philips’
2 x 4 x 450 kW Diacrodes | 2 x 2048 x 830 W SSA Equivalent to ‘SOLEIL’
2 x 16 x 106 kW tetrodes Equivalent to ‘Philips’
2 x 2048 x 830 W SSA Equivalent to ‘SOLEIL’

## Slide 12: New RF building
Whatever the solution, SSA or Tetrodes, the same building
Best possible location is between BA3 and BB3
Maximum ‘RF’ foot print will be 2 x 450 m2
Philips
Siemens
RF Faraday Cage
800 MHz
RF
workshop
New RF plants
BA3
BB3
CCC

## Slide 13: Cavities rearrangement
We already disassembled all cavities
(2001-2004 realignment campaign)
We know all needed specific tooling
It will be a huge challenge …

## Slide 14: Cavities rearrangement
… even if this will be (very) stressing …
…we are confident we can do it, however…

## Slide 15: LSS3 rearrangement

## Slide 16: Key RF devices
Three spare sections : ~ 3.5 years
  Refurbishment (missing items)
  Power tests
New power couplers : ~ 5 years
  More power and shorter -> new design
  Prototyping and tests
  Series and pre-conditioning (x 30)
New amplifiers : ~ 5 years
  New building
  Construction of amplifiers
  Long duration tests
New LLRF : ~ 4 years
  Design
  Train onto a spare cavity in the new RF building
  Test onto an existing system prior to deployment
Impossible to re-arrange cavities within LS1
Only 5 pickups / 17 devices to be reinstalled

## Slide 17: Schedule
2011
2012
2013
2015
2016
2017
2019
2014
Studies
Tendering
Construction
Installation
Commissioning
Start up
2018
Studies
Construction
coaxial lines, Pickups
New power couplers
Cavities Pickups vacuumCV, EL
Studies
Authorizations
Construction
Services (CV, EL)
#2
Spare sections
LLRF Design and proto
LLRF Tests
LLRF Series
New RF Building
LSS3 Tunnel Integration
New RF Power Amplifiers and LLRF
6 months cavities re-arrangement
2 months RF Power conditioning
4 months LLRF commissioning

## Slide 18: Persons involved
Dep-Group | Persons
BE-RF | Eric Montesinos, Thomas Bohl, Wolfgang Höfle, Urs Wehrle, Elena Shaposhnikova, Philippe Baudrenghien, SPS power team
BE-ABP | Patrick Bestmann, Yannis Papaphilippou
BE-ASR | Paula Carvalho Correia, Emmanuel Paulat
BE-BI | Christian Boccard, Patrick Odier
DGS-SEE | Guillaume Fontana, Cécile Pinto
EN-CV | Michel Obrecht, Mauro Nonis
EN-EL | Guillaume Gros, Joël Lahaye, Christophe Crombez
EN-HE | Caterina Bertone, Pascal Brunero, Serge Pelletier, Yann Seraphin
EN-MEF | Frédéric Galleazzi, Yvon Muttoni, David McFarlane
GS-SE | Luz-Anastasia Lopez-Hernandez, Evelyne Crocci-Torti, Antoine Kosmicki
TE-VSC | Paolo Chiggiato, Antonio Mongelluzzo
TE-MSC | Jérémie Bauche