## Slide 1: Physics and detectors at CLIC – a multi-TeV e+e- linear collider
Erik van der Kraaij
on behalf of CLIC physics & detectors study group
Vol. 1:
ACCELERATOR AND
TECHNICAL SYSTEMS
Vol. 3:
SUMMARY, COST AND STRATEGY
Vol.2:
PHYSICS AND DETECTORS AT CLIC
Conceptual Design Report
Conceptual Design Report
Conceptual Design Report

## Slide 2: Outline
Physics motivation
Accelerator design
  e+e- collisions, yet not LEP-like
Detector designs
  For unprecedented requirements
Particle Flow – imaging calorimetry
  How to cope with background

## Slide 3: CLIC physics
Precision measurements of new particles discovered at LHC:
Higgs, SUSY, …
Discrimination between competing models
Discovery of new physics at TeV scale
e+e- collisions up to √s = 3 TeV
Must be linear – too much synchroton radiation in storage rings.
hZ
Z → μ+μ-
susy Sparticles
ttbar
hνν

## Slide 4: Higgs production
√s = 3 TeV: WW fusion crosssection ~2x higher than max of higgsstrahlung
s-channel ~ 1/s
t-channel ~ log (s)
Mh = 120 GeV

## Slide 5: Higgs observables (Mh = 120 GeV)
with 500 fb−1 at √s = 500 GeV, except gHtt which is at √s = 800 GeV with 1 ab−1.
with 2 ab−1 at √s = 3 TeV, as shown below. These are pure statistical errors.
  gHμμ measurement can be improved
Example of CDR benchmark
channels
gHWW gHZZ gHbb gHcc gHττ gHtt

## Slide 6: Thresholds crossed as a function of energy
Assume LHC is fully explored – Many of the possible particles in the CLIC range will be discovered
 Design according to expected physics

## Slide 7: Outline
Physics motivation
Accelerator design
  e+e- collisions, yet not LEP-like
Detector designs
  For unprecedented requirements
Particle Flow – imaging calorimetry
  How to cope with background

## Slide 8: ILC and CLIC
linear colliders producing e+e- collisions
CLIC
ILC
Based on 2-beam, normal conducting, acceleration structure
Gradient 100 MV/m
Energy: 3 TeV, though will probably start at lower energy (~0.5 TeV)
Detector study focuses on 3 TeV
Based on superconducting RF cavities
Gradient 32 MV/m
Energy: 500 GeV, upgradeable to 1 TeV (+ lower energies: Higgs, ttbar,…)
Detector studies 0.5 – 1.0 TeV
Luminosities: few 1034 cm-2s-1
Notes: Superconducting accelerating structures
  Very low losses – High efficiency
  Long pulse trains: good for detectors and feedback
  Low peak power
  Lower frequencies
BUT: lower gradient: 31.5 MV/m (ILC design value)
  limited by: pulsed surf. heating, RF breakdown, structure damage

## Slide 9: CLIC acceleration
No individual RF power sources
Main beam for physics
high energy (9 GeV – 1.5 TeV)
current 1.2 A
Two Beam Scheme:
Drive Beam supplies RF power
12 GHz bunch structure
low energy (2.4 GeV - 240 MeV)
high current (100A)
Like a HV transformer - transformer ‘core’:
  Waveguides with RF waves
Notes: 12 GHz is a higher frequency than the 0.5ns between BXs.
  Time needed between the BXs, not to have them interfere & for the RF to come back to nominal.
The RFs cannot continuously be operated, hence the ‘long’ deadtime between trains.

## Slide 10: CLIC 3 TeV machine layout
48.3 km
Main Beam Generation Complex
Drive Beam Generation Complex

## Slide 11: CLIC energy staging
3 TeV Stage
Linac 1
Linac 2
Injector
Complex
I.P.
3 km
20.8 km
20.8 km
3 km
48.2 km
Linac 1
Linac 2
Injector
Complex
I.P.
1-2 TeV Stage
0.5 TeV Stage
Linac 1
Linac 2
Injector
Complex
I.P.
4 km
~14 km
4 km
~20-34 km
7.0-14 km
7.0-14 km
Lower energies would require only 1 drive beam generation complex
Notes: Lower E complex can run most of the time will rest is being built.
First stages only require one drive beam complex  saves money
BDS length remains the same
Turnaround magnets can be reused everytime

## Slide 12: Possible construction location
Interaction region, caverns and surface installation, as foreseen in the CDR, at CERN Prevessin
J. Osborne
CERN GS-SE

## Slide 13: The CLIC Test Facility (CTF3)
DRIVE BEAM
LINAC
CLEX
CLIC Experimental Area
DELAY
LOOP
COMBINER RING
10 m
4 A – 1.2 ms
150 Mev
1.5 GHz bunch spacing
32 A – 140 ns
150 Mev
12 GHz bunch spacing
Demonstrate Two Beam Acceleration and test Accelerating Structures
Study deceleration
Drive Beam generation. fully loaded acceleration, beam intensity and bunch frequency multiplication x8
RF Power Production and test Power Structures
Notes: Demonstrate Drive Beam generation (fully loaded acceleration, beam intensity and bunch frequency multiplication x8)
Demonstrate RF Power Production and test Power Structures
Demonstrate Two Beam Acceleration and test Accelerating Structures

## Slide 14: CLIC parameters
 | LEP 2 | ILC 0.5 TeV | CLIC 3 TeV
L [cm-2s-1]] | 5×1031 | 2×1034 | 6×1034
Crossing angle |  | 14 mrad | 20 mrad
BX separation | ~22 ms | 700 ns | 0.5 ns
# (gg  hadrons) / BX | negligible | 0.2 | 3.2
#Incoherent pairs / BX | negligible | 1 × 105 | 3 × 105
CLIC
CLIC: trains at 50 Hz, 1 train = 312 bunches, 0.5 ns apart
ILC: trains at 5 Hz , 1 train = 1300 bunches, 700 ns apart
156 ns
20 ms
Notes:   Occupancy = #hits / #readout-cells can reach large values
  trigger-less readout of whole train
  power pulsing of readout electronics, to minimize material needed for cooling

## Slide 15: Beam-induced backgrounds
Need pile-up rejection
Need to include background in simulation
  Detector starts at θ>10 mrad

## Slide 16: Luminosity spectrum
Includes beam energy spread and beamstrahlung
Ltot = 6 1034 cm-2s-1 ; L0.01 = 2 1034 cm-2s-1 (30% in “1% highest energy”)
√s is not known per event!
Much like the hadronic PDFs, need to fold in luminosity spectrum in simulation

## Slide 17: Outline
Physics motivation
Accelerator design
  e+e- collisions, yet not LEP-like
Detector designs
  For unprecedented requirements
Particle Flow – imaging calorimetry
  How to cope with background

## Slide 18: CLIC Detector Requirements (1/2)
High-resolution pixel detector to measure displaced vertices p = 1 GeV: σd0~20 μm (CMS: 90 μm) p = 100 GeV: σd0~5 μm (CMS: ~10μm)
momentum resolution p = 1 GeV: σ(pT)/pT = 0.1% (CMS: 0.7%) p = 100 GeV: σ(pT)/pT = 0.2% (CMS: 1.5%)
Need very good jet-energy resolution
E = 102 – 103 GeV: σ(Ej)/Ej ~ 4.0% – 3.5% ATLAS ~ 8.0% – 4.0%
Notes:   2.5 σ W/Z separation requires σE/E=3.5%, for Ej up to 1 TeV.

## Slide 19: CLIC Detector Requirements (2/2)
Per bunch crossing: 3.2 gg  hadrons events, 50 GeV visible energy
19 TeV dumped in the calorimeters per 156 ns bunch train.
Will have triggerless readout of full train. Need:
  Detector hit time-stamping
  Multi-hit storage/readout
  filtering algorithms at reconstruction level
1.4 TeV of background in reconstruction window
e+e- → H+H- → tbbt
+ 60 BX γγ → hadrons
8 jet final state
Notes: See fig. 2.12 of CDR vol2.

## Slide 20
Based on validated ILC designs, adapted to CLIC energy and timing conditions:
  Denser barrel HCAL (Tungsten, 7.5 λi)
  Redesign of vertex and forward detector regions (backgrounds)
Two general purpose CLIC detector concepts

## Slide 21
Two general purpose CLIC detector concepts
CLIC_ILD
CLIC_SiD
2.7 m
3.4 m

## Slide 22: Very Forward Region
QD0
Kicker
BPM
Spent beam
Beamcal
Lumical
ECAL
2.4 m
Notes: CLIC beam crossing angle is 20 mrad, (ILC: 14 mrad) => modifications of the design of the very forward region components:
LumiCal (40-100 mrad) : luminosity measurement
BeamCal (10- 40 mrad) : electron detection
Beam position monitor
Beam Kicker: intra train feedback
Final focus quadrupole: QD0
Anti-Solenoid: field compensation
Shielding masks: protect
upstream detectors and
BPM, Kicker, …

## Slide 23: CLIC_SiD vertex detectors
 | CLIC_SiD | CMS
Material X/X0 (90o) | ~1.1% (5 layer) | ~10% (3 layer)
Pixel size | 20 x 20 μm2 | 100 x 150 μm2
# pixels | 2.76 G | 66 M
Time resolution | 5-10 ns | <~25 ns
Power/pixel | <~0.2 μW | 28 μW
CLIC_SiD
170 mm
830 mm
Very low duty cycle of CLIC machine: 156 ns train, 20 ms pause
All subdetectors will implement power pulsing schemes at 50 Hz, to reduce power consumption and thereby material in cooling systems
Beampipe
4 mm Fe
.5 mm Be

## Slide 24: CLIC_ILD: TPC based tracking
Large TPC (329 < R < 1808 mm) for highly redundant continuous tracking (~ 200 measured points)
Particle ID through dE/dx
Little material in tracking volume (5% X0); <25% X0 in endcap
Complemented by silicon tracking system:
Independent tracking at low angles (FTD)
Silicon tracking layers surrounding TPC for timing and precision points (SIT, SET, ETD)
TPC acceptance down to 120 (>10 measurement points)
SIT acceptance down to 250
FTD acceptance down to 70

## Slide 25: TPC occupancies
High occupancies in the TPC, mostly due to gg  hadrons.
Consider pixelized readout in this region or suppress the inner pad rows.
Requires technology/layout changes
Full detector simulations:

## Slide 26: TPC beam tests at DESY with Large Prototype (2008-2011)
Micromegas (T2K readout) GEMs (Altro readout)
8-chip Ingrid module
Integrated version

## Slide 27: CLIC_SiD: all-silicon tracker
Outer tracker barrel
Vertex region
beam pipe
Forward outer tracker
1206 mm

## Slide 28: EM calorimetry
ECAL | CLIC_ILD, B = 4 T
Absorber/Active element | Tungsten / Si pads
Sampling layers | 20x 2.1 mm, 10x 4.2 mm
Cell size | 5.1 × 5.1 mm2
X0 and λI | 23 and 1
Example – SiD approach:

## Slide 29: Hadronic calorimetry
HCAL | CLIC_ILD & CLIC_SiD
Absorber (Barrel/F) | Tungsten / Steel
Sampling layers (B/F) | 75x10 mm / 60x 20 mm
Cell size | 30 × 30 mm2 (analog, e.g. SiPM)
λI | 7.5
 10 × 10 mm2 (digital, e.g. RPC)

## Slide 30: Tungsten HCAL prototype
Data taken 2010/11 at CERN-PS/SPS, mixed beams 1 – 300 GeV
Scintillator tiles 3x3 cm2 (in centre)
Read out by SiPM
Main purpose: Validation of Geant4 simulation for hadronic showers in tungsten

## Slide 31: SiPM analog HCAL testbeam
Time structure of shower:
First results demonstrate the importance of the high precision neutron tracking with QGSP_BERT_HP in Geant4 for the time evolution of hadronic showers in tungsten.
10 GeV pion
Notes: “Mean time of first hit for 10 GeV 􀀀 as a function of radial distance from the shower core (a tile index of 10 corresponds to
approximately 30 cm). The data are compared with simulations using QGSP BERT and QGSP BERT HP. The error bars and the width of the area in the case of QGSP BERT HP simulations show the statistical error, while for QGSP BERT the errors are omitted for clarity.”
While QGSP BERT HP gives an excellent description of the data, QGSP BERT shows very
large discrepancies, with significantly overestimated late contributions at larger radii. This demonstrates the
importance of the high precision neutron tracking in Geant4 for a realistic reproduction of the time evolution
of hadronic showers in tungsten.
“simulated with the QGSP BERT and QGSP BERT HP physics lists [6]. The latter provides
additional high precision neutron tracking, and is expected to give an improved description of the shower
evolution in heavy absorbers, while the former is the list mostly used in the simulation of LHC detectors and
for linear collider optimization studies.”

## Slide 32: RPC digital HCAL testbeam
120 GeV proton
With Fe, performed at Fermilab

## Slide 33: Outline
Physics motivation
Accelerator design
  e+e- collisions, yet not LEP-like
Detector designs
  For unprecedented requirements
Particle Flow – imaging calorimetry
  How to cope with background

## Slide 34: Particle Flow Calorimetry
EJET = EECAL + EHCAL
n
+

EJET = ETRACK + E + En
  Measure charged particle energies (60% of jet) in tracker.
  Measure photon energies (30%) in ECAL σE/E < 20%/E(GeV)
  Measure only neutral hadron energies (10%) in HCAL.

## Slide 35: Time development in hadronic showers
In steel 90% of the energy is recorded within 6 ns (corrected for time-of-flight).
In tungsten only 82% of the energy is deposited within 25 ns.
  Response is slower due to the much larger component of the energy in nuclear fragments.
  Need to integrate over > 25 ns in the reconstruction, keeping out the pile-up hits…
Notes: For the HCAL endcap with steel for the absorber material 90% of the energy is recorded within 6 ns (corrected for time-of-flight). For the tungsten absorber assumed for the HCAL barrel, only 82% of the energy is deposited within 25 ns. The calorimetric response of tungsten is slower than that of steel due to the much larger component of the energy in nuclear fragments.

## Slide 36: Reconstruction timing strategy
Assume can identify t0 of physics event in offline event filter
  define “reconstruction” window around t0
  All hits and tracks in window are passed to reconstruction.
CLIC hardware
Requirements
- Achievable in the calorimeters with a sampling each ~25 ns
….
….
Subdetector | Reco Window | Hit Resolution
ECAL | 10 ns | 1 ns
HCAL Endcap | 10 ns | 1 ns
HCAL Barrel | 100 ns | 1 ns
Silicon Detectors | 10 ns | 10/√12
TPC (CLIC_ILD) | Entire train | n/a

## Slide 37: Reconstruction in time
tCluster
After reconstruction have a list of Particle Flow Objects (PFOs)
Calculate energy weighted mean time of each cluster
  Obtain sub-ns resolution
  Use times to reject clusters and associated tracks
Radius
Time
Calorimeter
TPC
Si tracking/vertex
Notes:   charged particles – mostly matched to clusters
  photons – EM clusters
  neutral hadrons – clusters
- High granularity calorimeter - even low energy clusters have many hits
  - account for helical propagation time

## Slide 38: Reconstruction in time
After reconstruction have a list of Particle Flow Objects (PFOs)
Calculate energy weighted mean time of each cluster
  Obtain sub-ns resolution
  Use times to reject clusters and associated tracks
Neutral hadrons
Notes:   charged particles – mostly matched to clusters
  photons – EM clusters
  neutral hadrons – clusters
- High granularity calorimeter - even low energy clusters have many hits
  - account for helical propagation time

## Slide 39: Impact of Timing Cuts
1.2 TeV background
√s = 3 TeV, 500 GeV di-jet event

## Slide 40: Impact of Timing Cuts
85 GeV
1.2 TeV
Reject 93 % of background energy and < 1% of physics event
  much more effective than simple pT cut

## Slide 41: Jet Finding at CLIC
Using Durham kT à la LEP
  Timing cuts are effective, but not sufficient
e.g.
timing
Notes: At LEP, preferred jet-finding algorithm: Durham kT
  All particles in event clustered into the jets
  not appropriate for CLIC
Events at CLIC
  significant background from forward-peaked gg → hadrons
  events are often boosted along beam axis (beamstrahlung)
  “hadron collider” type algorithms more appropriate
kT algorithm at CLIC studied for benchmark physics analyses
  invariant under longitudinal boosts
  particles either combined with existing jet or beam axis
    reduces sensitivity to gg → hadrons

## Slide 42: Jet Finding at CLIC
Using Durham kT à la LEP
  Timing cuts are effective, but not sufficient
“hadron collider” kT : R = 0.7
  Even less background, timing cuts hardly any effect for this topology
To tackle background: timing cuts + jet finding
e.g.
timing
Notes: At LEP, preferred jet-finding algorithm: Durham kT
  All particles in event clustered into the jets
  not appropriate for CLIC
Events at CLIC
  significant background from forward-peaked gg → hadrons
  events are often boosted along beam axis (beamstrahlung)
  “hadron collider” type algorithms more appropriate
kT algorithm at CLIC studied for benchmark physics analyses
  invariant under longitudinal boosts
  particles either combined with existing jet or beam axis
    reduces sensitivity to gg → hadrons

## Slide 43: Test of di-jet mass reconstruction
Clear separation using di-jet invariant masses:
82 %
17 %
Full Simulation with background

## Slide 44: The 8 jet final state
1.4 TeV of background
MMC
902.4
906.3
e+e- → H+H- → tbbt
e+e- → HA → bbbb
Notes: Testcase for almost everything:
Secondary vertices, high multiplicity of tracks, high multiplicity of jets, high energies.
Natural width of these particles is 6 GeV.

## Slide 45: Top pairs at √s = 500 GeV
250 fb-1
Unbinned maximum likelihood fit of mass distributions
Comparable to ILD LOI mass resolution (0.11 GeV in all-hadronic final state)

## Slide 46: More detector benchmark channels

## Slide 47: Summary
CLIC CDR Volume 2 public and under review:https://edms.cern.ch/file/1160419/1/CLIC_CDR_Review_080911.pdf
Impact of background studied in detail
  Require high granularity in space and time
  Defines detector requirements and guides the future of ongoing R&D
With CDR achieved initial goal:
  Demonstrated ability to perform high precision physics in the CLIC machine environment
If you would like to give your support to the physics case and R&D towards a future linear collider based in CLIC technology, you are invited to sign up: https://indico.cern.ch/conferenceDisplay.py?confId=136364
– Does not imply any formal commitment –

## Slide 48: Backup slides - accelerator

## Slide 49: More physics potential studies

## Slide 50: CLIC next phases
2011-2016 – Goal: Develop a project implementation plan for a Linear Collider :
Addressing the key physics goals as emerging from the LHC data
With a well-defined scope (i.e. technical implementation and operation model,
energy and luminosity), cost and schedule
With a solid technical basis for the key elements of the machine and detector
Including the necessary preparation for siting the machine at CERN
Within a project governance structure as defined with international partners
Final CLIC CDR and
feasibility established
European Strategy
for Particle Physics
@ CERN Council

## Slide 51: CLIC next phases
2011-2016 – Goal: Develop a project implementation plan for a Linear Collider :
Addressing the key physics goals as emerging from the LHC data
With a well-defined scope (i.e. technical implementation and operation model,
energy and luminosity), cost and schedule
With a solid technical basis for the key elements of the machine and detector
Including the necessary preparation for siting the machine at CERN
Within a project governance structure as defined with international partners
After 2016 – Project Implementation phase:
Including an initial project to lay the grounds for full construction (CLIC 0 – a significant part of the drive beam facility: prototypes of hardware components at real frequency, final validation of drive beam quality/main beam emittance preservation, facility for reception tests – and part of the final project)
Finalization of the CLIC technical design, taking into account the results of technical studies done in the previous phase, and final energy staging scenario based on the LHC Physics results, which should be fully available by the time
Further industrialization and pre-series production of large series components with validation facilities
Final CLIC CDR and
feasibility established
European Strategy
for Particle Physics
@ CERN Council

## Slide 52: 3TeV Parameter Optimisation
Optimisation:
Minimise cost for fixed luminosity L0.01
Physics constraint
  L0.01> 0.3 L
No constraints on background
  Regarded as perturbation

## Slide 53: Injector complex & experimental area
Interaction region, caverns and surface installation, as foreseen in the CDR, at CERN Prevessin

## Slide 54
CLIC RF Power Source Layout
Drive Beam Accelerator
efficient acceleration in fully loaded linac
Power Extraction
Drive Beam Decelerator Section (2  24 in total)
Combiner Ring  3
Combiner Ring  4
pulse compression &
frequency multiplication
pulse compression &
frequency multiplication
Delay Loop  2
gap creation, pulse compression & frequency multiplication
RF Transverse Deflectors
140 ms train length - 24  24 sub-pulses
4.2 A - 2.4 GeV – 60 cm between bunches
240 ns
24 pulses – 101 A – 2.5 cm between bunches
240 ns
5.8 ms
Drive beam time structure - initial
Drive beam time structure - final
54
Drive beam generation

## Slide 55: Concept of staging
Lower energy can run most of the time during construction of next stage.
0.5 TeV stage
Tot. length ~14 km
Notes: Only at the higher energies will the second drive beam be needed.

## Slide 56: Concept First Stage
Lower energy machine can run most of the time during the construction of the next stage.

## Slide 57: Concept Second Stage
Physics results will determine the energies of the stages

## Slide 58: Concept of staging
Only at the higher energies will the second drive beam generation complex be needed.

## Slide 59: Potential New CLIC Staged Parameters
First stage ML structures are re-used
Notes: First stage ML structures are re-used

## Slide 60: Potential New CLIC Staged Parameters
First stage ML structures are re-used
Notes: First stage ML structures are re-used

## Slide 61: Choice of L*
Longer L* would be beneficial
detector design
  angular coverage
  shielding solenoid
final quadrupole stabilisation
But it reduces luminosity
-> use 3.5m/4.3m as a baseline
-> all studies performed at 3.5m, some at 4.3m
More effort in the future to understand
trade-off
Luminosity includes 20% overhead for imperfections
Vol 1, 2.5.3.7

## Slide 62: Comparison CLIC vs LHC detector
In a nutshell:
CLIC detector:
High precision:
  Jet energy resolution
    => fine-grained calorimetry
  Momentum resolution
  Impact parameter resolution
Overlapping beam-induced background:
  High background rates, medium energies
  High occupancies
  Cannot use vertex separation
  Need very precise timing (1, 2, 5, 10ns)
No issue of radiation damage (10-4 LHC)
Beam crossings “sporadic”
No trigger, read-out of full 156 ns train
LHC detector:
Medium-high precision:
  Very precise ECAL (CMS)
  Very precise muon tracking (ATLAS)
Overlapping minimum-bias events:
  High background rates, high energies
  High occupancies
  Can use vertex separation in z
  Need precise time-stamping (25 ns)
Severe challenge of radiation damage
Continuous beam crossings
Trigger has to achieve huge data reduction

## Slide 63: Nikhef: Alignment
Alignment of beamlines wrt each other
Based on RASNIK
In addition work on general alignment in CLIC and in CTF3

## Slide 64: Nikhef collab. on pre-alignment
Objectives: provide transverse positional data on targets distributed over 100 m, with an uncertainty of measurement better than 5 μm
(M. Beker)
Concept: RASCLIC is a 3 point alignment, which consists of a monochromatic light source, a diffraction plate and a pixel image sensor.
The position of a diffraction pattern is monitored on the image sensor, which provides the relative position of the three components.

## Slide 65: Nikhef collab. on pre-alignment
The concept was validated in an old tunnel named TT1 on 140 m.
A precision of 20 nm was reached
New agreement signed for improved and expanded system
(H. van der Graaf)

## Slide 66: Backup slides - CTF3

## Slide 67: The CLIC Test Facility (CTF3)
DRIVE BEAM
LINAC
CLEX
CLIC Experimental Area
DELAY
LOOP
COMBINER RING
10 m
4 A – 1.2 ms
150 Mev
1.5 GHz bunch spacing
32 A – 140 ns
150 Mev
12 GHz bunch spacing
Small scale version of the CLIC drive beam complex
Feasibility issues studied:
Drive beam generation
Beam driven RF power generation
Two beam acceleration & accelerating structures
Ultra low emittances & beam sizes
Alignment
Vertical stabilization
Operation and Machine Protection System
Notes: Demonstrate Drive Beam generation (fully loaded acceleration, beam intensity and bunch frequency multiplication x8)
Demonstrate RF Power Production and test Power Structures
Demonstrate Two Beam Acceleration and test Accelerating Structures

## Slide 68: Drive Beam Deceleration and Module: CLEX
CLIC Decelerator sector: ~ 1 km, 90% of energy extracted
Two-beam Test Stand (TBTS):
Single PETS with beam
Accelerating structure with beam
  wake monitor
  kick on beam from break down
  Integration
Test Beam Line (TBL):
Drive beam transport (16 PETS)
  beam energy extraction and dispersion
  wakefield effects
Califes: Probe beam photo-injector
Beam energy 175 MeV

## Slide 69: Two Beam Module
G. Riddone et al.
Integration aspects are important
  alignment
  vacuum
  transport
  cabling
  …
Beam tests of PETS are ongoing
accelerating structure installed
important goal 2010: two-beam acceleration with 100 MV/m
Some tests after 2010 e.g. wake monitors, design exists
Later full modules will be tested

## Slide 70: Two-Beam Acceleration: CLIC Test Facility (CTF3)
150 MeV e-linac
PULSE COMPRESSION
FREQUENCY MULTIPLICATION
CLEX (CLIC Experimental Area)
TWO BEAM TEST STAND
PROBE BEAM
Test Beam Line
3.5 A - 1.4 ms
28 A - 140 ns
30 GHz test stand
Delay Loop
Combiner Ring
total length about 140 m
magnetic chicane
Photo injector tests,
laser
Infrastructure from LEP
Demonstrate Drive Beam generation (fully loaded acceleration, beam intensity and bunch frequency multiplication x8)
Demonstrate RF Power Production and test Power Structures
Demonstrate Two Beam Acceleration and test Accelerating Structures

## Slide 71: Accelerating Structure Results
RF breakdowns can occur => no acceleration and deflection
Goal: 3 10-7/m breakdowns at 100 MV/m loaded at 230 ns
T18 and TD18 structures built and tested at SLAC and KEK
T18 reached 95-105 MV/m
Damped TD18 reaches an extrapolated 85 MV/m
  Second TD18 under test at KEK
  Pulsed surface heating expected to be above limit
CLIC prototypes with improved design (TD24) will be tested this year
  expect similar or slightly better performances
S. Doebert et al.
Average unloaded gradient (MV/m)
Breakdown probability (1/m)
CLIC goal

## Slide 72: Backup slides - beamsthralung

## Slide 73: Incoherent Pairs
r Bz
ϑ0
GUINEA-PIG used
Calculation with virtual photon
approximation (Q2max choice confirmed by benchmarking Ph. Bambade et al.)
Beam size effect is included
300,000 particles produced
Average energy is 70 GeV
Strong deflection by the beam
smaller deflection observed with CAIN, under study

## Slide 74: Hadronic Background
Based on equivalent photon approximation with
Q2max =
max(1GeV2,(s/100)0.43)
3.2 events per bunch crossing
Events are simulated with PYTHIA 6.4.20
Benchmarked with SLAC generator (T. Barklow et al.)

## Slide 75: Beam-induced backgrounds
  Detector starts at θ>10 mrad
Main backgrounds in detector:
  Incoherent pairs: 60 particles / BX
  γγ → hadrons: 54 particles / BX
Need pile-up rejection
Need to include background in simulation

## Slide 76: Background Summary

## Slide 77: CLIC detector – very forward region (closely linked to MDI)

## Slide 78: Integration of QD0 magnets and IP Feedback systems

## Slide 79: LumiCal
Measure luminosity using Bhabha events
e-
e+
e-
IP
e+
Events
Q, (rad)
located at z=2.6 m
geometrical acceptance: 38 – 110 mrad
fiducial acceptance: 44 – 80 mrad
62 pb at 3 TeV
statistical accuracy
for 500 fb-1: 1.8x10-4
(NB. luminosity spectrum measurement using large-angle Bhabha scattering, not treated here)

## Slide 80: LumiCal – preliminary design
(FCAL collaboration)
In CLIC_ILD:
located at z=2.6 m
total depth: 171 mm
inner radius: 100 mm
outer radius: 290 mm
40 layers:
3.5 mm W plates
320 mm Si sensors
550 mm connectivity
readout electronics
at outer radius

## Slide 81: LumiCal – accuracy
(systematics!)
ILC at 500 GeV: requiring 0.1% accuracy
  high statistics physics channels at 500 GeV
  e.g. e+e- -> WW or f f yield approx. 106 events for 500 fb-1
Statistical error 10-3
LumiCal accuracy should be the same or better
CLIC at 3 TeV: requiring 1% accuracy
    (e.g. 0.2 mrad or 0.5 mm accuracy on inner edge of LumiCal)
  decided in February 2009, at start of first simulations studies
  considered sufficient (?) w.r.t. statistics in typical physics processes
  considered realistic for CLIC (higher background!)

## Slide 82: BeamCal
Tag h.e. electrons at small angles
(possibly used to give feedback to beam steering – not studied)
40 layers W-Si
10 cm graphite
incoming beam
spent beam
In CLIC_ILD:
located at z=3.1m
total depth: 260 mm (w/graphite)
inner radius: 32 mm
outer radius: 150 mm
40 layers:
3.5 mm W plates
+ sensors

## Slide 83: BeamCal
A single h.e. electron and 10 BX of bg.
- Shown here: energy deposition in the 10th layer

## Slide 84: Coil parameters
CLIC_SiD magnet parameters:
Conductor total length: 38 km
For details about transient behavior of the coil after a quench ->LCD Note 2011-007, B. Curé

## Slide 85: Coil & Conductor
487 mm
960 mm
Cross section of the solenoid conductor and cut through the coil assembly

## Slide 86: QD0 & Final focus stabilisation
Final focus stabilisation to 0.15 nm ( f > 4 Hz) required
Achieved with combination of active and passive elements
Experiment side
Accelerator tunnel side

## Slide 87: Detector on IP – between 2 vertical walls
Vertical cut through the experiment
Shielding ring
chicanes

## Slide 88: Ring chicane Shielding technique
3-D View
Side View
Fixed
rings
Mobile
rings
gap 50 mm

## Slide 89: CLIC_ILD: Ring chicane and Coils

## Slide 90: Backup slides - detectors

## Slide 91: Two detectors in Push-Pull
e-
e+
Notes: Tunnel (and MDI) all the way up to the detector

## Slide 92: CLIC Detector Concepts Overview
System | CLIC_ILD | CLIC_SID
VTX+Tracker | TPC, Radius=1.8m | Silicon, Radius=1.2m
ECAL | W/Si | W/Si
HCAL Barrel | W/Scint | W/Scint
HCAL Endcap | Steel/scint | Steel/Scint
Solenoid: B-Field | 4 T | 5 T

## Slide 93: CLIC parameters
 | LEP 2 | ILC 0.5 TeV | CLIC 3 TeV
L [cm-2s-1]] | 5×1031 | 2×1034 | 6×1034
Crossing angle |  | 14 mrad | 20 mrad
BX separation | ~22 ms | 700 ns | 0.5 ns
IP size in x / y / z direction [nm] | 250 mm / 5 mm / 10 mm | 600nm / 6nm / 10mm | 45 nm / 1 nm / 40 mm
# (gghadrons) / BX | negligible | 0.2 | 3.0
#Incoherent pairs / BX | negligible | 1 × 105 | 3 × 105
CLIC
CLIC: 1 train = 312 bunches, 0.5 ns apart trains at 50 Hz
ILC: 1 train = 1300 bunches, 700 ns apart trains at 5 Hz
156 ns
20 ms
Notes:   Occupancy = #hits / #readout-cells can reach large values
  trigger-less readout of whole train
  power pulsing of readout electronics, to minimize material needed for cooling

## Slide 94: Optimization of interaction region
Direct hits from incoh. pairs for CLIC_ILD
3 TeV: High occupancy in inner-forward region, cut-off ~parabolic shape
500 GeV: situation similar, though lower rates
            place beam pipe outside high-occupancy region
3 TeV
500 GeV

## Slide 95: Vertex detectors
 | CLIC_ILD | CLIC_SiD | CMS
Material X/X0 (90o) | ~0.9% (3x2 layer) | ~1.1% (5 layer) | ~10% (3 layer)
Pixel size | 20 x 20 μm2 | 20 x 20 μm2 | 100 x 150 μm2
# pixels | 1.84 G | 2.76 G | 66 M
Time resolution | 5-10 ns | 5-10 ns | <~25 ns
Power/pixel | <~0.2 μW | <~0.2 μW | 28 μW
CLIC_ILD
CLIC_SiD
102 mm
170 mm
255 mm
830 mm
60 mm
77 mm

## Slide 96: Cooling: P~500 W in vertex detectors
Bot Sensor 200um
ASIC150um
Glue 50um
Connector
Top Sensor 200um
ASIC150um
Nanoport connector
A. Mapelli,
J. Buytaert
NA62 GTK
Forced air flow – may work in barrel region
  no extra material
  Up to 240 liter/s flow, ~40 km/h flow velocity
Water cooling – Sub-atmospheric pressure
  Can use thin PEEK pipes
  Need simulations to asses impact of material on performance
Micro-channel cooling – Integrate cooling channels in Si
  Could be solution for forward disks
  Connectors are major challenge
Notes: Need low-mass cooling solutions!

## Slide 97: Power pulsing and power delivery
≥ 5 mF
Power pulsing in ASICs
Very low duty cycle of CLIC machine: 156 ns train, 20 ms pause
All subdetectors will implement power pulsing schemes at 50 Hz, to reduce power consumption and thereby material in cooling systems
Efficient power delivery to front end  minimize cable volumes
Example: DC/DC step-down conversion (sLHC upgrades)
Example: Low drop-out regulators (LDO)
R&D needed to combine power pulsing with DC/DC or LDO and to minimize material + noise

## Slide 98: Tracking System
Barrel Tracker | CLIC_ILD | CLIC_SiD
Technology | TPC+Silicon strips | Silicon strips
Inner radius | 329 | 230
Max. samples | 2(Si), 224(TPC),1(Si) | 5
Outer radius | 1808 | 1239
Max. Z | 2250 | 578 to 1536
Forward Tracker | CLIC_ILD | CLIC_SiD
Technology | Silicon strips | Silicon strips
Inner radius | 47 to 218 | 207 to 1162
Max. samples | 5 | 4
Outer radius | 320 | 1252
Max. Z | 1868 | 1556

## Slide 99: Backup slides - reconstruction

## Slide 100: PandoraPFA
Topological Association Algorithms
Track-Cluster Association Algorithms
Reclustering Algorithms
Fragment Removal Algorithms
PFO Construction Algorithms
ConeClustering Algorithm
Looping tracks
Cone associations
Back-scattered tracks
Neutral hadron
Charged hadron
Photon
9 GeV
6 GeV
3 GeV
Layers in close
contact
9 GeV
6 GeV
3 GeV
Fraction of energy
in cone
Projected track position
Cluster first layer position
12 GeV
32 GeV
18 GeV
30 GeV Track
38 GeV

## Slide 101: Jet Finding at CLIC
Using Durham kT à la LEP
  Timing cuts are effective
  Yet all particles in event clustered into the jets
e.g.
  two jets + missing energy
TIGHT
timing
Notes: At LEP, preferred jet-finding algorithm: Durham kT
  All particles in event clustered into the jets
  not appropriate for CLIC
Events at CLIC
  significant background from forward-peaked gg → hadrons
  events are often boosted along beam axis (beamstrahlung)
  “hadron collider” type algorithms more appropriate
kT algorithm at CLIC studied for benchmark physics analyses
  invariant under longitudinal boosts
  particles either combined with existing jet or beam axis
    reduces sensitivity to gg → hadrons

## Slide 102: Jet Finding at CLIC
e.g.
  two jets + missing energy
TIGHT
timing
“hadron collider” kT : R = 0.7
  much of background clustered with beam axis
  timing cuts do less work
  relative impact of timing and jet-finding depends on event topology
To tackle background: timing cuts + jet finding
Notes: At LEP, preferred jet-finding algorithm: Durham kT
  All particles in event clustered into the jets
  not appropriate for CLIC
Events at CLIC
  significant background from forward-peaked gg → hadrons
  events are often boosted along beam axis (beamstrahlung)
  “hadron collider” type algorithms more appropriate
kT algorithm at CLIC studied for benchmark physics analyses
  invariant under longitudinal boosts
  particles either combined with existing jet or beam axis
    reduces sensitivity to gg → hadrons

## Slide 103: Reconstruction in time
tCluster
After reconstruction have a list of Particle Flow Objects (PFOs)
Calculate energy weighted mean time of each cluster
    sub-ns resolution
Use times to reject clusters and associated tracks
Reject PFOs from background
  e.g. neutral hadrons in Endcap
Neutral hadrons
Notes:   charged particles – mostly matched to clusters
  photons – EM clusters
  neutral hadrons – clusters
- High granularity calorimeter - even low energy clusters have many hits
  - account for helical propagation time

## Slide 104: Timing requirements in the pile-up
  integrate over > 20 BXs to accumulate calorimetric signals
  integrate over < 5 BXs for acceptable gg → hadrons backgrounds
Radius
Time
Calorimeter
TPC
Si tracking/vertex
  Excellent time resolution
  High granularity calorimetry
  Sophisticated reconstruction
  The way out:

## Slide 105: W/Z Separation
Separation calculated by applying optimal cut, minimising number of misidentified events.
For ideal Gaussian distributions, misidentification of 15.8% corresponds to 2 separation.
If tails present in distribution, separation drops below 2 even if main peaks remain 2 apart.
Obtainable separation limited by natural width of W and Z to identification efficiency of 94%.

## Slide 106: W/Z Separation
Separation between W and Z peaks with no background and with 60BX of background:

## Slide 107: W/Z Separation
For ideal Gauss, misidentification of 15.8% corresponds to 2 separation.
With tails in distribution, separation drops below 2 even if main peaks remain 2 apart.
Separation with & without background:

## Slide 108: Default PFO Selection

## Slide 109: Loose PFO Selection

## Slide 110: Tight PFO Selection

## Slide 111: Jet Finding at CLIC
At LEP, preferred jet-finding algorithm: Durham kT
  All particles in event clustered into the jets
  not appropriate for CLIC
Events at CLIC
  significant background from forward-peaked gg → hadrons
  events are often boosted along beam axis (beamstrahlung)
  “hadron collider” type algorithms more appropriate
kT algorithm at CLIC studied for benchmark physics analyses
  invariant under longitudinal boosts
  particles either combined with existing jet or beam axis
    reduces sensitivity to gg → hadrons
To tackle background: timing cuts + jet finding

## Slide 112: Backup slides - reconstruction resolutions

## Slide 113: Transverse impact-parameter resolution
d0: distance of closest approach to interaction point in R-phi plane
main benchmark parameter for vertex detector performance
Fast simulation: LiC detector toy tool, used for design optimisation
Full simulation: Geant4-based ILD/SiD frameworks, used for physics studies
CLIC_ILD:
Both full and fast simulation perform simple Gaussian hit smearing
Full simulation without TPC information
   Worse resolution for high momenta
CLIC_SiD:
Full simulation models clustering according to parametrisation of KPiX readout chip  added realism leads to worse resolution in full simulation, as expected
Fig. 4.4a
Fig. 4.4b

## Slide 114: Dependence on single-point resolution
Varied single-point resolution by +- 50% (~ pixel sizes 10x10, 20x20, 30x30 μm2)
Observed change in d0-resolution:
  +- 40% for p = 100 GeV
  +- 15% for p = 1 GeV
Resolution close to or better than target values for all cases
Pixel size is also constrained by:
  Expected background occupancy
  Ability to separate adjacent tracks in dense jets
Fig. 4.5a
Fig. 4.5b

## Slide 115: Dependence on distance to IP
Varied distance to interaction point, by changing radii of beam pipe and barrel vertex layers in CLIC_ILD model
Observed change in d0-resolution:
  3.2% / mm for high momenta (parameter ‘a’)
  0.8% / mm for low momenta (parameter ‘b’)
Distance to interaction point is constrained by direct hits from incoherent pairs (see André Sailer’s presentation on backgrounds)
Fig. 4.6

## Slide 116: Dependence on material
Very small amount of material in baseline designs
Realistic models for supports, cabling, cooling not available yet
Studied sensitivity of d0 resolution for low momenta on material in beampipe and silicon pixel layers of CLIC_ILD
Doubling beam-pipe thickness  ~20% worse resolution at 90o
Doubling material in silicon layers  ~20% worse resolution at 90o
Steeper slope in forward region
Fig. 4.7a
Fig. 4.7b

## Slide 117: Tracking performance CLIC_ILD

## Slide 118: Resolution vs. Jet Energy
Barrel region |cos | < 0.7, no background, no jet reconstruction:
At lower energies, CLIC_ILD benefits from its larger radius.
At higher energies, particle separation becomes more difficult; confusion term dominates energy resolution; particle flow can become energy flow. Both detectors show similar performance.

## Slide 119: Resolution vs. Angle
No background, no jet reconstruction:
Resolution for CLIC_SiD is worse in the forward region, due to reduced angular coverage. There is no HCAL coverage below  = 15.5.
Resolution for CLIC_ILD dips in barrel/endcap overlap region, due to gap between ECAL barrel and endcap. Leakage effects due to this gap are more pronounced at higher energies.
Notes: In barrel region, both detectors show only small variation with jet angle.

## Slide 120: Timing Cuts
No background, no jet reconstruction:
Impact of CLICPfoSelector timing cuts on the physics event is studied by applying the cuts without overlaying any background.
Whilst timing cuts result in degradation of jet energy resolution for low energy jets, the impact is small for jets above 500GeV.

## Slide 121: Backup slides - occupancies

## Slide 122: Occupancies in CLIC_ILD vertex region
Barrel cylinder layers
Forward disk layers
Direct hits from incoherent e+e- pairs dominate
Up to 3x10-4 hits/mm^2/BX in barrel region  1.9% train occupancy / pixel
Up to 5x10-4 hits/mm^2/BX in forward region  2.9% train occupancy / pixel (including factors for simulation uncertainty and clustering) for comparison: ATLAS/CMS pixel occupancy ~0.1% / BX
Dominik – sep’11

## Slide 123: Backgrounds in CLIC_ILD Calorimeters
ECAL Endcap layer 5-10 train occupancy:
HCAL Endcap layer 35-40 train occupancy:
5x5 mm2 cells
3x3 cm2 cells
Total energy release / train:
Up to 50% train occupancy in ECAL Endcap, not including safety factors
Up to 1000% train occupancy in HCAL Endcap, not including safety factors
Need several readouts per train
May need even higher granularity
37 TeV energy release / train
 challenge for (jet) reconstruction
Note: forward region not yet optimized for backscatters into HCAL
Dominik – sep’11

## Slide 124: Calorimeter endcap occupancies
High occupancy due to incoherent pairs in high-z region of HCAL endcap
Inadequate shielding from the very forward calorimetry region
Can be solved
layers 5 – 10
layers 35 - 45
Full detector simulations:
Notes: In the case of the ECAL the average is given for layers 5 – 10 which broadly correspond to maximum
energy deposit of typical EM showers. In the case of the HCAL the average is quoted for layers 35 – 45
where the maximum activity from the neutron background is observed.
However, the forward region of the
GEANT4 models of the CLIC_ILD and CLIC_SiD detector concepts were designed before the impact
of the scattered neutron background from the incoherent pairs interacting in the BeamCal was fully
understood. The level of background in the low radius region of the HCAL in the current detector
models is too high. However, there are a number of possible ways in which to reduce this component
of the background. These will be studied in the future and include: increased shielding between the
BeamCal and the inner regions of the HCAL; the possibility of using a different absorber which, unlike
plastic scintillator, is relatively insensitive to neutrons; and increasing the transverse segmentation to
resolve the occupancy issue.

## Slide 125: Radiation exposure in silicon layers
NIEL:
TID:
Non-Ionizing Energy Loss (NIEL):
Displacement damage in silicon
Obtained from hit rates scaled with tabulated damage factors
Total Ionizing Dose (TID):
Obtained from simulated energy loss in silicon layers
 | CLIC_ILD | LHC
NIEL VTX barrel [1-MeV-neq/yr] | 4x1010 | >~1014
NIEL FTD [1-MeV-neq/yr] | 5x1010 | 
TID VTX barrel [Gy/yr] | 200 | >~ 105
TID FTD [Gy/yr] | 180 | 
FTD
VTX barrel
 Small expected radiation exposure, compared to LHC experiments

## Slide 126: Backgrounds in the calorimeters
Calorimeter backgrounds per bunch-train (3 TeV)
Calorimeter backgrounds per bunch-crossing are manageable, ~ 60 GeV
Hence want to integrate over as few as possible BXs
Tight timing requirements – O(ns) !
Detector | gg→ hadrons
ECAL endcaps | 11 TeV
ECAL barrel | 1.5 TeV
HCAL endcaps | 6 TeV
HCAL barrel | 0.3 TeV
Total | 19 TeV
….
….
0.5 ns
ECAL

## Slide 127: CLIC detector – electronics

## Slide 128: 5 detector categories with similar readout specifications
Silicon pixel detectors
  Arrival time for 1 hit readout per train
  Zero suppression
Silicon strip detectors
  Arrival time for >1 hits per train
  Sampling of pulse at regular interval
  No zero suppression due to the large occupancies
TPC
  Analog pad readout for 1000 voxels per channel
Calorimeters
  Arrival time for >1 hits per train
  Sampling of pulse at regular interval
  Pulse heights higher than strip detectors  time resolution
  No zero suppression
Muon detectors
  Digital readout of > 1 hits per train with a multi-hit TDC
  Zero suppression

## Slide 129
Safety factor 5/2 for
incoherent pairs/γγ to hadrons, TPC no safety
per train

## Slide 130: Implementation Example: Analog Calo Readout

## Slide 131: DAQ aspects

## Slide 132: CLIC detector – R&D

## Slide 133: Hardware/engineering R&D
CERN LCD hardware/engineering R&D (needed beyond ILC existing developments):
Vertex detector
  trade-off between pixel size, amount of material and timing resolution
Hadron calorimetry
  Tungsten-based HCAL (PFA calo, within CALICE)
Electronics
  Power pulsing for all sub-detectors (50 Hz)
  Fast readout with pulse-height + time + multi-hit in 156 ns
Solenoid coil
  Large high-field solenoid concept, reinforced conductor (CMS/ATLAS experience)
Overall engineering design and integration studies
  In view of sub-nm precision required for FF quadrupoles
  For heavier calorimeter, larger overall CLIC detector size etc.
In addition at CERN: TPC electronics development (Timepix-2, S-ALTRO)

## Slide 134: Pixel-detector technology options
20x20 μm2 pixel sizes  need small feature sizes
Time-stamping ~5-10 ns  need high-resistivity sensor
0.1%-0.2% material/layer  allows for ~50 μm sensor + ~50 μm electronics
Read out full 156 ns bunch train, no trigger
Technology Options:
1) Hybrid
Thinned high-resistivity fully depleted sensors
Fast, low-power highly integrated readout chip
Low mass interconnects
2) Integrated technologies
Sensor and readout combined in one chip
Charge collection in epitaxial layer

## Slide 135: Pixel-detector in hybrid technology
110 μm
220 μm
Timepix3 design
X. Llopart
2x4 superpixel
Thinned depleted high-resistivity sensors, ~50 um active width Example: ALICE pixel upgrade  meet CLIC goals
Fast, low-power, highly integrated readout chips Example: Timepix3 (2012) 130 nm IBM CMOS
  50x50 μm2 pixels  needs further reduction (<~90 nm process)
  1.5 ns time resolution  exceeds CLIC goals
  P~350 mW/cm2  meets CLIC goals (with power pulsing)
Low-mass interconnects between sensor+readout
  cost driver  needs further R&D
Advantages:
Use industry-standard processes for readout
Factorize sensor and readout R&D
Drawbacks:
Higher material budget than integrated approach
Interconnects difficult/expensive
Handling/bonding of thinned structures difficult

## Slide 136: Pixel-detector in integrated technology
Mimosa 26
M. Winter
High resistivity
Low resistivity
Epitaxial layer:
Integrate sensor and readout in one chip
Signal collection through electron drift in epitaxial layer
Example: MIMOSA chip family, 0.35 μm CMOS process
50 μm total thickness  meets CLIC goal
<<1 μm depleted area  need to increase
100 μs readout time (rolling shutter)  need single-pixel r/o
18.4 μm pitch, σSP~4 μm  meets CLIC goal
P~250 mW/cm2  meets CLIC goal (with power pulsing)
Advantages:
Very low material budgets achievable
Very low power consumption possible
Drawbacks:
Custom-made processes (availability in 10 years?)
Difficult to get fast signal collection + good S/N
Fast readout not yet demonstrated

## Slide 137: Hardware R&D on the experiment
Pixel detector:
Integrated solid state sensors, deep submicron, small-pitch interconnect, low-mass cooling, ultra-thin materials
Main tracker
(silicon strip detectors 150 m2,
TPC gas detector)
Calorimetry:
>1000 m2 cost-effective
silicon sensors; Integrated HCAL sensor planes
Solenoid coil:
Reinforced conductor
tests. Materials
Power delivery, on/off at 50Hz, driven by front-end electronics
Final Focus: Active and passive stabilisation, alignment
6 m

## Slide 138: RPC digital HCAL testbeam
32 GeV pion
With Fe, performed at Fermilab

## Slide 139: Beam Halo Muons

## Slide 140: Beam halo muons
Target muons/bunch crossing < 1
  muons per lost particle ~ 10-4
  allowed loss ~10-6
Muon spoilers gain factor 10, i.e. allowed loss ~10-5
  further reduction may be possible
Main halo generation is elastic beam-gas scattering in the BDS
  expected loss 7 10-8, i.e. 0.05 muons with no spoilers
  Other sources to be reviewed

## Slide 141: Beam Halo muons
Most work for CDR concentrated on impact of gg → hadrons
  Also looked at beam halo muons
Simulated events with entire bunch train of beam halo muons
  For study assumed a bad case: 5 muons/BX through detector
In 150 ns from start of bunchtrain:
  ECAL
    Total = 1.5 TeV (54k hits)
    Barrel = 0.8 TeV (18k)
    Endcap = 0.7 TeV (36k)
  HCAL
    Total = 10.8 TeV (128k hits)
    Barrel = 5.3 TeV (32k)
    Endcap = 5.5 TeV (96k)
12 TeV
For this very conservative
level of background:

## Slide 142: Software Mitigation
Three steps of background reduction
  Initial reconstruction window of 10 ns (50 ns in HCAL barrel)
  Timing cuts at cluster level (TightPFOSelection)
  Build in beam halo muon rejection into particle flow reconstruction
For very conservative assumption of 5 muons per BX
2.2 TeV
420 GeV
30 GeV
Readout window
TightPFOSelection
+ dedicated reco. Alg.
Background rejection very effective due to high granularity calorimeters

## Slide 143: Impact on Physics
Tested in by looking at W reconstruction in
  Sample of 500 GeV hadronic W decays
  Again very conservative assumptions (5 muons/BX)
Two effects observed
  Extra energy from clusters from beam halo muons: 30 GeV
  Energy of reconstructed jets also biased “pick” up hits from muons: 30 GeV
Readout window
TightPFOSelection + reco. alg.

## Slide 144: Impact on W Reconstruction
muon halo (5/BX)
gg → hadrons
muon halo (1/BX)
Compare W mass reconstruction
  no background
  gg → hadrons
  5 muons per BX (very conservative)
  1 muon per BX (conservative)
Worst case as pattern recognition not optimal
Conclude: a beam halo muon background of 1 muon/BX is acceptable
  Machine background likely to be much lower than this

## Slide 145: Backup slides - physics examples

## Slide 146: Susy
Search reach in the mA − tan β plane for LHC and CLIC. The left-most coloured regions are current limits from the Tevatron with ∼7.5 fb−1 of data at √s = 1.96 TeV and from ∼1 fb−1 of LHC data at √s = 7 TeV.
Black line is projection of search reach at LHC with √s = 14 TeV and 300 fb−1 of luminosity.
Right-most red line is search reach of CLIC in the HA mode with s = 3 TeV.
Resolving SUSY breaking models and masses with CLIC: Shown are the nearly degenerate spectra of a mSUGRA model and a mGMSB model.
Assuming some of the SUSY masses are measured, with a spectrum of the type above predicted by the different models of Supersymmetry breaking, CLIC would be able to discern not only some of the slepton masses and the heavier charginos within the two models, but also the SUSY Higgs masses.
Notes: Search reach in the mA − tan β plane for LHC and CLIC. The left-most coloured regions are
current limits from the Tevatron with ∼ 7.5 fb−1 of data at √s = 1.96 TeV and from ∼ 1 fb−1 of LHC
data at √s = 7 TeV. The black line is projection of search reach at LHC with √s = 14 TeV and 300 fb−1 √
of luminosity [78]. The right-most red line is search reach of CLIC in the HA mode with s = 3 TeV.
This search capacity extends well beyond the LHC. A linear collider at √s = 500 GeV can find heavy Higgs mass eigenstates if their masses are below kinematic threshold of 250 GeV.
Resolving SUSY breaking models and masses with CLIC: Shown are the nearly degenerate spectra of a mSUGRA model and a mGMSB model. Assuming some of the SUSY particles masses are measured, with a spectrum of the type above predicted by the different models of Supersymmetry breaking, CLIC would be able to discern not only some of the slepton masses and the heavier charginos within the two models, but also the SUSY Higgs masses. For mSUGRA the soft masses are m0 = 175 GeV, m1/2 = 645 GeV, A0 = 0, with tan β = 10 and μ > 0. For mGMSB the number of messengers are nl = nq = 5, and ΛSUSY = 4·104 GeV, MMess = 1012 GeV, with tanβ = 10.

## Slide 147: Heavy gauge boson
Observation of new gauge boson resonances in the μ+μ− channel by auto-scan at 3 TeV. The two resonances are the Z1,2 predicted by the 4-site Higgsless model
Expected resolution with √s = 3 TeV and 1 ab−1 on the “normalised” leptonic couplings of a 10 TeV Z′ in various models, assuming lepton universality. The couplings can be determined up to a twofold ambiguity.
  Z′ mass is assumed to be unknown.
  χ, η, φ refer to various linear combinations of U(1) subgroups of E6; the SSM has the same couplings as the SM Z; and, LR is U(1) surviving in Left-Right model.
Notes: Fig. 1.15: Left: Observation of new gauge boson resonances in the μ+μ− channel by auto-scan at 3 TeV. The two resonances are the Z1,2 predicted by the 4-site Higgsless model of [64]. Right : Expected resolution at CLIC with √s = 3 TeV and L = 1 ab−1 on the “normalised” leptonic couplings of a 10 TeV Z′ in various models, assuming lepton universality. The couplings can be determined up to a twofold ambiguity. The mass of the Z′ is assumed to be unknown. χ, η, φ refer to various linear combinations of U(1) subgroups of E6; the SSM has the same couplings as the SM Z; and, LR is U(1) surviving in Left-Right model. The two fold ambiguity is due to the inability to distinguish (a,v) from (−a, −v).