## Slide 1: CALET Simulation
17, May. 2011
Yosui Akaike
Waseda University
~Simulation & Modeling Meeting in INFN Pisa~

## Slide 2: Outline
Detector Configuration
Trigger Condition
Detection Efficiency
Geometrical Factor
Energy Resolution
Particle Identification
  electrons/protons separation
  charge resolution of CHD and SciFi
Trigger Rate on ISS orbit

## Slide 3: Baseline Configuration
The current detector model in our simulation is composed of active parts and major absorber parts of the calorimeter
  This model consists of;
    28 plastic scintillator paddles - 3.2 x 44.8 x 1.0 cm3
    7168 SciFi ‘s 0.1 x 44.8 x 0.1 cm3
    Tungsten plates
    44.8 x 44.8 x 0.07 cm3 x 3
    38.4 x 38.4 x 0.07 cm3 x 2
    32.0 x 32.0 x 0.35 cm3 x 2
    192 PWO logs 2.0 x 2.0 x 32.0 cm3
    no PMT, APD/PD, frames, cables, etc…
  No gaps between scintillators in
    CHD, IMC and TASC
  Tentative size of spaces are
  assigned between :
    CHD-IMC
    IMC-TASC
TASC
IMC
CHD
(Some results in this presentation are made
by different version models
which have SIA in substitution for CHD)

## Slide 4: Shower Images
Gamma-ray 10GeV
Electron 1TeV
p 10TeV

## Slide 5: Trigger system
Trigger sources
  Sum of each 2 SciFi layers : 4 x 2 (X,Y) signals
  Sum of the top layer of TASC
  CHD
Trigger mode
  High energy shower
  (all particles > 10 GeV)
  Low energy shower
  (electrons > 1 GeV)
  Single (for calibration)
  (all particles)
IMC1+2
IMC3+4
IMC5+6
IMC7+8
TASC1
Trigger condition such as threshold for each trigger source should be optimized with simulation studies.
In order to eliminate background events of low energy protons, trigger condition should be set to obtain only particles initiating the cascade shower. CALET is equipped with several trigger sources and three trigger modes

## Slide 6: High Energy Shower Trigger
Target
  e > 10GeV
  γ > 10GeV
  p, nuclei > a several 10GeV
Trigger Condition
  ① TASC1 > 55MIP
  ② IMC7+8 > 15MIP
95%
The distribution of MIPs at the top TASC layer
The distribution of MIPs at IMC7+8, events which converted below IMC8 are ignored
98%
15MIP
The threshold of TASC1 is determined to detect 95% of the 10GeV electrons.
The threshold of IMC7+8 is determined to detect 98% of 10GeV gamma-rays, of which converted above IMC7. (Least 2 points (IMC7 and IMC8) are needed to reconstruct a tracking in IMC)
Non-showered events of proton and nuclei are rejected by these threshold.
IMC1+2, IMC3+4, IMC5+6 will be not used to;
①detect not only electrons but also gamma-rays.
②detect events incoming from the detector side.
p10GeV:3.7%
p30GeV:15%
γ ： 10GeV

## Slide 7: Detection Efficiency
Detection efficiency of electrons
Detection efficiency of gamma-rays
The detection efficiency of high energy shower trigger:
(electrons) 95%:10GeV, 99% >20GeV
(gamma-rays) ~ 80% > 10GeV
The ratio of the first conversion of gamma-rays above W6 is ~80%.
First conversion points of gamma-rays
W1
PWO
W2
W6
W7
― all triggered
― conversion points > W6

## Slide 8: Low Energy Shower Trigger
Target
  e > 1GeV
Trigger Condition
  ① IMC1+2 > 0.7 x 2(layers) MIP
  ② IMC3+4 > 0.7 x 2 MIP
  ③ IMC5+6 > 0.7 x 2 MIP
  ④ IMC7+8 > 5 MIP
  ⑤ TASC1 > 7MIP
  (eff.95 of 1GeV electrons)
The thresholds of IMC1+2, IMC3+4, IMC5+6 are determined to detect a single track.
The thresholds of IMC7+8, TASC1 are determined to detect 95% of the 1GeV electrons
- the target is only electrons
- the flux in this energy region is very high,
⇒ IMC1+2, IMC3+4, IMC5+6 will be also used to detect only full-contained events.
Detection efficiency of electrons

## Slide 9: Geometrical Factor
>
①
④
③
②
Classification by the shower axis geometry
Electrons
Gamma-rays
: number of generated events
: number of triggered events
: incident area
: solid angle ()

## Slide 10: Deposit Energy
Electron 10 GeV
― TASC
― TASC+IMC
Electron 1TeV
― TASC
― TASC+IMC
The incident energy of electrons and gamma-rays was estimated by the total deposit energy of IMC & TASC.
Gamma 100GeV
― TASC
― TASC+IMC

## Slide 11: Energy Resolution
○：TASC (②③④)
□：TASC (①)
●：TASC+IMC (②③④)
■：TASC+IMC (①)
①: full-contained events
②~④ : partially contained events

## Slide 12: Electrons / Protons identification
Electrons : 1TeV
Protons : 1~1000TeV (E-2.7dE)
Estimation of the proton rejection power at TeV region
e : p = 1 : 100 @10GeV
⇒ rejection power : ~104
e : p = 1 : 1000 @1TeV
⇒ rejection power : ~105
Requirement of proton rejection power
(Number of protons)
(generated) 1.6 x 106
↓
(triggered) ~52000
↓
(energy bin) ~8700
― e
― p
95%eff.

## Slide 13: Electrons / Protons identification
95% efficiency of electrons,
4 protons are contained.
⇒ Proton rejection power ：
~ 2.0 x 105 (90%C.L.)
(=FE)
(=RE)
>
①
④
③
②
Classification by the shower axis geometry
Scatter plots for electrons and protons.
: shower axis center
: ΔE at i-th layer, j-th PWO

## Slide 14: Detection efficiency of nuclei
High energy shower trigger
・IMC7+8 > 15MIP
・TASC1 > 55MIP
Detection Efficiency
N 5GeV
① these increase is influence of the backscattering of the events of which the interaction occur in the lower layer of TASC.
② In case of high z particles, non-showered events can be detected because of large dE/dx
(Fe) ~100% efficiency
(N) in low energy region (<10GeV);
①
②
②

## Slide 15: Deposit Energy of Nuclei
10TeV/A
100GeV/A
case of Fe
Fe 10TeV/A
Incident energy of nuclei was measured by of TASC.
The distribution of of heavy nuclei such as Fe depends on the target nucleus.
The number of secondary in case of heavy target is larger than the one of light target.
(Interaction model : DPMJET3)

## Slide 16: Energy resolution of nuclei
If we select events of which interaction occur above the top layer of TASC,
(Interaction model : DPMJET3)
r.m.s. / <ΔE>

## Slide 17: Charge resolution
The charge resolution of CHD and SciFi was estimated with;
- back-scattering
- quenching
The Np.e. was calculated from the ΔE, assuming the following typical values;
  CHD : Nphoton/MeV = 10000, Npe/MIP = 100
  SciFi : Nphoton/MeV = 10000, Npe/MIP = 10
CHD
SciFi
--- p (ΔE)
― p (NP.E.)
--- He (ΔE)
― He (NP.E.)
--- p (ΔE)
― p (NP.E.)
--- He (ΔE)
― He (NP.E.)

## Slide 18: Charge resolution
CHD : 1TeV/A (1year)
― p
― He
― B
― C
CHD : 10TeV/A (5year)
The number of the incident particles to detector was estimated as SΩ~ 0.07m2sr.
Events which the first collision occur at the top layer of TASC was selected.
SciFi : 100TeV/A (5years)
― p
― He
― C

## Slide 19: Estimation of the trigger rate on ISS orbit
The trigger rate on ISS is evaluated by estimation of cosmic ray flux including primary particles and albedo particles.
1. Estimated Flux on ISS Orbit (at an altitude of 400km)
primary cosmic rays are assumed by some satellite and balloon experiments
particle transportation in geomagnetism ・・・・・・ Cosmos, ATMNC3
(ATMNC3: Atmospheric Muon Neutrino Calculation code 3-dimensional version)
Model of geomagnetism --- IGRF2005
Model of atmosphere -----– US-standard1976
 | Geomag. | Atmos. | Heavy nuclei | Calc. time
Cosmos | ○ | ○ | ○ | △
ATMNC3 | ○ | ○ | △ | ○
2. Trigger rate with detection efficiency
detector response : EPICS
(high energy shower trigger) primary: Cosmos, albedo: ATMNC3
(low energy shower trigger ) primary: ATMNC3, albedo: ATMNC3
Output : particle kind, energy, zenith angle

## Slide 20: Trigger Rate on ISS orbit
The density map of trigger rate
(High Energy Shower Trigger)
e-:0.78, p:5.5, He:2.7,
C:0.47, Fe:0.11, the other:1.84
(High) Ave. of orbit ：11.4Hz
(Low) Ave. of 5 min. in highest latitude：108Hz
e-:8.3, p:74.8, the other：24.9
Longitude[deg.]
Latitude[deg.]
Energy Spectra
(High Energy Shower Trigger)
(Low Energy Shower Trigger)
Average of trigger rate

## Slide 22
Prototype Detector for SPS beam test
layer
layer
(2-6)
(7,8)
x
for Shower trigger
(same as CALET)
r.l. :
Only longitudinal direction
layer
st
for Shower trigger
nd ~
r.l. :
(2/3 of CALET)
Only longitudinal direction

## Slide 23
Example for events
Simulation electron
electron
posictron
Event viewer
particle density disclibed by Colors
the number is number of MIP
Number of MIP
Exp. Data electron

## Slide 24: Energy Deposit in IMC
24
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
Layer 6
Layer 7
Layer 8
All SciFi
Data : 215
Mean difference：
1.17%
Mean difference：
0.848%
Single event
Shower event
~70 MIP
Each Layer
Positron 10GeV
・Energy deposit in sum of each layer
It could find the first interaction point by layer 1~6
・Sum of energy deposit in IMC
Vertical: event count
Horizontal：Energy Deposit [MIP]
（Horizontal axis is Log scale）
Simulations & Exp. Data are consistent
Notes: 24

## Slide 25: Energy Deposit in TASC
25
Each Layer
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
Layer 6
Layer 7
Layer 8
Data : 215
Mean defference：
0.461%
Mean difference：
0.163%
~110 MIP
All PWO
Vertical: event count
Horizontal：Energy Deposit [MIP]
（Horizontal axis is Log scale）
Positron 10GeV
・Energy deposit in sum of each layer
Using data → Layer1:PMT, Layer2~8:APD
Consistent in each TASC layer (PMT-MIP is calibrated with this data)
・Sum of energy deposit in TASC (without Layer 7)
Simulations & Exp. Data are consistent
Notes: 25

## Slide 26: Energy Deposit in IMC
26
Each Layer
Layer 1
Layer 2
Layer 3
Layer 4
All SciFi
Data : 261&449
Mean diff：
6.88%
Mean diff：
1.70%
Layer 5
Layer 6
Layer 7
Layer 8
Positron 150GeV
・Energy deposit in sum of each layer
we can find the first interaction point by layer 1~5
・Sum of energy deposit in IMC
(Mean value of Geant4 results has a tendency to be lower)
Shower event
Single event
Simulations & Exp. Data are consistent
~280 MIP
Vertical: event count
Horizontal：Energy Deposit [MIP]
（Horizontal axis is Log scale）
Notes: 26

## Slide 27: Energy Deposit in TASC
All PWO
（without layer7）
27
Each Layer
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
Layer 6
Layer 7
Layer 8
Mean diff：
1.14%
Mean diff：
0.983%
Data : 449
APD disabled
Positron 150GeV
・Energy deposit in sum of each layer
Using data → Layer1:PMT, Layer2~8:APD
Consistent in each TASC layer
・Sum of energy deposit in TASC (without Layer 7)
Vertical: event count
Horizontal：Energy Deposit [MIP]
（Horizontal axis is Log scale）
There’s a difference of distribution (Difference of mean value : ~ 1%)
~1400 MIP
Notes: 27

## Slide 28: Energy Resolution
28
Energy Resolution in TASC
Define “Energy Resolution”, using histogram of energy deposit in TASC
Energy Resolution ： RMSTASC / < ETASC >
・ Simulation data have the same
tendency as Exp. data
In high energy region, resolution
degradation by shower leakage effects.
・ Resolution of Exp. data is lower
→ contaminant particles
→ multi-hit events
Shower leakage effects
preliminary
color ： Exp. & Geant4 & EPICS
Vertical axis ： Energy Resolution in TASC
Horizontal axis ： Energy of incident particles
Notes: 28

## Slide 29: Lateral Spread
29
Data : 451
IMC
TASC
Lateral shower spread of IMC, TASC
(Positron 10GeV)
・For energy weighted spread of IMC, Using events of 1mm inner side of IMC layer 8.
・In IMC, simulation and exp. data have a similar distribution. (Difference of mean value : ~4%)
・In TASC, simulation and exp. data have a similar distribution.
(1cm edge : only 2 PWO logs in each layer)
[ Formula of Energy Weighted Spread RE ]
Ex. TASC
Notes: 29

## Slide 30: Lateral Spread
30
Lateral shower spread of IMC, TASC
(Positron 150GeV)
・For energy weighted spread of IMC, Using events of 1mm inner side of IMC layer 8.
・In IMC, simulation and exp. data have a similar distribution. (Difference of mean value : ~3%)
・In TASC, there is a little difference in distribution. (Diffirence of mean value : ~2%)
Data : 449
[ Formula of Energy Weighted Spread RE ]
Ex. TASC
IMC
TASC
Notes: 30

## Slide 31: Angular resolution （electron）
Energy dependency of angular resolution
Example event （electron 10GeV）
IMC 1st layer
IMC8th layer
Shower core
Anguler distribution（electron10GeV）
black：Simulation red：exp data
Distribution of the incoming direction deciding from reconstructed shower analysis
Notes: 31

## Slide 32: e/p separation by IMC data
Distribution of shower spread (e10GeV and hadron 30GeV)
 | Electron selection | Hadrons rejection
Simulation | 91.2% | 98.9%
Exp. data | 88.2% | 98.4%
electron
Hadron
Weighted spread of shower particles
Deposit energy in ith SciFi
Deposit energy in jth SciFi
Core position of reconstructed shower
Notes: 32

## Slide 33: END