## Slide 1: MoEDAL/MAPP status 11/2025
Richard Soluk – MoEDAL Collaboration (Technical Coordinator) University of Alberta

## Slide 2: MoEDAL 2025
MoEDAL
Since last report no access (until this week)
  TPX group replaced LV power supply Tuesday due to radiation issues
  No other hardware changes

## Slide 3: MoEDAL MMT Magnetometer
MoEDAL
ETH Zurich magnetometer running at Columbia University
Conducted tests in October
  Minor changes to device
  Sensitivity excellent
  Noise level good
  Stability possibly better
Similar model available in Barcelona through the IFIC Valencia group still to be evaluated

## Slide 4: MAPP Outrigger
MoEDAL
CNC router to Alberta now installed and running
Used scintillator lent by the Alabama group cut into 20 pieces for the 4th layer of the outrigger
Now being polished before wrapping

## Slide 5: YETS 2025-2026
MoEDAL
YETS 2025-2026
MAPP
  Install 7th ADC board
  Finish cabling calibration LEDs
  Install calibration boards
  Install front veto panels
MoEDAL
  Remove 2025 NTDs
  Remove some NTD infrastructure and forward MMT
    Required for normal VELO alcove work
    Hopefully don’t need to remove VELO TOP
  Install new NTDs at end of YETS
  Move TPX low voltage power supply to electronics barrack
    Requires pulling a new cable (if possible)

## Slide 6: Extra slides
MoEDAL

## Slide 7: MAPP TS1 2025
MoEDAL
MAPP detector composed of 10 x 10 x 75 cm PS scintillator bars
  Read out by either 75mm or 90mm diameter PMTs
  398 of 400 bars installed and cabled
    Last 2 planned for TS1 but access was very limited
    Flame shield not opened

## Slide 8: MAPP Electronics TS1 2025
MoEDAL
Minor adjustments to electronics setup
Cabled 6 of the 7 ADC boards
  7th board only reads a small number of channels
  Each boards reads a horizontal slice through the 4 detector stations (64 channels/board)
  Each row of inputs being 4 colinear detectors
View from IP
Channel assignment of each of the MAPP ADC boards