## Slide 1: BI MD 2012 REQUESTS LSWG 08-Dec-2012

## Slide 2
BI MD Requests 2012
Monitor | Description | Remarks | E | Beam Types |  |  | Time
 |  |  |  | p/bunch | Patterns | Emit | 
BCT FBCT | Test new FBCT prototype to be installed during xstmas shut-down, in order to verify -bunch length dependence -beam orbit dependence | -Possibly included in BI blocks to maximize studies in parallel -Variable bunch length -Bumps | 450+3500 | xx | xx | any | xx
BPM | Non linearity for each BPM type, by mapping a H/V grid with bumps | -Results have a direct impact on aperture measurements, so it would be advisable to foresee these studies very early in the run | 450 | xx | 1 | any | 8h
 | BPM offset and polarity checks |  |  | xx | 1 | any | 8h
 | BPMSW relative phasing | -Requested but not completed in 2011 -Possibly included in BI blocks to maximize studies in parallel | 450 | xx | 1+1 | any | 2h
 | BPMWF response to different orbit modes |  |  | xx | xx | any | 2h
 | K-mod of triplet BPMs and other critical locations | -determine BPM center -done after each TS (not MD time?) | 450 | probe | 1 | any | 4x1h
BGI | Magnetic field impact on the image Absolute calibration with bumps Sensitivity vs pressure and energy Pressure Evaluation around BGI with BLMs | -Possibly included in BI blocks to maximize studies in parallel -Bumps -gas injection | 450+3500 | xx | xx | Uniform over bunches | xx
BSRT | Calibration B1 system vs WS, re-check B2 | -Not completed 2011 -Bumps -Possibly included in BI blocks to maximize studies in parallel | 450+3500 | variable | variable | variable | >=3h
 | Additional studies about detectors response vs bunch intensity, camera gains, color filters |  |  |  |  |  | xx
 | Study response to hor slits |  |  |  |  |  | >=2h
MATCHING | Establish minimum beam intensity for allowing enough signal/noise with present system | Inj and Dump into empty machine with variable bunch intensities, up to maximum allowed | 450 | variable | 1 | variable | >=2h

## Slide 3
BI MD Requests 2012
Monitor | Description | Remarks | E | Beam Types |  |  | Time
 |  |  |  | p/bunch | Bunch Patterns | Emit | 
BLM | Direct Dump BLMs calibration | -Not finished in 2011 -inj and dump | 450 | variable | 1 | any | 2h
LDM | Study response to variable beam sizes | Possibly included in BI blocks to maximize studies in parallel | 450+3500 | xx | xx | variable | xx
WS | Emittance comparison between SPS and LHC at injection | bunch by bunch is being tested in the SPS BWS 416 | 450 | variable | xx | variable | xx
 | test of automated settings determination for the PMT gain and filter | When available during the year Turn mode at first, later 40 MHz | 450+3500 | variable | xx | variable | xx
Q-Meas | Co-existence of the tune measurement and the damper systems (test various Q/Q' diagnostics schemes) | Complementary to W.Hofle MD | 450+3500 | xx | 1 | any | 3x4h
Q/Q’ meas | Lifetime and emittance dependence on Q/Q’ | -dQ<0.001 and dQ'<1, not met by present systems -Determine whether we can relax the requirements on Q/Q' control, e.g. lower FB bandwidth, larger Q', etc. | 450+3500 | xx | xx | variable | 2x8h
OFC/OFSU | -validate new and/or modified OFC/OFSU schemes and Settings. -test new control aspects to verify new OFC/OFSU versions which we are not allowed to deploy operationally otherwise | Can be done during commisioning (not MD) ? | 450+3500 | probe | 1 | any | 4x4h

## Slide 4
BI MD Requests 2012
Monitor | Description | Remarks | E | Beam Types |  |  | Time
 |  |  |  | p/bunch | Bunch Patterns | Emit | 
Head-Tail and Wall Current Monitors | -Beam-based HT and WCM calibration and tests -compensate for system effects that presently perturb the ghost/satellite | -need short bunch -needed to test the new instability trigger scheme in a controlled/known environment prior to being operationally use during the ABP-driven high-intensity MDs | 3500 | >2e11 | 1 | any | 3x2h
BBQ Pt7 | Continuous beta-beat measurements alternative to BPM method | Could be done in parallel for the beta-beat electronic (<1 um oscillations) but may nevertheless need dedicated beam, since the BPM can achieve this only with larger AC-dipole driven excitations. | 3500 | probe | 1 | any | 2x4h
AGM | Possibly test new optical line (to decouple steering from BSRT) | -closed orbit bumps | 450+3500 | xx | xx | xx | xx