## Slide 1: Longitudinal and RF MDs 2012
P. Baudrenghien for the LHC RF team

## Slide 2: Longitudinal studies
Loss of Landau damping during ramp
  Single-bunch, different long. emittances, ramp
  Measurements of longitudinal dipole and quadrupole oscillations. Measurements of transverse emittance evolution in parallel
  6 h
Measurement of longitudinal broad-band impedance
  Single-bunch, different intensities, 450 GeV
  Measurement of dipole and quadrupole oscillation frequencies to derive impedance
  6 h
Longitudinal stability for batch
  Several batches, vary long. emittance/capture voltage, 450 GeV
    Measure damping of dipole oscillations at injection
  Increase cavity impedance at fundamental (reduce fdbk gain)
    Measure the onset of coupled-bunch instabilities
  2 x 8 h
Leftover 2011
Leftover 2011
Road to higher intensity

## Slide 3: Improvements of present operation
Longitudinal blow-up studies
  2 or more equally spaced batches, 144b, ramp
  Alternative longitudinal blow-up & batch per batch blow-up at injection
  2 x 8h
Commissioning of the longitudinal damper acting via the main accelerating cavities
  Batch(es) 144 b, 450 GeV
  2 x 8h
Reduced heating?
Effects of IBS during filling reduced
Reduced capture losses (25 ns)
Damps dipole oscillations at injection? (enough BW?)

## Slide 4: The road to higher intensity
Voltage modulation around one-turn
  Few batches 144b, 450 GeV then ramp
  Modulation of the voltage phase set point at frev to follow transient beam loading and minimize klystron power
  2 x 8h
RF feedback optimization with circulating beam
  Few batches, 450 GeV then ramp
  inject RF noise with zero power spectral density on the Synchrotron Sidebands to measure RF fdbk response (close loop) with circulating beam
  4h
Required to reach nominal current with 25 ns. First test required before LS1
Required for stable operation with nominal current . First test required before LS1

## Slide 5: p-Pb preparation
Commissioning of the p-Pb rephasing using p
  1 batch 32b p in each ring, 450 GeV
  Automate the rephasing to get collisions in the detectors
  2 x 4h
  Best scheduled in the second half of 2012… but at least 2 months before the p-Pb run