## Slide 1: Largest of the Rings LHC Past, Present and Future
L. Bottura
CERN Centennial Superconductivity Symposium
The Roots of the LHC Technology
December 8th, 2011

## Slide 2: Outline
The LHC pre-history
The making of the LHC
Long live the LHC !
Is there life after the LHC ?

## Slide 3: Outline
The LHC pre-history
The making of the LHC
Long live the LHC !
Is there life after the LHC ?
L. Rossi, Superconductivity and the LHC: the early days, CERN Courier, 51(9), November 2011, pp.21-27

## Slide 4: 1984…
Diego Maradona goes to SSC
(Societa’ Sportiva Calcio) Napoli from FC Barcelona for a ridiculous13.5 billions Lire
The National Reference Design Study (RDS) for a 20 TeV proton machine, hosted by LBNL, DOE recommends proceeding with R&D for a Sine-qua-non Accelerator (the SSC)
Big Brother is in full control and rules

## Slide 5: 1984 ECFA – Lausanne
G. Brianti
CERN 87-05, G. Brianti and K. Hubner Ed.

## Slide 6: Earlier traces of the two-in-one concept
John P. Blewett, 1971
Assembly work at BNL
SSC high field option
Robert B. Palmer, Superconducting Accelerator Magnets: A Review of their Design and Training, ICHEP 92, SLAC-PUB-5899, 1992
Per F. Dahl, The SSC Dipole: Its Conceptual Origin and Early Design History, SSCL-320, 1990

## Slide 7: SSC vs. LHC
G. Brianti had various reasons for headaches in the race of the two projects:
  The existing LEP tunnel imposed a given radius and cross sectional space to the new accelerator – Field !
  The missing factor in energy (8.5+8.5 TeV for LHC vs. 20+20 TeV for SSC) needed to be compensated by a higher luminosity (design value of 1034 1/cm2 s for LHC vs. 1033 1/cm2 s for SSC) – Aperture and quality !
R&D focus was the key !
  High field: aim at 8 to 10 T bore field
  Two-in-one: to gain space in the crammed tunnel space for the widest possible magnet bore

## Slide 8: High field – NbTi
1987 – R. Perin and D. Leroy built with Ansaldo Componenti a 1-m single aperture model using a 12.6 mm wide Nb-Ti cable
1988 – The model magnet reached 8.55 T at the first quench and 9.3 T at 1.6 K in 4 quenches

## Slide 9: NbTi and superfluid helium
LHC largely profited from the SSC R&D on NbTi for both the critical current (3000 A/mm2) and the filament diameter (5 to 10 mm)
Still, superfluid He was a must !
Measurement of Ic of an LHC cable by M. Garber (BNL), 1992
4.2 K
1.8 K
+3 T

## Slide 10: High field – Nb3Sn
1989 – A. Asner built with Elin (AT) a 1 m single aperture model using a 17 mm cable and the wind-and-react technique
The magnet reached 9.5 T at 4.3 K, and was re-tested after 8 months, reaching 9.5 T after two quenches
A single coil in mirror configuration reached 10.1 T, breaking the barrier of 100 kGauss
S. Wenger, F. Zerobin, A. Asner,, IEEE Trans. Mag. 25(2), 1989, pp. 1636-1639
Cable edge
VAC bronze wire

## Slide 11: Commit !
1991 – LHC Pink Book the decision was taken to use the more conservative technology:
  NbTi twin aperture, fully coupled magnets
  Cooled over the whole length by superfluid helium at 1.9 K
1-m Models Twin Aperture (MTA) program addressing twin aperture features
Twin Aperture (long) Prototype (TAP) program addressing cooling of long magnets at 1.9 K

## Slide 12: TAP program
Construction at ABB (cold mass) and FBM-Hudson (cryostat) of a twin aperture magnet using HERA-style coils (ABB cable) under the leadership of J. Vlogaert and Ph. Lebrun
1992 – Tests at CEN Saclay, the magnet reaches 5.8 T at 4.3 K and 8.3 T at 1.8 K
D. Granier, et al., Performance of the Twin-Aperture Dipole for the CERN LHC, Proc. EPAC 1992, pp. 1414-1416

## Slide 13: MTA program
1993 – All models (including KEK models) reached rapidly the expected 8 T range at 4.3 K
However, at 1.9 K they fell short of the promised 10 T land, requiring long training to exceed the 9 T mark
In perspective, this was still 90 % to 95 % of the short sample limit, well above the practical operating point of 80 % of short sample, i.e. a badly sold success
D. Leroy and R. Perin, Development of High-Field Superconducting Magnets for the Large Hadron Collider, Proc. EPAC 1990, pp. 326-328

## Slide 14: LHC prototypes
1988 – CERN-INFN Agreement for the development of full-size (10 m), twin aperture prototypes (G. Bellini, E. Acerbi, L. Rossi at INFN, M. Bona at CERN)
1989 – Order placed by INFN to Ansaldo Componenti (IT) for the production of two prototypes (MTP1Ax, aka CERN-INFNx), followed by a CERN order for a third prototype (MTP1A3)
1990 – Orders placed by CERN at three more EU producers (Noell, Alstom-Jeumont, Elin-Holec)
17 mm Nb-Ti cable in two grades
6 blocks design
Al collars

## Slide 15: From SSC to Desertron to oblivion
1989 – Superconducting Super Collider (SSC) Laboratory established in Texas
1991 – Major construction start. Seventeen shafts sunk and 23.5 km (14.6 mi) of tunnel by late 1993
1987 – Heated debate on cost. Estimate of 4.4 B$ strongly supported by the Texas representative at Congress
1993 – Cost projection reaches 12 B$, similar to the ISS. Strong criticism triggered an audit from DOE
October 1993 – Congress cancels the project, after 2 B$ were spent in the program
Construction site
Main shaft
SSC buildings

## Slide 16: Science, policy and politics
1995 – The CERN-INFN 2 in the background (String-1) of Italian president O. Luigi Scalfaro, between R. Perin (left) and L. Maiani (right)
Training of the first MTP prototypes, from: R. Perin, Superconducting Magnets, Proc. PAC 1995, pp. 1282-1287
MTP1A1 re-born as CAST
December 1994 – LHC project approved by the CERN Council

## Slide 17: 15 m prototypes
1998 – The first 15-m long prototype reaches the LHC nominal operating field

## Slide 18: Outline
The LHC pre-history
The making of the LHC
Long live the LHC !
Is there life after the LHC ?

## Slide 19: LHC twin-aperture dipole magnets
R. Perin
C. Wyss
L. Rossi
Concept perfected (design), demonstrated (models and prototypes) and realized on a large industrial scale

## Slide 20: Fine cables
7 mm filaments
LHC inner cable
LHC outer cable cross section
6000 billets, 7500 km of superconducting cables with extremely tight property control
This is why we can ramp
Stumbling bock for SSC
D. Leroy

## Slide 21: Coil winding
Tight controls on
  Winding quality
  Dimensions (field quality)
Spectacular precision (typical waviness in the range of 20 mm)
By courtesy of E. Todesco (CERN)

## Slide 22: Magnet assembly
Industrial process challenges (e.g. welding)
Tight geometric tolerances
  Sagitta: 1 mm
  IC flanges: 0.7 mm
  Correctors: 0.3 mm
Geometry of dipoles

## Slide 23: Cryo-magnets and tests
An industrial approach to the laboratory work
Magnet reception, cryostating, preparation for cold test and “stripping” for installation
Magnet powering tests and magnetic measurements

## Slide 24: Magnet installation
Logistic and planning
Descent in the tunnel
Magnet transport and installation

## Slide 25: Interconnection
65’000 electrical joints
Induction-heated soldering
Ultrasonic welding
Very low resistance
HV electrical insulation
40’000 cryogenic junctions
Orbital TIG welding
Weld quality
Helium leaktightness

## Slide 26: Large scale use of HTS
3250 current leads
31 km of BSCCO-2223 tape

## Slide 27: The LHC superconducting magnet zoo
By courtesy of S. Russenschuck (CERN)

## Slide 28: Short Straight Sections
1994 – CEA short straight sections (SSS) prototypes reach CERN and are assembled in String-I
14 February 1996 – CNRS-CEA-CERN collaboration protocol signed for the procurement of 392 main quadrupoles and assembly in the LHC-SSS
2006 – production completed

## Slide 29: High luminosity insertion
LHC point 5

## Slide 30: World-Wide Works
World-Wide Works
Approximately 100 contracts and international contributions

## Slide 31: LHC !
Injection | (GeV) | 450
Flat-top | (TeV) | 7
Length | (km) | 26.7
Dipole field | (T) | 8.3
Aperture | (mm) | 56
Temperature | (K) | 1.9
Commisioned |  | 2008

## Slide 32: Oh, of course, some of the most impressive detectors ever built
CMS
ATLAS

## Slide 33: September 10th, 2008…
IR7
IR3
IR6
First turn !

## Slide 34: …September 19th, 2008…
Initiated by an unprotected quench of defective joint
Arcing in an interconnection
Magnet displacement
Over-pressure
NOTE: this is an intentional defect built for testing purposes

## Slide 35: …back to work in 2009…

## Slide 36: …November 30th, 2009…
LHC surpasses a proton beam energy of 1 TeV

## Slide 37: … March 30th, 2010
3.5 TeV operation

## Slide 38: Outline
The LHC pre-history
The making of the LHC
Long live the LHC !
Is there life after the LHC ?

## Slide 39: LHC luminosity in the future
The target for the projected LHC lifetime is 3000 fb-1
We will need an upgrade by ≈2021:
HL-LHC
M. Lamont (CERN), Private communication
Any reference to existing accelerators and physical quantities is purely accidental
≈ 300 fb-1 by 2020

## Slide 40: Scope of HL-LHC
Cryoplant for IR’s
Cryoplant for RF cavities
Crab cavities
collimation
IR quadrupoles
SC links

## Slide 41: Nb3Sn knocks at the door

## Slide 42: New magnets for HL-LHC
Short Model Coil
FReSCa2
Nb3Sn Dipole
11 T DS
Nb3Sn Dipole
MQXC
NbTi Quadrupole
HQ/LHQ
Nb3Sn Quadrupole
US-LARP program
Nb3Sn
NbTi

## Slide 43: US-LARP magnets
SQ
SM
TQS
LR
LQS-4m
HQ
TQC

## Slide 44: Nb3Sn cables poised to break limits
SMC cable, 1.25 PIT Nb3Sn wire

## Slide 45: SMC-3 at CERN
12.6±0.1 T
Thermal cycle

## Slide 46: Outline
The LHC pre-history
The making of the LHC
Long live the LHC !
Is there life after the LHC ?

## Slide 47: HE-LHC – (33 TeV cms)
2-GeV Booster
Linac4
SPS+,
1.3 TeV, 2030?
HE-LHC
2030?
By courtesy of R. Heuer

## Slide 48: The path to 20 T
By courtesy of P. Lee, Applied Superconductivity Center, NHMFL

## Slide 49: Magnets for HE-LHC
For a 17 + 17 TeV collider in the LHC tunnel: 20 T dipoles
Present idea: HTS/Nb3Sn/Nb-Ti nested coil magnet
Scenario set during the Malta workshop in Oct 2010
By courtesy of E. Todesco, CERN
low-grade
Nb3Sn
high-grade
Nb3Sn
HTS
Nb-Ti
Bcoil
Time for a genetic mutation ?!?

## Slide 50: A (maybe) 20 T cable
Roebel cables of punched HTS tapes after an idea of W. Goldacker (KIT)
Manufacturing by IRL Ltd.
First test at liquid helium (4.3 K) and in high field (10 T) show a current carrying capacity of 4 to 10 kA
By courtesy of J. Fleiter, Ph. Denis, G. Peiro, A. Ballarino (CERN)

## Slide 51: Conclusions – 1/2
The history of LHC is a history of applied superconductivity.
A history that started 100 years ago…
March 19th – First International Women’s Day
April 8th – K. Onnes discovers supraconductivity
May 25th: Pancho Villa raging in Mexico
August 22nd: Mona Lisa stolen
December 14th: Roald Amundsen reaches the South Pole

## Slide 52: Conclusions – 2/2
The history of LHC is also, and foremost, a history of people…
… our supporting sponsors, the DG’s in the period 1984-2010 that defined, defended and did the job
  Herwig Schopper
  Carlo Rubbia
  Christopher Llevellyn Smith
  Luciano Maiani
  Robert Aymar
  Rolf-Dieter Heuer
… two strong project leader of remarkable fiber that navigated very rough seas
  Giorgio Brianti
  Lyn Evans

## Slide 53: … and those who made it !