## Slide 1: SVD Mechanical Status
PXD-SVD Meeting, Vienna

## Slide 2: TDR Layout
The TDR version is no longer accurate
The windmill angle is mirrored
Mechanics had to be adapted to this change
Constraints from the CDC require a smaller radius in layer 5 and 6
Layer | Radius [mm] | Ladder # | Windmill ° | Overlap %
6 | 140 | 17 | 7 | 20.6
5 | 115 | 14 | 7 | 18.4
4 | 80 | 10 | 6 | 21.6
3 | 38 | 7 | 6 | 10.6

## Slide 3: New Layout
End rings are mirrored
Hybrid boards had to switch position
Cooling tubes are merely shifted
Origamis and sensors are mirrored

## Slide 4: Restrictions
KEK requests a dr of 20 mm between layer 5 and 6
Support shell max. radius = 155 mm (thickness 6 mm)
The reduction of the radii goes along with a reduction in ladders numbers
KEK requests an even number of ladders in each layer
Space restrictions require reevaluation of some components and concepts
The following studies show pros and cons of different radii configurations

## Slide 5: Iteration 1
Support shell Inner radius: 155 → 149 mm
Layer 6 radius: 140 → 134 mm
Layer 5 radius: 115 → 110 mm
Too many ladders in layer 5
Layer 6 can be pushed outwards by 1 mm
Layer | Radius [mm] | Ladder # | Windmill ° | Overlap %
6 | 134 | 16 | 7 | 16.5
5 | 110 | 14 | 5 | 28.6

## Slide 6: Iteration 2
Layer 6 radius increase
Layer 5 ladder count reduced
Overlaps in layer 6 and 5 are a bit high
Connectors in layer 5 are difficult to access
Layer | Radius [mm] | Ladder # | Windmill ° | Overlap %
6 | 135 | 16 | 7 | 15.2
5 | 110 | 13 | 5 | 14.7
Connectors overlap endring

## Slide 7: Iteration 3
Layer | Radius [mm] | Ladder # | Windmill ° | Overlap %
6 | 135 | 16 | 7 | 15.2
5 | 110 | 13 | 5 | 14.7
Nanonics connectors reduce overlap

## Slide 8: Iteration 4
Layer 5 radius reduced by 5 mm
Layer 5 ladder count reduced
Nice overlap in layer 5
Design does not require Nanonics connectors
Interferences in the forward region with layer 4
Layer | Radius [mm] | Ladder # | Windmill ° | Overlap %
6 | 135 | 16 | 7 | 15.2
5 | 105 | 12 | 5 | 7.8

## Slide 9: Iteration 4 Interferences
Occurring interference between layer 4 and 5
Solution is pending
Interferences

## Slide 10: Comparison of Iterations
Iteration 1 has too much overlap in layer 5 and 6, the connectors are difficult to access
Iteration 2 has a better overlap in layer 6, connectors in layer 5 are still a problem
Iteration 3: Nanonics connectors solve the overlap problem - expensive solution
Iteration 2+3 have a odd number of ladders in layer 5
Iteration 4 is the cheapest solution but the interference between layer 4 and 5 has to be solved

## Slide 11: dr between layer 5 and 6
Note: discussions regarding the distance from layer 5 to layer 6 should include the consideration that this distance is highly variable
Thus a range should be defined, not a distance

## Slide 12: Analytical Method to Calculate Overlap
Due to many changes in geometry it was necessary to evaluate the overlap before drawing the actual configuration
Formula is not interference sensitive

## Slide 13: Backward Cone
Length and outer diameter is fixed
End ring connection points will only be changed if absolutely necessary
Inner diameter will decrease a little
Flange attachment point is designed

## Slide 14: Forward Cone
Flange attachment area is stretched to accommodate PXD hardware
Inner diameter will be reduced
The shape is optimized for minimal deformation
The connecting mechanism for the cone halves will sit on the end flange and the layer 4/5 end ring

## Slide 15: End Ring Separation/Positioning
Guide pins and bushings are included in every end ring
Used to provide mechanical alignment between the detector halves
Bushing
Guide Pin

## Slide 16: Closing Mechanism
Three types of remote locking mechanisms are under investigation
Mechanism is needed to provide stability along the cone
Can not be accessed directly
Remote operation required
Operation needs to be repeatable and can not fail
Joint
Pushrod
“Snap-hook”

## Slide 17: “Snap-hook” Disengaged View
Force required to lock the system can be varied easily by changing the cantilever length
Locking force is larger than the engaging force
Picture shows the experimental setup with a movable pin
Prototype is expected to be finished until March 2012
Disengaged Hook

## Slide 18: Wedge Design
Wedge design is simple and effective
Requires little space
Pushrod needs to be blocked to avoid accidental unlocking
Relatively large force required to lock the mechanism
Wedge

## Slide 19: Rotation Lock
Most complex construction
Requires relatively low torque to lock up
The system is closed via a steel wire
Wire flexibility could cause the system to fail while unlocking
Mechanism is relatively large
“Snap-hook” design is currently preferred
Locking Mechanism
Sheathed Wire

## Slide 20: Separating the Halve Shells
The CAD drawing shows that it is possible to separate the halves without interferences
Interferences seen in the picture in layer 3 result from the dummy mechanics representing the sensor as well as the electronics
Mechanical mockup was built to proof the concept
No interference discernible

## Slide 21: PXD Integration
Concerns about interferences in the narrow support cone part
Identified interferences only concern Kapton calbes
Unless a component sticks out further than the Kapton cables, there are no serious interferences
Area of Interest

## Slide 22: Ladder and End Ring Positions
Sensor edges are defined as distances from IP
Anchor point is not fixed due to rapid changes in the design

## Slide 23: Discussion
Can we concur on a design to push onwards to prototyping?
Is KEK contributing to prototyping?
Which components can be manufactured at KEK?
Is manpower available at KEK for certain design details?
How much manpower/ budget is available for prototype production?