## Slide 1: CI update
CI team

## Slide 2: UK spending plan
BGC monitor 2 for LHC | UK (VAT not inclued) | Spend already |  | comments |  | Action | Who
Turbo pumps | £45,000 | £24,000 |  | HIPACE300: 4911 chf *4; HIPAC700: 6967 chf *1, Need 3 X HIPACE700, 2XHIPACE300 (has one extra each as spare) |  | For Ray to check | Chiara
Backing pumps | ?? |  |  | Will use current Edward back pump for testing. Issues, Rotary vane pump used right possibly introduce oil to the LHC, if using rotary vane, we need gate valves for every TMP. Multi-stage ACP28/40 over budget. (£10000/pump) |  | Decision what to do and Get quotation now | Gerhard
Vacuum chambers | £40,000 |  |  | Gas injection and dump by CI, and interaction chamber by CERN. Need a preliminary drawing for quotation and possible proforma invoice. |  | Send drawing and get quotation | Hao
Gate valves | £47,461 | £47,461 |  | Quotation is there |  | Quotation is ready but need to make order. | Gerhard
Skimmers and nozzles | £6,600 | Skimmers £3100 Nozzles: £3500 |  | Check the nozzle in CI. |  | Order sent out | Hao
Small vacuum parts (nozzle skimmer holder, etc) | £6,000 |  |  | This will be delayed. Bellows, skimmers holder. |  | Get another 2 sets of bellow | Hao
vacuum gauges | £8,000 | Ready to order |  | From CERN catalogue. 5 X penning (PTR20 502 or PTR18 502) 2 X (PTR 013 (CF16) or PTR15 012 (KF16), normally in stock |  | Order | Hao
Fluorescense imaging system(optics, intensified camera, cmos camera, filters) | £22,000 |  |  | One camera system in the original design. |  | Email sent but no reply. | Hao
Gas rack and injection system | ?? |  |  |  |  |  | Gerhard
Total 1 | £175,061 |  |  |  |  |  | 

## Slide 3: Simulation geometry for v3 replica
0.00
4.5 mm
33.1mm
168.5mm
405.7 mm
563.6mm
d: 400 µm
d: 2 mm
a
b
a: 0.7 mm b: 7.5 mm
a: 0.3 mm b: 7.5 mm
a: 0.2 mm b: 7.5 mm
a: 0.1 mm b: 7.5 mm
a: 1 mm b: 97.5 mm
d
d
a
b
Nozzle
1st Skimmer
2nd Skimmer
3rd Skimmer
IP
4th Skimmer
*Code upgrade to include background pressure calculation

## Slide 4: Simulation data
Nitrogen | inlet pressure [bar] | 6 |  |  |  | Number Density | 3.61E+16 | #/m3 |  |  |  | 
 |  |  | Pressure |  |  |  |  |  |  |  |  | 
 | 3rd skimmer size [mm] |  | Nozzle | Skimmer I | Skimmer II | Interaction chamber |  | max density | Den_reduction_factor |  | FWHM_x | FWHM_y
7.5 mm | 0.7 |  | 1.2610E-03 | 4.8116E-06 | 3.4058E-06 | 2.5038E-07 |  | 3.65E+16 | 1.01 |  | 2.15 | 24.05
 | 0.3 |  | 1.2610E-03 | 4.8085E-06 | 3.5456E-06 | 1.0743E-07 |  | 3.34E+16 | 0.91 |  | 0.95 | 24.00
 | 0.2 |  | 1.2610E-03 | 4.8115E-06 | 3.5796E-06 | 7.1906E-08 |  | 2.56E+16 | 0.70 |  | 0.55 | 23.95
 | 0.1 |  | 1.2610E-03 | 4.8112E-06 | 3.6158E-06 | 3.5828E-06 |  | 1.39E+16 | 0.50 |  | 0.35 | 23.85
 |  |  |  |  |  | Number Density | 6.25E+16 | #/m3 |  |  |  | 
Neon | inlet pressure [bar] | 6 | Pressure |  |  |  |  |  |  |  |  | 
 | 3rd skimmer size [mm] |  | Nozzle | Skimmer I | Skimmer II | Interaction chamber |  | max density | Den_reduction_factor |  | FWHM_x | FWHM_y
7.5 mm | 0.7 |  | 2.4552E-03 | 1.2644E-05 | 1.0003E-05 | 7.2864E-07 |  | 6.48E+16 | 1.12 |  | 2.15 | 24.05
 | 0.3 |  | 2.4552E-03 | 1.2654E-05 | 1.0392E-05 | 3.1453E-07 |  | 6.31E+16 | 0.99 |  | 0.95 | 24.00
 | 0.2 |  | 2.4552E-03 | 1.2650E-05 | 1.0488E-05 | 2.0957E-07 |  | 4.92E+16 | 0.79 |  | 0.55 | 24.05
 | 0.1 |  | 2.4552E-03 | 1.2653E-05 | 1.0589E-05 | 1.0502E-07 |  | 2.57E+16 | 0.41 |  | 0.25 | 24.05

## Slide 5: Upper: Nitrogen
Nitrogen
Neon
Convolution
Convolution