## Slide 1: SMC: rational and history
Gijs de Rijk
Cern
SMC review, 12th December 2011

## Slide 2: SMC as NED phase 1.5
3 FP6-CARE-NED partners CEA, CERN & RAL + LBNL started the informal project Short Model Coil beginning 2007
Aim: build a small, limited resources, racetrack magnet as successor to NED , awaiting a larger new initiative (FP7-EuCARD)
Roles:
  Project leaders: A. Devred and after 5 months G. de Rijk
            Afterwards M. Bajko and since 2 years J-C. Perez
  design CEA, RAL, CERN, LBNL
  Structure manufacturing CEA
  Coil manufacturing RAL, CERN
  Assembly CERN
  Test CERN
Planned SMC coil assemblies in 2007
  SMC1 14 strand cable, 1.25 mm Alstom IT strand, RAL insulation
    “classical route”
  SMC2 14 strand cable, 1.25 mm Alstom IT strand, ceramic insul.
    “innovative route”

## Slide 3: SMC1
The original design was reported in 2 reports (on CERN CDS)
  Mechanical Design of the SMC (Short Model Coil) Dipole Magnet / Regis, F (CERN) ; Manil, P (CEA) ; Fessia, P (CERN) ; Bajko, M (CERN) ; de Rijk, G (CERN) , EuCARD-PUB-2009-005. - 2009.
  Magnetic Design and Code Benchmarking of the SMC (Short Model Coil) Dipole Magnet / Manil, P (CEA) ; Regis, F (CERN) ; Rochford, J (RAL) ; Fessia, P (CERN) ; Canfer, S (RAL) ; Baynham, E (RAL) ; Nunio, F (CEA) ; de Rijk, G (CERN) ; Védrine, P (CEA) , EuCARD-PUB-2009-004. - 2010

## Slide 4: SMC and EuCARD-Fresca2
When EuCARD-WP7-HFM was started in 2009, the need for an SMC step in the Fresca2 construction was clearly identified (experience at LBNL)
The SMC project was partly ‘annexed’ into EuCARD
Aim of SMC in EuCARD:
  Learn to make coils and structure. Get experience with Nb3Sn
  Certify manufacturing procedures for the EuCARd-Fresca2 magnet
Planned Fresca2 preparation SMCs from 2009 (the numbering was changed)
  SMC1 cable: 14 strand, 1.25 mm Alstom IT
  SMC3 cable: 14 strand, 1.25 mm EAS-Bruker PIT
  SMC4 cable: 18 strand, 1.00 mm EAS-Bruker PIT
  SMC5 cable: 40 strand, 1.00 mm EAS-Bruker PIT: “Fresca2” cable
  (the numbering from SMC4 onwards has changed again since)
The SMC2 (Ceramic) stayed outside EuCARD

## Slide 5: This review
Question to the reviewers:
Is SMC the correct way for preparing the Fresca2 magnet project ?
What is eventually missing in the SMC program ?
  Taking into account that SMC is not the core of the EuCARD project, and that we are already late : we have announced to the EC that, at the official end of EuCARD (April 2013), only one FRESCA2 coil will be tested, and that the full dipole will be tested only at the end of 2013 (main deliverable of task 3)
Are there improvements to be done for SMC3b and further (the next ones to be built) ?