## Slide 1: LHC Beams Production Losses and impact on NON-LHC physics
With the help of:
Hannes Bartosik, Karel Cornelis, Heiko Damerau, Detlef Küchler, Gabriel Metral, Bettina Mikulec, Yannis Papaphilippou
With thanks to the OP-teams and Machine supervisor teams
IEFC Workshop 2012
7 – 9 March 2012
Rende Steerenberg

## Slide 2: Content
The LHC beams produced
LINAC2 & PSB
The PS
The SPS
Super Cycles and N0n-LHC physics
Conclusions
LHC BEAMS PRODUCTION

## Slide 3: The LHC Beams Menu
 | Overview of LHC beams |  |  |  |  |  |  |  |  |  | 
 | PSB extraction |  |  |  | PS extraction |  |  | SPS extraction |  |  | 
 | Ip / ring | ɛh and ɛv | nb | nb | Ip / bunch | ɛh and ɛv | nb | Ip / bunch | ɛh and ɛv | ɛlongit | nb
 | [x1011] | [mm ∙ mrad] | batches | bunches | [x1011] | [mm ∙ mrad] | bunches | [x1011] | [mm ∙ mrad] | [eVs] | bunches
 |  | 1σ, norm. |  |  |  | 1σ, norm. |  |  | 1σ, norm. |  | 
LHCPROBE | 0.05 - 0.2 | ≤ 1 | 1 | 1 | 0.05 - 0.2 | ≤ 1 | 1 | 0.05 - 0.2 | ≤ 1 | ≤ 0.3 | 1
LHCPILOT | 0.05 | ≤ 2.5 | 1 | 1 | 0.05 | ≤ 3 | 1 | 0.05 | ≤ 3.5 | ≤ 0.8 | 1
LHCINDIV | 1.2 | ≤ 2.5 | 1 | 1 to 4 | 1.2 | ≤ 3 | 1 to 4 | 1.2 | ≤ 3.5 | ≤ 0.8 | 1, 4 or 16
LHCINDIV (HI) | 2.5 | - | 1 | 1 to 4 | 2.5 | - | 1 to 4 | 2.5 | - | ≤ 0.8 | 1, 4 or 16
LHC150 | 5 | < 1.5 | 1 | 6 | 1.2 | < 2 | 12 | 1.1 | < 2.5 (1.6) | ≤ 0.8 | 1 - 4 x 12
LHC100 | Is being reviewed |  |  |  |  |  |  |  |  |  | 
LHC75 (SB) | 11 | 1.5 | 1 | 6 | 1.3 | 1.8 | 24 | 1.2 | 2 | ≤ 0.8 | 1 - 4 x 24
LHC50 (SB) | 24 | 3.5 | 1 | 3 x 2 | 1.75 | 3.5 | 36 | 1.45 | 3.5 | ≤ 0.8 | 1 - 4 x 36
LHC50 (DB) | 10 | 1.4 | 2 | 4 + 2 | 1.6 | 1.6 | 36 | 1.5 | 1.9 | ≤ 0.8 | 1 - 4 x 36
LHC25 (DB) | 16 | 2.5 | 2 | 4 + 2 | 1.3 | 2.5 | 72 | 1.1 5 | 3.5 | 0.7 | 1 - 4 x 72
There are at least 10 flavours of LHC beams that have been produced in the injectors, not all beams are readily available.
The ones used are:
  LHCPROBE
  LHCINDIV (normal and high intensity)
  LHC50 (DB) with 12 and 36 bunches
  LHC100 for p-pb collisions (low int.)
  LHC25 (mainly for scrubbing and MD’s)
Considered no longer necessary:
  LHCPILOT
  LHC50 (SB)
  LHC75
  LHC150
LHC BEAMS PRODUCTION

## Slide 4: How much protons were produced
LHC beams represent less than 1% of the total intensity produced by the PS.
To put this in perspective 7.5x1017 is less than 1 year of integrated PS extraction losses on the present CNGS beam.
Due to their low emittances the LHC beams generate little uncontrolled losses in the whole accelerator chain.
The majority of the losses are voluntary to tailor the beam to the required characteristics.
LHC BEAMS PRODUCTION
8.7x1019 of which ~7.5x1017
for LHC beams to SPS

## Slide 5: Content
The LHC beams produced
LINAC2 & PSB
The PS
The SPS
Super Cycles and N0n-LHC physics
Conclusions
LHC BEAMS PRODUCTION

## Slide 6: LINAC2 and PS Booster Injection
Courtesy of PSB team
LINAC2 will work around 165 mA.
  Tests to run at 175 mA showed too little gain in brightness.
The PS Booster uses at present a multi turn injection.
  Intrinsically lossy (50 MeV).
  εh + εh = f (intensity).
LHC BEAMS PRODUCTION

## Slide 7: PSB LHCINDIV Beam
Injection: ~1.2x1012 protons.
Intentionally badly captured (reduced long. Acceptance).
Additional longitudinal shaving, reduces intensity from ~2x1011 to ~0.2-1.2x1010 protons:
  Starts at ~350 ms after start of cycle.
  Duration: ~70 ms (depending on final intensity requirement).
Capture
Long. shaving
Long. shaving
RF voltage function Ring 3
Beam Current Transformers
LHC BEAMS PRODUCTION
Operation Display

## Slide 8: PSB LHC 50 ns beam
Injection: ~1.5x1012 protons.
Transverse shaving reduces intensity to 8.5x1011 protons:
  starts at 305 ms after start of cycle.
  Duration: ~10 ms.
Trans. shaving
Injection
Beam Current Transformers
Operation Display
LHC BEAMS PRODUCTION

## Slide 9: Content
The LHC beams produced
LINAC2 & PSB
The PS
The SPS
Super Cycles and N0n-LHC physics
Conclusions
LHC BEAMS PRODUCTION

## Slide 10: LHC 50 ns Double Batch Production
Double batch injection from PSB.
Single Bunch per PSB ring:
  1st batch  4 bunches.
  2nd batch  2 bunches.
Triple splitting in PS.
Acceleration.
Double splitting in PS.
Bunch rotation in PS.
ɛLong final = ɛLong init x 2.33/6.
Ɛh/v < Ɛnom and well preserved.
Courtesy of H. Damerau
Potential issues:
  Space charge at injection.
  CBI after γ-jump  ɛLong, τbunch, bunch-to-bunch intensity variations (feedback available).
  Satellites in kicker gap.
LHC BEAMS PRODUCTION

## Slide 11: Loss Sources of the LHC 50 ns beam
Slow losses more or less constant along the cycle.
No noticeable additional losses during RF manipulations.
LHC BEAMS PRODUCTION
Arbitrary units
1st injection
2st injection
B increase
Extraction
Operation Display
Very good transmission efficiency
Wall Current Monitor last turns
Low Energy

## Slide 12: Improved Operability
The 50 ns double batch beam only became really operational in 2011.
Two dedicated users for 12 and 36 bunch version were introduced:
  More cycles/beams to maintain (identical).
  Improved stability/reproducibility.
  Reduced switching time.
Continuous improvement on the RF beam control system improved stability.
The Operations teams became more and more autonomous in adjustments and optimization.
LHC BEAMS PRODUCTION

## Slide 13: Content
The LHC beams produced
LINAC2 & PSB
The PS
The SPS
Super Cycles and N0n-LHC physics
Conclusions
LHC BEAMS PRODUCTION

## Slide 14: LHC Beams and Losses in the SPS
During setting up and LHC filling preparation the beam is systematically dumped at 450 GeV on the TIDV.
A few % of the beam is systematically scraped away.
LHC BEAMS PRODUCTION
During 2011 run, new scrapers were used in LSS1 instead of the old ones in LSS5.

## Slide 15: LHC Beams in SPS compared to FT and CNGS
 | Total accelerated | dumped | scraped | Total cycle losses
FT | 5.85 x 1018 | 4 x 1017 | 0 | 9 x 1017
CNGS | 4.82 x 1019 | 6 x 1017 | 0 | 2.5 x 1018
LHC cycles | 7.3 x 1017 | 5.8 x 1017 | 1 x 1016 | 5 x 1015
Although much less protons are accelerated on LHC type cycles, the amount of protons on the beam dump is comparable to CNGS.
With the scrapers in LSS1, the lost beam is mainly intercepted by TIDH and TIDV.
LHC BEAMS PRODUCTION

## Slide 16: Impact of Scraper on the Radiation in LSS1
Comparison between 2010 (no scraper) and 2011 (scraper) surveys shows little impact from the scraper losses on LSS1 radiation levels.
LHC BEAMS PRODUCTION

## Slide 17: Impact of LHC Filling on SPS Physics 1/2
In 2011, the FT cycle was kept during the LHC filling, but the CNGS duty cycle was reduced from 65% to 15%.
With the very intense 50 ns beam at the end of 2011, the ZS suffered from sparking and the voltage had to be reduced so that slow extraction was off during LHC filling.
If ZS sparking problem persists with high intensities, we can consider removing the FT cycle out of the filling super cycle in 2012.
LHC BEAMS PRODUCTION

## Slide 18: Impact of LHC Filling on SPS Physics 2/2
Removing the FT cycle from the SC has some undesired operational consequences :
  The NA users will clearly have less beam.
  During the LHC filling, the NA timing events will have to continue.
  For the super cycle with FT, they want the NA timing events only during FT cycle.
  Interlocks will have to be disabled during LHC filling and re-enabled for FT physics.
  Fooling around with timing events and interlocks will increase the risk of mistakes and damage. Work on sequencer tasks to reduce those risks is ongoing.
  The FT cycle is not very demanding for PS and PSB (only two short cycles in 15.6 seconds). Taking it out will have certainly an effect on PS and PSB users.
LHC BEAMS PRODUCTION

## Slide 19: Transmission in the SPS with Q20
Higher transmission (less losses) with Q20 low gamma transition optics compared to nominal optics due to:
  Higher stability  low chromaticity sufficient.
  Smaller sextupole gradients for chromaticity correction due to higher dispersion.
Injection to the LHC (at least in MD) to be tried this year.
Q20 – low γt optics
50 ns LHC beam
LHC BEAMS PRODUCTION

## Slide 20: Content
The LHC beams produced
LINAC2 & PSB
The PS
The SPS
Super Cycles and N0n-LHC physics
Conclusions
LHC BEAMS PRODUCTION

## Slide 21: Parallel Versus Dedicated Filling
Assumption: 2 hours filling per 24 hours.
During parallel filling (~ 8.5% of the time):
  NA physics can continue, provided ZS does not spark.
  CNGS reduced from ~65% to ~15% duty cycle.
  ISOLDE reduced from ~37% to ~34% duty cycle.
  TOF and EAST no notable change.
  AD not affected.
During dedicated filling (problematic for SPS ZS too):
  No NA physics, no CNGS.
  ISOLDE from ~37% to ~39%.
  TOF reduced from ~8% to ~6%.
  EAST reduced from ~30% to ~10%.
  AD not affected.
Relatively little impact for majority of the PS/PSB users, but….
LHC BEAMS PRODUCTION

## Slide 22: Impact of High Intensity LHC Beams on NA
For intensities > 1.4x1011 ppb the SPS ZS voltage will have to be reduced  no NA physics possible:
  During parallel and dedicated filling.
  Also during the parallel MD’s with high intensity LHC beams.
  No NA cycle results in a major reduction for EAST in PS, but more or less neutral for ISOLDE.
LHC filling represents ~ 8.5% of the time.
Parallel MD’s:
  Only during day time (~ 40% of the time).
  Assume ¼ of all parallel MD’s to use high intensity LHC beams (~ 10% of the time).
This means a reduction of ~ 20% in the NA beam time.
LHC BEAMS PRODUCTION

## Slide 23: A Super Cycle Example
Removing the Fixed target cycle has knock-on effects in the PS and possibly in the PS booster.
  EAST (DIRAC) will suffer.
  Reshuffling will distribute the burden.
PS
SPS
Fixed target
physics
CNGS
CNGS
CNGS
CNGS
DIRAC
EA
DIRAC
DIRAC
DIRAC
DIRAC
EA
EA
EA
nTOF
nTOF
LHC BEAMS PRODUCTION

## Slide 24: Content
The LHC beams produced
LINAC2 & PSB
The PS
The SPS
Super Cycles and N0n-LHC physics
Conclusions
LHC BEAMS PRODUCTION

## Slide 25: Conclusions & Questions
The number of protons produced for LHC is less than 1% of the total amount of protons produced.
The LHC beam sizes are small:
  Therefore they produce few losses.
  The majority of the losses are made “on purpose” to obtain the correct beam characteristics.
  Many of them are at low energy, apart from SPS scraping and beam dumping.
  Other beam loss sources on LHC beams are actually due to equipment failures (see G. Metral talk earlier).
LHC beam with 1.4x1011 ppb means no NA.
  This results in approximately 20% less FT physics time.
Are there mitigation measures for ZS sparking ?
LHC BEAMS PRODUCTION