## Slide 1: ISOLDE feed-back on ALARA process
AP.Bernardes on behalf EN-STI-RBS team
IEFC - 07 March 2012

## Slide 2: OUTLINE
Introduction to ISOLDE target Area
ALARA principle
ALARA implementation for EN/STI/RBS
Feed-Back
Conclusion
07/03/2012 - IEFC

## Slide 3
Isolde Experimental hall 170
Isolde Target Area 179
Isolde area :
Route Democrite

## Slide 5: On-Line Isotope Mass Separator
Protons from Booster
1.4GeV@2μA
Picture from V.Barozier

## Slide 6: On-Line Isotope Mass Separator
Picture from V.Barozier
ALARA level II or III
- High dose rate
- Contamination

## Slide 7: OUTLINE
Introduction to ISOLDE primary Area
ALARA principle
ALARA implementation for EN/STI/RBS
Feed-Back
Conclusion
07/03/2012 - IEFC

## Slide 8: ALARA
ALARA principle (As Low As Reasonably Achievable)
Optimisation process
Reduction of individual and collective doses
RPE course extract
ALARA Principle

## Slide 9: ALARA Principle
CERN ALARA criteria
5 Criteria defined in EDMS 810176 “Critères et exigences ALARA”
Dose rate (H)
Individual Dose (Hi)
Collective Dose (Hc)
Atmospheric Contamination (CA)
Surface Contamination (CS)
ISOLDE

## Slide 10: ALARA Principle
ALARA tools at CERN (DGS-RP site: https://espace.cern.ch/rpps/wdp/default.aspx)

## Slide 11: ALARA Principle
ALARA tools at CERN (DGS-RP site: https://espace.cern.ch/rpps/wdp/default.aspx)
WDP: Work and Dose Planning (define which ALARA level I, II or III)
RWP: Radiological Work Permit (As well called DIMR “Dossier d’Intervention en Milieu Radioactif”)

## Slide 12: Number of ALARA at CERN since 2010 Data extracted from RWP directory (https://espace.cern.ch/rpps/wdp/default.aspx)
Chart: 
| ALARA level III | ALARA level II
ISOLDE | 16 | 33
Others | 4 | 37
80%
47 %
ALARA Principle
Data based on WDP/RWP stored on RWP Sharepoint directory

## Slide 13: OUTLINE
Introduction to ISOLDE primary Area
ALARA principle
ALARA implementation for EN/STI/RBS
Feed-Back
Conclusion
07/03/2012 - IEFC

## Slide 14: EN/STI/RBS ALARA Implementation
ALARA at ISOLDE
ALARA Level I : Formal WDP is optional
ALARA level II : Radiological Work Permit and Work and Dose Permit  Submitted to DGS/RP
ALARA level III :
- RWP and WDP done  Submitted to DGS/RP
- Presentation of ALARA principle during ENTM in presence of EN safety Officers (RSO and DSO)
- Approval request at the ALARA level III committee

## Slide 15: EN/STI/RBS ALARA Implementation
RWP and WDP
ALARA level III committee
Identification of different scenarios
Test of the different scenarios identified or suggested
Specific equipment development

## Slide 16
Shut-down 2008-2009
Extraction electrode changed manually –
Dosimeter ring: 4.5 mSv (finger contact limit value = 500 mSv)
Shut-Down 2009 -2010
Specific tool development on RP demand
Feed-back 2011 higher risk of dropping the electrode
Shut-down 2011-2012
Tool improvement to reduce the risk of dropping the electrode
Example 1: Specific equipment development

## Slide 17
Targets handled by hand
537 μSv recorded
Before shut-down 2011
Targets handled by hand and by robot
239 μSv recorded
Shut-down 2012
Targets handled by robot only
Dose phase I << 239 μSv
After LS1
Shut-down 2014
Example 2 : Specific equipment investment

## Slide 18
Example 2 : Specific equipment investment
Thanks to the collaboration of EN/HE/HT

## Slide 19
Example 3 : Specific equipment development and investment
5 m

## Slide 20: EN/STI/RBS ALARA Implementation
ISR 3
179 building
Example 4 : ISOLDE target transport during shut-down
Several option were possible

## Slide 21
Container located at ground level
Option N°1: Transport 179 to ISR3
Thanks to the collaboration of EN-HE-HH and DGS-RP

## Slide 22
Target box handled with remote handling device
5 m
Estimated collective dose :
≈ 290 man.µSv
Option N°1A: Transport 179 to ISR3
Thanks to the collaboration of EN-HE-HH and DGS-RP

## Slide 23
Estimated collective dose :
≈ 290 man.µSv
Target box handled with pallet truck
Option N°1B: Transport 179 to ISR3
Thanks to the collaboration of EN-HE-HH and DGS-RP

## Slide 24
Container on trailer
Option N°2: Transport 179 to ISR3
Thanks to the collaboration of EN-HE-HH and DGS-RP

## Slide 25
Estimated collective dose :
≈ 190 man.µSv
8 transports needed. Handling of one box at a time
One target box handled with remote handling device with class A container on truck
Option N°2A: Transport 179 to ISR3
Thanks to the collaboration of EN-HE-HH and DGS-RP

## Slide 26
Estimated collective dose :
≈ 120 man.µSv
Target boxes handled with forklift
Option N°2B: Transport 179 to ISR3
Thanks to the collaboration of EN-HE-HH and DGS-RP

## Slide 27
Simulation results
Intervention description | Estimation
Target box handled with remote handling device | ≈ 290 man.µSv
Target box handled with pallet truck | ≈ 290 man.µSv
2 target boxes handled with remote handling device with class A container on truck | ≈ 160 man.µSv
Target boxes handled with forklift | ≈ 120 man.µSv
≈ Expected dose save 150µSv compare to 2011
≈ In reality 90 µSv saved compare to 2011

## Slide 28
RWP and WDP
ALARA level III committee
Test of the different scenario :
1 day coordination
2 x 1 day for rehearsal and preparation
  2 person from DGS/RP
  3 person from EN/STI
  4 person from EN/HE
Equipment investment
Equipment development

## Slide 29: OUTLINE
Introduction to ISOLDE primary Area
ALARA principle
ALARA implementation for EN/STI/RBS
Feed-Back
Conclusion
07/03/2012 - IEFC

## Slide 30
ALARA tools feed-Back : WDP
Feed-Back
WDP very appropriate, very practical, simple
Good help for the optimisation process, useful to compare different scenarios
WDP not appropriate for operation with only contamination. WDP should not be requested in that case.
Proposition from ARWG (Alara Review Working Group) under preparation

## Slide 31: Feed-Back
Other ALARA Feed-back
 People should be encouraged to give realistic numbers on the WDP and not to over estimate the dose or time to allow optimisation to take place
 Tolerance of 150% is used by ISOLDE - Feed-back by RP welcome to explain difference and investigate if future changes are needed
Comparative approach

## Slide 32
ALARA tools feed-Back : RWP
Feed-Back
RWP good summary of the operation
Process of approval not defined, not clear
Follow-up of recommendations and comments not pratical, recommendation may appear at different places
Proposition from ARWG (Alara Review Working Group) under preparation

## Slide 33
ALARA criteria
Criteria should be considered as a help to assess the severity of the operation perhaps not as a management tool, or as an approval process definition
Feed-Back
Dose rate (H)
Individual Dose (Hi)
Collective Dose (Hc)
Atmospheric Contamination (CA)
Surface Contamination (CS)
No management involvement
Director for Accelerators and Technology
authorisation
Section or group leader involvement
II and III operation may be very similar
Proposition from ARWG (Alara Review Working Group) under preparation

## Slide 34: Feed-Back
Other ALARA Feed-back
ALARA reasonable should not be forgotten
Transport with container type A on trailer
Measured 302 µSv
Shut-down 2011
Transport with “surbaissé”
80 µSv measured
Until shut-down 2010
Acceptance by the management to increase the collective dose of the operation to secure transport by using a container type A on road and to reduce the consequences of a road accident

## Slide 35: Conclusion
ALARA very good principle – Request resources and investment
WDP very useful
RWP to be improved
RP participation very important and very much appreciate
Improvement of ALARA criteria on going thanks to ARWG (Test in field before validation of new approach very much appreciated)
Help to users on recommendations and feed-back follow-up (tool?) would be very much appreciated  ARWG proposition under preparation