## Slide 1: Using reconfigurable FPGAs in radioactive environments: challenges and possible solutions
Massimo Violante
Politecnico di Torino
Dip. Automatica e Informatica
Torino, Italy

## Slide 2: FPGA structure/technology
Logic Blocks & Interconnections
Configuration Elements
Antifuse
Flash
SRAM
Before programming

## Slide 3: FPGA structure/technology
Logic Blocks & Interconnections
Configuration Elements
Flash
SRAM
After programming
Antifuse

## Slide 4: Why FPGAs?
Antifuse FPGAs are used heavily as they allow shorter time to market, and lower costs for small volumes than ASICs
No versatility (one-time programmable)
SRAM-/Flash-based FPGAs are reprogrammable
The benefits of versatility:
  Reconfigurable computing
  Feature improvements over the years
  Bug fixing (!)
Source: Microsemi

## Slide 5: Bug fixing
Buggy Chip

## Slide 6: Reconfigurable FPGAs vs radiation
As a matter of fact, most of the reconfigurable FPGAs are soft w.r.t. radiation
To use them in radioactive environments it is compulsory to:
  Understand effects from the designers perspective
  Understand if/why mitigation techniques may fail
  Define validation flows

## Slide 7: Outline
Radiation effects in SRAM-/Flash-based FPGAs
Design mitigation issues
Design validation
Conclusions

## Slide 8: Outline
Radiation effects in SRAM-/Flash-based FPGAs
Design mitigation issues
Design validation
Conclusions

## Slide 9: Effects relevant for FPGAs
Single Event Effects (SEE)
Hard Errors
Soft Errors
Single Event Transient (SET)
Single Event Upset (SEU)
Functional Interrupt (SEFI)
Single Event Latchup (SEL)
Gate Rupture (SEGR)
Single Event Burnout (SEB)
Total Ionizing Dose
(TID)
Displacement Damage
(DD)
Addressed in this talk

## Slide 10: SRAM-based FPGA Architecture
BRAM
Xilinx Virtex-4QV
PowerPC
PowerPC
DSP
CLB
A B C D
Lookup Table (LUT)
‘0’
0
1
1
1
1
1
1
1
0
1
0
0
1
0
1
0
Boolean Function
F(A,B,C,D)
Notes: The configuration memory is spread throughout the device in a large array.
Each logic block contains its own configuration cells locally.
A data frame is a one bit vertical slice through the array.
The configuration logic identifies each frame with a unique address “minor” as
well as a unique address for the column that it lies in.
Configuration data is loaded serially or in byte-parallel into the interface where
it is assembled into a frame in a shift register.
The entire frame is loaded into memory all at once.

## Slide 11: SEU in SRAM-based FPGAs: CLB slice
Configuration memory bits
CLB slice
0
0
0
1
0
1
1
1
0
0
0
1
0
1
1
1
I1
I2
I3
I4
LUT
routing
LUT
Persistent effect (corrected by reconfig)
Transient Effect (corrected at next ffp load)
Notes: When we take a look in the FPGA architecture, there are two basic elements to implement the logic in a FPGA, the lookup table that is responsible to implement the logic functions as truth tables and the flip-flops. They are all located in the CLB slices. These basic elements are connected through a programmable routing that are multiplexers or pass transistors controlled by static memory cells.
When a SEU occurs in one of these memory cells: the configuration memory bits (LUTs and routing) or in the CLB flip-flop, the stored value is flipped, this creates a fault with a permanent effect in the case of LUT or routing, or a fault with a transient effect in the case of the CLB flip-flop.

## Slide 12: SRAM-based FPGA General Routing Matrix (GRM)
Direct connections
Hex connections
Direct lines
Double lines
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
Long lines
Hex lines
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
Fast connect
CLB
Xilinx Virtex-4QV

## Slide 13: SEU in SRAM-based FPGAs: Routing configuration cells
0
1
short
1
0
open
Direct connections:
Hex connections:
open
short
0
1
1
1
short
open
Persistent effect (corrected by reconfig)
Xilinx Virtex-4QV

## Slide 14: Flash-based FPGA
Microsemi ProAsic3

## Slide 15: SEE sensitivity
Configurable Logic Block called VersaTile
VersaTile
logic
Effect 1:
SET in the logic

## Slide 16: SEE sensitivity
Configurable Logic Block called VersaTile
ffp
VersaTile
X
Effect 2:
SEU in the ffp

## Slide 17: SEE sensitivity
Floating Gate (FG) switch
Effect 3:
SET in the logic path
SET in the routing path

## Slide 18: What to remember so far
SRAM-based FPGAs are soft against radiation
  User logic (SET)
  User memory (SEU, MBU)
  Control logic (SEU, SEFI)
  Configuration memory (SEU, MBU)
Flash-based FPGAs are soft against radiation
  User logic (SET)
  User memory (SEU, MBU)
  Control logic (SEU, SEFI)

## Slide 19: Outline
Radiation effects in SRAM-/Flash-based FPGAs
Design mitigation issues
Design validation
Conclusions

## Slide 20: Problems and solutions
The problems
  SEU
  SET
  SEL
  SEFI
  TID
The solutions
  Device-level solutions
    Make the device design rad tolerant
  Design-level solutions
    Make your design rad tolerant
Which is the best solution?

## Slide 21: Which is the best solution?
From the designer perspective the answer is easy: device-level solutions
  Problem solved at the root
  No need to put extra-effort to design for SEE mitigation and validate the resulting design
However, few devices are ready (?) today
  Atmel AT280 (SRAM-based, old concept, poor back-end tools)
  Xilinx Virtex-5QV (SRAM-based, ITAR restricted, expensive)
  No Flash-based device available

## Slide 22: A pragmatic compromise
Select among commercial devices those that are immune to TID and SEL
Design your application for SEE mitigation using
  Appropriate system architecture for SEE removal
  Appropriate circuit architecture for SEE masking

## Slide 23: System Architecture
Payload FPGA on-chip configuration is refreshed periodically
SRAM-based FPGAs
  To remove SEE in c.m.
FLASH-based FPGAs
  To anneal TID effects
Period depends on the radiation environment
Payload FPGA
Configuration
Memory Backup
System
Controller
Config
Bus

## Slide 24: Architecture for SEE masking
D1.1
D1.2
Your design

## Slide 25: Architecture for SEE masking
D1.1
D2.1
D3.1
V1
V1
V1
D1.2
D2.2
D3.2
V2
V2
V2
V3
V3
V3
TMR Domain
Voter Partition
In SRAM-based FPGAs this is logic+FF
In Flash-based FPGAs it is only FF
Your design

## Slide 26: Architecture for SEE masking
All masking techniques are based on the single-fault assumption (1 SEE = 1 fault in the design)
But
SEE in the configuration memory may produce multiple faults

## Slide 27: An example: original circuit
The bitstream
The original netlist
0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0

## Slide 28: An example: single effect
The bitstream
The corrupted netlist
0 | 1 | 0 | 0 | 0 | 0
* | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
10
An open circuit is created

## Slide 29: An example: multiple effects
The bitstream
The corrupted netlist
0 | 1 | 0 | 0 | 0 | 0
1 | 0 | * | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
01
A short circuit is created

## Slide 30: Why TMR may fail?
The SEE modifies the same signal in two domains  SEE is producing multiple effects not masked by voters
Domain 1
Domain 2
Domain 1
Domain 2
Original netlist
SEE-corrupted netlist

## Slide 31: An example
Design: TMR design (in theory any SEE should be mitigated)
Fault injection in config. mem. (about 20 Mbits)
Resource | Failure
LUT | 71
Global routing | 3,503
CLB Local routing | 53
CLB configuration | 1
Total | 3,628

## Slide 32: What to remember so far
SRAM-/Flash-based FPGAs may be OK for radioactive environments provided that
  Proper device is selected (TID, SEL)
  Design mitigation is used
SEE mitigation is needed  huge costs
  3x FFs, 3x IO, >4x user logic, >20% on clock frequency
Mitigation may fail due to multiple effects of SEE in configuration memory  validation needed

## Slide 33: Outline
Radiation effects in SRAM-/Flash-based FPGAs
Design mitigation issues
Design validation
Conclusions

## Slide 34: Validation approaches
Qualitative validation via design inspection before place & route
Quantitative validation after place & route
  Simulation-based validation
  Emulation-based validation
Main issue in quantitative validation: amount of faults to be simulated
  20 Mbits in config. mem., 1 M functional input vectors @ 100 MHz  about 2.3 days to perform exhaustive fault injection

## Slide 35: Activities @ PdT
# of SEU
# of input vectors
Design-oriented configuration memory analysis
Static analysis
# of SEU
# of input vectors

## Slide 36: Config. mem. analysis
Reverse engineer the configuration memory of FPGA of choice
0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
Configuration bitstream
FPGAs resources
Configuration memory bits layout

## Slide 37: Config. mem. analysis
Read the place & routed design and build the netlist/bitstream association
For each bit of the bitstream:
  Flip the bit and update accordingly the netlist
  Is the original netlist corrupted (does the error arrive to outputs or memory element)?
    Yes  the bit is sensitive
    No  the bit is not sensitive
Analysis is done looking at the error propagation path, and it does not consider workload

## Slide 38: Operational modes
Discovery mode: it analyzes the bitstream while neglecting mitigation schemes
  Lists sensitive bits
TMR mode: it analyzes the bitstream while automatically recognizing (X)TMR mitigation scheme
  Lists bits that violate (X)TMR scheme (domain crossing events)
  List bits that produce warnings (may lead to domain crossing events in case of accumulation)

## Slide 39: Domain crossing events
D1.1
D2.1
D3.1
V1
V1
V1
D1.2
D2.2
D3.2
V2
V2
V2
V3
V3
V3
TMR Domain
Voter Partition

## Slide 40: Domain crossing events
D1.1
D2.1
D3.1
V1
V1
V1
D1.2
D2.2
D3.2
V2
V2
V2
V3
V3
V3
One Single Event Upset (SEU) in the configuration memory provokes two circuit modifications in two TMR domains in the same TMR partition  The fault propagates beyond the voter boundary

## Slide 41: Warnings
D1.1
D2.1
D3.1
V1
V1
V1
D1.2
D2.2
D3.2
V2
V2
V2
V3
V3
V3
One SEE in the configuration memory provokes two circuit modifications in two voter partitions  The fault stops at the voter boundary

## Slide 42: TMR-mode algorithm
The algorithm recognizes automatically TMR domains, voters, and voter partitions
Forward error propagation:
  Find all the paths from the fault site to the circuit outputs, or memory elements
  Is the fault propagating to only one of the voter inputs?
    Yes  the bit is not sensitive
    No  the fault propagates to at least two inputs of a voter in the same partition  the bit is sensitive
V
V

## Slide 43: The report
Detailed report is produced for Xilinx devices
Resource: PIP Block Adr 0 Maj Add 6 Min Add 14 Bit 156
Involved PIP : Y1 -- S2BEG2
FAR: 0x000c1c00 Bit: 156
Net = data_bus_IBUF_TR

## Slide 44: Example
X-TMR LEON3 processor on Xilinx xc2v6000
  20 Mbits in config. mem., 1 M functional input vectors @ 100 MHz
2,603,950 are SEE-sensitive for the design (computed in about 2 hours vs 2.3 days)
3,628 SEUs lead to actual application failure for the considered workload (fault injection completes in about 7 hours)

## Slide 45: Complete design flow
XST synthesis
TMR tool
Input design
Output design
PAR
bitstream
STAR
List of sensitive bits
VPLACE
Robust placement
Robust bitstream
FLIPPER
Workload
Fault coverage
RoRA/PAR

## Slide 46: Outline
Radiation effects in SRAM-based FPGAs
Design mitigation issues
Design validation
Conclusions

## Slide 47: Conclusions
SRAM-/Flash-based FPGAs are very attractive for bringing reconfiguration in radioactive environments
Bullet-proof (i.e., rad-hard) devices are not ready
Solutions are available based on rad-tolerant devices (no TID/no SEL), however
  It is the designer responsibility to implement mitigation
  It is the designer responsibility to validate the mitigation
  Zero failure may not be possible thus estimating residual error rate is mandatory

## Slide 48: Acknowledgment
Monica Alderighi
Niccolò Battezzati
Fabio Casini
Fernanda Lima Kastensmidt
David Merodio Codinachs
Luca Sterpone
Atmel, France
Boeing Satellite Systems, USA
EADS-IW, France
European Space Agency, The Netherland
Thales Alenia Space, Italy