## Slide 1
E.Chiaveri on behalf of the n_TOF Collaboration
Proposal for n_TOF Experimental Area 2 (EAR-2)
CERN-INTC-2012-029

## Slide 2: ITEMS
Why EAR-2
Scientific Motivation
Facility Performance
Dosimetry and Radiation Damage
Radiation Protection Analysis
Civil Engineering & Beam Line Study
Budget, Staff & Tentative planning
Summary

## Slide 3: Study for n_TOF 2nd experimental area
n_TOF target
New experimental area at 19 m (EAR-2)
Experimental area at 185 m
Future EAR-2: flight path ~19 m at 90° with respect to the proton beam

## Slide 4: Why AREA-2?
The main advantages of EAR-2 are:
Neutrons fluxes on average increased by a factor 25
Very small mass samples (< 1 mg)
Very small cross-sections
Much shorter time scales measurement

## Slide 5: Scientific Case for EAR-2
Astrophysical Research
Nuclear Technology Application
Basic Nuclear Research
Examples of EAR-2 Proposals

## Slide 6: EAR-2: Nuclear Astrophysics
important candidates :
79Se, 90Sr, 93Zr, 107Pd, 135Cs, 147Pm, 163Ho,171Tm, 182Hf, 204Tl
very small samples
very small cross sections
important candidates :
86Kr, 88Sr, 138Ba, 140Ce, 208Pb; isotopes of C, O, Ne, Mg
  short measuring times
important candidates :
64Zn, 70Ge, 76Ge, 80,82Kr, 86,87Sr, 95,96Mo, 104Pd, 164,166Er, 198Hg

## Slide 7: EAR-2 Nuclear Technology Application
Important Candidates:
Fission Cross Section :238Pu (87.7 y)/241Pu (14.1 y) 244Cm(18.1 y) 242mAm(141y) 243Cm (29.1y)
Capture Cross Section : 242Am (141 y)/ 243Cm (29.1 y) 231Pa(32400 y)
Higher neutron flux
Very small samples

## Slide 8: Basic Nuclear Research
Higher neutron flux
Shorter time scale
Open the door to dedicated proposals devoted to the investigation of nuclear level and Photon Strength Functions (PSF)

## Slide 9: LIST OF EXAMPLES OF EAR-2 PROPOSALS
Measurement of the 25Mg(n,α)22Ne cross section
Neutron capture measurement of the s-process branching point 79Se
Destruction of the cosmic γ-ray emitter 26Al by neutron induced reactions
Measurement of 7Be(n,p)7Li and 7Be(n,a)4He cross sections, for the cosmological Li problem.
Astrophysical research

## Slide 10: LIST OF EXAMPLES OF EAR-2 PROPOSALS
Cross sections and prompt -ray emission of fissile Pu isotopes
The role of 238Pu and 244Cm in the management of nuclear waste: simultaneous measurements of their capture and fission cross sections
Measurements of (n,xn) reaction cross sections for heavy target nuclei
Fission cross section of the 230Th(n,f) reaction
First measurement of the capture (and fission) cross sections of the fissile 245Cm
Cross section and angular distribution of fragments from neutron-induced fission of 232U
Nuclear Technology Application

## Slide 11: Neutron Fluence
Maximum Gain: 27 (keV Region)
Reference for EAR1 : FLUKA Simulations with fission collimator (d = 8 cm)

## Slide 12: Neutron Fluence Comparison to EAR1
Energy Interval | EAR1 |  | EAR2 |  | Gain
 | [ n / cm2 / pulse ] | Error [%] | [ n / cm2 / pulse ] | Error [%] | 
0.02 – 10 eV | 1.07e5 | 0.2 | 1.64e6 | 2.0 | 15.4
0.01 – 1 keV | 3.98e4 | 0.3 | 1.07e6 | 1.4 | 26.8
1 – 100 keV | 5.02e4 | 0.2 | 1.36e6 | 1.3 | 27.0
0.1 – 10 MeV | 1.76e5 | 0.1 | 3.00e6 | 0.9 | 17.1
10 – 200 MeV | 4.15e4 | 0.3 | 4.78e5 | 2.0 | 11.5
Total Range (0.02 eV – 200 MeV) | 4.14e5 | 0.08 | 7.54e6 | 0.6 | 18.2
Reference for EAR1 : FLUKA Simulations with fission collimator (d = 8 cm)

## Slide 13
25x higher fluence in EAR-2 wrt EAR-1
10x times less alphas/gamma during neutron arrival
250x times higher neutron rate
Neutron rate

## Slide 16: Dosimetry and Radiation Damage Studies
Characterization and calibrations of passive and active dosimeters as well as of detectors.
Test in its stray radiation field the radiation resistance of electronic and structural components as well as of cables
Perform irradiation of various material and electronic devices for dosimetric studies, detector development, radiation damage on electronics

## Slide 17: Dosimetry and Radiation Damage Studies
1 MeV (Si) equivalent neutron fluence rate. This quantity is a measure for displacement damage in (electronic) silicon-based devices. It can be correlated to its long term damage
Ambient dose equivalent (H*(10)) rate. This quantity is of relevance for passive and active dosimeters and radiation monitors

## Slide 18: Neutron Fluence for Irradiation
Neutron Tube has 32 cm diameter
at 1.5 m from the target center
Total: 6.22e1015 n / cm^2 / 7e12 ppp

## Slide 19: Radioprotection Analysis
There are two radiation protection aspects:
Radiation levels in accessible areas induced by the neutron flux between the target and the experimental area
Use of radioactive samples in the form of unsealed sources

## Slide 20: Radioprotection Analysis
Three dimension view of the experimental area as it is implemented in FLUKA for shielding calculations.

## Slide 21: Overview of the n_TOF spallation target area
n_TOF target pit
Technical gallery (@10 m from pit)
EAR2 (@20 m from pit, above ground)
Existing hole
To be built
ISR

## Slide 22: n_TOF EAR-2 surface and underground installations
Additional shielding for an upgrade of the facility for testing electronics components or material tests, which will be done without collimator, can be implemented in a second building stage by adding a base plate around the building and by positioning concrete shielding blocks as a wall around the facility

## Slide 23: Beam line with Permanent magnet
Permanent magnet

## Slide 24: Cost EAR-2

## Slide 25: Cost Ear-2

## Slide 26: Staff EAR-2

## Slide 27: Staff EAR-2

## Slide 28: Planning EAR-2

## Slide 29: EAR-2 Proposal-Conclusion
The n_TOF Collaboration Board in the meeting of Lisbon strongly supports the Proposal for EAR-2

## Slide 30: Summary
The n_TOF facility is already unique in the world in terms of the instantaneous neutron flux and low background
The addition of the EAR-2 with its enhanced capabilities will increase the physics reach of the installation
EAR-2 will open new opportunities in the measurement of neutron-induced reactions with unprecedented accuracy for various important fields of physics:
  nuclear technology, nuclear astrophysics and stellar evolution, basic research, medical applications, dosimetry and radiation damage