## Slide 1: Start of Fill RF MDs in 2012
P. Baudrenghien BE-RF

## Slide 2: Start of Fill (SOF) MD
There is not much we can do in the RF with End of fill: we have high intensity beam and almost full bucket. Playing with this type of beam is not recommended
There are many RF MDs that can be conducted at 450 GeV, with nominal batch injection and nothing changed in the rest of the machine. In that situation a 2-4 hours timeslot with the machine at injection settings could be used very effectively for short SOF MDs
The MD beam would then be dumped and the machine proceeds with physics fill.

## Slide 3: Good candidates SOF RF MDs (1)
Longitudinal stability for batch (RFStabBatch_2012). Only changes with respect to physics fills are the LHC capture voltage, the SPS longitudinal emittance and the filling pattern
Longitudinal blow-up studies (RFBlowUp_2012). At least the batch per batch blow-up at injection (potential reduction of the transverse emittance growth caused by IBS) can be tested with a series of nominal batches injected. (Of course the blow-up in the ramp needs a formal MD)
Longitudinal damper (RFLongDamp_2012) is active at injection only. Must be commissioned with nominal batch at injection.

## Slide 4: Good candidates SOF RF MDs (2)
Voltage modulation around 1 turn (RFVoltageMod_2012). Its final implementation will make it active after the filling is complete. But we must first (MP concerns) test it at injection with 2 or more nominal batches.
RF feedback optimization with circulating beam (RFFdbkOptimWithBeam_2012). Again the first tests should be done with 1 or few nominal batches at injection (MP concerns). Would later be used in ramp and physics also.

## Slide 5: Limits on SOF MD
We must define limits on the accepted deviation from nominal parameters so that it does not take ages to rollback to injection for physics...
I suspect that BT, BI and ADT can also benefit from SOF MDs

## Slide 6: 25 ns MD. RF request
The RF will keep on making observations/adjustments with the 25 ns beam
With the present scheme (constant field over one turn) the beam loading depends on the beam current averaged over ~3 microsec
With 72b batch we do not reach peak value
We want to ramp at least 1 batch with 288 b

## Slide 7: Additional material

## Slide 8: Longitudinal and RF MDs 2012
P. Baudrenghien for the LHC RF team

## Slide 9: Longitudinal studies
Loss of Landau damping during ramp
  Single-bunch, different long. emittances, ramp
  Measurements of longitudinal dipole and quadrupole oscillations. Measurements of transverse emittance evolution in parallel
  6 h
Measurement of longitudinal broad-band impedance
  Single-bunch, different intensities, 450 GeV
  Measurement of dipole and quadrupole oscillation frequencies to derive impedance
  6 h
Longitudinal stability for batch
  Several batches, vary long. emittance/capture voltage, 450 GeV
    Measure damping of dipole oscillations at injection
  Increase cavity impedance at fundamental (reduce fdbk gain)
    Measure the onset of coupled-bunch instabilities
  2 x 8 h
Leftover 2011
Leftover 2011
Road to higher intensity

## Slide 10: Improvements of present operation
Longitudinal blow-up studies
  2 or more equally spaced batches, 144b, ramp
  Alternative longitudinal blow-up & batch per batch blow-up at injection
  2 x 8h
Commissioning of the longitudinal damper acting via the main accelerating cavities
  Batch(es) 144 b, 450 GeV
  2 x 8h
Reduced heating?
Effects of IBS during filling reduced
Reduced capture losses (25 ns)
Damps dipole oscillations at injection? (enough BW?)

## Slide 11: The road to higher intensity
Voltage modulation around one-turn
  Few batches 144b, 450 GeV then ramp
  Modulation of the voltage phase set point at frev to follow transient beam loading and minimize klystron power
  2 x 8h
RF feedback optimization with circulating beam
  Few batches, 450 GeV then ramp
  inject RF noise with zero power spectral density on the Synchrotron Sidebands to measure RF fdbk response (close loop) with circulating beam
  4h
Required to reach nominal current with 25 ns. First test required before LS1
Required for stable operation with nominal current . First test required before LS1

## Slide 12: p-Pb preparation
Commissioning of the p-Pb rephasing using p
  1 batch 32b p in each ring, 450 GeV
  Automate the rephasing to get collisions in the detectors
  2 x 4h
  Best scheduled in the second half of 2012… but at least 2 months before the p-Pb run