## Slide 1: ESS CM Requirements
2.5 GeV Proton 2.86 ms pulse at 14 Hz Availability > 95%
Transfer energy to beam;
Confine proton longitudinally;
Steer proton longitudinally.
 | Length (m) | Input Energy (MeV) | Frequency (MHz) | Geometric β | # of Sections | Temp (K)
RFQ | 4.7 | 75 × 10-3 | 352.2 | -- | 1 | ≈ 300
DTL | 19 | 3 | 352.2 | -- | 3 | ≈ 300
Spoke | 58 | 50 | 352.2 | 0.57 | 14 (2c) | ≈ 2
Low Beta | 108 | 188 | 704.4 | 0.70 | 16 (4c) | ≈ 2
High Beta | 196 | 606 | 704.4 | 0.90 | 15 (8c) | ≈ 2
HEBT | 100 | 2500 | -- | -- | -- | --

## Slide 2: ESS CM Requirements (Criteria, Performance for interfacing to external systems
Operating temperature : 2K
Coupler: 1 MW (ultimate 2 MW)
MAWP He tank / Nb cavity < 6 bar / 2 bar warm
Cavity operating pressure stability ~ 1 mbar
Alignment: better than 0.3%
Use magnetic shielding

## Slide 3: ESS CM Requirements
Radiation Hard Equipment, ALARA
Systems are safe for personal and equipment
Implement Diagnostic instrumentation
Operating cost lower than 108 euro  Limit static heat low to minimize energy consumption
Cooling Architecture  Modularity to optimize Reliability, Availability, Maintainability