## Slide 1: Design of a SHORT Cryomodule for the Superconducting Proton Linac of CERN
IPNOrsay – CNRS
Sébastien ROUSSELOT
Patxi DUTHIL
Patricia DUCHESNE
Philippe DAMBRE
Denis REYNET
CERN
Vittorio PARMA
Arnaud VANDE CRAEN
Paulo AZEVEDO
Lloyd R. WILLIAMS
Ofelia CAPATINA
CEA
Stéphane CHEL
Guillaume DEVANZ

## Slide 2: contents
- Context of the SPL
- =1 cryo-module in a possible SPL layout
=1 cavity layout
2K Heat loads
Segmented configuration, dimensions
- Goal & motivations of the short cryomodule
Goal & motivations
Cryostat specific main objectives
- Cryogenic aspects
Short cryomodule cryogenic scheme
Cooling lines
Filling lines
Coupler cooling lines
- Cavity Supporting System
The supporting system concept
The vacuum vessel/coupler interface
The inter-cavity supporting system
- Short cryomodule layout
- Vacuum vessel design
Constraints
Requirements
Vacuum vessels and tooling concepts
Cold magnetic shielding
Thermal shielding
- Summary

## Slide 3: Context of the spl
CERN’s expected new LHC injection line (former plans)
LP-SPL: Low Power-Superconducting Proton Linac (4 GeV)
PS2: High Energy PS (~ 5 to 50 GeV – 0.3 Hz)
sLHC: “Super-luminosity” LHC (up to 1035 cm-2s-1)

## Slide 4: Goal & motivations of the short cryomodule
General orientation:
Focus on R&D for key technologies for a high-intensity proton source (HP SPL) for a neutrino facility
In particular, for the cryo-module development:
Development, construction and test of β=1 elliptical cavities, 704 MHz
Development, construction and test of RF couplers
Test of a string of 4 β=1 cavities in a machine-type configuration
This program calls for the design and construction of a short cryo-module for testing purposes
CERN’s new scientific strategy: R&D for a High Power SPL (HP-SPL)

## Slide 5: =1 cryo-module in a possible SPL layout
The He vessel includes specific interfaces for the cryomodule integration:
Inter-cavity supports
1 cryogenic feed
External magnetic shielding via cryoperm™ (not shown)
Tooling (in/outside the clean room)
Requirement | Value
β | 1
Frequency | 704.4 MHz
Qo | 5 x 109
Gradient | 25 MV/m
Operat. T | 2 K
=1 cavity layout
CEA cavity design
Cryogenic connection
Reserve port
Stainless steel He vessel
Tooling interface
Tooling interfaces
Tooling interface

## Slide 6
=1 cryo-module in a possible SPL layout
2K Heat Loads (per =1 cavity)
Operating condition | Value | 
Beam current/pulse lenght | 40 mA/0.4 ms beam pulse | 20 mA/0.8 ms beam pulse
cryo duty cycle | 4.11% | 8.22%
quality factor | 10 x 109 | 5 x 109
accelerating field | 25 MV/m | 25 MV/m
Source of Heat Load | Heat Load @ 2K (per cavity) | 
Beam current/pulse lenght | 40 mA/0.4 ms beam pulse | 20 mA/0.8 ms beam pulse
dynamic heat load per cavity | 5.1 W | 20.4 W
static losses | <1 W (tbc) | ~ 1 W (tbc)
power coupler loss at 2 K | <0.2 W | <0.2 W
HOM loss in cavity at 2 K | <1 | <3 W
HOM coupler loss at 2 K (per coupl.) | <0.2 W | <0.2 W
beam loss | 1 W | 1 W
Total @ 2 K | 8.5 W | 25.8 W

## Slide 7: =1 cryo-module in a possible SPL layout
« Segmented » architecture with warm quads and a cryo distribution line
Warm quadrupole
Cryogenic Distribution Line
Jumper
=0.65 cryomodule (3 cavities)
=1 cryomodule (8 cavities)
60 β=0.65 cavities in 20 cryomodules
184 β=1 cavities in 23 cryomodules
SRF linac  500 m long
Heat loads for SPL high-b module
Static load estimated to 2.5 % of total load.
Assessment of static load is of minor importance at this state
(end of conceptual design)

## Slide 8: Goal & motivations of the short cryomodule
  Mechanical design
  Cryogenics (Heat loads, T and P profiles, segmented machine layout)
  Designed for 0%-2% test (for 1.7% expected tunnel slope)
The short cryomodule design strategy
4 cavities less
Test-bench for RF testing on a multi-cavity assembly driven by a single or multiple RF source(s)
Enable RF testing of cavities in horizontal position, housed in machine-type configuration
Validate the design of critical components like RF couplers, tuners, HOM couplers in their real operating environment  short cryomodule design
Goal
Design and construct a ½-lenght cryomodule
for the test of 4 β=1 cavities (instead of 8 in a machine type cryomodule)
in conditions as close as possible to a machine-type cryomodule

## Slide 9: Goal & motivations of the short cryomodule
Cryostat specific main objectives
Learning of the critical assembly phases:
From the assembly of cavities in the clean room to the a cryomodule test
Alignment/assembly procedure
Proof of concept of “2-in-1” RF coupler/cavity supporting:
Fully integrated RF coupler: assembly constraints
Active cooling effect on cavity alignment
Operation issues:
Cool-down/warm-up transients, thermo-mechanics, heat loads
Alignment/position stability of cavities
Cryogenic operations (He filling, level controls, RF coupler support tube cooling)
Cryostat and tooling overview
Technical solutions focus on the ½-lentgh cryomodule
But technical solutions are developed for the full length cryomodule
(Specifically the tooling for the cryostating)

## Slide 10: Cryogenic aspects
Thermal shield (50-75K)
Coupler
cooling
Pumping line
Bi-phase pipe
Cavity top supply
Cavity cooling down lines
Coupler
cooling
Short cryomodule cryogenic scheme
SM18 connexion valves

## Slide 11: Cryogenic aspects
Cooling lines
Requirements: 1 cooling line per cavity
Cavity cooling down lines
Expectation (machine): 1 cooling line for the hole string of cavities ?
Mass flow rate 2.5g/s per cavity

## Slide 12: Cryogenic aspects
Requirements: 1 JT valve may allow for the filling of the first cavity then for the filling of the others via a roman fountain (successive helium fall filling via the diphasic pipe)
Slope : 1.7% (ajustable from 0 to 2% for the tests)
Filling lines
Cavity top supply
Mass flow rate 10g/s

## Slide 13: Cryogenic aspects
Requirements: If slope = 0% or in case of a problem with the roman fountain (superfluid)
1 filling line per cavity (each being equipped with a JT valve)
Slope : (0% for the tests)
Filling lines
(Prototype only:
priority = test bench for a string of 4 cavities)
Cavity top supply
Mass flow rates 2.5g/s per cavity

## Slide 14: Cryogenic aspects
Coupler cooling line
Requirements: One single line for the cooling of the couplers.
4 outlets with 4 control valves @ 300K
1 vaporizer (boiler)
Vaporizer
Outlets
Mass flow rate 0.8g/s

## Slide 15: Cavity Supporting system
Intercavity supports
RF coupler double-walled tube flange fixed to vacuum vessel
The RF coupler (its double-walled tube) provides:
fixed point for each cavity (thermal contractions)
mechanical supporting of each cavity on the vacuum vessel
The intercavity supports provide:
a 2nd vertical support to each cavity (limits vertical self-weight sag)
relative sliding between adjacent cavities along the beam axis
enhancement of the transverse stiffness to the string of cavity
(increases the eigenfrequencies of first modes)
The concept

## Slide 16: Cavity Supporting system
Coupler / Vacuum vessel interface
Interface  fixed point, compensation of the geometrical defaults {coupler + cavity}
Detail designed done
A mock-up is under construction by CERN
To be tested (Q1/2012)
Status:

## Slide 17: Cavity Supporting system
Free space for supports
Inter-cavity supports
Thermal contraction:
Longitudinal
  4.5 mm
Transversal
  1.15 mm
  Max displacement
  of beam axis = 0.6 mm (transient)
   deformation of helium tank
Vertical
  1.2 mm
  Blocked
   deformation of helium tank
Detail designed under progress
A mock-up is under construction by CERN
To be tested (Q1/2012)
Status:
“rigid”{Coupler+cavity}
2 supports

## Slide 18: Vacuum Vessel design
≈6000
≈7000
Constraints
Constraints due to the assembly method of the string of cavities
  Pre-Alignment in the clean room required (interconnection bellows)
  Cavities cleaned and filled with nitrogen (1020mbar)  2 x valves minimum
Impact on the vacuum vessel global size

## Slide 19: Vacuum Vessel design
246
1130
Ø480
Øint1200 min
minimum
Outer part of the coupler disassembled
Constraints due to the supporting System:
  Cavities supported and fixed by the lower flange of the double-wall tube of the coupler
  Size of the power coupler
  Size of the vacuum gauge
Ø600
Coupler Bearing Ports
Impact on the vacuum vessel global size
Constraints
h1500

## Slide 20: Vacuum vessel design
Bearing Ports
Maintenance access ports
Requirements
Access to the tuner, the HOM, without decryostating
Maintenance aspects :

## Slide 21: Vacuum vessel design
Vacuum vessel concepts
Cylindrical vacuum vessel (LHC type)
Bottom aperture
Top apperture
 Horizontal cryostating
 Vertical cryostating
Vacuum vessel with longitudinal aperture

## Slide 22
Horizontal cryostating Tooling Studies
Reference beam path
and rolling frame
Rolling reference tool
Cantilever tooling
Vertical Cryostating Tooling Study
  3 concepts were studied (8 cavities cryomodule)
  Assembly procedure
    dressing of the string of cavities
    alignment
    cryostating
  1 concept was studied (8 cavities)
Vacuum vessel design - Tooling
All tools were compared (for long and short cryomodule)

## Slide 23: Vacuum vessel design
1054
1021
Retained concept
7400
Cylindrical vacuum vessel with long top aperture
Main dimensions
Aperture sealing
Prototype (short cryomodule) : polymer seal placed in a groove / (soft) welding
Machine cryomodule (long) : welding
Aperture concept
e=6mm
e=10mm
Øint800

## Slide 24: Vacuum vessel design
Maximum deflection = 0.65mm
Max sliding between cover and flange = 0.65mm
Mechanical studies
  Static analysis
  Different loading scenarii (linked to the cryostating procedure)
    VV Weight
    VV Weight + loading with the string of cavities
    Vacuum
    Transport
  Buckling (linear) analysis
Construction study
A company was consulted to verify the possibility (and cost) of constructing this vacuum vessel.
NB: The company (CMI) is currently in charge of 3 vacuum vessels (being 9, 10 and 11m long) for spare connection cryostats for the LHC.
 The vessel fulfills mechanical requirements (optimization still needed)
 The vessel seems to be feasible (with a 20% higher cost – 1 unit)

## Slide 25: Cryostat components
Cold magnetic shielding
2 concepts were studied:
Discontinuous shielding:
Continuous shield:
Need to be mounted before the tuner
End cap closures:
- lack of space
- needs of several apertures (tuner supports)
→ solution abandoned
Alternative solution (CERN):
magnetic shield inside the cavity LHe tank
→ difficulty to manufacture the tank
→ solution abandoned
(now for the prototype;
could be studied again
in the future)
Solution retained

## Slide 26: Cryostat components
Thermal shielding
Several concepts were studied (some for a cylindrical vacuum vessel)
Favored solution:
Continuous shield 2 (or 3) main parts
50K
300K
Interfaced on the coupler flange

## Slide 27: Cryostat components
Cryogenic distribution
Diphasic line + filling line + 2K phase separator
One component
Assembled separately outside the clean room
Tightness can be fully tested independently
Mounted on the string of cavities during the dressing phase
Filling lines
Diphasic line 80mm 2K, 31mbar
Coupler cooling line
Cooling line
Coupler cooling line (+boiler)
The line is assembled on the couplers during the dressing phase
The vapor generator (boiler) is integrated in the string of cavities

## Slide 28: Cryostat components
Cryogenic distribution

## Slide 29: SUMMARY
A ½-lenght cryomodule for the full test of 4 β=1 cavities is being design for the CERN
Issued from a collaboration between different institutes, it will be as similar as possible to a machine-type cryomodule for a possible SPL machine
For now:
Cryo-module requirements are settled
Most of the conceptual choices are made (cavity supporting system, cryogenic scheme…)
Conceptual design study is (nearly) over  review: November 4th 2011
Still needing of some conceptual design work (cryogenic jumper connection, thermal shield)
Perspectives:
Detailed design is beginning (mid 2012)
Test of the cryomodule  2014
  http://indico.cern.ch/categoryDisplay.py?categId=1893 ]
SPL on indico:

## Slide 30: Thank you for your attention