## Slide 1: Beams of refractory elements
Laser break-up molecules and ionization
N. Imai, B.A. Marsh, M. A. Czapski, D. Fink, V. Fedosseev,
T.M. Mendonca, S. Rothe, R. Rossel, M. Seｌiverstov, T. Stora

## Slide 2: Refractory elements
melting points ~ 2000 K

## Slide 3: Molecular beams
ZrF3+ @ ORSAY
by isocele2 Z. Phys. A 309, 185 (1982)
HfF3+ @ isolde
NIMB 62(1992)535
SrF 2powder + CF4 gas
3He beam
ZrF3+ was extracted by Plasma ion source
Ta foil + CF4 gas
p beam
HfF3+ was extracted by
Plasma ion source

## Slide 4: Laser-induced breakup + ionization
F
Zr
F
Zr1+
Laser-dissociation
Resonant-ionization

## Slide 5: Feasibility study
Producing ZrF+
Laser radiation of 2 steps:
breaking up molecules,
ionizing Zr
S. Soorkia et al.,
J. Phys. Chem. A, 2011, 115 (34), pp 9620–9632,
TOF spectrum
w/He+ CH3F gas (2%)
ZrF
285nm + 400~470nm
TOF tube
ZrF1+

## Slide 6: Basic parameters
Ionization of Zr : Zr  Zr+ + 1e-
Ionization energy Zr(I)
= 6.63390 eV ~2 x 355nm (3.5 eV)
cross section ~ 4x10-17 cm2 (Fe)
Bonding energy of ZrF : ZrF  Zr +F
= 6.3 eV (!?) ~2 x 355nm (3.5 eV)
cross section ~ 5x10-19cm2 (SF6) !?

## Slide 7: Test with 355nm@ LARIS lab.
Ablation laser
532 nm (2.3 eV)/
1064 nm (1.16 eV)
Pulsed gas flow
Ar
+
CF4 gas
-Top view-
UV laser: 355 nm (3.5 eV)
of Nd/Yag
TOF tube
skimmer
MCP
Zr rod
Valve and lasers are operated with 10 Hz.
Solenoid
valve

## Slide 8: TOF spectrum w/only Ar
90Zr
91Zr
92Zr
94Zr
96Zr
90ZrO
91ZrO
92ZrO
94ZrO
96ZrO
Ablation laser: 355 nm 8 mJ
UV(non-resonant ionization): 355 nm 2.3 mJ

## Slide 9: TOF spectrum w/Ar + CF4(6%)
Large enhancement!
Only Ar
Ar+CF4
Ablation laser: 532 nm 8 mJ
UV(non-resonant ionization): 355 nm 2.3 mJ
ZrO
ZrO + ZrF
Zr
ZrF+ peaks were seen but
disappeared in several
minuets.
Zr+ peaks were enhanced and seemed stable.
We couldn’t distinguish the breakup and ionization effect.

## Slide 10: UV as dissociator and excitator
Confirmation of ZrF
Optimizing enhancement of Zr w/CF4
Chart: 
Pulse height of 90Zr [V]
HV of MCP
-3000  -2800V
CF4 > 6% may be too much.
A few % is enough to enhance the 90Zr.
Time [s]
CF40.2%
@556
CF40.5%
@1061
CF41%
@2635
CF41.5%
@3870
CF4 2.4%
@4138
CF4 3.3%
@4914
CF4 4.3%
@5663
5.8%@6315
CF4 closed
@7730

## Slide 11: Non resonant ionization of Zr
Only Ar
Ar+ CF4(2.4%)
Ablation laser:
1064 nm 3mJ
Dissociation + Ionization:
355 nm 2mJ
Yield of 90Zr+ was enhanced by 1 order of magnitude!

## Slide 12: Mass spectrum
Zr+
ZrO+
No ZrF+ was seen w/Ar +CF4
Ratio of Zr/ZrO doesn’t change so much

## Slide 13: UV (355nm) power dependence
Ar+CF4
Ar only
Only Ar gas flow
Zr  Zr+ : 6.6 eV
2. Ar + CF4 (2.4%) gas flow
Zr  Zr+
and
ZrF  Zr + F
Zr  Zr+
No difference between Ar and Ar+CF4
Breaking-up molecules seems saturated.

## Slide 14: Possible mechanism
ZrF = Zr + F – 6.3 eV
ZrF + CH3 = Zr +CH3F -1.82 eV
ZrF+CF3 = Zr+CF4 -0.83 eV
0.83 eV = 1520 nm
1064 nm Nd:Yag is enough ?
S. Soorkia et al.,
J. Phys. Chem. A, 2010, 114 (18), pp 5655

## Slide 15: On-going works…
Resonant ionization:
1st step 281.4920 nm + 532 nm
= 543218 cm-1
Molecular breakup:
3rd hw (355nm), 2nd hw (532nm), 1064 nm of Nd:Yag
power dependence/time difference will be checked.
Removing of ZrO from Zr rod
Etching the Zr rod with acid prior to ablation
53506.0 cm-1
= 6.6 eV
0 cm-1
I.E.
35514.53 cm-1
= 4.4 eV
4d25s5p t 3F
J=2
4d25s2 a 3F
J=2
281.4920 nm (air)
532 nm
3.5 mJ UV
+ 6mJ 532 nm

## Slide 16: How to implement at ISOLDE?
VADIS + RILIS
  Breaking-up molecule:
VADIS cavity w/several eV ?
or breakup laser ?
  Resonant ionization: RILIS
The resonant ionization scheme hasn’t
been established yet.

## Slide 17: Summary
Feasibility study of breaking-up refractory element fluoride is on-going with ablation + TOF spectrometer of Zr.
In the case of non-resonant ioniztion, with small injection of CF4 in Ar gas, large enhancement of Zr+ peaks were observed.
Both laser for resonant ionization of Zr and break-up molecules are ready.
Further investigation of the phenomenon provides promising experimental opportunity.

## Slide 18: Outlooks
Implementation with VADIS + RILIS
Establishment of resonant-ionization:
hopefully 3 steps-resonant ionization

## Slide 19: La Fin

## Slide 20: Mass spectrum of resonant ionization
In both cases, only Zr peaks
were observed.