## Slide 1: Development of innovative resistive GEM alpha detectors for earthquakes prediction and homeland security
INFN Bari, Bari, Italy
UNAM, Mexico
INFN Padova, Padova, Italy
INFN Frascati, Frascati, Italy

## Slide 2
Haiti Earthquake building damage
Earthquakes are one of the most powerful natural disasters annually taking thousand
of human lives and destroying homes and industrial infrastructures.
Hence the early prediction of earthquakes is a very important task.

## Slide 3: It is known that before an earthquake some precursor phenomena happen: earth surface movements and stress, changes in radio waves propagatio and several others. In the last decade, some studies have shown the possibility to correlate elevated concentrations in the soil of gas Rn, or rapid changes in soil or groundwater radon concentration, to the early prediction of earthquakes
Rn

## Slide 4
Rn accumulation from rocks
Crack or cavity
Ground water
Rn accumulation from rocks
Crack or cavity
Ground water
New cracks
Normal process of accumulation of Rn in
cavities, cracks and ground water
a)
b)
Before the earthquake the soil and rocks
start deforming, cracking and release
Rn accumulated in old cracks, cavities
ground water
Rn
New cracks
Soil
For reliable prediction of the earthquakes one has to take into account and analyze all the precursor phenomena.
INFN Bari and Bari University in close collaboration with other scientific centers over the World are deeply involved in systematic study pre-earthquake phenomena, for example they have a radio station

## Slide 5: To the aim of verifying such studies on a more solid statistical ground one has to create a wide network of cheap, compact and high sensitivity Rn detectors

## Slide 6
Rn accumulation from rocks
Crack or cavity
Drilled well
Our Rn detector
for continuous
monitoring the
Rn level
How the Rn variations can be monitored in field by our detectors?
They should be installed in wells or in cavities and cracks in rocks
Radio antenna
For sending signals
INFN Bari, Bari University and UNAM plan to develop and install a
network of such detectors in the region when weak earthquakes are often happen

## Slide 7: There are of course comemrcial deetctors of Rn:
Scintillators based
Solid-state detectors based
Gaseous ionization chambers
However, their price is too high for this particular application

## Slide 9: In the past we have developed gaseous detectors of Rn exploiting two new features:
1) Gas multiplication
2) Drift of negative ions in air and electron detachment in high electric field
(See for example: G. Charpak et al., NIM A628,2011,187)

## Slide 10
A simple competitor to commercial devices:
Advantages:
simple,
low cost,
robust,
has sufficient sensitivity for
the earthquake application

## Slide 11
1) Results obtained with Am:
Typical signals measured with
a single –wire counter (basic lay-out)
operating in air and irradiated by
241Am source
Mean signal amplitude produced by alpha particles vs. the
voltage applied to detectors having a cathode diameter of 60 mm and different anode wires
Ionization chamber signal
The pulse amplitudes vs. the voltage measures with
a single-wire counter having

## Slide 12
Counting rates vs. the applied voltage measured in
Ar and in air at the same conditions (alpha particles,
D=60mm, da=100 μm)
Efficiency of alpha particles detection is ~100%
Counting rate vs. Vd for alpha particle (blue) and for 60 keV
photons (rose) measured with a basic design of the single
wire counter
Oscillogramm of pulses
produced by 241Am measured
in 100% humid air

## Slide 13
2) Basic studies with 220Rn (Thoron)
High sensitivity can be achieved only if the noise pulses rate is suppressed almost to zero
Typical shape of pulses produced in the single-wire counter by Thoron: a) smooth pulses, b) pulses containing 1-2 peaks
a)
b)
Typical pulse shape of noise pulses
Counting rate vs. time as measured by the single-wire counter in
which air contaminated with Thoron was injected(T0=56sec).

## Slide 14
Distribution of the noise width
and Thoron induced pulses
(Lab View program)
Pulse height spectrum of Thoron
and noise pulses
(Lab View program)
Noise pulses rejection technique:

## Slide 15
Counting rate vs. time after injection into the basic design (at t=2min) air contaminated with 222Rn.
At t=40 min the detector for a few second was flushed with a clean air
3) Measurements with 222Rn
In case of measurements of the
220Rn or 222Rn the air having
traces of these radioactive elements
was introduce in to the detector.
Their concentration was
evaluated from the counting rate
produced by alpha particles.
samples of air containing Rn were
also independently measured by the
experts from the French company
ALGADE

## Slide 16
Long-term measurement performed with the ionization chamber:
the counting rate decrease with a good accuracy corresponds to
the decay of the 222Rn (T0=5500min)
Comparative measurements with a single-wire counter operating at low voltages
( plateau region):
Counting rate vs. time when the radon contaminated
air was introduces (at t=0sec) into the ionization
chamber and at t=40sec it was flushed with clean air.
The fast decrease of the counting rate is mainly due to
the Po decay

## Slide 17
Cathode cylinder
(ss or mesh)
Alpha track
Anode wires
Cathode wires
However, the most efficient suppression of noise pulses was achieved with MWPC
(a copy of Sauli drift tube)
Standard electronics: each anode wire was connected to its own amplifier which after the amplitude discrimination produces
a standard square pulse 1μs long. These pulses were sent in parallel to a simple “majority” unit which generate an output
pulse it there was two or more coinciding input signals. These generated pulses were counted by a standard scaller.
In measurements with alpha particlesonly those event were chosen and counted when two or more wires produce signals within
a few μs gate.
In this design a large fraction
of primary electrons
escaped attachment
R. Bouclier et al., NIM A2521986,393

## Slide 19: The aim of this proposal is to challenge these wire-type detectors and develop simpler, cheaper and even more sensitive Rn detector prototypes based on new designs of resistive GEMs.

## Slide 20: 10x10cm2 RETGEM

## Slide 21: Potential advantages of GEM
Large volume
Simpler
Lower price

## Slide 22
Alpha source
Alpha tracks
Single or double RETGEMs
6 cm
-Vdr
-V1
-V2
Gas vessel
Ar or air
RETGEM-based Rn detectors with large drift region were already preliminary tested

## Slide 23: Print of the LabView screen showing a pulse-height spectrum of alpha particles measured with a single stage RETGEM operating in Ar at a pressure of 1 atm
Pulse-height spectrum of alpha particles measured with a single stage RETGEM operating in air. The voltage across the RETGEM was 3200 V, the thickness of the drift gap 2 cm.
Some preliminary results obtained with a single –step RETGEM

## Slide 24
In air the drift voltage was 2.5kV
Raw data:

## Slide 25
Counting plateau
100% efficiency was easily achieved
Operate stably even in humid air

## Slide 26
Efficiency for alphas detection 100%
-6 kV on the divider
+3.6kV on the bottom
Print of the LabView screen in the case of double
RETGEM operating in air
Efficiency:
ε=Nair/NAr
(practically no spurious
pulses-nair~0)
Nair=NAr

## Slide 27: Security
British authorities as well as other countries are seriously consider developing a monitoring system capable to survey large areas-up to 25 km2
See for example: CLASP call for developing a system for:
“rapid detection and assessment of the severity and spatial extend of radiological
contamination (particularly by alpha and beta emitters) over areas of up to 5x 5km2”, 2011

## Slide 28
Proposed resistive GEMs can be a good option for this task due to their low cost, high sensitivity and the possibility to detect alpha particles from the distance more than 4cm from the examined surface. Moreover, recent test show that GEM detector operating in ambient air is capable to detect beta radiation and soft x-ray radiation

## Slide 29: The work plan, deliverables and the budged
Task | Starting date- ending date | Duration in months
Development special designs of resistive GEMs capable to operate in 100 %humid air | January 3-April 30 | 4
Developing a full prototype | May1-June 30 | 2
Tests at CERN | July 1-October 30 | 4
Tests in Bari University and UNAM | November1_December 30 | 2
Table 2
Institutions- members of the RD51collaboration participating in this project | Contribution from collaborating institutions (kSFr) | Expected contribution from the RD51 common fund (kSFr)
INFN Bari | 1 | 1
UNAM | 3.333 | 3.333
INFN Padova | 2.333 | 2.333
INFN Frascati | 2.333 | 2.333
Table 3.
Material budged | Amount in kSFr | Notes
Development of new R-TGEMs capable t operating in 100% humid air | 4 | In close collaboration with the TE/MPE workshop
Production of these R-TGEM | 2 | TE/MPE workshop
Frontend electronics | 2 | Modification of existing battery feed compact amplifiers
Development of a prototype of a battery feed HV supply | 3 | Bari-CERN
Equipment rent from CERN electronic pool | 1 | 

## Slide 30: Conclusions
1. Preliminary RETGEM looks like an attractive option for the outdoor application such as monitoring of Rn or radio contaminations on large areas
2. The aim of the project is to demonstrate this

## Slide 31: Backup

## Slide 32
222Rn (3.8 days
218Po (3 min)
5,5MeV alpha
2214Pb (26.8min)
6MeV alphas
214Bi (20min)
214Po (165μs)
beta
beta
210Pb (22.3 years)
7.7 alphas
2104Pb (5 days))
beta

## Slide 33
-V
+V
1MΩ
10MΩ
15 MΩ
10MΩ
1MΩ
1MΩ
Alpha source
Alpha tracks
2-6 cm
2-5 mm
RETGEMs
A set up with the resistive chain divider
55Fe

## Slide 34
Commercially available Rn detectors are very expensive ~1000Euro
Atmos 12px