## Slide 1
C-Band, Siwss FEL and SPARC photo injector high power testing summary
Nicholas Shipman
05/09/2012

## Slide 2
In this talk I will attempt to summarise the work of Riccardo Zennaro, Juergen Alex, Alessandro Citterio and others at PSI who have been carrying out high gradient tests on test structures to study.
I will also compare those from the SPARC photo injector energy upgrade structure which can be found in the following paper:-
Design, Fabrication and high power RF test of a C-Band accelerating structure for feasability study of the SPARC photo-injector energy upgrade.
D. Alesinin et. al.
Tiara-conf-WP8-2011-001
Details of the first test structure tested at PSI, which is not presented here, can be found in the following paper:-
Design, construction and power conditioning of the first C-Band test accelerating structure for SWISSFEL.
R. Zennaro et. al.
THPPC024 IPAC 2012
Talk Overview

## Slide 3: Swiss FEL test setup
Klystron:- newly developed, Toshiba E37210, 100Hz, 50MW, 3us
Modulator:- presently equipped with Scandinova K2-2S
No pulse compressor as of yet.
Mode launchers mechanically connected with flanges, RF chokes provide coupling
Full structure will be linearly tapered, 2m long with 113 cells
Test structures are constant impedance with 11 cells.

## Slide 4: SPARC Test setup
High power tested at KEK
SLED style pulse compressor
Final structure will be 1.4m long with 71 cells
Test structure is 0.54m long with 22 cells

## Slide 5: Swiss FEL testing overview
4 test structures have been built.
Structures 1, 2 and 3 have been tested.
Structure 4 has not yet been tested.
Structures 1 and 2 are identical and have large irises
SPARC testing overview
One prototype structure has been tested.

## Slide 6: Comparison of cell geometry
SPARC Cell
Swiss FEL Large Iris
(Test structures 1 and 2)
Swiss FEL Small Iris
(Tests structures 3 and 4)
Geometrically the SPARC Cell and the Swiss FEL large iris cell were quite similar.

## Slide 7: Comparison of parameters
Parameters | Structure 3 Small iris | Structure 2 Large iris | Sparc
a | 5.612 | 7.257 | 7.0
t | 2.5 | 2.5 | 2.5
b [mm] | 21.988 | 22.432 | 21.13
f [GHz] | 5.7124 | 5.7202 | 5.7107
Q(Cu) | 11007 | 11100 | 10260
vg/c [%] | 1.36 | 3.18 | 2.83
r’/Q [kΩ/m] | 8.518 | 7.2 | 7.487
r’ [MΩ/m] | 93.76 | 79.92 | 76.82
Es/Ea | 2.25 | 2.25 | 2.155
Hs/Ea [mA/V] | 2.84 | 2.51 | 2.58
Sc/Ea2 [mA/V] | 0.495 | 0.642 | 0.61
Courtesy of Vasim Khan
With the exception of the cell dimensions these parameters were calculated using HFSS

## Slide 8
Courtesy of Vasim Khan
Swiss FEL large iris
Es/Ea
Hs/Ea
Sc/Ea2
Swiss FEL small iris
Es/Ea
Hs/Ea
Sc/Ea2

## Slide 9
SPARC cell
Courtesy of Vasim Khan
Es/Ea
Hs/Ea
Sc/Ea2
The radius of curvatures used for the PSI structures were a ‘best guess ‘ but the parameters calculated form the simulations closely matched the parameters given.
The geometry for the SPARC cell was exact as given in the paper, the calculated parameters agreed well with the exception of the peak surface field which differed by

## Slide 10: SPARC results
After ~ 1.108 conditioning pulses
Tp = 200ns

## Slide 11: Swiss FEL results
Structure 2 had seen about 7.105 conditioning pulses and structure 3 about 2.106
Before these measurements were taken.

## Slide 12: Comparison of different measurements

## Slide 13: Maximum surface electric and magnetic fields
Es = 250 MV/m or higher has been achieved in several cases: very low or zero group velocity
Waveguide
damped

## Slide 14: Power flow related quantities: Sc and P/C
Sc = 4 - 5 MW/mm2
P/C = 2.3 – 2.9 MW/mm

## Slide 15: Comparison of C-Band design parameters

## Slide 16: PSI Future Plans
Start testing structure 4 in 2 or 3 weeks
Structure 4 has a J-coupler which is the same as the coupler which will be on the output of the full 2m structure.
In November the pulse compressor will be tested.
In February the 2m structure will be tested.