## Slide 1
The 4th Asian Triangle Heavy Ion Conference(ATHIC2012)
2012.11.14~17
RAON
Heavy ion accelerator for
rare isotope science
Sun Kee Kim
Rare Isotope Science Project (RISP)
Institute for Basic Science (IBS)

## Slide 2
RAON
“라온”
a pure Korean word
meaning Delightful, Joyful, Happy,…
“with a wish that this accelerator
would be a delightful gift for scientists
all over the world and for the bright
future of mankind.”

## Slide 3: Brief History
International Science Business Belt(ISBB) plan (2009.1)
Preliminary Design Study (2009.3-2010.2)
Conceptual Design study (2010.3-2011.2)
International Advisory Committee(2011.7)
Institute for Basic Science(IBS) established(2011.11)
Rare Isotope Science Project(RISP) launched(2011.12)
      Rare isotope accelerator complex is the representative facility of IBS
Technical Advisory Committee(2012.5)
Baseline Design Summary (2012.6)
International Advisory Committee(2012.7)
Technical Design (present – 2013.6)

## Slide 4
Location

## Slide 5
Bird Eye View of IBS
Institute for Basic Science

## Slide 6
4. Organizational Structure
4
Auditor
President
Scientific Advisory Board
Secretariats
Office of
Policy Planning
Office of
Research Services
Office of Administrative Services
Research Center
(Headquarters)
Research Center
(Extramural)
Accelerator Institute
(Affiliated Institution)
Board of Directors
Research Center
(Campus)
IBS consists of 50 research centers, supporting organizations, and affiliated research institutes
Each Research Center : ~50 staff, average annual budget ~ 9 M USD
The number of staff: 3,000 (2017, including visiting scientists and students)
Annual Budget: USD 610 million (2017, including operational cost for the Accelerator Institute)
Organization of IBS (Institute for Basic Science)
Rare Isotope Science Project
16 centers were selected so far !

## Slide 7
Organization of RISP
RISP
Director
Advisory Committee
(IAC, TAC, PAC)
Experimental Systems Division
· ISOL Team
· Detector Systems Team
· Application Facility Team
· Beam Physics & Injector Team
· SCL Team
· IF & RF Team
· Cryogenic & Control Team
· Civil Engineering Team
· Conventional Facilities Team
· Nuclear Physics Team
· Particle & Astrophysics Team
Accelerator Systems Division
Theory
Division
· Management & Planning Team
· Research Management Team
· Information & Cooperation Team
Administration
Division
Conventional Facilities
Division
Project Management Group

## Slide 8
Chart: 
| 8 | 6 | 1 | 7 | 20 | 15 | 19 | 16 | 11 | 17 | 12 | 26 | 9 | 30 | 14 | 37 | 38 | 35 | 82 | 29 | 13 | 48 | 58 | 56 | 50 | 53 | 22 | 5 | 34 | 28 | 24 | 25 | 33 | 3 | 80 | 55 | 42 | 32 | 27 | 51 | 47 | 41 | 40 | 57 | 52 | 31 | 39 | 83 | 81 | 49 | 79 | 21 | 73 | 23 | 90 | 92 | 62 | 74 | 4 | 88
 | 65 | 18 | 10 | 3 | 1.4 | 1.1 | 0.25 | 0.25 | 0.15 | 0.15 | 0.05 | 0.006 | 0.0037 | 0.0032 | 0.002 | 0.00046 | 0.00046 | 0.00029 | 0.00017 | 0.0001 | 8.7e-05 | 7.2e-05 | 5.7e-05 | 3.1e-05 | 2.4e-05 | 1.6e-05 | 1.3e-05 | 6.9e-05 | 1.9e-05 | 1.4e-05 | 2.4e-06 | 1.7e-05 | 2.6e-05 | 3.1e-06 | 1.9e-05 | 2.1e-06 | 1.3e-05 | 2.1e-06 | 1.1e-05 | 1e-06 | 0.00016 | 0.0006 | 0.000137 | 1.2e-05 | 1.4e-05 | 2.6e-05 | 1.3e-07 | 5e-09 | 1e-17
Where am I from ?
Origin of elements

## Slide 9
Elemental Abundance in Solar system
Light elements were produced by Big-bang
Heavy elements up to Fe were produced by nuclear fusion in Stars
Elements heavier than Fe were produced by consecutive capture of
neutrons followed by beta decays (in violent astronomical processes
Such as Supernova explosion)
 s-process, r-process  still to be understood!
Origin of elements

## Slide 10
ㅊ
Hendrik Schatz, Physics Today, Nov. 2008, p. 40
To understand the neutron rich isotopes is crucial to explain r-process
Isotope ratio in the solar system
Evidence of r-process
“Our bodies are debris of Supernovae”
Origin of elements

## Slide 11
Origin of elements

## Slide 12
Nuclear Physics
Nuclei with excessive neutrons
New elements
Equation of state of nucleus
Origin of elements
Nucleosythesis
Evolution of stars, neutron stars, supernovae
Nuclear astrophysic
Research area with rare isotopes
Basic data for next generation nuclear reactor
Transmutation of nuclear waste
Nuclear Data - Energy
Atomic trap
Fundamental Symmetries
Atomic/Particle Physics
Application for the society
Pure Science
Material Science
New material development
New method of characterization
-NMR / SR
New medical theraphy
Genetic modification
New isotopes for medical imaging
Bio & medical application

## Slide 13
Bragg Peak of Heavy Ion Beam
Secondary Effect by Alpha Particle
due to Heavy Ion Beam
PET Image by Annihilation
γ
γ
8B
8Be*
4He + 4He
b
8B
Rare Isotope Beam
1
2
3

## Slide 14
RI Beam production
Stopping
Stopped Beam
Experiment
(Traps)
ISOL(Isotope Separator On-Line)
proton  thick target (eg. Uranium Carbide)  spallation or fission of target nuclei(low energy)
RI Ions
Reacceleration
RI Beam
Cyclotron
Proton 70 MeV, 70 kW
IF(In-Flight Fragmentation)
Heavy stable isotope beam  thin target  fragmentation of projectile (high energy)
RI ion beam
Fast Beam
Experiment
Driver LINAC
Heavy ion
e.g. U : 200MeV/u, 400 kW

## Slide 15
High intensity rare isotope beam with ISOL and IF methods
70MeV, 1mA proton beam, 238U target - 70kW ISOL system
200MeV/u, 8.3pμA, 238U beam and other stable isotope beam - 400kW IF system
High current high purity neutron-rich RI beam
For example, 132Sn : ~250MeV/u, ~ 108 pps
- ISOL + acceleration
Production of exotic beams combining ISOL and IF methods
Simultaneous operation of IF and ISOL systems
Accelerator : RAON
Design Consideration for the future
Wide variety of isotope beams
Upgradable to higher energy and higher intensity
World leading RI beam facility for longer term

## Slide 16
Research Field | Theme | Topics | Example reactions Apparatus | Beam | Production
Nuclear Science | Origin of elements/ Stellar Evolution | r-process waiting point | ∙ 123Nb, 124Mo, 125Tc, 126Ru ∙ Decay Station | ∙ primary beam(PB) : 238U - E: 200 AMeV - Intensity: > 1 pμA | ∙ IF
 |  | Contribution of isomer interaction to nucleosynthesis | ∙ 26mAl+p→ 27Si+γ ∙ Recoil Spectrometer | ∙ PB : 28Si ∙ SB : 26mAl - E: < 5 AMeV - Intensy: > 107 pps | ∙ IF
 |  | Escape process to rp-proces | ∙ 15O+α→ 19Ne+γ ∙ Recoil Spectrometer | ∙ PB : p(ISOL), 16O(IF) ∙ SB : 15O - E: < 10 AMeV - Intensity: > 1010 pps | ∙ ISOL ∙ IF
 |  | Superheavy elements | ∙ 64Ni + 238U → 299120 + 3n ∙ SHE spectrometer | ∙ PB: 64Ni - E: < few AMeV - Intensity: > few pμA | ∙ Stable Ion Beam
 | Nuclear structure and Nuclear force | Nuclear structure of rare isotopes with neutron magic number near 126 | ∙ 144Xe + 208Pb →196Yb + X ∙ Decay Station | ∙ SB: 144Xe - E: > 100 AMeV - Intensity: > 106 pps | ∙ ISOL
 |  | Symmetry energy | ∙ 132Sn+119Sn→X+Y ∙ Large Acceptance Spectrometer | ∙ PB:p(ISOL), 238U(IF) ∙ SB: 132Sn - E: 10~250 AMeV - Intensity: > 107 pps | ∙ ISOL (Low E) ∙ IF (High E)
 | Nuclear data | Neutron capture cross section | ∙ p + Be, Li, C ∙ neutron irradiation facility | ∙ PB: p - 70 MeV (p) - 1 kHz ~10 MHz pulse beam | ∙ Cyclotron
Science topics

## Slide 17
Research Field | Theme | Topics | Example reactions Apparatus | Beam | Production
Atomic and Molecular Physic | Mass and spectroscopy of rare isotopes | Study of rare isotopes near neutron Dripline | ∙ medium mass n-rich beam ∙ Atomic trap facility | ∙ PB: p(ISOL), 238U(IF) ∙ SB : 132Sn toward neutron drip line - E: < 60 keV - Intensity: > 1 pps | ∙ ISOL ∙ IF
Material Science | Characterization of new material | Local Electromagneic structure of material | ∙ Low Mass RI beam ∙ β-NMR, β-NQR ∙ μSR spectroscopy | ∙ PB : 8Li, 11Be, 15O, 17Ne, muon - E: < ~10 keV - Intensit: > 108 pps | ∙ ISOL ∙ IF
Bio and Medical Science | Understanding | Biological optimization of heavy ion therapy and on-line imaging of dose of nuclear therapy | ∙ Low Mass RI beam ∙ RI irradiation facility | ∙ SB : 8B, 9C, 11C - E: 200~400 AMeV - Intensity: > 107 pps | ∙ ISOL ∙ IF
Science topics

## Slide 18
80m
IF system
128.5m
70m
Low Energy Experiments
Nuclear Astrophysics
Material Science
β-NMR
Driver Linac
LEBT
ECR-IS (10keV/u, 12 pμA)
RFQ (300keV/u, 9.5 pμA)
MEBT
SCL1 (18.5 MeV/u, 9.5 pμA)
100m
20m
Chg. Stripper
SCL2 (200 MeV/u, 8.3 pμA for U+79)
(600MeV, 660 μA for p)
Post Accelerator
CB : Charge Breeder
HRMS : High Resolution Mass Separator
100m
250m
20m
SCL3
375m
MEBT
100m
ECR-IS
Cyclotron
(p, 70 MeV, 1mA)
ISOL system
Atom/Ion Trap
Gas Catcher
High Energy Experiments
Nuclear Structure/
Symmetry Energy
110m
RF Cooler
RFQ
CB
HRMS
ISOL
Target
μSR, Medical
IF Target
IF Separator
 | Driver Linac |  |  |  | Post Acc. | Cyclotron
Particle | H+ | O+8 | Xe+54 | U+79 | RI beam | proton
Beam energy(MeV/u) | 600 | 320 | 251 | 200 | 18.5 | 70
Beam current(pμA) | 660 | 78 | 11 | 8.3 | - | 1000
Power on target(kW) | 400 | 400 | 400 | 400 | - | 70
Concept of RAON

## Slide 19
80m
IF system
128.5m
70m
Low Energy Experiments
Nuclear Astrophysics
Material Science
β-NMR
Driver Linac
LEBT
ECR-IS (10keV/u, 12 pμA)
RFQ (300keV/u, 9.5 pμA)
MEBT
SCL1 (18.5 MeV/u, 9.5 pμA)
100m
20m
Chg. Stripper
SCL2 (200 MeV/u, 8.3 pμA for U+79)
(600MeV, 660 μA for p)
Post Accelerator
CB : Charge Breeder
HRMS : High Resolution Mass Separator
100m
250m
20m
SCL3
375m
MEBT
100m
ECR-IS
Cyclotron
(p, 70 MeV, 1mA)
ISOL system
Atom/Ion Trap
Gas Catcher
High Energy Experiments
Nuclear Structure/
Symmetry Energy
110m
RF Cooler
RFQ
CB
HRMS
ISOL
Target
μSR, Medical
IF Target
IF Separator
RI Ions
Reacceleration
RI ion beam
Stopping
RI Beam
Fast Beam
Experiment
Stopped Beam
Experiment
(Traps)
Cyclotron
Proton 70 MeV, 70 kW
Driver LINAC
Heavy ion
e.g. U : 200MeV/u, 400 kW
Concept of RAON

## Slide 20
Injector
SCL2
Charge Stripper
Cyclotron
ISOL system
IF system
High Energy
Lab
Low Energy
LAB
SCL1

## Slide 21
Driver Linac - Injector
ECR-IS | 
Ion Source | Proton to Uranium
Energy | 10 keV/u
RF power | 10 kW
Emittance | 0.1π mm-mrad
Current | 400 euA (238U33+, 238U34+)
RF Frequence | 28 GHz
LEBT | 
Beam Energy | 10 keV/u
Particles | 238U33+, 238U34+
Emittance growth | < 10 %
Beam Current | 12 pμA
RF Frequency | 40.625 MHz
RFQ | 
Input energy | 10 keV/u
Output energy | 300 keV/u
Emittance (rms) | 0.12πmm-rad
Frequence | 81.25 MHz
Input charge | 33, 34 (Uranium-238)
Input current | 12 pμA
Output current | 9.5 pμA
MEBT | 
Beam Energy | 300 keV/u
Emittance growth | <10 %
ECR-IS
LEBT
RFQ
MEBT

## Slide 22
Candidate for charge stripper
He Gas Liquid Lithium Solid Carbon
(BNL) (ANL) (MSU)
MEBT
Rebuncher + Quad. Mag.
81.25 MHz
Q = 33+, 34+
Linac-1
QWR : 81.25 MHz, β= 0.047
HWR : 162.5 MHz , β= 0.12
Q = 77+, 78+, 79+ 80+, 81+
Linac-2
SRR1 : 325 MHz , β= 0.30
SRR2 : 325 MHz , β= 0.53
500 keV/u
18.5 MeV/u
400 kW
@200 MeV/u
(for 238U)
Charge state : 33.5+ → 79+
Charge stripper section
Driver Linac SC Linac(SCL)

## Slide 23
Driver Linac SC Linac(SCL)
 | SCL1 |  |  | SCL2 | 
 | Segment 1 | Segment 2 |  | Segment 3 | Segment 4
Injection Energy | 0.3 MeV/u | 2.5 MeV/u |  | 18.5 MeV/u | 70.9 MeV/u
Output Energy | 2.5 MeV/u | 18.5 MeV/u |  | 70.9 MeV/u | 200 MeV/u
Cavity type | beta=0.047 QWR | beta=0.12 HWR |  | Beta = 0.30 SSR | beta = 0.53 SSR
Frequency | 81.25 MHz | 162.5 MHz |  | 325 MHz | 325 MHz
No. of Cavities | 24 | 138 |  | 88 | 136
No. of Cyromodule | 24 | 14 | 16 | 22 | 17
Cavity/Cryomodule | 1 | 3 | 6 | 4 | 8
# QD | 48 | 60 |  | 44 | 34
length | 25.5 | 71.0 |  | 66.0 | 101.8

## Slide 24
Driver Linac SC Linac(SCL)
[1 QWR + 1 QD] x 24
[3 HWR + 1 QD] x 14
[6 HWR + 1 QD] x 16
[4 SSR + 1 QD] x 22
[8 SSR + 1 QD] x 17
beam box example
(courtesy of SPIRAL2)
SCL1
SCL2

## Slide 25
In-flight Fragment Separator
Pre-separator: S-shape
Main separator: C-shape
Max. magnetic rigidity= 9 Tm
Yields at Be target
238U, 200 MeV/u, 400 kW
U92+
132Sn
Distribution at beam dump
Distribution at final focal point
Separator | 
Momentum acceptance | ± 5% (± 3% )*
Angular acceptance | ± 50 mrad (± 40 mrad)*

## Slide 26
ISOL system
Target | 
Type | 70 kW multi-layered fission target
Material/density | UCx / 2.5 g/cm3
fission rate(expected) | 1.3 × 1014 fission/s
132Sn expectation | 2 × 1010 /s
HRMS(High Resolution Mass Separator) | 
Mass Resolution | 45,000
Bρ | 0.33 Tm

## Slide 27
- Design of the experimental facilities in conceptual level
- User training program with the international collaboration
Nuclear Structure
Nuclear Matter
Nuclear Astrophysics
Atomic physics
Nuclear data by fast neutrons
Material science
Medical and Bio sciences
Facilities for the scientific researches
Large Acceptance Multi-Purpose Spectrometer (LAMPS)
Korea Recoil Spectrometer (KRS)
Atom & Ion Trap System
neutron Time-of-Flight (n-ToF)
β-NMR
Reseach Facilty for Heavy Ion Therapy
27
HIgh resolution Detector for Nuclear Structure measurement

## Slide 28
Recoil Spectrometer | 
Maximum magnetic rigidity | ~ 1.5 Tm
Mass resolution (DM/M) | < 0.5 %
Momentum resolution (Dp/p) | ~ 0.05 %
Angular acceptance | ± 100 mrad
Background reduction | < 10-15
Experimental Systems – Recoil Spectrometer
Wien Filter
F0
F1
F2
F3
F4
F5
F6
RI beams
Recoil tagging
Reaction
RI beams
Recoils
Detectors
protons
RI beams
Recoils
Gamma-array
g-rays
n-rich RI beams (A= 80~140) from ISOL
- (d,p) reactions for r-process
Recoil tagging by recoil spectrometer
DE-E telescope array @ F0
Recoil separation with p-rich RI beams from ISOL system
- radiative capture reactions : (p,g), (a,g) reactions
- gamma-array @ F0, recoil detection @ F6
SHE search with SI beams (64Ni, 58Fe)
232Th + 58Fe → 290-x116 + xn, 232Th + 64Ni → 296-x118 + xn
244Pu + 58Fe → 299120 + 3n, 238U + 64Ni → 299120 + 3n

## Slide 29
Large Acceptance Spectrometer | 
Beam | < 250 MeV/u (> 108 pps)
Magnet | SC solenoid (homogeneous 1T magnetic field within ± 70 cm from the center) dipole magnet (Max. B = 6T, rotatable)
TPC | 1x1.2 m2, 3π Sr coverage, GEM Based pad readout
Neutron Detector | 10x10x200 cm3 forward array, 30 cm thick surrounding TPC, energy resolution < 0.1
Si layer | 10 - 30 mm Si strip detectors, 350 mSr coverage
CsI | high energy resolution, 350 mSr coverage
Gamma Detector | energy resolution ~ 10 MeV
Experimental Systems
LAMPS at low-energy exp. hall
(LAMPS-L)
Experimental Observables for Esym
Particle ratios
  n/p, 3H/3He, 7Li/7Be, etc.
  p-/p+
Collective flow
  v1 & v2 of n, p, and heavier clusters
  Azimuthal angle dependence of n/p ratio w.r.t. the R.P.
Pygmy dipole resonance
  Energy spectra of gammas
  Sizes of n-skins for unstable nuclei
Various isospin-dependent phenomena
  Isospin fractionation and isoscaling in nuclear multifragmentation
  Isospin diffusion (transport)

## Slide 30
Conventional Facilities

## Slide 31
Baseline Design Summary (June 2012)
Technical Design Report (by June 2013)
First SCL Module
Start Installation
Ground breaking : 2014
SAR clear : early 2016
Schedule and Major Milestone

## Slide 32
감사합니다
Thank you

## Slide 33: ISOL Yield Estimation
εr
εi
εtrans
εcb
εacc
target
release
ionization
transport
charge breeding
post acc.
Efficiency of each component
Beam Intensity (pps)
Isotope | Half-life | Yield@target (pps) | Overall eff.(%) | Expected Intensity(pps)
78Zn | 1.5 s | 2.19 x 1010 | 0.04 | 1 x 107
90Kr | 32 s | 1.99 x 1012 | 1.00 | 2 x 1010
94Kr | 0.2 s | 1.29 x 1011 | 0.51 | 7 x 108
97Rb | 0.17 s | 1.02 x 1011 | 0.88 | 9 x 108
124Cd | 1.24 s | 4.98 x 1011 | 0.02 | 1 x 108
132Sn | 40 s | 1.95 x 1010 | 0.45 | 8 x 107
133In | 0.18 s | 3.75 x 107 | 0.18 | 7 x 104
142Xe | 1.22 s | 2.84 x 1010 | 2.08 | 6 x 108
144Cs | 1.01 s | 6.01 x 1010 | 0.12 | 7 x 107
* Overall efficiency was estimated using the information from existing ISOL systems.
(HRIBF, CERN-ISOLDE, KEK-ISOL, etc.)

## Slide 34: More Exotic RI Beams
r-process
LISE++ calculation
EPAX2 model
dp/p = 2.23%
Target thickness and beam line parameters are optimized for each nuclide
N =82
N =50
Z = 28
Z =50
Nuclide | Estimated Intensity (pps)
110Y | 1.8
110Zr | 1.8
114Nb | 1.1
116Mo | 3.8
118Tc | 1.4
Reach new n-rich isotope with rates of 10-3 ~ 10 pps
Operational mode: 142Xe(ISOL)  Post-Accelerator  Driver Linac  IF target  Fragment Separator  Experiments
Note that ~103 times larger than 136Xe (350 MeV/u, 10 pnA)+Be