## Slide 1: Overview of CERN 2011 Test
Overview of CERN 2011 Test
神奈川大工，早大理工A，横国大工B，
Univ. of SienaC，INFN FlorenceD，INFN Rome Tor VergataE，NASA GSFCF
田村忠久，鳥居祥二A，片寄祐作B，小澤俊介A，赤池陽水A，
植山良貴A，伊藤大二郎A，苅部樹彦A，近藤慧之輔A，仁井田多絵A，
Pier MarrocchesiC，Paolo MaestroC，Gabriele BigongiariC，Simone BonechiC，
Gianmaria CollazuolC，Oscar AdrianiD，Nicola MoriD，Alessandro GherardiD，
Francesco PalmaE，Cristian De SantisE，Roberta SparvoliE，John William MitchellF

## Slide 2
CAL
Components of CAL
・ CHD （CHarge Detector）
・ IMC （IMaging Calorimeter）
・ TASC （Total AｂSorption Calorimeter）
electron 1 TeV
（Simulation）
Image data
IMC
・SciFi belts (1㎜Sq. SciFi 448)
・XY directions 2belts in one layer
・W boards between 8 layers
（0.2 r.l. ×5 + 1 r.l. ×2）
・SciFi 7168 read out with
112 64ch MaPMT
・MaPMT read out with
VA32HDR14.3（GM-IDEAS）
TASC
・PWO logsof 19×20×326 ㎜3
・16 logs ×12 layers（27 r.l.）
・Readout
1st layer: PMT
2～12 layers: APD/PD
CHD
・Plastic Scintillator
32×450×10 ㎜3
×14 bars×2 layers
・PMT readout

## Slide 3: Set up of detectors for CERN2011
Proto-type of CALET(one directional)
・trigger scintillators
・Si strip detector
4 layers
・CHD
4 SciBar
・IMC
SciFi belts 8 layers
・TASC
PWO 3×12 layers
・Moving table

## Slide 4
Test to take cosmic-ray muon data
with the detectors standing in waseda
IMC
TASC
TASC
FEC

## Slide 6
・Japan（10）: Waseda U. 8、Kanagawa U. 1、YNU 1
・Italy（10）: Siena U. 4、Firenze U. 2、Rome U. 3、 Padoba U. 1
・USA（1）: GSFC 1
21 shifters

## Slide 7
Beam test at CERN-SPS
・2011/9/19～28
・Beam line: T2-H4
・electron/positron（10～290 GeV/c）
・proton（30～350 GeV/c）
・moun（150 GeV/c）
CHD, IMC, TASC
on the moving table
Si strip detector
to determine beam position
Trigger
scintillator
+ PMT
Beam

## Slide 8: Configuration of detectors setup

## Slide 11: Cherenkov Detctor (proton 30 GeV/c)
Cerenkov counter1 [ADC counts]
Cerenkov counter2 [ADC counts]

## Slide 12: HV setting values
MaPMT
  Layers e/p muon
  1,2 : -800 V -800 V
  3,4 : -800 V -800 V
  5,6: -700 V -800 V
  7,8: -600 V -800 V
TASC-PMT
  Top -478 V, Middle: -490 V, Bottom: -470 V
APD
  TASC-FEC1 (Jura): 405 V, TASC-FEC2 (Saleve): 420 V

## Slide 14
Example of event monitor
positron 290 GeV/c
APD(H)
APD(L)
PD(H)
PD(L)
SciFi
IMC
TASC
Beam

## Slide 15: Beam position
BEAM
Center (H:55.94, V:-122.55)
Horizontal: center ± 100 mm (3 points)
Vertical: center + 20 mm (2 points)

## Slide 16: An example of beam profile (Si tracker)
Proton 30GeV （RunNo.288）

## Slide 17
Event Statistics
・Beam position
3 points in horizontal
（center, ±10㎝）
2 points in vertical
（center, +2㎝）
・electron/position
381 k events
・proton
1,950 k events
・muon
230 k events

## Slide 18: Temperature monitor for SPS2011
Data logger (HIOKI Memory HiLogger 8430)
Thermocouple
Position |  | Logger ch
IMC-1 | SciFi Belt | Ch 10
IMC-2 | SciFi Belt | Ch 9
IMC-3 | FEC surface | Ch 8
Environment |  | Ch 6
TASC-1 | PWO 1st | Ch 3
TASC-2 | PWO 6th | Ch 2
TASC-3 | PWO 7th | Ch 1
Environment
TASC-1
IMC-3
IMC-2
IMC-1
TASC-3
TASC-2

## Slide 19: History of temperature during beam test
TASC-3
TASC-2
TASC-1
IMC-3
IMC-2
IMC-1

## Slide 20: Calibration of temperature sensors
Temperature and humidity Chamber
The measurement range 20-30℃, 1℃ step
There is a systematic differential depend on thermocouple type (K and T)
→ Wrong setting of Logger(?)

## Slide 22: Temperature monitor for SPS2011
Normalized by IMC-1
The distribution of measurement less than 2% relatively